3GPP TSG-RAN WG3 #114-e	R3-215862

Online, 01 – 11 Nov, 2021

Agenda Item:	14.1

Source:	Huawei (moderator)

Title:	Summary of Offline Discussion on MRDC1_BLCRs

Document for:	Approval

# Introduction

CB: # MRDC1_BLCRs

- Endorse BL CRs, if agreeable

- Check R3-215106

(HW - moderator)

Summary of offline disc R3-215862

# For the Chairman’s Notes

R3-214631 CPAC BL CR to TS 36.420 (China Telecommunications)				Endorsed

R3-214640 SCG BL CR to TS 36.423 (Nokia, Nokia Shanghai Bell)				Endorsed

R3-214641 SCG BL CR to TS 37.340 (ZTE Corporation)					Endorsed

R3-214642 SCG BL CR to TS 38.401 (Huawei)						Endorsed

R3-214643 SCG BL CR to TS 38.423 (Ericsson)						Endorsed

R3-214644 SCG BL CR to TS 38.473 (Samsung)						Endorsed

R3-214645 CPAC BL CR to TS 36.423 (Nokia, Nokia Shanghai Bell)			Endorsed

Note that please the BL CR rapp include the change “shall stop the timer TDCoverall except for a CPAC request if TXnDCoverall is running.” in next revision after this meeting.

R3-214646 CPAC BL CR to TS 37.340 (Huawei)						Endorsed

Note that please the BL CR rapp change the CPAC related call flows as separate sections if RAN2 decides to do so, after this meeting.

R3-214647 CPAC BL CR to TS38.401 (ZTE)						Endorsed

R3-214648 CPAC BL CR to TS 38.423 (Ericsson)					Endorsed

Note that please the BL CR rapp include the change “shall stop the timer TXnDCoverall except for a CPAC request if TXnDCoverall is running.” in next revision after this meeting.

R3-214649 CPAC BL CR to TS38.463 (Qualcomm)					Endorsed

R3-214650 BLCR to TS 38.473 for Conditional Pscell Change/Addition (CATT)		Endorsed

R3-215106 (TP to 37.340 CPAC BL CR) Correction on MN initiated inter-SN CPC (Huawei)	Merged

To be merged in the BL CR in next version after this meeting without a separate TP.

And for the change of EN-DC part, in case the discussion in AI 14.3 decides to use Data Forwarding Address Indication, BL CR rapp to update the change accordingly when merge the TP.

# Discussion

There are 13 papers submitted in this agenda item, including 12 BL CRs for endorsement, and one TP from the BL CR Rapp to fix an error of the BL CR.

## SCG Baseline CR endorsement

### R3-214641 SCG BL CR to TS 37.340 (ZTE Corporation)

If you have any comment to this BL CR, please input:

| Company | Comment |
| --- | --- |

Moderator Summary: propose to endorse this BL CR.

### R3-214642 SCG BL CR to TS 38.401 (Huawei)

If you have any comment to this BL CR, please input:

| Company | Comment |
| --- | --- |
| Lenovo, Motorola Mobility | Some parts have not been agreed yet, e.g., procedures in E1 interface. |
| ZTE | Agree with Lenovo. It could be better to add some editor’s notes to the contents that have not been agreed. |
| Huawei | No change comparing to the version endorsed from last meeting, and there is a note in each section: Editor’s note: It is FFS if the UP shall be informed about the status of the SCG resources. What should be added? |

Moderator Summary: propose to endorse this BL CR.

### R3-214643 SCG BL CR to TS 38.423 (Ericsson)

If you have any comment to this BL CR, please input:

| Company | Comment |
| --- | --- |

Moderator Summary: propose to endorse this BL CR.

### R3-214640 SCG BL CR to TS 36.423 (Nokia, Nokia Shanghai Bell)

If you have any comment to this BL CR, please input:

| Company | Comment |
| --- | --- |

Moderator Summary: propose to endorse this BL CR.

### R3-214644 SCG BL CR to TS 38.473 (Samsung)

If you have any comment to this BL CR, please input:

| Company | Comment |
| --- | --- |

Moderator Summary: propose to endorse this BL CR.

## CPAC Baseline CR endorsement

### R3-214646 CPAC BL CR to TS 37.340 (Huawei)

If you have any comment to this BL CR, please input:

| Company | Comment |
| --- | --- |
| Lenovo, Motorola Mobility | In the new running CR R2-2110427 prepared by CATT to be agreed in RAN2 meeting, CPA/CPC descriptions are captured separately from the existing text in legacy. Some alignment is needed. |
| Huawei | Agree with Lenovo that if RAN2 changes the way, i.e. have separate sections, RAN3 BL CR can be changed to use the same format, let’s wait for RAN2 endorsement for the running CR, we can try to align RAN3 BL CR this or next meeting, it is not a big issue. |
| E/// | We would say it is not a good practice that the new approach was not adapted from the beginning, especially after companies raised concern in RAN3 about the ambiguity of implementing CPAC in the existing sections. Thanks to the updates in RAN2, RAN3 has time to restructure accordingly. |

Moderator Summary: propose to endorse this BL CR, and after this meeting please the BL CR rapp change the CPAC related call flows as separate sections if RAN2 decides to do so.

### R3-214647 CPAC BL CR to TS38.401 (ZTE)

If you have any comment to this BL CR, please input:

| Company | Comment |
| --- | --- |

Moderator Summary: propose to endorse this BL CR.

### R3-214631CPAC BL CR to TS 36.420 (China Telecommunications)

If you have any comment to this BL CR, please input:

| Company | Comment |
| --- | --- |

Moderator Summary: propose to endorse this BL CR.

### R3-214645 CPAC BL CR to TS 36.423 (Nokia, Nokia Shanghai Bell)

If you have any comment to this BL CR, please input:

| Company | Comment |
| --- | --- |
| Lenovo, Motorola Mobility | In the text below, to avoid confusion, maybe better to remove the second “except for a CPAC request” since the TXnDCoverall is not really running in case of CPAC request “If the en-gNB admits at least one E-RAB, the en-gNB shall start the timer TDCoverall when sending the SGNB ADDITION REQUEST ACKNOWLEDGE message to the MeNB except for a CPAC request. The reception of the SGNB RECONFIGURATION COMPLETE message shall stop the timer TDCoverall except for a CPAC request if TXnDCoverall is running.” |
| ZTE | Not sure for this change, maybe need a separate TP for this change. |
| E/// | An alternative is to remove the change and keep the legacy for this part. Since this is a simple change, no separate TP may be needed. Whenever there is a TP to capture all agreements in TS 36.423, this can be added. |

Moderator Summary: propose to endorse this BL CR, and please the BL CR rapp include the change “shall stop the timer TDCoverall except for a CPAC request if TXnDCoverall is running.” in next revision after this meeting.

### R3-214648 CPAC BL CR to TS 38.423 (Ericsson)

If you have any comment to this BL CR, please input:

| Company | Comment |
| --- | --- |
| Lenovo, Motorola Mobility | In the text below, to avoid confusion, maybe better to remove the second “except for a CPAC request” since the TXnDCoverall is not really running in case of CPAC request “ If the S-NG-RAN node admits at least one PDU session resource, the S-NG-RAN node shall start the timer TXnDCoverall when sending the S-NODE ADDITION REQUEST ACKNOWLEDGE message to the M-NG-RAN node except for a CPAC request. The reception of the S-NODE RECONFIGURATION COMPLETE message shall stop the timer TXnDCoverall except for a CPAC request if TXnDCoverall is running.” |
| ZTE | Not sure for this change, maybe need a separate TP for this change. |
| E/// | Same as above |

Moderator Summary: propose to endorse this BL CR, and please the BL CR rapp include the change “shall stop the timer TXnDCoverall except for a CPAC request if TXnDCoverall is running.” in next revision after this meeting.

### R3-214649 CPAC BL CR to TS38.463 (Qualcomm)

If you have any comment to this BL CR, please input:

| Company | Comment |
| --- | --- |

Moderator Summary: propose to endorse this BL CR.

### R3-214650 BLCR to TS 38.473 for Conditional Pscell Change/Addition (CATT)

If you have any comment to this BL CR, please input:

| Company | Comment |
| --- | --- |

Moderator Summary: propose to endorse this BL CR.

## TP R3-215106 to 37.340 CPAC BL CR

Based on [13], in Current CPAC TS 37.340 BL CR, there is an obvious error in the MN initiated inter-SN CPC, i.e. after the CPC execution, currently it is said that the MN sends SN Release Request towards the source SN to stop providing user data to the UE and start data forwarding, it is incorrect.

For MR-DC, the MN should send Xn-U Address Indication, the TP propose the following change:

10.5.2 MR-DC with 5GC MN initiated SN Change The MN initiated SN change procedure is used to transfer a UE context from the source SN to a target SN and to change the SCG configuration in UE from one SN to another. This procedure can also be used to initiate inter-SN CPC. The Secondary Node Change procedure always involves signalling over MCG SRB towards the UE. //skip the unchanged part 6. If the RRC connection reconfiguration procedure was successful, or the CPC execution procedure is completed, the MN informs the target SN via SN Reconfiguration Complete message with the included SN RRC response message for the target SN, if received from the UE. In inter-SN CPC, the MN sends the SN Release Request message(s), to the other candidate SN(s), if any, for the cancellation of CPC preparation, and the MN sends the Xn-U Address Indication message to the source SN to stop providing user data to the UE and, if applicable, to start data forwarding. 7. If configured with bearers requiring SCG radio resources the UE synchronizes to the target SN.

Do you agree with the proposed change for MR-DC with 5GC part?

| Company | Yes/No | Comment |
| --- | --- | --- |
| Huawei | Yes |  |
| Lenovo, Motorola Mobility | Yes with comment | But MN will send SN Release Request to source SN at some time point? Is it right understanding that MN will send SN Release Request together with Xn-U Address Indication? |
| ZTE | Yes with comment | I share the same view as Lenovo, but according to the step6, it is already captured. However, the change in this TP is not a correction. I wonder if this separate TP is needed or merged into other TPs. |
| Huawei2 |  | To Lenovo: The MN will send SN Release Request to the source SN in step 16 in the existing call flow. To ZTE: It is a correction of the existing BL CR. |
| E/// | ? | The change is not a correction as ZTE said, so it should not be discussed in BL CR. Same as above, whether we need to consider a separate section as for other CPAC sections. |

Moderator Summary: seems all companies are fine for the change after clarification, but some companies think that it should be captured without a TP.

Propose to capture it in the BL CR in next version after this meeting without a separate TP.

For EN-DC, based on previous agreements, in EN-DC, the MN should trigger the new Conditional PSCell Change Notification procedure, and in [7] the corresponding change is provided.

10.5.1 EN-DC The Secondary Node Change procedure is initiated either by MN or SN and used to transfer a UE context from a source SN to a target SN and to change the SCG configuration in UE from one SN to another. In inter-SN CPC, this procedure initiated either by MN or SN is also used to configure CPC configuration. NOTE 1: Inter-RAT SN change procedure with single RRC reconfiguration is not supported in this version of the protocol (i.e. no transition from EN-DC to DC). The Secondary Node Change procedure always involves signalling over MCG SRB towards the UE. MN initiated SN Change //skip the unchanged part 6. If the RRC connection reconfiguration procedure was successful, or the CPC execution procedure is completed, the MN informs the target SN via SgNBReconfigurationComplete message with the encoded NR RRC response message for the target SN, if received from the UE. In inter-SN CPC, the MN sends the SgNB Release Request message(s), to the other candidate SN(s), if any, for the cancellation of CPC preparation, and the MN sends the Conditional PSCell Change Notification message to the source SN to stop providing user data to the UE and, if applicable, to start data forwarding. 7. If configured with bearers requiring SCG radio resources, the UE synchronizes to the target SN.

It is noticed by the moderator that there are several papers submitted in AI14.3 about whether to revert previous agreement on the new X2AP procedure, by reusing X2AP Data Forwarding Address Indication procedure, if it is agreed in AI 14.3 to revert the previous agreement, the MN should trigger the Data Forwarding Address Indication procedure in this part.

Do you agree with the proposed change for EN-DC?

Moderator’s Note: in case the agreement on X2AP new procedure is reverted, it is needed to update the change to “the MN sends the Data Forwarding Address Indication message”

| Company | Yes/No | Comment |
| --- | --- | --- |
| Huawei | Yes | And agree with Moderator’s Note, in such case, this TP needs to be revised. This is a correction to the existing BL CR. |
| Lenovo, Motorola Mobility | Yes |  |
| ZTE | Yes with comment | The change in this TP is not a correction. I wonder if this separate TP is needed or merged into other TPs. |
| E/// | ? | This is not in the scope of BL CR. In principle, if any update is required, but not purely editorial changes, company is invited to provide own TP in the corresponding section. As moderator mentioned, this is related to the discussion under 14.3. |

Moderator Summary: seems all companies are fine for the change after clarification, but some companies think that it should be captured without a TP. One company think it is not in the scope of BL CR seems misunderstand the question.

Propose to capture it in the BL CR in next version after this meeting without a separate TP.

# Conclusion, Recommendations [if needed]

If needed

# References

R3-214631 CPAC BL CR to TS 36.420 (China Telecommunications)	CR0023r3, TS 36.420 v16.0.0, Rel-17, Cat. B

R3-214640 SCG BL CR to TS 36.423 (Nokia, Nokia Shanghai Bell)	CR1609r3, TS 36.423 v16.7.0, Rel-17, Cat. B

R3-214641 SCG BL CR to TS 37.340 (ZTE Corporation)	draftCR

R3-214642 SCG BL CR to TS 38.401 (Huawei)	CR0176r4, TS 38.401 v16.7.0, Rel-17, Cat. B

R3-214643 SCG BL CR to TS 38.423 (Ericsson)	CR0633r3, TS 38.423 v16.7.0, Rel-17, Cat. B

R3-214644 SCG BL CR to TS 38.473 (Samsung)	CR0777r4, TS 38.473 v16.7.0, Rel-17, Cat. B

R3-214645 CPAC BL CR to TS 36.423 (Nokia, Nokia Shanghai Bell)	CR1610r3, TS 36.423 v16.7.0, Rel-17, Cat. B

R3-214646 CPAC BL CR to TS 37.340 (Huawei)	draftCR

R3-214647 CPAC BL CR to TS38.401 (ZTE)	CR0174r5, TS 38.401 v16.7.0, Rel-17, Cat. B

R3-214648 CPAC BL CR to TS 38.423 (Ericsson)	CR0634r3, TS 38.423 v16.7.0, Rel-17, Cat. B

R3-214649 CPAC BL CR to TS38.463 (Qualcomm)	CR0641r1, TS 38.463 v16.7.0, Rel-17, Cat. B

R3-214650 BLCR to TS 38.473 for Conditional Pscell Change/Addition (CATT)	CR0795r3, TS 38.473 v16.7.0, Rel-17, Cat. B

R3-215106 (TP to 37.340 CPAC BL CR) Correction on MN initiated inter-SN CPC (Huawei)