3GPP TSG-RAN WG3 #114	R3-215874

1 - 11 November 2021

Online

Agenda Item:	17.2

Source:	Nokia, Nokia Shanghai Bell - Moderator

Title:	Summary of Offline Discussion – Slicing 2 – Service Continuity

Document for:	Approval

# Introduction

This is the summary document for the following come back:

CB: # RANSlicing2_Service_Continuity

- Check progress in other groups

- Solutions to support service continuity

- Capture agreements and open issues

- Provide CRs if agreeable

- LS to SA5?

(Nok - moderator)

Summary of offline disc R3-215874

# For the Chairman’s Notes

Propose the following:

Agree TP … .

# First Round

According to the Work Item, the scope of RAN3 work for service continuity is mostly to address the case of slice resource shortage.

In the conclusion of the study phase (see [1] for detailed descriptions), 3 solutions had been identified for the work item:

- Multi-Carrier Resource Sharing

- Configuration based solution

- Resource Re-partitioning solution

## Multi-Carrier Resource Sharing Solution

For Multi-Carrier Resource Sharing, all companies seem to converge that it can be supported today already with no stage 3 standards impact.

Q1: do you think that Multi-Carrier Resource Sharing can be supported without standards impact?

| Company | Comment |
| --- | --- |
| Nokia | No stage 3 standards impact foreseen. For stage 2 at least Nokia would foresee some description needed. |

Tdoc R3-214817 asks a question on whether the “other cell” can be outside of the RA (Registration Area). One reason is that the PDU session belongs to a slice which was authorized or “allowed” as per the Allowed NSSAI in the RA, but is this slice also necessarily “allowed” for this UE in the other cell if it does not belong to the RA?

Q2: do you think that the “other cell” as per the Multi-Carrier Resource Sharing description can be outside the current RA (Registration Area) of the UE?

| Company | Comment |
| --- | --- |
| Nokia | We would like to discuss and clarify this point in the stage 2 BL CR for 38.300. |

Moderator’s summary:

Majority of companies think …

Proposal 2: TP...

## Configuration based on Re-partitioning Solutions

New restrictions or Policies?

As a high level summary, the Configuration Based solution and Re-Partitioning Based solution basically consist of using the resources which can be of other slices as reported in the TR 38.332:

But the following needs to be further studied, e.g., for the S-NSSAI 1,

-	it can explicitly use resources belonging to which S-NSSAIs;

-	it can use the dedicated but not used resources of other S-NSSAIs;

-	it can preempt the used prioritized and/or shared resources from other S-NSSAIs.

The first question is whether there should be some new restrictions or policies that govern allowing such usage of resources of other slices. For example, tdoc R3-215541 proposes that new restrictions/policies should be defined and come from 5GC. Tdoc R3-215224 think instead that restrictions and policies already exist and come from O&M (SA5 involvement).

Q3: in your view should there be some new restrictions or policy to govern the slice resource usage and if yes, should they come from 5GC or O&M ?

| Company | Comment |
| --- | --- |
| Nokia | There is no need of new policies. The current policies controlled by O&M according to SA5 model are good enough. The RRM policy ratios can already be controlled via SA5 O&M and this can be done after monitoring the RRM policy resource utilization also at SA5 O&M. |

Allowing use of dedicated pools of other slices?

Referring to SA5 model in TS 28.541, the resources of other slices which could be used temporarily could potentially be in the shared pool (1), in the prioritized pool to which the overloaded slice belongs (2), in a prioritized pool not including the overloaded slice (3).

Some companies propose to extend SA5 model to additionally allow using resources of a dedicated pool of another slice (4).

Q4: what is your view on newly allowing the usage of resources belonging to the dedicated pool of another slice and ask SA5 about it?

| Company | Comment |
| --- | --- |
| Nokia | We are clearly against such extension. This would deny completely the definition of dedicated pool of SA5 and overlap with the already existing concept of prioritized pool. |

Pre-emption Aspects?

Some companies foresee to introduce pre-emption rules across slices. To be defined whether and how this interacts with the exiting QoS framework e.g. interaction with ARP concept.

Q5: what is your view on this pre-emption aspect?

| Company | Comment |
| --- | --- |
| Nokia | We are OK to further investigate and introduce/adapt pre-emption rules taking slicing into account if the impact remains limited. |

New Resource Type(s)?

Some companies foresee that some new measurement types could be reported (e.g. related to transport resources) for the monitoring by O&M in line with the following statement from the TR 38.332:

This solution is applicable to scenario 1. In this solution, the resource limits for a particular slice in the RAN are relaxed (possibly for a limited time period). This is applicable for resource types which have been hard-partitioned between slices, or where a limit per slice has been defined according to the SLA. For example, such an approach could be applied individually (or jointly) to the following:

-	spectrum resource (e.g. slots, beams, carriers etc);

-	transport resources (e.g. backhaul capacity);

-	hardware resources (e.g. specific processors, processing load, intra-RAN logical nodes such as a gNB-CU-UP).

The current resource type in TS 28.415 is:

| resourceType | The resource type of interest for an RRM Policy. allowedValues: PRB, PRB UL, PRB DL (for NRCellDU, GNBDUFunction) RRC connected users (for NRCellCU, GNBCUCPFunction) DRB (for GNBCUUPFunction) See NOTE 2and NOTE 4 |
| --- | --- |

That would presumably also mean that the associated policy control (RRM policy ration) becomes also standardized in SA5. The question is whether new resource types might be needed (e.g. R3-215129)

Q6: what is your view on the need of introducing new resource type(s) to be monitored and asking SA5?

| Company | Comment |
| --- | --- |
| Nokia | So far the existing resource type(s) defined in TS 28.415 seem good enough. The management of other resource types could be left to implementation restrictions and policies without the need of new external measurement reporting and control. |

Pre-emption Aspects?

Some companies are proposing that standards add new reports from gNB to AMF whenever resources of other slices are used (e.g. data volume start/duration/stop in R3-215541). Justification would be mostly for charging reasons.

Q7: what is your view on the need for new reporting signalling from gNB to AMF?

| Company | Comment |
| --- | --- |
| Nokia | There is no need to report to AMF when resources of other slices are used dynamically as this is related to resource usage and not to charging events. The monitoring of resource usage is instead reported to SA5 O&M and that is for potential adjustment of RRM slicing ratios. |

Moderator’s summary:

Majority of companies think …

Proposal 2: TP...

# Second Round

Moderator’s summary:

Majority of companies think …

Proposal 2: TP...

# Conclusion

The following is proposed:

Proposal 1: TP...

# References

TR-38.832, Technical Report: Enhancement of RAN Slicing