3GPP TSG-RAN WG3 #114bis	R3-221003

17 - 26 Jan 2022

Online

Agenda Item:	9.3.4

Source:	CATT - Moderator

Title:	Summary of Offline Discussion – NAS PDU delivery

Document for:	Approval

# Introduction

This is the summary document for the following come back:

CB: # 11_NAS_PDUDelivery

- If the NAS-PDU IE is received for the PDU session, the NG-RAN node shall pass it to the UE regardless of the outcome of the PDU Session Resource Modification?

- The NG-RAN node shall pass the NAS-PDU IE received for the PDU session to the UE when modifying the PDU session configuration. The NG-RAN node does not send the NAS PDUs when all the QoS flows to be added or modified are failed, no QoS flow to be released and no PDU Session Aggregate Maximum Bit Rate is included, even if e.g. the NG-U UP TNL modification is successful?

- The PDU session NAS PDU is sent only when the PDU session management procedure is successful?

- AMF may only update “PDU Session Aggregate Maximum Bit Rate” without impact any DRB related parameters, in this case, PDU level NAS PDU has to be sent to UE. The IE is only not delivery to the UE when all the data flow configured failed which not related to parameter update related to PDU sessions?

- Check group understanding case by case, capture agreements and provide CRs if agreeable

(CATT - moderator)

Summary of offline disc R3-221003

I plan to have two rounds of email discussion. The first round focuses on scenarios and solutions and discuss the potential CRs/LS in the second round. Please provide your views of first round before  00:00 UTC Friday January 21th

# For the Chairman’s Notes

Propose the following:

# First Round

In this meeting, different proposals on how to update the current paragraph on NAS PDU delivery are raised[1][2][3][4][5][6].Before working on solutions, we would like to discuss the behaviour of NG-RAN node/SMF in different scenarios on this issues first.

  - Scenarios

According to [1], there are 3 scenarios on NAS Modification.

Scenario 1: NAS Modification containing parameters transparent to the gNB, i.e. modification of RQI timer.

In this case, obviously, the N1 SM information should always be delivered to UE. Moreover, we think the NAS message could be transferred via Downlink NAS message transfer instead of PDU Session Modification Request message in this scenario.

Proposal 1: The N1 SM information should always be delivered to UE in scenario 1.

Q1:Companies are invited to provide views on above analysis:

| Company | Agree or not | Comments |
| --- | --- | --- |
| Huawei | See comments | The PDU session NAS-PDU contents is transparent to the NG-RAN node. Then the NG-RAN node is not aware of any parameters contained the NAS-PDU (though it can *guess* something based on the other NGAP IEs which is not “trustable”), thus can not easily make such decision. Our view is to have simple NG-RAN node handling of the PDU session-NAS-PDU for the medication case (align with the PDU session setup case) CATT: The case for PDU session setup and PDU session modify is different. For PDU session setup, if the procedure succeeds, it means as least one flow is established which for sure should deliver the NAS-PDU to UE. However, for PDU session modify, if the procedure succeed, it is possible that only TNL address is successful updated while other modification which has related NAS PDU failed.The two procedure is different. |
| Ericsson |  | NAS PDU is transparent. Further, what SMF does with the NAS PDU should not be mixed with what NGAP should do. There are on different layers and we should not break. Comments apply to the below two Qs. |
| CATT | Yes |  |
| CMCC | Agree | If NAS-PDU (which is expected to be NAS-level PDU Session Modify Command) only contains RQI timer, then we agree Proposal 1. |
| Radisys |  | NAS PDU is transparent to NG-RAN. We don’t have to make complex logic in NG-RAN trying to understand what may be there in the NAS PDU. A simple and common rule for NAS PDU delivery should be decided in case of PDU session Modify failure. |
| Nokia | Yes |  |
| ZTE | Agree |  |
| Samsung |  | The answer to this question is Agree. But we also think the contents in NAS PDU should be decoupled with the NG-RAN behavior. |

Scenario 2: NAS Modification containing parameters linked to a modification requested to gNB in the PDU Session Modify request transfer IE e.g. addition/Modification/release of QoS Flow, PDU session AMBR.

For this scenario, we have to check the IEs included in PDU Session Modify request transfer IE. In PDU Session Modify request transfer IE, several kinds of information are included as below:

Type1: IEs which include information that would always be accepted by NG-RAN node and has associated NAS PDU at the same time:

PDU session AMBR, QoS flow to be released.

Type2: IEs that include the information that may be rejected by NG-RAN node

Qos flow to be add/modified

Type3: IEs which include information that would always be accepted by NG-RAN node while has no associated NAS PDU:

UL TNL information, network instance, security indication.

In the following table, we provide analysis on the behavior of NG-RAN node and SMF in different cases:

| The IEs included in PDU Session Resource Modify Response Transfer IE | Is the PDU session modification successfully? i.e. PDU Session Modify response transfer IE is included in the response message instead of PDU Session Modify unsuccessful transfer IE. | Whether NG-RAN node would send the NAS-PDU to UE? | Whether SMF would send another N1 SM information to UE after receive the N2 feedback from NG-RAN node? |
| --- | --- | --- | --- |
| Case1: Only Type 1 IE | Yes | Yes | No |
| Case 2: Only Type 2 IE And the add/modify is completely or partially successful | Yes | Yes | No for completely successful scenario. |
|  |  |  | Yes for partially successful scenario. The SMF would send another PDU Session Modify Command message to do the re-synchronization between UE and network. |
| Case 3: Only Type 2 IE And all the add/modify failed | No | No According to current statement in 38.413,the NG-RAN node would not send the NAS PDU to UE in this case. Another reason is that for UE triggered PDU session modification procedure, the expected feedback in UE side would be either PDU Session Modification Reject message or PDU Session Modification Command message, not both of them. | Yes If the QoS flow addition/modification is triggered by UE, the SMF would send N1 message PDU Session Modification Reject to UE.(see note1) If the modification is triggered by SMF/AF, no message is needed since the modification completely failed and the status in NG-RAN, CN and UE are already aligned. |
| Case 4:Type 1 IE + Type 3 IE | Yes | Yes | No |
| Case 5: Type 2 IE +Type 3 IE And the add/modify is completely or partially successful | Yes | Yes | Same as case 2 |
| Case 6: Type 2 IE +Type 3 IE And all the add/modify failed. | Yes | No | Same as case 3 |
| Case 7:Type 1 + Type 2 And the add/modify is completely or partially successful. | Yes | Yes | Same as case 2 |
| Case 8: Type 1 + Type 2 And all the add/modify failed | Yes | Yes | Yes The SMF need to send another PDU session modify command message to do the re-synchronization i.e.to remove the added flow /revoke the modification included in the previous N1 SM information which is delivered to UE. |

Note 1: This comes from the following statement in 23.502:

If the PDU Session modification is UE triggered and the N2 SM information indicates modification failure, the SMF shall reject the PDU session modification by including a N1 SM container with a PDU Session Modification Reject message (see clause 8.3.3 of TS 24.501 [25]) in the Nsmf_PDUSession_UpdateSMContext Response in step 7b. Step 8 is skipped in this case.

Q2:Companies are invited to provide views on above analysis:

| Company | Agree or not | Comments |
| --- | --- | --- |
| Huawei | See comments | See comments to Q1. Also it seems to us that RAN3 can not give solution based on the possible NAS-PDU contents (even so, it will not be exhaust). Our view is that we need a simple solution for the NG-RAN node, instead of *guessing* the NAS-PDU contents for the NG-RAN to make a decision. Also we are not sure that PDU session AMBR update will be always be successful, e.g., if the calculated UE-AMBR is not acceptable? |
| CATT | Agree |  |
| CMCC | Agree | However, we can expect that whether companies agree or not depends on whether the classification of above-mentioned three types could be accepted. We support such classification because it is reasonable. So the main question is: whether the successful modification on Type3 IEs while unsuccessful modification on Type2 IEs is counted as the case that ‘N2 SM information indicates modification failure’ which leads to different understandings. Our understanding tend to that it is a modification failure, because Type3 IEs have nothing to do with the content of NAS-PDU. Regarding whether Session AMBR will always be updated successful, we tend to agree, because we can only find the following text in 38.413, - If the PDU Session Aggregate Maximum Bit Rate IE is included in the PDU Session Resource Modify Request Transfer IE, the NG-RAN node shall store and use the received PDU Session Aggregate Maximum Bit Rate value when enforcing traffic policing for Non-GBR QoS flows for the concerned UE as specified in TS 23.501 [9]. That is to say, Session AMBR will always be stored upon reception, and the calculation of UE-AMBR is the next step which will not lead to a ‘failure’ to accept Session AMBR. In addition, let’s assume if Session AMBR can be rejected, then we consider a case when QoS flow add/modify are all successful while Session AMBR is modified unsuccessful, how can SMF know Session AMBR is not updated successful? Since PDU session resource modification response/reject do not contain any feedback related to Session AMBR, under such case, the mismatch between SMF and NG-RAN will happen. So our understanding is that Session AMBR will always be updated successful, and we hope it could be a common understanding as the first step. |
| Radisys |  | Same view as HW |
| Nokia |  | Because gNB cannot guess what is in the NAS PDU we need a simple handling such as always transfer the NAS PDU. The NAS DU may contain the RQI timer. |
| ZTE |  | Same view as Huawei |
| Samsung |  | We expect a simple NG-RAN node behavior solution. |

Scenario 3: NAS Modification containing both parameters transparent to the gNB and parameters linked to a modification requested to gNB in the PDU Session Modify request transfer IE.

Obviously, scenario 3 is the combination of scenario 1 and scenario 2.Since in most cases in scenario 2(i.e. case 1,2,4,5,7,8),NG-RAN node would always send the NAS PDU to UE, there is no problem for the combination of scenario 1 and scenario 2 in these cases.

Then we check the combination of case 3/6 in scenario 2 and scenario 1. First, we would like to analyse whether the update of RQ timer would only be included in network request PDU session modification procedure. According to the following statement in 24.501, it seems the update of RQ timer could only be included in network-requested PDU session modification procedure.

If the RQ timer value was received neither in the UE-requested PDU session establishment procedure of the PDU session nor in any network-requested PDU session modification procedure of the PDU session, the default standardized RQ timer value is used.

Observation: If the RQ timer is included in the N1 PDU Session Modification Command message, the NAS modification procedure could only be initiated by network not UE.

Then according to the previous analysis, the NG-RAN node would not send the NAS PDU to UE in case 3/ 6. Considering it is network-requested PDU session modification procedure, the SMF would not send N1 message PDU Session Modification Reject to UE. To make it work, it would send another N1 message PDU Session Modification Command which only include RQ timer to UE considering the previous N1 NAS message is not delivered to UE.

To make scenario 3 work, the behavior of NG-RAN node and SMF in scenario 3 is summarized as below:

|  | Is the PDU session successfully modified?i.e. | Whether NG-RAN node would send the NAS-PDU to UE | Whether SMF would send another N1 SM information to UE |
| --- | --- | --- | --- |
| Scenario 3-1: Combination of scenario 1+case (1,2,4,5,7,8) in scenario 2 | Yes | Yes | Same as what it is in the corresponding case in scenario 2 |
| Scenario 3-2: Combination of scenario 1+ case 3 in scenario 2 | No | No | SMF would send another N1 message PDU Session Modification Command which only include RQ timer to UE considering the previous N1 NAS message is not delivered to UE. |
| Scenario 3-3 Combination of scenario 1+ case 6 in scenario 2 | Yes | No | SMF would send another N1 message PDU Session Modification Command which only include RQ timer to UE considering the previous N1 NAS message is not delivered to UE. |

Q3:Companies are invited to provide views on above analysis:

| Company | Agree or not | Comments |
| --- | --- | --- |
| Huawei |  | See our comments above. |
| CATT | Yes |  |
| CMCC | Agree |  |
| Radisys |  | Same comments as above |
| Samsung |  | See our comments above. |

For the following statement, there are two understandings:

If the PDU Session modification is UE triggered and the N2 SM information indicates modification failure, the SMF shall reject the PDU session modification by including a N1 SM container with a PDU Session Modification Reject message (see clause 8.3.3 of TS 24.501 [25]) in the Nsmf_PDUSession_UpdateSMContext Response in step 7b. Step 8 is skipped in this case.

Understanding 1: SMF would send PDU Session Modification Reject message to UE if SMF found that the UE requested modification on the PDU session is rejected by NG-RAN node no matter other modifications e.g.TNL address update included in the same N2 message succeeds or not.

Understanding 2: SMF would send PDU session Modification Reject message to UE only when all the modification request include in the N2 message failed. In another word, SMF would not send the PDU Session Modification Reject message to UE if SMF found that all the UE requested modification on the PDU session is rejected by NG-RAN node while other modifications without related NAS PDU e.g.TNL address update succeed.

Q4:Companies are invited to provide views on the above two undersantding:

| Company | Which one is your undersantding | Comments |
| --- | --- | --- |
| CATT | Understanding 1 | When the SMF provide N1 feedback on UE trigger N1 message PDU session modification request message, it only care about the UE triggered modification request is accepted or not. |
| CMCC | 1 |  |

3.2 Solutions

3 alternatives are provided in this meeting as below:

Alternative 1: If the NAS-PDU IE is received for the PDU session, the NG-RAN node shall pass it to the UE

For this alternative, obviously, it contradicts with case 3/6 in scenario 2 and scenario 3-2/3-3.

Alternative 2: The NG-RAN node shall pass the NAS-PDU IE received for the PDU session to the UE when modifying the PDU session configuration. The NG-RAN node does not send the NAS PDUs associated to the failed PDU sessions to the UE or If the NAS-PDU IE is received for the PDU session, the NG-RAN node shall pass it to the UE when the NG-RAN reports the PDU Session Resource Modify Response Transfer IE contained in the PDU SESSION RESOURCE MODIFY RESPONSE message in case the concerned PDU session is successfully modified.

For this alternative, obviously, it contradicts with case 6 in scenario 2 and scenario 3-3.

Alternative 3: The NG-RAN node shall pass the NAS-PDU IE received for the PDU session to the UE when modifying the PDU session configuration. The NG-RAN node does not send the NAS PDUs when all the QoS flows to be added or modified are failed, no QoS flow to be released and no PDU Session Aggregate Maximum Bit Rate is included, even if e.g. the NG-U UP TNL modification is successful.

It seems this alternative is aligned with above analysis.

Observation: It seems alternative 3 is aligned with the analysis on scenarios and also the current statement in RAN3 spec and SA2 spec.

However, for this issue, we do acknowledge that the scenarios are complicated and it seems not a best way to always listed all the IEs/cases in the spec as alternative 3 does. With that, we propose the following two options:

Option 1: Adopt alternative 3 and send a LS to SA2/CT1 on the decision in RAN3 and confirm whether the understanding on the behavior of SMF in RAN3 is correct or not, especially in case 3,6,8 of scenario 2 and scenario 3-2/3-3.

Option 2: Adopt alternative 1 which is the cleanest one in RAN side and inform SA2/CT1 to update their spec, e.g. remove the description that If the PDU Session modification is UE triggered and the N2 SM information indicates modification failure, SMF shall reject the PDU session modification by including a N1 SM container with a PDU Session Modification Reject message.in 23.502.

It has to be noted that option 2 is not backward compatible. For example, if a new NG-RAN node with a new version interacts with a SMF of old version, UE would still receive both N1 message PDU Session Modification Command and N1 message PDU Session Modification Reject for the same N1 message PDU Session Modification Request which would cause error inside UE. From this point of view, option 2 seems also not preferable

Companies are invited to provide views on which option is preferred, or any other options:

| Company | Option1 or Option 2 | Any other option? |
| --- | --- | --- |
| Huawei | Neither. | Alternative 2: only when the PDU session modify is successful, the NAS-PDU is delivered. It keeps aligned with the NG-RAN RAN node handling for the NAS-PDU in the PDU session resource setup request message the SMF can directly be aware of the NAS-PDU delivery result upon the PDU Session Resource Modify Response Transfer IE For option 1 (alternative 3): Complicated handling for the NG-RAN node. The NG-RAN will have to decide based on the NGAP IEs to make decision. what if the PDU-session-AMBR modify will be failed. For option 2 (alternative 1): In case of all QoS flows to be added are failed, the NAS-PDU has to be delivered. The NG-RAN will have the different handlings of the NAS-PDU with respect to the PDU session resource setup request message. |
| Ericsson | Alternative 2 should be the way forward. The exact wording need to be discussed. | The key point is that “NAS-PDU” is sent to the UE when the PDU session modification is successful. Otherwise it is not sent. |
| CATT | Prefer alternative 3 but open on all possible solutions |  |
| CMCC |  | We may firstly decide under what cases NAS-PDU should be delivered then to come up with the most appropriate CR. |
| Radisys |  | NAS PDU is sent to UE if PDU session modification is successful, else need not be sent. |
| Nokia | Option 1 |  |
| ZTE | Alternative 1 | It is the most straightforward solution and the mis-match between UE and Network can be handled by Core network. |
| Samsung |  | Let’s firstly conclude on Q1~Q4. Then decide how to make proper CR. |

# Conclusion

The following is proposed:

Proposal 1: TP...

# References

R3-220369 Correction of NAS PDU delivery Nokia, Nokia Shanghai Bell, Orange, Verizon Wireless

R3-220537 Discussion on NAS PDU delivery during PDU session modification procedure  CATT

R3-220613 Discussion on PDU session related NAS-PDU delivery  Ericsson

R3-220681 Correction of PDU session resource modify Huawei, China Unicom, Orange

R3-220871 Discussion on PDU session resource modify CMCC

R3-220958 Correction of NSA PDU Delivery for PDU SESSION RESOURCE MODIFY Procedure ZTE