3GPP TSG-RAN WG3 #114bis-e	R3-221054

Online, 17-26 Jan 2022

Agenda Item:	13.4.1

Source:	Nokia (moderator)

Title:	Summary of Offline Discussion on CB: # 1307_IAB_Res_Multiplex

Document for:	Approval

# Introduction

CB: # 1307_IAB_Res_Multiplex

-Converge on details for Xn signalling

- Should new Xn procedures tackle multiple functions, e.g. exchange of QoS info/BAP parameters, resource configuration

-Converge on details for F1 signalling

-Can it be agreed that no enhancements are needed for time alignment of resource configuration across nodes?

(Nok - moderator)

Summary of offline disc R3-221054

The discussion has two phases:

Phase 1: Identify potentially achievable agreements for online discussion.

Phase 2: TBD

The deadline for Phase 1 is Thursday, Jan 20th, 23:59:59 UTC. This allows the moderator to prepare the proposals on Friday for Monday’s online session.

# For the Chairman’s Notes

Propose to capture the following Agreement:

…

# Phase 1 Discussion

## Issue 1: Resource compatibility between the two parents

In RAN3#112-e, RAN3 send a LS to RAN1 asking for RAN1 feedback on IAB resource multiplexing and 3 options:

For scenario 1 and 2, RAN3 considers the following solutions (other solutions are not precluded) for the resource coordination between the parent link and the child link:

- Option 1: The child node’s gNB-DU cell resource configuration is matched to the parent node’s gNB-DU’s resource configuration.

- Option 2: The parent node’s gNB-DU resource configuration is matched to the child node’s gNB-DU’s resource configuration.

- Option 3: A boundary node should connect only to a new parent with which it has a non-conflicting TDD and H/S/NA pattern beforehand.

For Scenario 2, RAN3 considers the following solutions (other solutions are not precluded) for the coordination between two parent links:

- Option 1: The gNB-DU cell resource configuration of the parent node controlled by the F1-terminating donor of the boundary node, is matched to another parent’s gNB-DU’s resource configuration.

- Option 2: The gNB-DU cell resource configuration of the parent node controlled by the non-F1-terminating donor of the boundary node, is matched to another parent’s gNB-DU’s resource configuration.

- Option 3: The secondary leg of a boundary node is established only towards a secondary parent whose H/S/NA configuration is compatible with the H/S/NA configuration of the master parent beforehand.

RAN1 reply LS ([1]) states:

RAN1 note that Option 1 and Option 2 may cause service interruption to child IAB nodes and associated UEs for network topologies without proper resource coordination and Option 3 is very restrictive.

RAN1 notes that all above options are feasible also for semi-matched configurations, where not all DL and UL slots match, albeit with a reduced performance. Additionally, reconfigurations of the parent and/or child resource configurations can align resource configurations before or during the inter-donor migration procedures and after to further align the migrating node(s) with its new parent node.

Contribution ([1]) and ([5]):

- For Resource coordination between parent link and child link or between parent links, option 1 and option 2 are both supported for the resource coordination.

Q1: Please share your view whether it is acceptable that “option 1 and option 2 are both supported”.

| Company | Comment |
| --- | --- |

Summary:

Suggest following proposal:

Proposal

## Issue 2: F1AP impact

* Whether need enhancement in F1AP messages (F1 SETUP REQUEST, GNB-DU CONFIGURATION UPDATE, GNB-CU CONFIGURATION UPDATE messages).

Contribution ([1]): F1AP messages (F1 SETUP REQUEST, GNB-DU CONFIGURATION UPDATE, GNB-CU CONFIGURATION UPDATE messages) need to be enhanced to include include IAB specific UFD pattern in Intended TDD DL-UL Configuration NR IE, and time/frequency domain HSNA configuration information for CLI management.

* whether use gNB-DU UE F1AP ID to identify the child IAB node

Regarding on how to identify the child IAB node, contribution [1][2][5] propose to use gNB-DU UE F1AP ID.

* Information to be included in F1AP GNB-DU RESOURCE CONFIGURATION message.

Contribution ([1]):

- F1AP GNB-DU RESOURCE CONFIGURATION message needs to be enhanced to transfer parameters for frequency domain multiplexing support, including Rel-17 frequency-domain IAB-DU-Resource-Configuration-H/S/NA-Config, RB Set Configuration, Frequency Domain H/S/NA Configuration Reference SCS.

- Frequency Domain IAB-DU Resource Configuration needs to be added in F1AP message for TDD, FDD UL/DL respectively.

- Frequency information and Carrier List info which indicates the SCS-specific carriers of DU cell needs to be added in the F1AP GNB-DU RESOURCE CONFIGURATION message for the child DU cells so that the parent node could determine the location of each RB set.

- F1AP needs to be enhanced to transfer parent IAB DU’s time domain/frequency domain resource configuration for DC scenario, via GNB-DU RESOURCE CONFIGURATION message.

- The enhancement to the gNB-DU Cell Resource Configuration IE is:

| HSNA Frequency Domain Configuration List |  | 0..1 |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| >Reference Subcarrier Spacing | M |  | ENUMERATED (kHz15, kHz30, kHz60, kHz120, spare3, spare2, spare1, …) | Indicates reference SCS to be applied to HSNA Frequency Domain Configuration Item at a given IAB-DU's cell. |  |  |
| >RB Set Configuration | M |  | ENUMERATED (2, 4, 8, 16, 32, 64,...) | Indicates the RB set size in number of PRBs used for frequency domain H/S/NA configuration of a given IAB-DU's cell, as specified in 38.213. |  |  |
| >HSNA Frequency Domain Configuration Item |  | 1..<maxnoofHSNASlots> |  |  |  |  |
| >>>HSNA Downlink List |  | 1..<maxnoofRBSets> |  |  | - |  |
| >>>>HSNA Downlink | O |  | ENUMERATED (HARD, SOFT, NOTAVAILABLE) | HSNA value for downlink symbols for each RB set in a slot. |  |  |
| >>>HSNA Uplink List |  | 1..<maxnoofRBSets> |  |  | - |  |
| >>>>HSNA Uplink | O |  | ENUMERATED (HARD, SOFT, NOTAVAILABLE) | HSNA value for uplink symbols for each RB set in a slot. |  |  |
| >>>HSNA Flexible List |  | 1..<maxnoofRBSets> |  |  | - |  |
| >>>>HSNA Flexible | O |  | ENUMERATED (HARD, SOFT, NOTAVAILABLE) | HSNA value for flexible symbols for each RB set in a slot. |  |  |

Contribution ([2]):

- Activation Timing IE.  (Moderator’s NOTE:  This will be discussed later once the Xn part is agreed)

- The enhancement to the gNB-DU Cell Resource Configuration IE is:

| HSNA Configuration List |  | 1..<maxnoofRBSets> |  |  | - |  |
| --- | --- | --- | --- | --- | --- | --- |
| >Resource Block Set Index | O |  | INTEGER (1..<maxnoofRBSets>) |  | - |  |
| >Reference SCS | O |  | ENUMERATED (scs15, scs30, scs60, scs120) | Indicates the reference SCS of the cell HSNA configuration. |  |  |
| >HSNA Slot Configuration List |  | 1..<maxnoofHSNASlots> |  |  |  |  |
| >>HSNA Slot Configuration Item |  |  |  |  | - |  |
| >>>HSNA Slot Configuration Index | O |  | INTEGER (1..5120) |  | - |  |
| >>>HSNA Downlink | O |  | ENUMERATED (HARD, SOFT, NOTAVAILABLE) |  | - |  |
| >>>HSNA Uplink | O |  | ENUMERATED (HARD, SOFT, NOTAVAILABLE) |  | - |  |
| >>>HSNA Flexible | O |  | ENUMERATED (HARD, SOFT, NOTAVAILABLE) |  | - |  |

Contribution ([5]):

- The enhancement to the gNB-DU Cell Resource Configuration IE is:

| RB Set Size | O |  | ENUMERATED (2, 4, 8, 16, 32, 64, …) |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| RB Set SCS | O |  | ENUMERATED (scs15, scs30, scs60, scs120, ...) | The values scs15, scs30, scs60 and scs120 corresponds to the sub carrier spacing in TS 38.104 [17]. |  |  |
| IAB HSNA Slot Configuration List |  | 0..1 |  |  |  |  |
| >Link ID Per-link Configuration | O |  | gNB-DU UE F1AP ID | Indicates whether the configuration pertain only for one link. If omitted, the configuration applies to whole DU cell. |  |  |
| >HSNA Slot Configuration Item list |  | 0..1 |  |  |  |  |
| >>HSNA Slot Configuration Item |  | 1..<maxnoofHSNASlots > |  |  |  |  |
| >>>HSNA RB Set Configuration Item |  | 1..<maxnoofRBSets> |  |  |  |  |
| >>>>HSNA Downlink | O |  | ENUMERATED (HARD, SOFT, NOTAVAILABLE) | HSNA value for downlink symbols in a slot. | - |  |
| >>>>HSNA Uplink | O |  | ENUMERATED (HARD, SOFT, NOTAVAILABLE) | HSNA value for uplink symbols in a slot. | - |  |
| >>>>HSNA Flexible | O |  | ENUMERATED (HARD, SOFT, NOTAVAILABLE) | HSNA value for flexible symbols in a slot. | - |  |

Contribution ([6]):

- Extension to Intended TDD DL-UL Configuration IE

- gNB-DU Cell Resource Configuration IE should be extended to include an instance of RB Set Configuration, Frequency-domain HSNA Configuration, Child-specific NA Resource Configuration

- Add Child-node’s Frequency Configuration, parent-node’s resource configuration, and Peer DU Resource Configuration to GNB-DU RESOURCE CONFIGURATION message

Q2: Please share your view on following F1AP aspects:

- Q2-1: Whether need enhancement in F1AP messages (F1 SETUP REQUEST, GNB-DU CONFIGURATION UPDATE, GNB-CU CONFIGURATION UPDATE messages).

- Q2-2: whether use gNB-DU UE F1AP ID to identify the child IAB node

- Q2-3: whether it is agreeable for the Extension to Intended TDD DL-UL Configuration IE in Contribution ([6])

- Q2-4: The information to be included in GNB-DU RESOURCE CONFIGURATION message.

- Q2-5: Information to be included in gNB-DU Cell Resource Configuration IE and preference on IE structure from contribution ([1]), [2] ([5]), or ([6]).

| Company | Comment |
| --- | --- |

Summary:

Suggest following proposal:

Proposal .

## Issue 3: XnAP impact

* whether a new XnAP procedure is needed

Contribution [1]: a new XnAP procedure is introduced, and uses UE-Associated signaling. The XnAP ID is retained after UE Context Release

* whether use same new Xn procedure for the exchange of QoS info/BAP parameters, and for the coordination of resource configuration

Contribution ([3]) propose the new Xn procedure introduced for the exchange of QoS info/BAP parameters is also used for the coordination of resource configuration.

* whether revert previous agreement and only use the new XnAP procedure for resource coordination

Contribution ([2]) propose to revert the previous agreement (as below), and Only use the new XnAP procedure

The F1-terminating donor of the boundary node forwards the boundary IAB node’s resource configuration information to the non-F1-terminating donor, via following XnAP procedures:

- retrieve UE context procedure,

- handover preparation procedure,

- SN addition procedure,

- MN initiated SN modification procedure.

- SN initiated SN modification procedure

* Whether need enhancement in XnAP messages (i.e. XN SETUP REQUEST/RESPONS, NG-RAN NODE CONFIGURATION UPDATE ACKNOWLEDGE message) to include IAB specific UFD pattern in Intended TDD DL-UL Configuration NR IE, and time/frequency domain HSNA configuration information for CLI management.

Contribution [1]: XnAP messages (i.e. XN SETUP REQUEST/RESPONS, NG-RAN NODE CONFIGURATION UPDATE ACKNOWLEDGE message) need to be enhanced to include IAB specific UFD pattern in Intended TDD DL-UL Configuration NR IE.

* Whether need enhancement on Time alignment of resource configurations across nodes

Contribution ([2]): To ensure a synchronous activation of new semi-static resource configurations, the System Frame Number and the Slot Index from which the configuration is valid is added to the XnAP and the F1AP signalling.

Contribution ([3]) ([5]): No enhancements to be made to further improve time alignment of resource configurations across nodes.

NOTE: the impact to F1AP will be discussed later.

* Detailed info to be exchanged over Xn, and the Structure of the IE

Last meeting agreed following info to be exchanged over Xn:

- Activated cell list.

- H/S/NA resource configurations.

- DL/UL resource configurations.

- Multiplexing info.

- Cell specific signal/channel configurations, including at least: SSB information, CORESET 0, and RACH configurations) from/for different parent nodes.

- other higher layer parameters listed in R1-2110573

Contribution ([1]) proposes:

- boundary DU’s cell specific signal/channel configurations needs to be transferred via XnAP messages as well.

- transfer parent IAB DU’s time domain/frequency domain resource configuration for DC scenario, e.g. via SN addition procedure, MN initiated SN modification procedure, SN initiated SN modification procedure.

Contribution ([2]) proposes following:

| IE/Group Name | Presence | Range | IE type and reference | Semantics description | Criticality | Assigned Criticality |
| --- | --- | --- | --- | --- | --- | --- |
| Activated Cells List |  | 0.. 1 |  | List of cells configured in the boundary gNB-DU | YES | reject |
| >Activated Cells Item |  | 1.. <maxnoofServedCellsIAB> |  |  | EACH | reject |
| >>NR CGI | M |  | 9.2.2.7 |  | - |  |
| >>Multiplexing Info | O |  | 9.2.2.b | Contains information on multiplexing with cells configured for collocated IAB-MT. Defined in TS 38.473 [x], section 9.3.1.108. | - |  |
| >>HSNA resource Configurations | M |  | 9.2.2.c | Contains Hard, Soft, N/A information and DL/UL configurations for either TDD or FDD configurations. | - |  |
| >>IAB STC Info | O |  | 9.2.2.d | STC configuration of boundary-node IAB-DU’s cell. Defined in TS 38.473 [x], section 9.3.1.109. | - |  |
| >>RACH Config Common | O |  | OCTET STRING | Corresponds to the rach-ConfigCommon as defined in subclause 6.3.2 of TS 38.331 [8]. | - |  |
| >>RACH Config Common IAB | O |  | OCTET STRING | Corresponds to the IAB-specific rach-ConfigCommonIAB-r16 as defined in subclause 6.3.2 of TS 38.331 [8]. | - |  |
| >>CSI-RS Configuration | O |  | OCTET STRING | Corresponds to the NZP-CSI-RS-Resource as defined in subclause 6.3.2 of TS 38.331 [8]. | - |  |
| >>SR Configuration | O |  | OCTET STRING | Corresponds to the SchedulingRequestResourceConfig as defined in subclause 6.3.2 of TS 38.331 [8]. | - |  |
| >>PDCCH Configuration SIB1 | O |  | OCTET STRING | Corresponds to the PDCCH-ConfigSIB1 as defined in subclause 6.3.2 of TS 38.331 [8]. | - |  |
| >>SCS Common | O |  | OCTET STRING | Corresponds to the subCarrierSpacingCommon as defined in subclause 6.2.2 of TS 38.331 [8]. | - |  |
| Parent gNB-DU Served Cells List |  | 0.. 1 |  | This information is present when a secondary leg for a DC-capable boundary IAB-node is set up. The information pertains to the resources allocated to the boundary IAB-MT on the existing leg. | YES | reject |
| >Parent gNB-DU Served Cells Item |  | 1.. <maxnoofServedCellsIAB> |  |  | EACH | reject |
| >>NR CGI | M |  | 9.2.2.7 |  | - |  |
| >>Multiplexing Info | O |  | 9.2.2.b | Contains information on multiplexing with cells configured for collocated IAB-MT. Defined in TS 38.473 [x], section 9.3.1.108. | - |  |
| >>HSNA resource Configurations | M |  | 9.2.2.c |  | - |  |
| >>IAB STC Info | O |  | 9.2.2.d | STC configuration of boundary-node IAB-DU’s cell. Defined in TS 38.473 [x], section 9.3.1.109. | - |  |
| >>RACH Config Common | O |  | OCTET STRING | Corresponds to the rach-ConfigCommon as defined in subclause 6.3.2 of TS 38.331 [8]. | - |  |
| >>RACH Config Common IAB | O |  | OCTET STRING | Corresponds to the IAB-specific rach-ConfigCommonIAB-r16 as defined in subclause 6.3.2 of TS 38.331 [8]. | - |  |
| >>CSI-RS Configuration | O |  | OCTET STRING | Corresponds to the NZP-CSI-RS-Resource as defined in subclause 6.3.2 of TS 38.331 [8]. | - |  |
| >>SR Configuration | O |  | OCTET STRING | Corresponds to the SchedulingRequestResourceConfig as defined in subclause 6.3.2 of TS 38.331 [8]. | - |  |
| >>PDCCH Configuration SIB1 | O |  | OCTET STRING | Corresponds to the PDCCH-ConfigSIB1 as defined in subclause 6.3.2 of TS 38.331 [8]. | - |  |
| >>SCS Common | O |  | OCTET STRING | Corresponds to the subCarrierSpacingCommon as defined in subclause 6.2.2 of TS 38.331 [8]. | - |  |
| Activation Timing | O |  |  |  | - |  |
| >Activation SFN | M |  | INTEGER(0..1023) | Indicates from which SFN of the receiving node the configuration is valid. | - |  |
| >Activation Slot Index | O |  | INTEGER(0..319) | Indicates from which slot of the indicated SFN of the receiving node the configuration is valid. | - |  |

Contribution ([4]) proposes following:

| Activated Cells List | O | 0..1 |  | List of cells served by the collocated IAB-DU. | YES | ignore |
| --- | --- | --- | --- | --- | --- | --- |
| >Activated Cells List Item |  | 1 .. <maxnoofServedCellsIAB > |  |  | EACH | ignore |
| >>NR CGI | M |  | 9.2.2.7 |  | - |  |
| >>IAB STC-Info | O |  | 9.2.2.x1 | Contains cell SSB Transmission Configuration (STC) information of an IAB-DU or IAB-donor-DU. | - |  |
| >>ControlResourceSetZero | O | INTEGER (0..15) |  | This IE is to configure CORESET#0 of the initial BWP (see TS 38.213 [40], clause 13). | - |  |
| >>RACH Config Common | O |  | OCTET STRING | Corresponds to the rach-ConfigCommon as defined in subclause 6.3.2 of TS 38.331 [10]. | - |  |
| >>RACH Config Common IAB | O |  | OCTET STRING | Corresponds to the IAB-specific rach-ConfigCommonIAB-r16 as defined in subclause 6.3.2 of TS 38.331 [10]. | - |  |
| >>Multiplexing Info | O |  | 9.2.2.x2 | Contains information on multiplexing with cells configured for collocated IAB-MT. | - |  |
| >>RB Sets List | O | 0..1 |  | List of non-overlapping RB sets in a DU cell. |  |  |
| >>>RB Sets List Item |  | ENUMERATED (4,8,16) |  |  | - |  |
| >>>> RB Set Configuration | O |  | 9.2.2.x3 | Contains the information on staring frequency point and the number of PRBs of an RB set | - |  |
| >>>>CHOICE IAB-DU Cell Resource Configuration-Mode-Info | O |  |  |  | - |  |
| >>>>>TDD |  |  |  |  | - |  |
| >>>>>>TDD Info |  | 1 |  |  | - |  |
| >>>>>>>gNB-DU Cell Resource Configuration-TDD | M |  | gNB-DU Cell Resource Configuration 9.2.2.x4 | Contains TDD resource configuration of gNB-DU’s cell. | - |  |
| >>>>>FDD |  |  |  |  | - |  |
| >>>>>>FDD Info |  | 1 |  |  | - |  |
| >>>>>>>gNB-DU Cell Resource Configuration-FDD-UL | M |  | gNB-DU Cell Resource Configuration 9.2.2.x4 | Contains FDD UL resource configuration of gNB-DU’s cell. | - |  |
| >>>>>>> gNB-DU Cell Resource Configuration-FDD-DL | M |  | gNB-DU Cell Resource Configuration 9.2.2.x4 | Contains FDD DL resource configuration of gNB-DU’s cell. | - |  |

Contribution ([6]):

- Add Peer DU Resource Configuration in Served Cell Information NR IE

Q3: Please share your view on following XnAP aspects:

- Q3-1: whether a new XnAP procedure is needed

- Q3-2: whether use same new Xn procedure for the exchange of QoS info/BAP parameters, and for the coordination of resource configuration

- Q3-3: whether revert previous agreement and only use the new XnAP procedure for resource coordination

- Q3-4: Whether need enhancement in XnAP messages (i.e. XN SETUP REQUEST/RESPONS, NG-RAN NODE CONFIGURATION UPDATE ACKNOWLEDGE message) to include IAB specific UFD pattern in Intended TDD DL-UL Configuration NR IE, and time/frequency domain HSNA configuration information for CLI management.

- Q3-5: Whether need enhancement on Time alignment of resource configurations across nodes

- Q3-6: Detailed info to be exchanged over Xn, and preference on IE structure from contribution [2], [4], ([6]).

| Company | Comment |
| --- | --- |

Summary:

Suggest following proposal:

Proposal .

## Any other issues

| Company | Comment |
| --- | --- |

# Phase 2 Discussion

# Conclusion, Recommendations

# References

R3-220142, Discussion on resource multiplexing in IAB (ZTE)

R3-220166, (TP for IAB BL CR for TS 38.423 and TS 38.473) Inter-Donor Resource Coordination in IAB Networks (Ericsson)

R3-220297, IAB multiplexing enhancements (Qualcomm Incorporated)

R3-220805, (TP for NR_IAB_enh BL CR for TS 38.423) IAB resource multiplexing (Huawei)

R3-220825, (TP for BL CR for TS 38.473) Resource multiplexing (Nokia, Nokia Shanghai Bell)

R3-220590, PHY layer configurations for Rel-17 IAB (Qualcomm Incorporated)