3GPP TSG-RAN WG3 #114bis-e							 R3-221008

17-26 January 2022

Online

Agenda Item:	30.1

Source:	ZTE (moderator)

Title:	Summary_of_offline_disc_CB # 16_IoToverNTN

Document for:	Approval

# Introduction

This contribution is to kick off the following discussion.

CB: # 16_IoToverNTN - Check the LS from other groups and focus on WID scope - Taking the NR NTN as the baseline, identify RAN3 related issues and discuss the corresponding solutions - LS to SA2? - Capture agreements and open issues - Provide stage2/3 BL CRs if agreeable, split work (ZTE - moderator) Summary of offline disc R3-221008

For the first round, we focus on the technical issues of this WI and try to reach some agreements. The deadline is Wednesday, January 19th, 07:00am UTC.

For the second round, we focus on the work split on BL CRs, the LS to SA2/RAN2 and any other left issue in the first round. The deadline is Monday, January 24th, 13:00 UTC.

# For the Chairman’s Notes

<TBD>

# Discussion - Second Round

<TBD>

# Discussion - First Round

## Issue 1: Clarification on LS

Two LSs on EPS support for IoT NTN has been received from CT1 and SA2 in [1] and [2] respectively.

For the LS from CT1, as no issue is identified, there is no need to reply the LS from CT1.

For the LS from SA2, regarding the multiple TAC reporting issue, we should wait for the progress in NR NTN WI, therefore, no reply LS to SA2 is needed in this meeting.

The following proposal could be taken into consideration:

Proposal 1: There is no need to reply the LSs from CT1 and SA2.

Question 1: What’s your opinion on the LS from CT1 and SA2, do you agree with the above proposal?

| Company | Agree or Disagree | Comment |
| --- | --- | --- |
| ZTE | Agree |  |
| Ericsson | Agree |  |
| Qualcomm | Agree | Although multiple TAC reporting seems not be in [2], this is confusing; simply note this for follow up in next meeting; for now focus on the actual content of [2] |
| Huawei | Agree | With regard to the LS from CT1 and SA2, there is no need to respond. |
| Nokia | Agree |  |

Moderator’s summary:

<TBD>

## Issue 2: Mapped cell identity used for ULI, Paging Optimization, AoI and PWS

In [3], [4] and [5], the CGI mapping on ULI, Paging Optimization AoI and PWS has been raised. As shown in [6] and [7], the AoI could be removed out of the description.

According to TS 36.331, the PWS and handover are not supported in NB-IoT, therefore, an Editor’s Note should be added in the description, e.g. Editor’s Note: PWS and handover procedures are not supported for NB-IoT UEs, and this part could be revised.

Considering the ULI, as discussed in [3], the UE using CP CIoT EPS optimization only cannot provide the fine UE location information to eNB, and the current description of the CGI indicated as part of ULI is not precise. However, this issue should be further checked by SA2. A similar concern is also provided in [8].

The following proposals could be taken into consideration:

Proposal 2: Add an Editor’s Note to indicate the PWS and handover are not supported for NB-IoT UEs in the 36.300.

Proposal 3: Whether the UE using CP CIoT EPS optimization only can provide the fine UE location information to eNB should be checked by SA2.

Question 2: What’s your opinion on the description of the mapped cell identity, do you agree with the above proposals?

| Company | Agree or Disagree | Comment |
| --- | --- | --- |
| ZTE | Agree |  |
| Ericsson | Disagree with p2; agree with p3 | On p2: Sec. 4.10 of TS 36.300 already lists the functions not applicable for NB-IoT UEs; no need to capture this again. On p3: already covered in our draft LSout (0398). |
| Qualcomm | P3 ok P2 seems not needed | As per Ericsson’s comments. |
| Huawei | Partly agree | 1. No strong view on whether P2 is needed. But since AoI is also not supported, if the Editor’s Note will be added, why not add AoI as well? Just like PWS and handover procedures. Or does it mean both NB-IoT and eMTC not support AoI? 2. For Proposal 3, it definitely has impact to SA2, but RAN3 should also discuss it as RAN3 should be responsible for ULI report and mapping. LS to SA2 is already provided. In addition, as mentioned in [8], we may need LS to RAN2 asking whether coarse location can be obtained. |
| Nokia | See comments | P2: No. There maybe no need to add the EN, since 36.300 Section 4.10 describes all functions (including PWS, HO, etc) not applicable to NB-IOT. BTW, all EN should be removed in the final agreed CR. P3: ok. It is in 0398. |

Moderator’s summary:

<TBD>

## Issue 3: Switch-over

In both [6] and [7], the Switch-over has been introduced, while, as discussed in Issue 2, the handover is not supported for NB-IoT, an Editor’s Note should be also added in the corresponding description in the 36.300, e.g. Editor’s Note: The NB-IoT UEs should be excluded for this feature, and this part could be revised.

The following proposal could be taken into consideration:

Proposal 4: Add an Editor’s Note to indicate the NB-IoT UEs should be excluded for the Switch-over procedure in the 36.300.

Question 3: What’s your opinion on the description of the Switch-over, do you agree with the above proposal?

| Company | Agree or Disagree | Comment |
| --- | --- | --- |
| ZTE | Agree |  |
| Ericsson | Disagree | Given that switchover relies on mobility, mobility is clearly not applicable to NB-IoT UEs, and this is already captured in current TS 36.300 (see our answer to the above question), there’s no need for a dedicated editor’s note. |
| Qualcomm | Also sort of disagree | It does seem redundant, however maybe it is ok to have a note stating that since switch-over relies on mobility procedure, it does not apply for NB-IOT. |
| Huawei |  | One question: Does no handover strictly equal to no switch-over? Switch-over happens for feeder links, even UE itself not support handover, satellite can still move and change gateway right? |
| Nokia | Disagree | Refer to comments on P2. We prefer to use normative text rather EN. Please refer to the following text from R3-220409 [6] For BL UEs and UEs in enhanced coverage, the transfer of the affected UE(s) context between the two eNBs at feeder link switch over is performed by means of either S1 based or X2 based handover… Similar style should be used in other sections when there is a need. |

Moderator’s summary:

<TBD>

## Issue 4: Clarification on country-specific routing

In both [6] and [7], the NNSF has been introduced, and the corresponding stage 2 description over S1 is also given in [9] and [10].

As indicated in Issue 2, the handover is not supported for NB-IoT, an Editor’s Note should be also added in the corresponding description in the 36.300, e.g. Editor’s Note: The NB-IoT UEs should be excluded for this function, and this part could be revised.

In [11], [12] and [13], the IE agreed in NR NTN WI (i.e. UE Context Reference at Source) for target eNB to identify an existing UE could be reused in IoT over NTN WI. And the naming of the corresponding IE should be decided among the three options, including UE Context Reference at Source, UE Context Reference at eNB and UE Context Kept at Source. As the UE Context Reference at Source IE has already been introduced over S1 for inter-system handover from gNB with direct forwarding, the name of this IE cannot be reused directly. While, for the two remaining names, it depends on companies’ preference.

In [11], the LTE-M satellite indication is added in the UE CAPABILITY INFO INDICATION message, as the eNB is able to be aware of the LTE-M UE is access via the NTN cell or TN cell, therefore, the existing LTE-M indication seems to be enough, there is no need to introduce the LTE-M Satellite Indication. And the necessity of the IE should be further evaluated.

The following proposals could be taken into consideration:

Proposal 5: Add an Editor’s Note to indicate the NB-IoT UEs should be excluded in NNSF function in the 36.300.

Proposal 6: The IE for target eNB to identify an existing UE should be reused over S1 with a new name.

Proposal 7: The necessity of the LTE-M satellite indication should be further evaluated.

Question 4: What’s your opinion on the issues related to country-specific routing, do you agree with the above proposals?

| Company | Agree or Disagree | Comment |
| --- | --- | --- |
| ZTE | Agree |  |
| Ericsson | Disagree with p5, p7; partially agree with p6 | On p5: no need for an editor’s note on NNSF (see our replies to the above questions) On p6: The IE is definitely needed, but it’s unclear to us why it should be renamed. We prefer to maintain the same name, since the function is the same as its NR NTN counterpart. On p7: SA2 agreed to have such a dedicated “LTE-M satellite indication” from the RAN. Yes, we assume the contents will be the same as the terrestrial equivalent (to be checked with RAN2 and covered by our draft LS). |
| Qualcomm | See text | P5 – see no need for this: it would be nice if I could easily correlate where this proposal comes from P6 – ok, and stay with NTN terminology please P7 – first this is agreed by SA2, second access in reduced bandwidth resources is not the same as the UE being cat M. So there is nothing to evaluate, just details of how to do it. |
| Huawei | See text | P5: Why exclude NB-IoT from NNSF? I think we still need to figure out a method trying to make sure NB-IoT UE choose the correct AMF. P6：Same concern as Ericsson P7: We tend to prefer adding the LTE-M satellite indication. |
| Nokia | See comments | P5: this is not correct. Why should the NB-IOT UE be excluded in NNSF? P6: why need a new name? regarding the concern with inter-system HO, it may not be an issue. Current text is In case of inter-system handover from gNB with direct forwarding, if the target eNB receives the UE Context Reference at Source IE in the Source eNB to Target eNB Transparent Container IE, it may use it for internal forwarding as specified in TS 37.340 [47]. In our case, new text may be added. P7: ok. We prefer to add it, but can wait for RAN2 decision |

Moderator’s summary:

<TBD>

## Issue 5: Identification and restriction of satellite access

In [11]-[16], the RAT Restrictions for NTN has be introduced over S1 and X2 for the identification and restriction of satellite access, while two options of codepoint have been provided on the RAT Restriction Information and the RAT Type IE. Taking S1 as an example, in [11], the 4-codepoint option is applied, while in [12] and [13], the 8-codepoint option is applied. The difference is whether to differentiate the detailed IoT constellations or not. Based on the agreement in SA2 (S2-2109197), the eight RAT types have been specified, including NB-IoT(LEO), NB-IoT(MEO), NB-IoT(GEO), NB-IoT(OTHERSAT), LTE-M(LEO), LTE-M(MEO), LTE-M(GEO) and LTE-M(OTHERSAT). Therefore, the 8-codepoint option should be applied.

The following proposal could be taken into consideration:

Proposal 8: Apply the 8-codepoint option for the RAT Restriction Information IE and RAT Type IE over S1 and X2.

Question 5: What’s your opinion on the RAT restrictions of satellite access for IoT over NTN, do you agree with the above proposal?

| Company | Agree or Disagree | Comment |
| --- | --- | --- |
| ZTE | Agree |  |
| Ericsson | Agree to further discuss | It depends whether we define “RAT type” based on UE capability (LTE-M / IoT) or on access type (NTN). This might be worth further clarification with SA2. We welcome further discussion on this point. |
| Qualcomm | No | “Based on the agreement in SA2 (S2-2109197”, there are actually 12 RAT Type values for satellite support of cellular CIoT – check – but we don’t need them all RAT Type is used for access check by CN (TA indicator); now we have only two types of cells, E-UTRA or NB-IOT x4 constellations (so NOT LTE-M for sure), i.e. 8 combinations An alternative / equivalent option is to add a new TAC attribute with values GEO, MEO, LEO, OTHERSAT (actual RATs in a TA = combination of this + legacy) – this is probably the simplest For Mobility Restrictions, since there is no NB-IOT mobility, and since LTE-M and other UEs move around freely in E-UTRA cells, then we only need four codepoints (or bits) - GEO, MEO, LEO, OTHERSAT . |
| Huawei |  | Yes, better to align with SA2. Thanks Qualcomm for clarification. |
| Nokia |  | Agree with QC |

Moderator’s summary:

<TBD>

## Issue 6: O&M Requirements

In both [6] and [7], the O&M Requirements have been captured, while, according to [3], whether to explicitly list OAM requirements or to simply reference the relevant section of TS 38.300 should be decided by RAN3. Based on the agreements in RAN1, the Ephemeris parameters in NR NTN WI could be reused in IoT over NTN WI, and there is no obstacle to list the O&M Requirements explicitly in the 36.300.

The following proposal could be taken into consideration:

Proposal 9: Explicitly List O&M Requirements in 36.300.

Question 6: What’s your opinion on the O&M requirements, do you agree with the above proposal?

| Company | Agree or Disagree | Comment |
| --- | --- | --- |
| ZTE | Agree |  |
| Ericsson | No strong opinion | It depends on what we think will happen when implementing IoT NTN. If we envisage some commonality in network infrastructure for both NR NTN and IoT NTN, OAM requirements can be listed in one place (e.g. 38.300) and only referenced in the other (e.g. 36.300). If we prefer to keep separate (and potentially diverging) descriptions, then we go for duplicate sections. |
| Qualcomm | No strong opinion | Similar to Ericsson, slight thought it may be better to have separate text for safety, but could be convinced either way. One possibility is to start by just referring to 38.300 and check if any deltas are needed |
| Huawei | Partly agree | We are fine to list OAM requirements, but also there is no harm to discuss other ways. |
| Nokia |  | QC approach is fine, e.g. start by just referring to 38.300. |

Moderator’s summary:

<TBD>

## Issue 7: Potential enhancements on energy saving

In [18], the enhancements to reduce the UE energy consumed during the mapped cell ID determination have been discussed. However, as there is no objective related to the enhancements in the WID, this issue is out of the scope and should be not discussed in this release.

The following proposal could be taken into consideration:

Proposal 10: The potential enhancements on energy saving are not included in Release 17.

Question 7: What’s your opinion on this issue, do you agree with the above proposal?

| Company | Agree or Disagree | Comment |
| --- | --- | --- |
| ZTE | Agree |  |
| Ericsson | Agree, contribution-based | In principle we agree with the Moderator – the WID is clear. However, this can be based on contributions. Incidentally, 0828 does not seem to bring up any RAN3-related issues: it describes information exchange between UE and network, so it seems more in RAN2 scope (sent to RAN3 for information, perhaps?). |
| Qualcomm | Agree | Indeed 0828 is not a RAN3 paper, so nothing actionable for us. If RAN2 comes up with something that needs support, we can of course take a look. But indeed we should keep scope extremely narrow in rel-17. |
| Huawei | Agree | This seems to be RAN2 discussion. In addition, we kindly note that not all IoT UEs are static, there is already moving IoT device on field of Mobike. |
| Nokia |  | Disagree, but ok with majority view. |

Moderator’s summary:

<TBD>

## Issue 8: Any other aspect

Question 8: Please add any further aspects that are in scope and were not included in the above:

| Company | Comment |
| --- | --- |

Moderator’s summary:

<TBD>

# Conclusion, Recommendations [if needed]

If needed

# References

R3-220085  Reply LS on EPS support for IoT NTN in Rel-17  CT1

R3-220122  Reply LS on EPS support for IoT NTN in Rel-17  SA2

R3-220397  Proposal for IoT NTN Baseline CRs  Ericssom, Qualcomm Incorporated, Huawei, Nokia, Nokia Shanghai Bell

R3-220739	Discussion on NB-IoT and eMTC Support for NTN  CATT

R3-220982  Discussion on NB-IoT and eMTC Support for NTN  ZTE, Samsung, Eutelsat

R3-220409  Introduction of IoT and MTC NTN in E-UTRAN Stage 2  Nokia, Nokia Shanghai Bell, Ericsson, Huawei, Qualcomm Inc.

R3-220983  NB-IoT/eMTC support for Non-Terrestrial Networks  ZTE, CATT, Samsung

R3-220469  Discussion about location report and mapping in NTN-IoT  Huawei

R3-220314  NNSF for IoT NTN providing access over multiple countries  Qualcomm Incorporated, Ericsson, Huawei, Nokia, Nokia Shanghai Bell

R3-220984  NAS Node Selection Function for NB-IoT/eMTC NTN nodes providing access over multiple countries  ZTE, CATT, Samsung

R3-220399	Support of NTN RAT identification and NTN RAT restrictions  Ericsson, Huawei, Qualcomm Incorporated, Nokia, Nokia Shanghai Bell

R3-220740  NB-IoT/eMTC NTN support of identification and restriction of satellite access  CATT

R3-220985  IoT NTN support of identification and restriction of satellite access  ZTE, Samsung

R3-220462	Support of NTN RAT identification and NTN RAT restrictions  Huawei, Ericsson, Qualcomm Incorporated, Nokia, Nokia Shanghai Bell

R3-220741  NB-IoT/eMTC NTN support of identification and restriction of satellite access  CATT

R3-220986  NB-IoT/eMTC NTN support of identification and restriction of satellite access  ZTE, Samsung

R3-220398  [draft] LS on IoT NTN Open Issues  Ericsson

R3-220828  Discussion on the mapped cell ID determination and energy saving  Nokia, Nokia Shanghai Bell