3GPP TSG-RAN WG3 #114-bises	R3-221064

Online, 17-26 January 2022

Agenda Item:	9.3.5.1.

Source:	Huawei (moderator)

Title:	Summary of Offline Discussion on CB: # 1903_Pos_OnDemandPRS

Document for:	Approval

# Introduction

CB: # 1903_Pos_OnDemandPRS -Discussions related to PRS Configuration Request/Response - What information to include in such procedures? - LMF to provide assistance information to NG-RAN and NG-RAN to complete PRS configuration? - LMF to have some level of control on PRS resources? -Discussions related to TRP Information Response - What information to include in such procedures? - Depending from RAN2 progress? - Any stage 2 CR to endorse? - Capture agreements and provide TPs if agreeable (HW - moderator) Summary of offline disc R3-221064

The moderator propose to complete the comment by 20th Thursday end of business PCF.

The Draft SoD will be provided by 21st Friday, for comment until 9h00 UTC 24th Monday.

The online session is 14h00 UTC 24th Monday.

# For the Chairman’s Notes [TBC]

Propose the following:

R3-20xxxa, R3-20xxxc merged

R3-20xxxc rev [in xxxg] – agreed

R3-20xxxd rev [in xxxh] – agreed

R3-20xxxe rev [in xxxi] – agreed

R3-20xxxf rev [in xxxj] – endorsed

Propose to capture the following:

Agreement text…

Agreement text…

WA: carefully crafted text…

Issue 1: no consensus

Issue 2: issue is acknowledged; need to further check the impact on xxx. May be possible to address with a pure st2 change. To be continued…

# Discussion

## Introduction of release 17 positioning enhancements TS 38.470

The CR propose to introduce the PRS configuration Exchange procedure in TS 38.470.

### Q. Should the CR, Introduction of release 17 positioning enhancements R3-220549 [3], be agreed?

If not, please clarify why.

If yes, and some minor revisions are needed please provided its in the table, if not minor please provide a draft correction in tracking change in the dedicated folder.

| Company | Comment |
| --- | --- |
| CATT | It should be discussed in CB: # 15_PositionCorrec Moderator: thank you to spot the mistake, please if possible reconsider the question after correction. |
| Huawei | Yes |
| Ericsson | Yes |
| Qualcomm | Yes |
| Nokia | Yes |

## On-demand PRS parameters

The following discussion and the questions are based on the contributions R3-220352 [1], R3-220512 [2] and R3-220719 [3]. All proposals of these contributions should be reflected in the questions below, however some “overall” proposal are not directly reflected assuming it is agreed to introduce new signalling for the On-demand PRS, if some aspects are missing please use the last one “Others” to comment.

### Q Is there an impact of “Number of DL PRS frequency layers” to NRPPa?

The companies are invited to comment.

Note: In [1] the proposal 1 is that  “Number of DL PRS frequency layers” has no impact to NRPPa.”.

| Company | Comment |
| --- | --- |
| CATT | In our understanding, the same TRP might contain multiple frequency layers. In this case, the frequency layer information needs to be introduced into each TRP. |
| Huawei | We do understand that there could be 4 frequency layers for each TRP and the on-demand DL PRS could be initiated per frequency as requested by RAN1. |
| Ericsson | We have same view as CATT. We can indicate the FLs of the TRP for which the on-Demand PRS info is related to. |
| Qualcomm | The DL-PRS parameter are per frequency layer, so it seems there some are NRPPa impacts. |
| Nokia | We are fine to introduce Number of DL PRS frequency layers (max 4) |

### Q. Is it acceptable to encode the On-demand PRS TRP Information IE as [1] with FFS?

If not, please clarify why.

Note: the alternative proposed in [2] is to wait for RAN2, and in [4] to remove the IE in favour a new IE.

| Company | Comment |
| --- | --- |
| CATT | The available values of some parameters may not be continuous, in this case, the mode of maximum and minimum value may not be suitable. Therefore, the usage of BITSTRING can be considered, and it provides more flexibility. |
| Huawei | It is acceptable, we understand this is pending to RAN2 progress |
| Ericsson | We do not understand why there are separate IEs for the minimum and the maximum of the bandwidth and periodicity, especially that they have the same codepoints? Can’t this be unified by providing 2 IEs with a value range? This would reduce overhead…on the assumption that RAN2 had agreed on the value ranges. |
| Qualcomm | It is not quite clear why the max/min in the request is needed (e.g., PRS Bandwidth Minimum; PRS Bandwidth Maximum, etc.) since this seems TRP capabilities. |
| Nokia | Fine to include with FFS, and also open to alternative encodings. |

### Q. How to introduce the start/end time of DL PRS transmission and the ON/OFF indicator?

The companies are invited to express their view. e.g. on explicit indicator or not, on granularity of the request from the LMF, the possibility for the gNB to “OFF” the resource, on the benefit or concern against the proposal of [1, 2, 4], etc …

Note: each proposals [1, 2, 4], provide different level of granularity in request, in response and in removal …

| Company | Comment |
| --- | --- |
| CATT | Based on the proposals from RAN1, LMF is allowed to add and delete PRS resources dynamically using “ON/OFF Indicator”，and the granularity is either per resource, or per resource set, or per UE. So to support the feature, it is proposed to define a PRS Resource to Modify List, which contains the PRS Resource Set Ids/PRS Resource Ids to be modified. |
| Huawei | Well we do see overall ON/OFF sent by the LMF and the gNB could select the granularity in the response. Same for the “start/stop”. Is it reasonable to have ON/OFF per resource? It seems to us the granularity should be decide by RAN3 …. The re-use of the Time Stamp (9.2.42) or similar seems better than re-defined the IE The LS in R3-220094, file R1-2112976 row 144 indicates some FFS in ON/OFF, We suggest to put FFS in the draft and postpone the discussion or at least take a decision on granularity? |
| Ericsson | The PRS Configuration exchange procedure is not UE specific. As LMF only has full picture; it should aggregate the results from several UEs before deciding to turn on/off beams. Otherwise, a beam considered not useful for a UE may be useful for another UE. Please also consider that PRS is a broadcasted signal. On the proposal itself, LMF should recommend the PRS resource set, PRS resource, or (implicitly based on the PRS resource set IDs) the TRP ID of the TRPs to be turned on/off |
| Qualcomm | The start/end time could be implemented as a "start time" (SFN InitTime) and a "duration". |
| Nokia | The start/end time and ON/OFF indicator could be left out for now, to allow further careful thinking. |

### Q. Related to the Requested DL PRS Transmission Characteristics IE, is it acceptable to take the encoding of [1] as draft, with necessary FFS, and provide update, comment on the document as needed?

If yes, the moderator invite Nokia to provide a draft TP for the Requested DL PRS Transmission Characteristics IE, including associated dedicated new IE for NRPPa.

The companies are invited to comment, correct and put FFS as needed.

If needed, Huawei is volunteer for the pending F1 when NRPPa will be stable.

Note:  the contributions [2, 4] provide alternative, e.g., corrections, new name, could be commented in the draft.

| Company | Comment |
| --- | --- |
| CATT | Yes |
| Huawei | See update as FFS in the Draft -Adding Number of frequency layer. - FFS the ON/OFF and Start/Stop see above. -Delete Resource Set ID, delete Resource ID, as those are assigned by gNB. LMF only need to recommend parameter information. - Replace time definition by the time stamp 9.2.42 like with FFS More comment and change may follow in the Draft. |
| Ericsson | We acknowledge the efforts of companies, but would like to postpone and call for companies coordination for next meeting to carefully check the RAN1/RAN2 agreements before agreeing on a TP and having to track “floaty” FFSes in NRPPa/F1AP that are depending on RAN2 FFS. |
| Qualcomm | Yes |
| Nokia | Yes. In order to make progress, we are fine with Huawei’s suggestion. If there is still concern (e.g. from Ericsson), we could scale back a bit further and leave out the start/stop time and ON/OFF indicator for now, which seems to be the most “floaty” aspect 😉. |

### Q. Does any other proposal is missing?

If any proposal, from [1, 2, 4] is missing, please comment:

Note:

| Company | Comment |
| --- | --- |

# Conclusion, Recommendations [TBC]

If needed

# References

R3-220352,  (TP for NR_pos_enh BL CR for TS 38.455) Further details of on-demand PRS (Nokia, Nokia Shanghai Bell) other

R3-220512, (TP for POS BL CR for TS 38.455 & TS 38.473) on on-demand PRS (Huawei)	other

R3-220549, Introduction of release 17 positioning enhancements (Qualcomm Incorporated)	CR0079r, TS 38.470 v16.5.0, Rel-17, Cat. B

R3-220719, (TP for Positioning BL CR 38.455) Further Consideration on on-demand PRS (CATT)	other