3GPP TSG-RAN WG3 #114bis-e	R3-221068

Online, 17-26 January 2022

Agenda Item:	20.2.1

Source:	Qualcomm Incorporated (moderator)

Title:	Summary of Offline Discussion on Network Identifier Handling

Document for:	Approval

# Introduction

CB: # 2002_NTN_NWID

-How to define the inclusion of TAI information in the ULI?

- Should a location-derived TAI be represented? Should it be obtained from existing IEs or from new IEs?

- Send reply LS to SA2?

-Is there the need for a stage 2 correction to describe mapped cell ID availability only after AS security establishment?

-Capture agreements and provide TPs if agreeable

(Qualcomm - moderator)

Summary of offline disc R3-221068

# For the Chairman’s Notes

Propose the following:

R3-20xxxa, R3-20xxxc merged

R3-20xxxc rev [in xxxg] – agreed

R3-20xxxd rev [in xxxh] – agreed

R3-20xxxe rev [in xxxi] – agreed

R3-20xxxf rev [in xxxj] – endorsed

Propose to capture the following:

Agreement text…

Agreement text…

WA: carefully crafted text…

Issue 1: no consensus

Issue 2: issue is acknowledged; need to further check the impact on xxx. May be possible to address with a pure st2 change. To be continued…

# Discussion

Note for the purists: TAC and TAI are used below somewhat randomly, please ignore any discrepancies until we deal with stage 3 TPs 😊

## Signalling of TAI information in ULI: general understanding

RAN3 has received an LS from SA2 [1] informing that it has agreed an overall solution containing both solutions C and D (as previously discussed).

For our discussion, the most useful item from SA2 is probably the description provided in S2-2109097 (CR to 23.501) which is copied below, with the text highlighted being the most pertinent:

5.4.11.X Tracking Area handling for NR satellite access Editor’s note: References to RAN TSs are needed after RAN WGs have further progressed their work on TA handling in NTN. In case of NR satellite access with moving cells, in order to ensure that each TA is earth-stationary even if the radio cells are moving across the earth’s surface, the NG-RAN may change the TAC values that are broadcast in a cell’s system information as the cell moves, as described in TS 38.XXX. NG-RAN may broadcast a single TAC per PLMN and cell and change that TAC value as the cell moves. Alternatively, the NG-RAN may broadcast more than one TAC for a PLMN and add or remove TAC values as the cell moves. The NG-RAN provides either the single broadcast TAI or all broadcast TAIs to the AMF as part of the ULI, whenever the ULI is included in the NGAP message as described in TS 38.413 [34]. The NG-RAN indicates, if known, also the TAI where the UE is geographically located. NOTE: The AMF may take the TAI where the UE is geographically located into account to generate a suitable Registration Area for the UE.

The moderator would like to check that there is a common understanding of the SA2 requirement:

Req1: ULI contains all broadcast TAIs (either single or multiple) in all cases.

Req2: If known, ULI contains the TAI where the UE is geographically located.

The moderator would also note that Req2 does not depend on Req1, i.e., in case of moving cell with single cell TAC broadcast, it is still possible and/or useful to identify the TAI where the UE is geographically located

Q1: Do you agree with the above requirements, and also that Req2 is not dependent on Req1?

| Company | Comment |
| --- | --- |

## Signalling of TAI information in ULI: multiple TAI

Following Req1, it seems that ULI should contain an optional list of TACs.

Considering the signalling proposals provided [2,4,5,67,9,10], they all include a full list of TAIs as a new IE in ULI.

As far as the moderator can recall, in all cases except one, there is no attempt to use the legacy IE as part of the group of TAIs broadcast – although this is briefly discussed in [2] as an option. One significant difference is that [2] proposes to have this within a NTN specific IE, but we can consider this in the next level of detail as it is linked to how the location-based TAI is handled.

In [7], there is an attempt to combine legacy with the additional list, and the legacy IE is that with highest probability of location. But this seems anyway incomplete since the location-based TAI may not be in the broadcast TAI group (we revisit this in the next section).

It may therefore be possible to try to agree this point, since almost all proposals align, and so the moderator would like to propose the following:

Proposal 1: A list of TACs is added to ULI as a new optional IE (exact structure and level FFS).

Q2: Do you agree with Proposal 1?

| Company | Comment |
| --- | --- |

## Signalling of TAI information in ULI: location-based TAI

For this there are two main options, whether to attempt to reuse the legacy TAC or not:

- Option 1: Refs [2,5,10] code this as a new optional IE (also [2] moves it within a NTN specific IE, together with the TAC list)

- Option 2: Refs [4,6,7,9] propose to reuse the legacy TAC IE (although semantics are not aligned)

In the first option, the new IE carries the location information if present. The legacy IE could still be used for the single TAC broadcast case, but even this is not necessary. Note that [2] forks this completely, either the legacy IE is used and we have legacy handling, or a NTN-specific set is used with optional location-based TAI and any number of broadcast TACs.

In the second approach:

- Refs [4,6] state that the legacy TAI can be used to indicate the location-based TAI, [6] states that this is always the case for NTN (in semantics)

- Ref [7] has semantics that tie this to >1 TAC broadcast and NG-RAN could not decide which one is the location TAI. But this approach seems problematic since (1) it implies that the location-based TAI is always broadcast, which is not correct, and (2) AMF cannot know whether or not this TAI is location-based and indeed which TAIs are broadcast (bearing also in mind that it might be needed for single TAI broadcast)

- Ref [9] does not have any new semantics for the location-based TAI, so it seems that the AMF assumes that this is contained in the legacy IE.

From the moderator’s perspective, both options are possible in theory provided all signalling scenarios are covered. This seems fine with the first option. For the second option, one point to check is the requirement to indicate the TAI where the UE is geographically located – which applies “if known”. However, if the legacy IE is used (which is mandatory), the AMF cannot know whether the signalled TAI is based on location or not, and so what use to make of it. It may also be useful to clarify if this also operates in case of single TAC and moving cell.

Q3: Please state your preference in terms of option 1 and option 2 (reuse or legacy IE). Please explain this preference and if possible address / comment on the issues mentioned above.

| Company | Comment |
| --- | --- |

## Stage 2 text

In [8], it is proposed to add the following text in stage 2:

When a cell broadcast multiple TACs for a PLMN, the gNB may report all broadcasted TACs of the selected PLMN to the AMF as part of ULI. In case the gNB knows the UE’s location information, the gNB may determine the TAI the UE is currently located and provide that TAI (if known) to AMF as part of ULI.

The moderator would like to ask if companies support such an inclusion and/or if there are any comments or suggestions on the text.

Q4: Do you agree with the above stage 2 proposal? Any comments / suggestions?

| Company | Comment |
| --- | --- |

## Other issues

Please feel free to add any issues or aspects missing from the above, if need be they can be taken up in a second round.

| Company | Comment |
| --- | --- |

# Conclusion, Recommendations [if needed]

If needed

# References

R3-220121, “LS on TAC reporting in ULI and support of SAs and FAs for NR Satellite Access”, (SA2), LS in

R3-220283, “(TP for TS38.413 BL CR on NTN) Handling TA reporting in ULI (Qualcomm Incorporated), other

R3-220284, “[DRAFT] Reply LS on LS on TAC reporting in ULI and support of SAs and FAs for NR Satellite Access (R3-220121/S2-2109337) (Qualcomm Incorporated), LS out To: SA2 CC: RAN2, CT1

R3-220394, “Multi TAC handling and reporting in NTN” (China Telecommunication), discussion

R3-220466, “Further discuss on multiple TAC issues” (Huawei), other

R3-220629, “TAC Reporting in ULI for NTN” (Ericsson LM), other

R3-220713, “(TP for NTN BL CR 38.413) TAI reporting in ULI” (CATT), other

R3-220826, “(TP for BL CR for TS 38.300) mapped cell ID determination after AS security and TAC reporting” (Nokia, Nokia Shanghai Bell), other

R3-220827, “(TP for BL CR for TS 38.413) TAC reporting for support multiple TAC broadcast over the air”,  (Nokia, Nokia Shanghai Bell), other

R3-220895, “(TP for BL CR 38.413) TAC Reporting in ULI for NTN”, (ZTE), other