3GPP TSG-RAN WG3 #1124bis-e	draft R3-221264

Online, 17-26 January 2022

Agenda Item:	20.2.5

Source:	Ericsson

Title:	Country Routing and Cause Value for UE Context Release

Document for:	Discussion, Agreement

# Text Proposal for TS 38.300 BL CR

START OF CHANGES

### 16.x.6	AMF (Re-)Selection by gNB

The gNB implements the NAS Node Selection Function specified in TS 38.410 [16].

For a RRC_CONNECTED UE, when the gNB is configured to ensure that the UE is using an AMF that serves the country in which the UE is located. If the gNB detects that the UE is in a different country to that served by the serving AMF, then it should perform an NG handover to change to an appropriate AMF, or initiate an UE Context Release Request procedure towards the serving AMF. The AMF may decide to de-register the UE.

END OF CHANGES