3GPP TSG-RAN WG3 #114bis	R3-220999

17 - 26 January 2022

Online

Agenda Item:	9.3.1.1

Source:	Nokia, Nokia Shanghai Bell - Moderator

Title:	Summary of Offline Discussion – Direct Data Forwarding E1 Aspect

Document for:	Approval

# Introduction

This is the summary document for the following come back:

CB: # 7_DirectDataFwd_E1aspects

- Solution3: Nokia, Nokia Shanghai Bell, CATT, China Telecom

- Solution1: Ericsson

- Add a note that in case of EPC to 5GC direct data forwarding for dis-aggregated node case, one multiple DL Forwarding UP TNL Information may correspond to multiple E-RAB IDs? Huawei, Samsung, China Telecom

- Solution down selection, try to close this topic, capture agreements and provide CR if agreeable

(Nok - moderator)

Summary of offline disc R3-220999

# For the Chairman’s Notes

Propose the following:

Agree TP … .

# First Round

During previous RAN3 meetings, the discussion on inter-system data forwarding with non-shared SgNB was discussed. Two solutions are left on the table as described below:

Solution 1: CU-CP requests one data forwarding address from the CU-UP using the existing signalling. CU-CP feedback the tunnel address to the two E-RABs in Handover Request Ack message to 5GC. With this, the data from the two E-RABs in the source node will be sent to one DRB buffer in the target (ref R3-211957/R3-212545/R3-212356)

Solution 3: Add Data Forwarding from E-UTRAN Request List to the DRB To Setup List in PDU Session Resource To Setup List within Bearer Context Setup Request message and Data Forwarding from E-UTRAN Response List to the DRB Setup List in PDU Session Resource Setup List within Bearer Context Setup Request message (ref R3-211642/R3-211642/R3-211958).

These solutions primarily aim at addressing handover from 4g to 5g in the case where there are more E-RABs at source compared to target. For example, 2 E-RABs at source and only one DRB at target.

Companies were supposed to check whether solution 1 has any product implementation issue and also check the efficiency of the solutions.

Down selection of the solution 1 and solution 3

Check with CT4 specification and potential product implementation whether there is any issue for solution 1.

Product implementation issue with solution 1

The use case is 2 E-RABs at source and one DRB at target. End marker packets are sent by source eNB over the two forwarding tunnels. According to solution 1 these 2 forwarding tunnels will end up at the same tunnel endpoint. This is the Y shape. At the same time fresh data may have arrived at target gNB.

Tdoc R3-220673 claims that this Y shape is not an issue because CT4 allows this, quoting:

A receiving GTP-U entity should be prepared to receive GTP-U packets from different source IP addresses

However, the problem is not there. What is not clear is if a receiving entity is prepared to receive end markers from 2 different sources, which CT4 doesn’t tell.

Indeed, from target receiving entity the following sequence of packets may be seen arriving at the same tunnel endpoint:

- Step1: Forwarded packets (source E-RAB1 and E-RAB2)

- Step 2: End markers (source E-RAB1)

- Step 3: Forwarded packets (E-RAB2)

- Step 4: End markers (E-RAB2)

Unless the target entity starts to sniff in the source address of incoming packets, the receiving entity cannot differentiate from where the packets come. Please note also that the target receiving entity has also no idea of how many sources there are…

The receiving entity therefore think at step 2 that no more forwarded packets will follow. Therefore, this is an unexpected situation that forwarded packets are still received during step 3 after end marker packets of step 2 which can create an abnormal condition at receiver side.

Q1: is do you first acknowledge that the sequence of events step1, step 2, step 3, step 4 can arrive with solution 1 at receiving CU UP?

| Company | Comment |
| --- | --- |
| Nokia | Yes. |
| CATT | Yes |
| Ericsson | Yes, for a short time |
| China Telecom | Yes |
| Huawei | Yes |
| ZTE | Yes |

Q2: if yes, does it create an issue for product implementation?

| Company | Comment |
| --- | --- |
| Nokia | It may in some implementations. |
| CATT | Yes |
| Ericsson | Probably not. Companies who think this might cause an issue can ask their CT4 delegates and bring detailed arguments to RAN3 |
| Huawei | Probably not. Our view is that this scenario is not a typical one (two E-RABs mapped to one DRB) for inter-system handover. If any implementation issue is foreseen, the target CU-CP can even not consider to enable this case. Another point is that when the target CU-UP receives the Direct Forwarding Path Availability IE setting to “inter-system direct path available”, it can have its own implementation handlings. |
| ZTE | Agree with Huawei |

Efficiency issue with solution 1

Let us take again the same sequence at target receiving side at the same tunnel endpoint:

- Step1: Forwarded packets (source E-RAB1 and E-RAB2)

- Step 2: End markers (source E-RAB1)

- Step 3: Forwarded packets (E-RAB2)

- Step 4: End markers (E-RAB2)

As said, also fresh data has arrived at target gNB.

One implementation can be that target gNB CU UP at step 2 think that data forwarding is over. Assuming that it does not bother or fail (see answer to Q1 and Q2) it can switch to now deliver the fresh packets. In this best case without failure, the target gNB will miss the forwarded packets of step 3 which will never be delivered.

Tdoc R3-220636 says that “this is not a problem because inter-system is not supposed to be lossless”: but if we don’t care at all to minimize the loss why are we then discussing data forwarding? 😊

So obviously even if we are not lossless, we do data forwarding to at least minimize the loss of packets; and obviously solution 1 will lose more packets that solution 3.

In solution 3 for which separate tunnels are used the target CU UP knows that two forwarding tunnels have been setup. Therefore, the target CU UP can wait for the end markers of the two forwarding tunnels to be received before switching to fresh data (i.e. after step 4).

Q3: as demonstrated above, do you agree that even if solution 1 does not lead to a failure it results in more loss of packets compared to solution 3?

| Company | Comment |
| --- | --- |
| Nokia | Yes. As per the example. We don’t necessarily say that this I critical, but this is a fact. |
| CATT | Yes |
| Ericsson | It may, for a short while, depending on the implementation. But inter-system DF is not lossless so this is a non-issue. Even in that case, inter-system DF will minimize the loss compare to no DF. If few packets loss is such an issue, maybe the remapping scenario should not be chosen by the target node |
| China Telecom | Yes |
| Huawei | Agree with Ericsson. |
| ZTE | Agree with Ericsson. |

In view of the above, solution 1 is less robust and more lossy than solution 3 but it has the merit to be simpler. Therefore, the following question:

Q4: in view of the above, which solution are you now preferring and why?

| Company | Comment |
| --- | --- |
| Nokia | Solution 3. |
| CATT | Solution 3 |
| Ericsson | Solution 1. It seems that proponents of solution 1 do not answer to the “why” question. For solution 1, this is obvious: specification impact is lower, and there is no need to implement a new solution for something which is already supported in the specifications. |
| China telecom | Solution 3 |
| Huawei | Solution 1 |
| ZTE | Solution1 Prefer the solution with less spec impact |

Moderator’s summary:

Majority of companies think …

Proposal 2: TP...

# Second Round

Moderator’s summary:

Majority of companies think …

Proposal 2: TP...

# Conclusion

The following is proposed:

Proposal 1: TP...

# References

- RP-172109, Revised Work Item on New Radio (NR) Access Technology, NTT DOCOMO, Inc.