3GPP TSG-RAN WG3 #114bis-e							R3-221103

17-26 Jan 2022 Online

Agenda Item:	9.2.1

Source:	CATT (moderator)

Title:	                Summary of Offline Discussion on CB: # 93_ASNCorrec

Document for:	Approval

# Introduction

CB: # 93_ASNCorrec

-Check the ASN.1 issue and try to find BC way, if agreeable

(CATT - moderator)

Rev in R3-221103

# For the Chairman’s Notes

Propose the following:

R3-20xxxa, R3-20xxxc merged

# Discussion

In [1],the following issue is indicated:

The Asn.1 for NRNeighbour-Information is not correct.The highlighted part should be CSI-RSTransmissionIndication not EARFCNExtension:

NRNeighbour-Information ::= SEQUENCE (SIZE (1.. maxofNRNeighbours))OF SEQUENCE {

nrpCI							NRPCI,

nrCellID						NRCGI,

fiveGS-TAC						FiveGS-TAC	OPTIONAL,

configured-TAC					TAC			OPTIONAL,

measurementTimingConfiguration	OCTET STRING,

nRNeighbourModeInfo				CHOICE {

fdd		FDD-InfoNeighbourServedNRCell-Information,

tdd		TDD-InfoNeighbourServedNRCell-Information,

...

},

iE-Extensions						ProtocolExtensionContainer { {NRNeighbour-Information-ExtIEs} } OPTIONAL,

...

}

NRNeighbour-Information-ExtIEs X2AP-PROTOCOL-EXTENSION ::= {

{ID id-CSI-RSTransmissionIndication		CRITICALITY ignore	EXTENSION EARFCNExtension	PRESENCE optional},

...

}

And it is proposed to correct the ASN.1 for NRNeighbour-Information-ExtIEs IE directly with NBC CR.

Question1: Do you agree to adopt the NBC CR to fix the error?

| Company | View |
| --- | --- |
| CATT | Yes |
| Huawei | yes |
| E/// | Yes, as commented online. BC way might be a bit ugly 😊 and it seems not necessary here. |

Question 2: If the answer the Q1 is no, please provide your suggestion on how to fix it.

| Company | View |
| --- | --- |

# Conclusion, Recommendations [if needed]

If needed

# References

R3-221087, Correction on the ASN.1 for neighbor cell information, CATT,Ericsson,Huawei