# 3GPP TSG-RAN WG3 #114bis-e	R3-221172

# was R3-221074

# Online, 17-26 Jan 2022

# Agenda Item:	22.2.2

# Source:	Huawei (moderator)

# Title:	Summary of discussion on MBS2_SessMgmt

# Document for:	Approval

# Introduction

CB: # MBS2_SessMgmt

- Procedures and detail IEs for broadcast session setup/release/(update or reset)?

- Introduce new IEs in the PDU session resource modify/setup procedures for UE MBS context?

- Single or separate multicast distribution setup/release procedures (involving E1AP and NGAP)?

- Whether mapped QoS flow info is necessary for PDU session resource modify/setup procedure?

- Whether to combine multicast and broadcast session distribution setup/release procedures?

- Single or separate procedures for multicast session activation/deactivation/update?

- Introduce alternative IP address to MB-SMF container in distribution setup/response message to support IPv4&6?

- Procedures and detail IEs for admission control?

- Whether RAN3 needs to introduce NG-RAN node triggered procedures for PDU session resources procedures for MBS?

- LS to SA2?

- Focus on key issues, capture agreements and open issues, provide TPs if agreeable

(HW - moderator)

Summary of offline disc R3-221074 rev in R3-221172

# For the Chairman’s Notes

Agree TPs and LS:

- Broadcast TP 38.413 Nokia R3-220353 revised to R3-221166, Agreed

- Multicast TP 38.413 Huawei R3-220692 revised to R3-221167, Agreed

- Multicast TP 38.401 Ericsson R3-220593 revised to R3-221168, Agreed

- Multicast TP 38.410 CATT R3-220546 revised to R3-221169, Agreed

- Multicast TP 38.300 ZTE R3-220731 revised to R3-221170, Agreed

- Draft LS to SA2 to inform progress and check whether/what they expect as a feedback for some messages, e.g. session activation in R3-221171, Agreed

Agreements:

- Introduce Session Status (activation/deactivation) in Distribution Setup Response message.

- Introduce MBS QoS Flow level Parameters in Distribution Setup Response

- Do not provide the full list of (MBS Are Session ID + MBS Service Area) information for the MBS Session in PDU Session Resource Setup/Modify Request message.

- Introduce Multicast Session Update Failure message.

Open issues:

- Whether to include MBS QoS Flow Level Parameters in Multicast Session Activation Request.

- Whether to provide a list of {MBS Are Session ID + MBS Service Area} in Session Activation Request message and Distribution setup Response message.

- Whether to provide a single {MBS Service Area + (optional) MBS Area Session ID} in the Session Activation Request message and Distribution setup Response message, and PDU Session Resource Setup/Modify Request message.

- If and how to support associated PDU Sessions with deactivated UP connection.

# Discussion _ First Round

## Turn Previous WAs to agreements

In the last meeting, there were some WAs about MBS session management, as following:

- WA: introduce new MB-SMF containers in TS 38.413, subject to SA2/CT4. Applicable for both MC and BC.

- WA: Separate NGAP procedures are used to support Distribution Setup and Distribution Release.

- WA: use separate NGAP procedures. For location dependent Multicast MBS service, the procedure is used to setup/release the NG-U tunnel for an area Session

Question 1: do you agree to turn these previous WAs to agreements?  If not, please give your reasons.

| Company | Answer | Comment |
| --- | --- | --- |
| Huawei | Agree |  |
| CATT | Agree |  |
| Nokia | Agree 1 and 2 NOK for 3 | 3 is unclear with regards to the meaning of “an” vs “one”. For the location dependent it should be possible that gNB can trigger the distribution request for multiple Service Areas (and associated Area sessions) at a time otherwise it would break the service if every time UE moves from a non-supporting cell to a supporting cell of same gNB the N3 tunnel needs to be setup.. Huawei2：the RAN node can trigger multiple Distribution Setup procedure in parallel, using one Distribution setup procedure to only setup one shared NG-U tunnel, will make the procedure/messages simpler and cleaner comparing with one message to setup multiple tunnels. To progress, it is suggested to turn this WA to agreement. And it is fine to change the “an area session” to “one area session”. |
| Samsung | Agree |  |
| Lenovo, Motorola Mobility | Agree |  |
| ZTE | 1,2 agree. #3 needs clarification. | Generally fine for all WAs RAN3 made in previous meeting. Just a little clarification for the #3: For location dependent Multicast MBS service, the NGAP procedures MBS Distribution Setup and MBS Distribution Release are used to setup/release the NG-U tunnel for one area session. |
| CMCC | Agree |  |
| Ericsson |  | ad 1) as long as the MB-SMF containers are defined by RAN3, this is the way to go. ad 2) ok, ad 3) where does the WA: use separate NGAP procedures come from and to which topic does it refer to? Bear in mind, that the “For location dependent ...” part was agreed already at RAN3#114-e. |
| Qualcomm | Agree |  |
| NEC | Agree |  |

## Broadcast Session Management

A set of agreements/WAs were achieved in previous meetings on Broadcast Session Management, and inn last meeting, whether the Distribution Setup procedure and Distribution Release procedure can be reused for BC is FFS.

In contribution [1][6], shared NG-U is established during the session start procedure, i.e. the 5GC may provide IP multicast address in Session Start Request, and then the gNB may provide DL TNL Address in Session Start Response if unicast transmission is used.

In contribution [10] [18], it is proposed to define the Distribution Setup procedure and Distribution Release procedure, to be reused by both broadcast and Multicast.

- Option 1: Established during Broadcast Session Setup Request/Response, similar to 4G eMBMS.

- Option 2: Upon receiving the Broadcast Session Setup triggered from 5GC, RAN triggers Distribution Setup procedure towards 5GC.

Question 2: which option do you prefer to establish the shared NG-U tunnel for broadcast session?

| Company | Both acceptable? | Preference | Comment |
| --- | --- | --- | --- |
| Huawei | Yes | Option 1 | Both solution are acceptable to us, we have to make a decision as soon as possible to complete the work. For BC, option 1 is a more timely and efficient solution. |
| CATT | Probably not | Option 1 | For multicast, the setup of NG-U tunnel is triggered by join procedure. We could not quite understand why this procedure is also needed for broadcast since the setup of broadcast service does not rely on the request from UE. |
| Nokia | Yes | Either OK |  |
| Samsung |  | Option 1 | We think option 1 is more simple. |
| Lenovo, Motorola Mobility | Yes | Option 1 | We share the same view with Huawei that option 1 is more efficient for broadcast. |
| ZTE | No | Opt1 | Based on our understanding, the mechanisms of BC and MC is not the same. For a BC session, the involved gNB does not have MBS INACTIVE period. Hence, as long as the gNB allocates the resource for the BC session, it shall prepare to receive the upcoming BC data packet via the new established shared N3 tunnel. In other words, this two procedures are highly linked to each other in BC. To reduce the procedure complexity, we only prefer option 1. |
| CMCC | Yes | Either OK |  |
| Ericsson |  | Option 2 | This was offered as a kind of compromise last time. If we would like to have common NG-U shared bearer control procedures, we should go for option 2. At least, this function is common for MC and BC. |
| Qualcomm |  | Option 1 | Option 1 is simple and efficient. |
| NEC | No | Option 1 | Multicast and Broadcast have different features, |

It is proposed in contribution [10] to introduce a NG-RAN node triggered MBS Session Resource Release Required procedure, to enable the NG-RAN node indicating that the NG-RAN can no longer provide any resources for the MBS Session, which is applicable for both, broadcast and multicast.

In LTE Embms, there is a Reset procedure to reset all or part of the MBMS sessions in case of the failure of RAN node or CN node, considering of similarity for NR MBS, it is straight forward to introduce a Broadcast Reset procedure [15], which can be used in case of the failure in the RAN node or CN node.

From the moderator point of view, the reset procedure can trigger the release of the MBS Session from both RAN and CN node, and can release multiple services via a single message, it is strongly recommended to introduce it to management the broadcast sessions.

Question 3: Do you agree to introduce Broadcast Session Reset procedure? If not, please elaborate the reason.

| Company | Answer | Comment |
| --- | --- | --- |
| Huawei | Yes | Broadcast session uses non UE associated signaling, in case of the failure in RAN or CN, it is strongly recommended to have a Broadcast Rest procedure to remove all or a list of Broadcast Sessions, in all or part of cells. |
| CATT | Yes | It is reasonable |
| Nokia | OK |  |
| Samsung |  | Not sure about it. In case of the failure in RAN node or CN node, all the services will be impacted. The normal Reset procedure can be triggered. Huawei2: as discussed in RAN3#114-e meeting in the LTE correction AI, the normal Reset procedure is understood by many companies to only reset UE related things. And on the other hand, it is quite needed to reset all or part of the BC sessions. |
| Lenovo, Motorola Mobility | Yes |  |
| ZTE | No | We prefer to support MBS Session update procedure for BC. The BC session update procedure is described in clause 7.3.3, TS 23.247. We do not see strong advantage to challange SA2’s decision. |
| CMCC |  | No strong view. Considered the limit time in R17, prefer to postpone to next release. |
| Ericsson | No | It appears at if the “Reset” procedure is a procedure to allow NG-RAN to release BC MBS Session resources. That function we support for both, BC and MC. A Reset procedure that tackles a multitude of BC (or MC) sessions is not needed. |
| Qualcomm |  | This should be low priority topic for now. |
| NEC | No | Session update procedure works rather than Session Reset procedure for Broadcast. |

## Multicast Session Management

In the last meeting, whether a single procedure or separate procedures should be used for activation/ update/ deactivation is FFS.

In contributions [7][17][18], it is proposed to use a single non-UE associated NGAP procedure  (e.g., multicast session update)to support MBS session activation/deactivation and MBS session update procedure.

In contributions [10][12], it is proposed to use separate non-UE associated NGAP procedures to support MBS session activation, MBS session deactivation and MBS session update.

- Option 1: single (Multicast Session Update) procedure to support Multicast Session Activation/Deactivation/Update

- Option 2: 3 separate procedures to support Multicast Session Activation/Deactivation/Update

Question 4: For Multicast Session Activation/Deactivation/Update, which option do you preferred?

| Company | Both acceptable? | Preference | Comment |
| --- | --- | --- | --- |
| Huawei | Yes | Option 1 | Although we proposed to use option 2 in [12], but we see the simplicity of solution 1, and even in solution1, we can also make the AMF (if preferred by RAN3) be aware of the Session Status. Therefore for RAN3 progress, we support to use option 1. Yan: sorry for typos. |
| CATT | Yes | Option 1 | The information that needs to be included in these messages are very similar and also these message share very common functionalities. It is useless to define multiple procedures which share the similar functions. |
| Nokia | No | Option 2 | Session update is quite different since it can update service area or MBS profile whereas activation/deactivation are agnostic to service areas and MBS profile. But activation and deactivation could possibly be combined |
| Samsung | Yes | Option 2 | We prefer option 2 if the AMF can be aware of the session status. Otherwise, option 1. |
| Lenovo, Motorola Mobility | Yes | Option 1 | We do not see a big difference between option 1 and option 2. Both can work. But we would prefer to have a common procedure if possible. |
| ZTE | No | Opt1 | We prefer to use single procedure to support MC session act/deact/update functions. For functionality perspective, all of these three functions are the modification/changing of the existing multicast session. And the involved multicast session will keep existing after these modifications. Also, option 1 is much simpler than option 2 and can reduce RAN3 work load. |
| CMCC | Yes | Option 1 | Adhering to the principle of simplifying the procedure, we support Option 1. |
| Ericsson | No | Option 2 | Different functions in different procedures, common functions in common procedures, UE-dedicated in UE-dedicated - Very simple principles, easy to implement, easy to test. |
| Qualcomm |  | Option 2 | Activation/deactivation and update are quite different. |
| NEC | Yes | Option 2 | It would be less signaling if we adopt non-UE associated signaling. |

How to perform admission control was marked as open issue in the last meeting. In contribution [7], it is said that the NG-RAN node implements admission control during MBS session activation procedure. In contribution [13], it is also proposed to introduce admission control results in the MB-SMF container in MULTICAST SESSION ACTIVATION RESPONSE message.

Question 5: Do you agree to perform admission control at session activation, and RAN node provides the admission control result to 5GC in session activation response? if not, please elaborate the reason.

Editor’s Note: if in Q4 a single update procedure is selected, the “session activation” mentioned in this question will be “session update”.

| Company | Answer | Comment |
| --- | --- | --- |
| Huawei | Agree | Upon receiving the session activation, the RAN node will allocate radio resources for the MRB, it is straight forward to do the admission control during session activation, and provide the result in the response message. |
| CATT | Agree | Similar view with Huawei |
| Nokia | No | SA2 has not foreseen to report the admission result to 5GC because for multicast it doesn’t make sense. Which CN entity would use this information? SMF? MB-SMF? NEF? AF? This is not planned by SA2. The activation procedure is just to inform the gNBs early so that gNBs does not send UEs to Idle mode. Please also note that the activation is not sent to all gNBs therefore the proposal does not make sense. |
| Samsung | Agree |  |
| Lenovo, Motorola Mobility | Agree | Same view with Huawei. |
| ZTE | agree | After deactivation, gNB has to release the allocated resource for the multicast. But the MBS session context is still recorded at RAN side. If a new UE camps in this gNB and needs join the MBS session, admission control is necessary. |
| CMCC | Agree |  |
| Ericsson | Agree in principle | very happy to read the first part of the proposal. the second part of the question, i.e. concerning the result of the admission control is a bit more tricky (and also applies to BC): is there a “partial” success possible and who (which entity) would be interested in receiving a “partial” success? or is it an “all or nothing” approach, ie either the gNB accepts the session in the whole session area or not at all. Shouldn’t we contact SA2 (probably also SA6) on that? |
| Qualcomm | Agree |  |
| NEC | Agree |  |

Based on SA2 TS 23.247, it is proposed in contribution [12] that the MBS QoS Flow Level QoS Parameters and the MBS service area information(s) associated with the same MBS Session should be provided in the Multicast Distribution Setup Response message during session establishment when the UE join, and in the Multicast Session Update Request message. On the other hand, in [8] [17], it is proposed to include these information in Multicast Session Update Request message. In [9], it is proposed to include these information in Session Activation Request message.

- Option 1: provide in Distribution Setup Response

- Option 2: provide in Session Update Request

- Option 3: provide in PDU Session Resource Setup/Modify Request

- Option 4: provide in Session Activation Request

Question 6: which option(s) do you prefer to provide the MBS QoS Parameters and Service Area Information which are common for all UEs join the same service to the gNB?

| Company | Answer | Comment |
| --- | --- | --- |
|  | Opt 1 | Opt 2 | Opt 3 | Opt 4 |  |
| Huawei | YES | YES | NO | NO | For option 1, it can be used during session establishment when the UE join. For option 2, it is agreed that the MBS QoS Parameters and Service Area Information can be updated during Multicast Update procedure. For option 3, it can work, but not efficient, providing the informations common for all UEs is not suitable for per UE signaling, i.e. PDU Session Resource Setup/Modify Request. For option 4, do not see the need, unless in Q4 a single update procedure is selected to support activation/deactivation/update. |
| CATT | Prefer no | Yes | No | Yes | For 1, we prefer to keep the function of Distribution Setup procedure restricted to NG-U tunnel setup. For 2 and 4, since we propose to support MBS Session activation and MBS session update via one procedure, we think the admission control should be supported in this procedure. For 3, we think admission control should be per MBS session not per UE. |
| Nokia | partly | Yes | Yes | NO | For option 1 the list of services areas can be included in the distribution setup response as planned by SA2, but there is no need to send the MBS profile because the MBS profile is sent in the PDU session Setup Request/Modify (see 3). Indeed, receiving the MBS profile in PDU Session setup/modify is important to be able to start setting the radio resources immediately in parallel to setup the N3 (and not in sequence!) For option 2, it is agreed that the MBS QoS Parameters and Service Area Information can be updated during Multicast Update procedure. For option 3, as said above, it is important to enable setting up the radio resources as soon as possible. Even if less efficient from pure signaling perspective the size of message doesn’t care for RAN3. For option 4, no need because the activation request is just to let gNBs prevent sending UEs to idle because the session is resuming. |
| Samsung | No | Yes | No | Yes | Agree with CATT |
| Lenovo, Motorola Mobility | Yes? | Yes | No | Yes | At least option 4 should be supported. If we have a common procedure for activation and update, option 2 should also be supported. We are not sure whether Option 1 should be supported. If the MBS QoS profile and MBS service Area are provided by activation, why option 1 is needed? |
| ZTE | partly | YES | YES | No | Opt1: this is not necessary if the QoS parameters can be transported via opt2&3. Opt2, Opt3: according to TS 23.247, if the QoS parameters other than ARP needs to be updated, SMF shall trigger UE associated PDU Session Modification procedure for each UE as defined in TS 23.502. Otherwise, if only the ARP of QoS parameters is updated, MB-SMF triggers non-UE associated NGAP multicast session update procedure for all joined UEs. Opt4: same view with HW. |
| CMCC | Yes | Yes | No | Yes | For option 1, we should align with TS 23.247 where the QoS Parameters can be provided in Distribution Setup Response. For option 2, QoS Parameters and the MBS service area information should be provided in session update request. For option 3, same view with Huawei and CATT. For option 4, we agree the single procedure to support Multicast Session Activation/Deactivation/Update. |
| Ericsson | NO | NO | NO | YES | Option 3 is the worst of all. ad all) Having more than one option needs to be carefully looked at, we would not advise that. ad further thoughts) Please do also bear in mind that at Xn HO, I guess we have the common understanding that we follow the principles of transferring MBS Session Context of active MC sessions to the target gNB and doing a kind of “path switch” == “Distribution Setup”, although this would mean that this may be done at each and every Xn HO, we also understood that the option of having an Xn based exchange of information of active MBS Session Context information. Another option of course would be to spend a bit of time and let the Distribution Setup procedure trigger Activation. ad 1) Taking into account the moderators thought on Admission Control in Question 5, it is not evident why MBS Session Resource parameters should be available before Session Activation, which would be the case if you provide it in 1) ad 2) first activating and then updating the MBS Session in order to provide up-to-date MBS Session parameters is rather cumbersome - and against any well-established protocol design rules. ad 1) distribution tree build up before session activation does still not look like a sound concept yet. SA2 concept was built around the scenario of “joining during active session”, but didn’t that all scenarios into account. only concentrates on “joining during active session” where the distribution tree setup is fine to have as specified, but this is not the case of inactive sessions: why should a gNB “decide” (as shown in step 1 in 23.247 §8.2.4.1) to establish shared NG-U if there is no reason to do so? Why to establish shared NG-U for location dependent services for inactive MBS sessions if it is in general not clear whether it will be actually used (again: why would the gNB wish to establish NG-U resources?). ad all) provision of Session Area information is performed via over-the-top service announcement and NAS (see 23.247 §6.2.2), there is no need to have it available at NG-RAN during inactive sessions. |
| Qualcomm | No | Yes | Yes | No | #1 No needed, because gNB received QoS and area before this procedure in #3. #2 We already agreed Update procedure can update QoS profile. #3 This is aligned with SA2. #4 This is just activation. If QoS update is needed, it should use #2. |
| NEC | No | Yes | No | Yes | Agree with CATT |

From the NG-RAN node point of view, for an ongoing multicast service, 5GC will inform the session status to the NG-RAN node via the session activation/deactivation procedure. But when the first UE serviced by the NG-RAN node triggers the establishment of the service at the NG-RAN node, based in current TS 23.247, there is no session activation procedure triggered by the 5GC, but the NG-RAN node has to be informed about the activation/deactivation status to decide whether to allocate radio resources.

It is proposed in contribution [7] for MB-SMF to initiate a MBS session activation procedure to inform NG-RAN node of the state of MBS session after the completion of shared delivery establishment. But currently in 7.2.5.2 TS 23.247, there are only two cases to trigger MBS Session Activation procedure:

7.2.5.2 MBS session activation procedure The following can trigger the MBS session activation procedure: - AF requests MB-SMF to activate the MBS session; - MB-UPF receives the multicast data and notifies MB-SMF.

Considering of the MBS join and Session establishment procedure call flow defined in TS 23.247 7.2.1.3, it seems straight forward to simply include a session status in the Distribution Setup Response message.

Question 7: Which option do you prefer to inform session status during session establishment?  Why?

Note that this question is how to inform the session status during the 7.2.1.3 of TS 23.247.

- Option 1: provide in Session Activation Request, i.e. CN triggers a separate session activation procedure during the MBS join and Session establishment procedure

- Option 2: provide in Distribution Setup Response

- Option 3: provide in PDU session setup/modify

| Company | Answer | Comment |
| --- | --- | --- |
| Huawei | Option 2 | Option 1 requires a separate procedure to be triggered by the MB-SMF during the session establishment which is currently not supported, and if option 1 is used, the session activation procedure will also be triggered during/after Distribution setup, therefore option 2 is a simpler and efficient solution. |
| CATT | Option 1 | It makes the functions of different procedures clear. |
| Nokia | Option 3 | The session status should be provided in the PDU session setup/Modify together with MBS profile so that the gNB can setup the radio resources as soon as possible. The other options create delay and are not acceptable. |
| Samsung | Option 1 | It is acceptable also for option 2. But option 2 combined two functions. |
| Lenovo, Motorola Mobility | Option 2? |  |
| ZTE | Opt2 | From simplicity perspective, opt2 is acceptable. |
| CMCC | Option 2 | Do not need to introduce additional session activation procedure. Option 2 meets the requirement for efficiency. |
| Ericsson | Option 1 | wouldn’t that be the straightforward approach? one single, unique trigger for setting up resources and triggering admission control? |
| Qualcomm | Option 2 |  |
| NEC | Option 1 | It is straightforward to provide it in Session Activation Reques |

In contribution [13], it is proposed to introduce a Multicast Session Notify procedure to notify that the QoS flow(s) or MBS session(s) to be released or not fulfilled anymore or fulfilled again by the NG-RAN node.

As mentioned before Q2, it is proposed in contribution [10] to introduce a NG-RAN node triggered MBS Session Resource Release Required procedure, to enable the NG-RAN node indicating that the NG-RAN can no longer provide any resources for the MBS Session, which is applicable for both, broadcast and multicast.

- Option 1: RAN triggered Session Notify procedure, similar to PDU Session Notify.

- Option 2: RAN triggered Session Release Required procedure

Question 8: which option do you preferred to enable the RAN node to inform 5GC that the RAN node is not able to provide the service for now?

| Company | Answer | Comment |
| --- | --- | --- |
| Huawei | Option 1 | Similar to PDU Session Notify, after Notify procedure, once the RAN node have enough RAN resources, it may trigger another notify procedure to resume the service. After RAN triggered Release procedure, once the RAN node have more resources to be used, it is not able to trigger the establishment of the service, unless anther RAN triggered Multicast Session Setup procedure is defined… |
| Nokia | NONE | Multicast is not unicast. There is no CN entity to manage this admission result. See previous answer about reporting resource allocation status to CN nodes. Nothing is foreseen in TS 23.247. This would need to first be discussed in SA2. |
| Samsung |  | Tend to agree with Nokia. Probably need to coordinate with SA2. |
| Lenovo, Motorola Mobility | Option 1 |  |
| ZTE | Opt2 | Currently, the session notify procedure is not applicable based on SA2’s definition in TS 23.247. Considering part is high related to SA2, RAN3 does not have enough time budget on discussing this part with SA2 in next following meeting. =========content in TS23.247============ 6.6 QoS Handling for Multicast and Broadcast services For MBS services, the network shall support QoS control per MBS session. The 5G QoS model and parameters as defined in TS 23.501 [5] clause 5.7 also apply to MBS services with the following differences: - Reflective QoS is not applicable; - Wireline access network specific 5G QoS parameters do not apply to MBS services; - Alternative QoS Profile is not applicable; - QoS Notification Control is not applicable; =========content in TS23.247============ |
| CMCC | None | In our view, we should align with TS 23.247. If we really need this function, since the limited time in Rel-17, the discussion for this function should be postponed to next release. |
| Ericsson | none | Notification Control, which is what we are talking here about, is not applicable for 5G MBS (see chapter 6.6 in 23.247) |
| Qualcomm | Option 2 or none | Notification control is not applicable to MBS. So, option 1 is excluded. Option 2 is the only option if we want to support gNB requested release. Defer to R18 is also fine. |
| NEC | None | Unnecessary to prioritize this issue in this release. |

## Others

If you have other important issues to be discussed, please include in the table below.

Question x: xxxxx [company]

| Company | Answer | Comment |
| --- | --- | --- |
| Nokia |  | As indicated at the beginning in 3.1, it is necessary to include multiple Area Session IDs and associated Service Areas in the distribution setup request in order to enable a gNB to setup multiple tunnels at same time and avoid break of service when UE moves. Huawei2: same comment as in Q1, the RAN node can trigger multiple Distribution Setup procedure in parallel, using one Distribution setup procedure to only setup one shared NG-U tunnel, will make the procedure/messages simpler and cleaner comparing with one message to setup multiple tunnels. To progress, it is suggested to turn this WA to agreement. And it is fine to change the “an area session” to “one area session”. |

Question E-1: In order to complete the full set of BC/MC MBS Session Resource control procedures the gNB shall be enabled to request the release of MBS Session Resources (e.g. due to being pre-empted by other PDU/MBS Sessions) [Ericsson]

| Company | Answer | Comment |
| --- | --- | --- |
| Ericsson | Yes | Yes please |

Question E-2: How to answer the open issue in TS 23.247 §7.2.1.3. [Editor's note:	The implication of not triggering PDU Session UP activation in NG-RAN when SMF informs the NG-RAN of UE join requires RAN collaboration.]Do you agree to answer this open RAN-specific suggested in Annex B in R3-220593 [9] including also feedback on §7.2.5.2? [Ericsson]

| Company | Answer | Comment |
| --- | --- | --- |
| Ericsson | Yes | as indicated in [9] |

Question E-3: Do you agree to answer the open RAN-specific issue in TS 23.247 §7.2.3.6 [Editor's Notes: RAN confirmation is required] as suggested in Annex B in R3-220593 [9]? [Ericsson]

| Company | Answer | Comment |
| --- | --- | --- |
| Ericsson | Yes | as indicated in [9] |

Question y: yyyyy [company]

| Company | Answer | Comment |
| --- | --- | --- |

# Discussion _ Second Round

## Turn Previous WAs to agreements

For this part, we apologies that in first round, as pointed by E///, the last bullet was wrong, which should be a copy paste issue…sorry for that.

RAN3 has already made the following agreement in RAN3#114-e meeting:

For location dependent Multicast MBS service, the MBS Distribution Setup/Release procedure is used to setup/release the NG-U tunnel for an area Session.

The three working assumptions proposed to be turned into agreements in this CB should be:

- WA: introduce new MB-SMF containers in TS 38.413, subject to SA2/CT4. Applicable for both MC and BC.

- WA: Separate NGAP procedures are used to support Distribution Setup and Distribution Release.

- WA: Different procedures are used for “Multicast Session Activation/Deactivation” and “Broadcast Session Start/Stop”.

Based on the inputs in section 3.1, companies are fine for 1 and 2, and based the submitted papers, companies should also be fine for 3.

Proposal 1: turn the three previous WAs into agreements. (no comment foreseen)

- Introduce new MB-SMF containers in TS 38.413, subject to SA2/CT4. Applicable for both MC and BC.

- Separate NGAP procedures are used to support Distribution Setup and Distribution Release.

- Different procedures are used for “Multicast Session Activation/Deactivation” and “Broadcast Session Start/Stop”.

## Broadcast Session Management

About the two options listed to setup shared NG-U for BC in Round 1 Question 2:

- Option 1: Established during Broadcast Session Setup Request/Response, similar to 4G eMBMS.

- Option 2: Upon receiving the Broadcast Session Setup triggered from 5GC, RAN triggers Distribution Setup procedure towards 5GC.

With two companies fine for both options, there are 8 companies support option 1, 3 companies for option 2, but option 2 is not acceptable by two companies, therefore the moderator propose to adopt option 1 as the way forward.

Proposal 2: for BC, establish the shared NG-U during Broadcast Session Setup Request/Response, similar to 4G eMBMS.

With proposal 2, we would like to further discuss the information elements to be included in the BC session setup/modify/release related messages, by using R3-220353 [1] as the starting point, we could get the following proposals:

Proposal 3: Include Session ID, Area Session ID (optional), Service Area information, MB-SMF container: MBS Session Information Request Transfer/MBS Session Information Modify Request Transfer, in the BROADCAST SESSION SETUP/MODIFICATION REQUEST messages.

Proposal 3-1: The MBS Session Information Request Transfer IE includes: shared NG-U TNL Information, MBS QoS Flows To Be Setup List (QFI, QoS Flow level QoS parameters). 
The MBS Session Information Modify Request Transfer IE may include: shared NG-U TNL TNL Information, MBS QoS Flows To Be Setup or Modify List (QFI, QoS Flow level QoS parameters)

Proposal 4: Include Session ID, Area Session ID (optional), and MB-SMF container: MBS Session Information Response Transfer, in the BROADCAST SESSION SETUP/ MODIFICATION RESPONSE messages.

Proposal 4-1: The MBS Session Information Response Transfer IE includes: DL UP Transport Layer Information (optional).

Do you agree with Proposal 3, 3-1, 4 and 4-1? Any comments?

| Company | Answer | Comment |
| --- | --- | --- |
| Huawei | Agree |  |
| CATT | OK with 3,3-1,4 | For 4-1,a question for clarification is that it means the MB-SMF needs to store the established QoS flow for each cell. Then in the subsequence broadcast update procedure, the MB-SMF should request the modification per cell since the admitted flow in each cell is different.Is it a little complicated？ |
| NEC | Agree |  |
| Ericsson |  | P2: you have to give me agreement on E1 in exchange for ignoring my compromise from last time. thank you so much. Huawei: Many thanks for compromise, please find the updated Proposal 10’. Note that we are now only fine to introduce the Session Release Required for Broadcast only, as things are a little bit different for multicast. P3: do we agree to have the same SMF container for BC and MC defined to be included in the respective NGAP messages? Huawei: no, we did not, and to me they have to be different, as for Broadcast, the MB-SMF container will include shared NG-U tunnel information, which will not there for MC. P3-1: please replace “IP Multicast TNL Information” by “Shared NG-U tunnel TNL information”. and “MBS QoS Flows To Be Setup or Modify List” by “MBS QoS Flows To Be Setup List”. What to do in case of location dependent sessions, shouldn’t TNL info come with Session Area ID? Huawei: for the IP Multicast TNL Information is used because it will be included in the MB-SMF container to the NG-RAN node, which is different to other normal tunnels. For the QoS Flows to be setup or modify, is used because this MB-SMF container can be used in both Broadcast Session Setup and Modification procedures. Session ID is in the first level IE in the message, and is aware by the AMF, so the TNL info comes with Session Area ID currently. P4/4-1: What to do in case of location dependent sessions, shouldn’t TNL info come with Session Area ID? Huawei: Session ID is in the first level IE in the message, and is aware by the AMF, so the TNL info comes with Session Area ID currently. P4-1: not ok to agree now on per-cell handling. too few discussions on that. Huawei: fine to remove for now, see updated proposal 4-1. |
| Qualcomm | Agree |  |
| Lenovo, Motorola Mobility | Agree | Agree with the updated proposals. |
| ZTE | agree |  |
| Samsung | agree |  |

For Round 1 Question 3, the Broadcast Session Reset procedure is proposed, 4 companies support, three companies said no, 2 company would like to postpone it to Rel-18. Considering that there are only 1.5 meetings left, moderator would like to propose the following:

Proposal 5: Discuss Broadcast Session Reset procedure in Rel-18 MBS WI.  Ericsson: but this doesn’t need to be minuted Huawei: ok

## Multicast Session Management

For Round 1 Question 4, for Multicast Session Activation/Deactivation/Update, 5 companies support single procedure, 4 companies support separate procedures, we see a good compromise from Nokia seems also from QCOM to have a common procedure for Session Activation and Deactivation, and another procedure for Session Update. As all the solutions works, to progress, moderator strongly recommend companies to compromise, and propose to use the good compromise from Nokia to close this discussion.

Proposal 6: Define one procedure to support both Multicast Session Activation and Multicast Session Deactivation.

Proposal 7: Define one procedure to support Multicast Session Update.

For Round 1 Question 5, 8 companies agree to perform admission control at session activation, 1 company disagree. And 7 companies agree that the RAN node provides the admission control result to 5GC in session activation response, one company has concern.

Proposal 6-1: Perform admission control at session activation, and RAN node provides the admission control result (marked as to be further checked) to 5GC in session activation response.

For Round 1 Question 6, on using which options to provide the MBS QoS Flow Level QoS Parameters and the MBS service area information(s) associated with the same MBS Session:

|  | Yes | Yes, but | No |
| --- | --- | --- | --- |
| Option 1: provide in Distribution Setup Response | 3 | 2 | 4 |
| Option 2: provide in Session Update Request | 8 |  | 1 |
| Option 3: provide in PDU Session Resource Setup/Modify Request | 3 |  | 7 |
| Option 4: provide in Session Activation Request | 5 |  | 4 |

With these inputs, moderator would like to provide the following proposal:

Proposal 7-1: include the MBS QoS Flow Level QoS Parameters and the MBS service area information(s) associated with the same MBS Session in the Multicast Session Update Request message FFS on whether to provide these information in Distribution setup response and PDU Session Resource Setup/Modify Request message message or not.

Do you agree with Proposal 6-1 and 7-1? Any comments?

| Company | Answer | Comment |
| --- | --- | --- |
| Huawei | Agree |  |
| CATT | Agree |  |
| NEC | Agree |  |
| Ericsson | 6-1 agree 7-1 object, go for option 4, please. | P6-1: Agree P7-1: There is no question that the MBS Session parameters need to be included in the Modification procedure. But what we don’t understand is why you would send out an Activation message w/o session parameters and right after it a Modification parameters? why aim would you follow? what is the principle/philosophy behind? We cant see any good reason Huawei: The Session Update procedure has to be able to provide these informations, as the CN can update these parameters. To progress, let’s update Proposal 7-1 to support providing these information in Session Activation as well. |
| Qualcomm | 6-1 agree 7-1 partial | Why not include MBS QoS parameters and area info in PDU Session Resource Setup/Modify Request? |
| Nokia | NOK | Just follow SA2 TS 23.247. We object the addition in the Activation Request. We object any result sent back to 5GC (not foreseen in TS 23.247!). |
| Lenovo, Motorola Mobility | Agree | We tend to agree to include MBS QoS parameters in the Activation request. |
| ZTE | 6-1 ok 7-1 partial | We share the same view with QCM.We also prefer to add MBS QoS parameters and area info in PDU session resource setup/modify request. |
| Samsung | Agree |  |

For Round 1 Question 7, about how to inform the session status during session establishment,

- Option 1: provide in Session Activation Request, i.e. CN triggers a separate session activation procedure during the MBS join and Session establishment procedure

- Option 2: provide in Distribution Setup Response

- Option 3: provide in PDU session setup/modify

- companies support option 2, 3 companies support option 1, and 1 company support option 3.

Considering that these solutions seems can be supported in parallel, as the RAN node needs to get the accurate session status, there is no harm for RAN3 to support all of these 3 options, and we in RAN3 can easily support these, i.e. add the session status IE in Distribution Setup Response and in the PDU Session Setup/modify. Then the core network will be able to provide the accurate session status to RAN by whichever the way.

Proposal 8: include Session Status in Distribution Setup Response and PDU session setup/modify, then the CN can inform RAN about the session status via either using Session Activation Request, or using Distribution Setup Response, or PDU Session Setup/Modify Request.

Do you agree with Proposal 8? Any comments?

| Company | Answer | Comment |
| --- | --- | --- |
| Huawei | Agree |  |
| CATT |  | Our view is only option 1 is needed. However, to make progress ,we could accept both option1 and option 2 to facilitate the status aware when NG-U tunnel is setup. Could not quite understand the reason for introducing option 3. |
| NEC | Agree |  |
| Ericsson | no | agree with CATT, only option 1 is needed. We shouldn’t include more options just for the sake of compromise and reduce the set of options to the most reasonable and necessary ones. |
| Huawei |  | To CATT and Ericsson, we see strong view to use option 3 from Nokia in the first round discussion, therefore we made proposal 8 to allow all, make everyone equally happy/unhappy. Let’s keep Proposal 8 as it is, and discuss online. |
| Qualcomm | Agree |  |
| Nokia | Agree |  |
| Lenovo, Motorola Mobility | Agree |  |
| ZTE | agree |  |
| Samsung | agree |  |

In section 4.1. it is proposed to turn previous WA to agreement on “Separate NGAP procedures are used to support Distribution Setup and Distribution Release.”, besides NGAP, in order to establish the shared NG-U, in case of CU-CP and CU-UP split deployment, we need to introduce a E1AP related non-UE associated procedure, as proposed in R3-220488 [4] R3-220489 [5].

Proposal 9: Introduce two separate non-UE associated Class1 E1AP procedures：

- Multicast Distribution Setup procedure, triggered by the gNB-CU-UP

  - in case the gNB-CU-UP decides or is configured to use unicast transport for multicast distribution sessions, it includes the DL GTP-U tunnel info in the Multicast Distribution Setup Request.

  - in case the DL GTP-U tunnel info is not included in the Multicast Distribution Setup Request, the gNB-CU-CP shall provide IP multicast DL tunnel info to the gNB-CU-UP, to enable IP multicast transport.

- Multicast Distribution Release procedure, triggered by the gNB-CU-UP or gNB-CU-CP

Do you agree with Proposal 9? Any comments?

| Company | Answer | Comment |
| --- | --- | --- |
| Huawei | Agree |  |
| CATT | Agree |  |
| NEC | Agree |  |
| Ericsson |  | Is this comback handling E1AP? ??? Huawei: it is quite straight forward…this E1AP procedure is just used to establish shared NG-U. if no technical concern, let’s keep this proposal. |
| Qualcomm | Agree |  |
| Nokia | Partly | The E1 distribution setup should be triggered by CU CP. |
| Lenovo, Motorola Mobility | Agree |  |
| ZTE | agree | We think Nokia is correct. |
| Samsung | agree |  |
| Ericsson 3 | disagree | I can’t agree on that poaching approach |

For Round 1 Question 8, about enable the RAN node to inform 5GC that the RAN node is not able to provide the service for now:

- Option 1: RAN triggered Session Notify procedure, similar to PDU Session Notify.

- Option 2: RAN triggered Session Release Required procedure

4 companies said none, 2 companies select option 1 and 1 company select option 2, 1 company select option 2 or none. Although moderate thinks that this is a good to have function, and either option 1 or option 2 are acceptable, but considering of the 4.5 none and the limit of time, it may not essential for Rel-17, moderator suggest to discuss it in Rel-18.

To Ericsson, for the newly add Question E-1, it is coved by this option 2 in this Round 1 Question 8.

Ericsson: if we decide on that, we should remove any specific information in the response messages (like cell lists etc) and only allow successful termination of setup procedures if the whole gNB can provide the service and inform other groups

To Ericsson, you said none in the first round Question 8 discussion….

To progress, the Proposal 10 is changed to:

Proposal 10’:.

Nokia: we disagree. Please just follow SA2 TS 23.247.

For the new question from Nokia in section 3.5, due to the mistake by the moderator in section 3.1, as clarified in section 4.1, moderate thinks that we do not need to re-discuss the previous agreement, therefore there is no further proposal on it, hope you are fine for it.

Nokia: ok for us. Thanks for the clarification.

For the new Question E1 from Ericsson in section 3.5, please see the discussion in proposal 10 (sorry wrong number), hope you are fine for it. Ericsson: we don’t understand the relation between proposal 9 and E1

For the new Question E2 from Ericsson in section 3.5, moderator remembers that we discussed it in last meeting, see Question 2-8 in R3-215985 last meeting sod, the previous summary and proposal at that time were:

Summary: all companies agree that in such case the gNB does not need to setup unicast PDU Session level UP tunnel, and no DRB., 5 companies do not see the impact to RAN3 other procedures, 1 company thinks that there will be no SMF <->NG-RAN communication. From moderator point of view, the MBS Session ID, the mapped unicast QoS Flow information, will still need to be carried in the PDU Session Modify/Setup procedure.

Nokia: No, this is wrong.

We do not see the need to re-discuss this topic as anew, start from scratch, as we did not get any agreement for this at the end last meeting, moderator would like to check companies view on the previous proposal again.

Proposal 11: In case the PDU Session modify/Setup only includes information related to the multicast session and mapped unicast QoS flows, the MBS capable gNB will not setup DRB for these MBS mapped unicast QoS flows.

Proposal 11: In case the UP of an associated PDU Session is not activated, e.g. joining is performed only by means of NAS signaling, the information about which TMGI the UE has joined is provided to the gNB my means of NGAP UE Context signaling.

Do you agree with Proposal 11? Any comments?

| Company | Answer | Comment |
| --- | --- | --- |
| Huawei | Agree |  |
| CATT | Agree |  |
| NEC | Agree |  |
| Ericsson | this does not work | A PDU Session Resource has to setup NG-U termination and resources for at least one QoS flow. Not doing so would change the state model introduced in Rel-15: i.e. either the UP is setup == PDU Session Resource Context exists in NG-RAN, or UP is not setup == PDU Session Resource does not exist in NG-RAN. Please have a look e.g. into NGAP, where the respective IEs are mandatory ones. The condition to not setup a DRB/NG-U termination in NG-RAN do not exist in NGAP. It is simply impossible. (I hope there is no need to copy NGAP parts here) So, if a UP for the associated PDU Session Resource is not setup - join information needs to come out side the PDU Session Resource context, i.e. on UE Context level -->>SA2 to be informaed - intra-gNB mobility with MRB only is possible (F1 allows DRB less contexts) but not inter-gNB. so either the UE re-connects at the target or at least one QoS flow needs to be setup, as DRB-less HO is not supported -->> NG-RAN triggered PDU Session Resource UP activation necessary. we request E2 to be agreed. Huawei: how about establish the PDU Session Level UE specific NG-U tunnel, only not setup DRB for these MBS mapped unicast QoS flows? See updated Proposal 11. [Ericsson 2: no way, please, keep the principles of PDU Session Resource Control as of today. This was always the understanding of Rel-17 discussions so far. We are adamant on that, really.] |
| Qualcomm | Agree |  |
| Nokia | Agree with updated proposal 11 |  |
| Lenovo, Motorola Mobility | Agree |  |
| ZTE | agree |  |
| Samsung | Agree |  |

For the new Question E3 from Ericsson in section 3.5. That is for the Editor’s notes to be checked by RAN3 for mobility, i.e. based on the SA2 LS on the outstanding SA2 issues, which should be discussed in 22.3 as it covers both mobility between supporting nodes and mobility between supporting and non-supporting nodes, chair moves the papers on that to AI 22.3.1, please moderator of that CB (ZTE) also take the inputs for R3-220593 into account.

## TPs to be updated

Many good papers submitted in this AI, based on the submitted papers, in order to capture all the agreement we made during this meeting, or previous meetings (if missing), the following TPs to be updated are proposed by the moderator, hope you are fine for it.

- Broadcast TP 38.413 Nokia R3-220353

- Multicast TP 38.413 Huawei R3-220692

- Multicast TP 38.460/38.461 Lenovo R3-220488/489 (if Round 2 proposal 2 agreed)

- Multicast TP 38.401 Ericsson R3-220593

- Multicast TP 38.410 CATT R3-220546

- Multicast TP 38.300 ZTE R3-220731

Note: please TP owners ask for Tdoc number revision (can be done after Thursday online meeting), and update the TPs before the end of Monday Jan 24.

# 5	Progress made during online discussion _ Jan 20

Introduce new MB-SMF containers in TS 38.413. Applicable for both MC and BC.

Separate NGAP procedures are used to support Distribution Setup and Distribution Release.

Different procedures are used for “Multicast Session Activation/Deactivation” and “Broadcast Session Start/Stop”.

Broadcast Session Management:

For BC, establish the shared NG-U during Broadcast Session Setup Request/Response.

Include Session ID, Area Session ID (optional), Service Area information, MB-SMF container: MBS Session Information Request Transfer in the BROADCAST SESSION SETUP message and MBS Session Information Modify Request Transfer in the MODIFICATION REQUEST message.

-The MBS Session Information Request Transfer IE includes: shared NG-U TNL Information (optional) (carry IP multicast address), MBS QoS Flows To Be Setup List (QFI, QoS Flow level QoS parameters).

-The MBS Session Information Modify Request Transfer IE may include: shared NG-U TNL Information (optional), MBS QoS Flows To Be Setup or Modify List (QFI, QoS Flow level QoS parameters).

Include Session ID, Area Session ID (optional), and MB-SMF container: MBS Session Information Response Transfer, in the BROADCAST SESSION SETUP/ MODIFICATION RESPONSE messages.

-The MBS Session Information Response Transfer IE includes: DL UP Transport Layer Information (optional).

Multicast Session Management:

Define separate procedures to support both Multicast Session Activation and Multicast Session Deactivation.

Define one procedure to support Multicast Session Update.

Perform admission control at session activation, if needed, and RAN node either accept the activation by sending session activation response message or reject the activation by sending activation failure message.

Include the MBS QoS Flow Level QoS Parameters and the MBS service area information(s) associated with the same MBS Session in the Multicast Session Update Request message.

Open issues

For BC, introduce a Broadcast Session Release procedure, triggered by the NG-RAN node. Including one messages: BROADCAST SESSION REQUIRED message?

Include this question into the draft LS to SA2

For MC, CN can inform RAN about the session status via either using Session Activation Request, or using Distribution Setup Response, or PDU Session Setup/Modify Request?

For MC, provide the MBS QoS Flow Level QoS Parameters and the MBS service area information(s) associated with the same MBS Session information in the following messages:

a) Session Activation Request message No: Nok

b) PDU Session Resource Setup/Modify Request message No: E///, CATT

c) Distribution Setup Response message No: ZTE

Separate the MBS QoS Flow Level QoS Parameters and the MBS service area information(s) and the corresponding messages for further discuss, a) or c)?

For 3rd  Round:

- Check the details of TPs based on agreements

- Continue the discussion on issential open issues related to basic functionality

Broadcast TP 38.413 Nokia R3-220353 revised to R3-221166

Multicast TP 38.413 Huawei R3-220692 revised to R3-221167

Multicast TP 38.401 Ericsson R3-220593 revised to R3-221168

Multicast TP 38.410 CATT R3-220546 revised to R3-221169

Multicast TP 38.300 ZTE R3-220731 revised to R3-221170

# 6 Discussion _ Third Round

## 6.1	Stage 3 details on the agreed Multicast procedures

## Moderator summary: agree the NGAP Multicast TP directly.

Continue discussing the leftover open issues discussed online, moderator would like to discuss some stage3 IE details on the agreed Multicast Session management related messages, to help the progress of TP updates.

### Distribution Setup Procedure and Distribution Release Procedure:

Based on the agreements we made so far, and the SA2 TS section 7.2.1.4, 7.2.2.4, the following proposals are made:

Proposal 1: Include MBS Session ID, Area Session ID (optional), and MB-SMF container: MBS Distribution Setup Request Transfer in DISTRIBUTION SETUP REQUEST message.

Proposal 1-1: The MBS Distribution Setup Request Transfer IE includes MBS Session ID, Area Session ID (optional), DL Transport Layer Information (optional).

Proposal 2: Include MBS Session ID, Area Session ID (optional), and MB-SMF container: MBS Distribution Setup Response Transfer in DISTRIBUTION SETUP RESPONSE message.

Proposal 2-1: The MBS Distribution Setup Response Transfer IE includes MBS Session ID, Area Session ID (optional), shared NG-U TNL Information (optional) (carry IP multicast address).

Proposal 3: Include MBS Session ID, Area Session ID (optional), Cause, and MB-SMF container: MBS Distribution Setup Unsuccessful Transfer in DISTRIBUTION SETUP FAILURE message.

Proposal 3-1: The MBS Distribution Setup Unsuccessful Transfer IE includes MBS Session ID, Area Session ID (optional), Cause.

Proposal 4: Include MBS Session ID, Area Session ID (optional), Cause, and include MB-SMF container: MBS Distribution Release Request Transfer in DISTRIBUTION RELEASE REQUEST message.

Proposal 4-1: The MBS Distribution Release Request Transfer IE includes MBS Session ID, Area Session ID (optional), Cause, and shared NG-U TNL Information (optional, present in case unicast shared NG-U tunnel is used).

Proposal 5: Include MBS Session ID, Area Session ID (optional) in DISTRIBUTION RELEASE RESPONSE message.

Do you agree with the above Proposals? Any comments?

| Company | Answer | Comment |
| --- | --- | --- |
| Huawei | Agree |  |
| Nokia | OK |  |
| Lenovo | Yes |  |
| Ericsson | Yes, we have some comments. | The question is why for location dependent sessions, during inactive sessions, the whole distribution tree would need to be kept maintained based on session area id information. this requires quite a lot of processing, as per UE location information needs to be checked against the session area definition. especially for small session areas this is quite some effort. So, in general, for inactive sessions, we would advocate/urge to allow implementation specific choice of not keeping the NG-U distribution tree resources. Huawei: for inactive session, it is up to the NG-RAN node whether to trigger the release of the shared tunnel, by using the Distribution Release procedure. |
| ZTE | agree |  |

### Multicast Session Activation procedure and Multicast Session Deactivation procedure:

Based on the agreements we made so far, and the SA2 TS section 7.2.5.2, 7.2.5.3, the following proposals are made:

Proposal 6: Include MBS Session ID and MB-SMF container: Multicast Session Activation Request Transfer in MULTICAST SESSION ACTIVATION REQUEST message.

Proposal 6-1: The Multicast Session Activation Request Transfer IE includes: MBS Session ID.

Proposal 7: Include MBS Session ID and MB-SMF container: Multicast Session Activation Responses Transfer in MULTICAST SESSION ACTIVATION RESPONSE message.

Proposal 7-1: The Multicast Session Activation Response Transfer IE includes: MBS Session ID.

Proposal 8: Include MBS Session ID, Cause and MB-SMF container: Multicast Session Activation Unsuccessful Transfer in MULTICAST SESSION ACTIVATION FAILURE message.

Proposal 8-1: The Multicast Session Activation Unsuccessful Transfer IE includes: MBS Session ID, Cause.

Proposal 9: Include MBS Session ID and MB-SMF container: Multicast Session Deactivation Request Transfer in MULTICAST SESSION DEACTIVATION REQUEST message.

Proposal 9-1: The Multicast Session Deactivation Request Transfer IE includes: MBS Session ID.

Proposal 10: Include MBS Session ID and MB-SMF container: Multicast Session Deactivation Response Transfer in MULTICAST SESSION DEACTIVATION RESPONSE message.

Proposal 10-1: The Multicast Session Deactivation Response Transfer IE includes: MBS Session ID.

Do you agree with the above Proposals? Any comments?

| Company | Answer | Comment |
| --- | --- | --- |
| Huawei | Agree |  |
| Nokia | OK |  |
| Lenovo | Yes | Whether Area Session ID should be included? |
| Ericsson | NO | The Session Activation has to contain MBS Session parameters. That is all we ask. Then the question on why the MBS Session Parameters are provided in the bearer establishment procedures, if the admission control is done at activation. This is quite some protocol design folly Huawei: let’s focus on agreements made so far in the TP, others to be discussed in 6.2. |
| ZTE | agree |  |

### Multicast Session Update procedure:

Based on the agreements we made so far, and the SA2 TS section 7.2.6, the following proposals are made:

Proposal 11: Include MBS Session ID, (optional) Area Session ID, and MB-SMF container: Multicast Session Update Request Transfer in MULTICAST SESSION UPDATE REQUEST message.

Proposal 11-1: The Multicast Session Update Request Transfer IE includes: MBS Session ID, (optional) Area Session ID, MBS Service Area information, (optional) MBS QoS Flows To Be Setup or Modify List (QFI, QoS Flow level QoS parameters), (optional) MBS QoS Flows To Be Release List (QFI).

Proposal 12: Include MBS Session ID, (optional) Area Session ID in MULTICAST SESSION UPDATE RESPONSE message.

Do you agree with the above Proposals? Any comments?

| Company | Answer | Comment |
| --- | --- | --- |
| Huawei | Agree |  |
| Nokia | OK |  |
| Lenovo | Yes |  |
| Ericsson | OK |  |
| ZTE | ok |  |

### MBS Context in UE Specific signaling:

Based on the agreements we made so far, the TPs in submitted papers, and the SA2 TS section 7.2.1.3, the following proposals are made:

Note that in Proposal 13-1, for location dependent service, the MBS Area Session ID for the area the UE is current accessing from, has to be included, to enable the NG-RAN node to trigger the per area session id shared NG-U tunnel.

Proposal 13: Include (optional) MBS Session Information Setup List IE in the existing PDU Session Resource Setup Request Transfer IE.

Proposal 13-1: The MBS Session Information Setup List IE includes: List {MBS Session ID + (optional) MBS Area Session ID, and a List of (MBS QFI + (optional) Associated Unicast QFI)}.

Proposal 14: Include (optional) MBS Support Indicator IE in existing PDU Session Resource Setup Response Transfer IE.

Proposal 15: Include (optional) MBS Session Information Setup or Modify List IE, (optional) MBS Session Information Remove List IE in the existing PDU Session Resource Modify Request Transfer IE.

Proposal 15-1: The MBS Session Information Setup or Modify List IE includes: List {MBS Session ID + (optional) MBS Area Session ID, and (optional) List of (MBS QFI + Associated Unicast QFI)}.

Proposal 15-2: The MBS Session Information Remove List IE includes a list of {MBS Session ID, (optional) MBS Area Session ID, Cause}.

Proposal 16: Include (optional) MBS Support Indicator IE in existing PDU Session Resource Modify Response Transfer IE.

Proposal 17: Include (optional) MBS Support Indicator IE in existing Path Switch Request Transfer IE.

Proposal 18: Include (optional) MBS Session Information Setup List IE in existing PDU Session Resources To Be Setup List IE.

Proposal 19: Include (optional)	MBS Session Information Setup List IE in existing UE Context Information – Retrieve UE Context Response IE.

Do you agree with the above Proposals? Any comments?

| Company | Answer | Comment |
| --- | --- | --- |
| Huawei | Agree |  |
| Nokia | OK |  |
| Lenovo | Yes |  |
| Ericsson | partly ok | If this goes along the agreed definition of “associated qos flow information” (see TP for 38.401), this is ok, as long as this associated qos flow information is optional (as agreed) not ok for the session area ID Huawei: the Associated Unicast QFI is optional, but the MBS QFI should be there. As we agreed long time before: Acknowledge that MBS related information within the associated PDU Session Resource Context may not include associated QoS flow information if interworking with non-supporting RAN nodes is not required; The area session id which related to the cell in which the UE is currently access from, has to be provided, otherwise, how can be NG-RAN node trigger the Distribution setup for that area session… |
| ZTE | ok |  |

## 6.2	Continue discussion on the leftover issues

### Open issue 1: Session Activation Status during MBS join and Session establishment procedure

(Note that this is not an open issue for optimization, all solutions are not supported for now)

Background of this open issue: in the TS 23.247 section 7.2.1.3, the MBS join and Session establishment procedure, it is not clear how to inform NG-RAN about the session activation status.

And it is noticed that the Multicast Session Activation procedure is currently not included in that procedure, and in section 7.2.5.2, there are only two cases for the CN to trigger MBS Session Activation procedure:

7.2.5.2 MBS session activation procedure The following can trigger the MBS session activation procedure: - AF requests MB-SMF to activate the MBS session; - MB-UPF receives the multicast data and notifies MB-SMF.

There are three candidate solutions listed:

a) Session Activation Request message

b) PDU Session Resource Setup/Modify Request message

c) Distribution Setup Response message

Unfortunately, for each of these three solutions, there is objection from one or two companies.

For these three solutions, the RAN3 specification changes will be:

- For a) CN need to trigger a Session Activation procedure towards RAN. (only stage 2 change needed, but one more step)

- For b) and c), a new Activation Status IE needs to be introduced in a message which is currently has to be transmitted in that scenario.

From moderator point of view, all of these three solutions will lead to very small RAN3 impact.

BUT, from moderator and moderator’s SA2 colleague’s point of view, we are negative for a), as:

- Existing session activation procedure requires MB-SMF to notify 1) corresponding SMFs and 2) NG-RAN nodes, to activate the resources and enable the UE to receive multicast data in the connected mode.

- If we simply reuse the existing activation procedure, upon receiving the request to establish a new tunnel from NG-RAN, the MB-SMF needs to contact all related SMFs/RAN nodes and of course such notifications are unnecessary and unpersuasive.

- Otherwise, if we modify the existing activation procedure, then the solution becomes, firstly, the MB-SMF has to send two separated messages to RAN: 1) the response message to the NG-RAN during tunnel establishment (i.e., Nmbsmf_MBSSession_ContextUpdate response), with containing N2 MB-SM container (QoS profile, tunnel info, MBS service area…); 2) the other message with only containing the session status in N2 MB-SM container (i.e., Namf_MBSCommunication_N2MessageTransfer Request). Note that only 2) is the message is belong to the so-called session activation procedure, which is far from current SA2 defined session activation procedure.

- Using separated messages does not bring benefits but only causing signaling overheads and extra complexity of the MB-SMF.

Proposal 20: Exclude using a) Session Activation Request message to inform Session Activation Status during MBS join and Session establishment procedure.

Do you agree with the above Proposal? If not, please clarify the issues listed above for a)?

| Company | Answer | Comment |
| --- | --- | --- |
| Huawei | Agree |  |
| Nokia | Agree |  |
| CATT |  | Our previous preference is to use session activation request. To make progress, we are Ok to use Distribution Setup Response message |
| Lenovo | Yes |  |
| Ericsson | NO | the minimum approach would be to not include session parameters into PDU Session signalling. We are still adamant on including session parameters into activation, also in order to follow the agreement to have admission control performed at session activation. a single trigger for that purpose is reducing implementation of different options. |
| ZTE | Yes |  |

Moderator agree with the proponent of b) that b) can inform the status to RAN node earlier than c), RAN can start to allocate radio resources a little bit earlier. Considering that the DL data will probably come after Distribution Setup, and the session status is not a per UE information, moderator slightly prefer to use c) instead of b).

Proposal 21: Using c) Distribution Setup Response message to inform Session Activation Status during MBS join and Session establishment procedure.

Is this proposal acceptable for you? If not, please clarify why.

| Company | Answer | Comment |
| --- | --- | --- |
| Huawei | YES |  |
| Nokia | No | Leave it open between b and c for next meeting. |
| CATT | Yes |  |
| Lenovo | Yes |  |
| Ericsson | see above |  |
| ZTE | yes |  |

### Open Issue 2: Whether the MBS QoS Flow Level QoS Parameters should be included in the following messages?

a) Session Activation Request message

b) PDU Session Resource Setup/Modify Request message

c) Distribution Setup Response message

It was agreed to include the MBS QoS Flow Level QoS Parameters in Multicast Session Update Request, besides that there are proposals to capture it in the list of messages as well.

As commented online, for PDU Session Resource Setup/Modify Request message, the NG-RAN node actually can get these information via the QoS parameters provided for the mapped unicast flow. Therefore it seems fine for companies to exclude b) for now.

Seems if the RAN node is able to get these MBS Flow QoS parameters based on the QoS Parameters provided for the mapped unicast flow’s information, all these solutions are not needed, but no, we need to consider the previous agreed potential homogeneous deployment, i.e. all RAN nodes support MBS, the mapped QFI information may not be provided in the PDU Session Setup/Modify, in such case we may still need to use a) and/or b) to provide the MBS QoS Flow Level QoS Parameters, otherwise a Multicast Session Update will have to be triggered.

For a) and c), as discussed in open issue 1, it is proposed (proposal 20) to not use Multicast Session Activation procedure during the MBS join and Session establishment procedure, therefore in such scenario the MBS QoS Flow Level QoS Parameters has to be provided via c), therefore moderator would like to propose:

Proposal 22: Include MBS QoS Flow Level QoS Parameters in Distribution Setup Response message. FFS on Session Activation Request message.

Is this proposal acceptable for you? If not, please clarify why.

| Company | Answer | Comment |
| --- | --- | --- |
| Huawei | YES |  |
| Nokia | OK |  |
| CATT | Yes |  |
| Lenovo | Yes |  |
| Ericsson |  | only in a package: Activation and Distribution (if you really insist), but prefer to not include it in Distribution at all. |
| ZTE | yes |  |

### Open Issue 3: Whether the MBS Service Area Information should be included in the following messages?

a) Session Activation Request message

b) PDU Session Resource Setup/Modify Request message

c) Distribution Setup Response message

Note that as discussed in Proposal 13-1 and 15-1, the MBS Area Session ID in which the UE is currently accessing from has already been provided in b), therefore here we are discussing about:

- MBS Service Area Information for that MBS Area Session

- MBS Service Area Information for that MBS Session, i.e. a list of (MBS Are Session ID + MBS Service Area).

- A subset of the MBS Service Area Information for that MBS Session (e.g. concerning the gNB or TA of RA where the UE is located)

From moderator point of view, it is quite obviously that 2) should not be carried by UE specific signalling, as in case of location dependent service, the information may be a big one. 1) could also be large, e.g. if the area session includes a long list of cells/TAIs.

Proposal 23: Exclude using b) PDU Session Resource Setup/Modify Request message to provide 2) the MBS Service Area Information for the MBS Session.

Is this proposal acceptable for you? If not, please clarify why.

| Company | Answer | Comment |
| --- | --- | --- |
| Huawei | YES |  |
| Nokia | OK |  |
| CATT | OK |  |
| Lenovo | Yes |  |
| Ericsson | OK | so, why is it then not possible to also exclude the MBS Session parameters altogether from PDU Session signalling? |
| ZTE | yes |  |
| (not needed due to p23) |  |  |

### Open Issue 4: How to support a joined UEs with deactivated UP connection for an associated PDU Session

There is still not sufficient answers provided on how a joined UE can be supported if the associated PDU Session Resource does not exist due to deactivated UP connection, as per TS 23.247 §7.2.1.3 step 5.

Proposal liaise to SA2 to clarify that the possibility to not activate UP connection for a PDU Session associated with a MC session implies that the gNB serving the CM-CONNECTED UE would need to be informed by means different than NGAP PDU Session related signalling. NGAP provides the means to inform the gNB on UE Context level.

Is this proposal acceptable for you? If not, please clarify why.

| Company | Answer | Comment |
| --- | --- | --- |
| Ericsson | YES | this goes along with the fact that for a PDU Session with deactivated UP connection no DRB and no N3 is established. A PDU Session Resource in RAN consists at least of one DRB. We are not available to change those fundamental principles |
| Huawei |  | We see no consensus/support on this aspect, contribution driven in next meeting, or component propose it in SA2 directly. |

## 6.3	Questions to SA2

Besides provide RAN3 progress/achieved agreement to SA2, it was decided to ask several questions related to Session Management during online discussion,

For BC, introduce a Broadcast Session Release procedure, triggered by the NG-RAN node. Including one messages: BROADCAST SESSION REQUIRED message? Include this question into the draft LS to SA2 Draft LS to SA2 to inform progress and check whether/what they expect as a feedback for some messages, e.g. session activation in R3-221171

Moderator propose the following wording:

Question1 to SA2: From CN point of view, whether it is beneficial to introduce a RAN initiated Broadcast Session Release Require procedure, to trigger the CN to initiate Broadcast Session Release procedure? To be used in case RAN is not able to provide the service over radio, due to e.g. lack of radio resources.

Question 2 to SA2: From CN point of view, in case of Multicast Session Activation or Multicast Session Update procedure, if RAN is not able to active the session or update the session, e.g. due to lack of radio resources, whether it is needed to report the activation or update failure to CN?

Any comments?

| Company | Comment |
| --- | --- |
| Nokia | OK to ask Q1. Q2 is clear in TS 23.247. |
| CATT | OK for both |
| Lenovo | Yes |
| Huawei3 | For Q2, better to check with SA2, also for Update procedure. To Nokia, can you tell the detailed section? I did not find it… |
| Ericsson | Q1: we do not want to ask in Q1 whether it is “beneficial”, but rather inform them on our protocol choice and ask them to align with it. Huawei: we like your proposal, but based on the inputs from companies, it is better to check the benefit first. Q2: also there, we should inform SA2 that we discussed failure scenarios for MC Session Activation/Update and decided to include the possibility to reject the request as a whole, i.e. Rel-17 does not foresee a “partial success” with detailed information on e.g. which areas failed to setup MBS resources Huawei: ok, and then we need to add a failure message in the Session Update procedure as well. |

# 7 References

R3-220353 (TP for 38.413) Stage 3 for Broadcast Session (Nokia, Nokia Shnaghai Bell, Huawei)	other

R3-220355 (TP for 38.413) Stage 3 for MBS Context and UE MBS Context  (Nokia, Nokia Shanghai Bell)	other

R3-220356 (TP for 38.413) Stage 3 for User Plane Shared Delivery Tunnel (Nokia, Nokia Shanghai Bell)	other

R3-220488 (TP to TS 38.460 BL CR) Support of Shared NG-U Distribution Setup and Release (Lenovo, Motorola Mobility, Huawei, Qualcomm Incorporated)	other

R3-220489 (TP to TS 38.463 BL CR) Support of Shared NG-U Distribution Setup and Release (Lenovo, Motorola Mobility, Huawei, Qualcomm Incorporated)	other

R3-220545 TP for 38.413 on session management for broadcast service (CATT)	other

R3-220546 TP for 38.410 on session management for multicast service (CATT)	other

R3-220547 TP for 38.413 on session management for multicast service (CATT)	other

R3-220593 [TP for BL CR38.401] Last exit: “Point to multipoint” - or: “one for all” taken seriously (Ericsson)	other

R3-220594 [TP for BL CR 38.413, 38.423] on Session Management for NR MBS (Ericsson)	other

R3-220692 (TP to TS 38.413 BL CR) Shared NG-U tunnel establishment and release (Huawei, CBN, China Unicom, China Telecom, Lenovo, Motorola Mobility, Qualcomm Incorporated)	other

R3-220693 (TPs to TS 38.410, 38.413 BL CRs) Multicast Session Activation Deactivation and Update (Huawei, CBN, China Unicom, China Telecom, Lenovo, Motorola Mobility)	other

R3-220694 (TPs to TS 38.300, 38.410, 38. 413 BL CRs) Multicast Admission Control (Huawei, CBN)	other

R3-220695 (TP to TS 38.413 BL CR) MBS information in PDU Session Management procedures (Huawei, CBN, China Unicom, China Telecom)	other

R3-220696 (TPs to TS 38.410, 38.413 BL CRs) Reset of Broadcast Sessions over NG interface (Huawei)	other

R3-220731 ( TP for TS 38.300) Management of multicast session (ZTE Corporation)	other

R3-220732 (TP for TS 38.413) Management of multicast session (ZTE Corporation)	other

R3-220856 MBS Session management over NG for multicast (CMCC)	discussion

R3-220884 (TP to TS 38.300) MBS session management over NG (CMCC, Huawei)	other

# Comments

































	





