3GPP TSG-RAN WG3 #114bis-e	R3-221032

Online, 17-26 Jan 2022

Agenda Item:	14.1

Source:	Huawei (moderator)

Title:	Summary of discussion on MRDC1_BLCRs

Document for:	Approval

# Introduction

CB: # MRDC1_BLCRs

- Endorse BL CRs if agreeable

- Check details in R3-220153, agree the TP if agreeable

(HW - moderator)

Summary of offline disc R3-221032

# For the Chairman’s Notes

//to be added

# Discussion

There are 14 contributions submitted to this AI, including 5 BL CRs for SCG, 8 BL CRs for CPAC, and 1 TP to CPAC BL CR to 36.423.

Question 1: do you have any comment on the SCG BL CRs? If so, please elabore in the tabluars below:

| Company | Comments to R3-220046 SCG BL CR to TS 37.340 (ZTE) |
| --- | --- |
| Nokia | Some parts of the text in the BL CR are marked in yellow – why? |

| Company | Comments to R3-220047 SCG BL CR to TS 38.401 (Huawei) |
| --- | --- |
| Samsung | 8.4.x.6 SN initiated SN Modification with SCG Activation AS IS 5. The SN-DU sends the UE CONTEXT MODIFICATION RESPONSE message to the SN-CU, indicates that the SCG is deactivated. Should To BE 5. The SN-DU sends the UE CONTEXT MODIFICATION RESPONSE message to the SN-CU, indicates that the SCG is deactivated. |

| Company | Comments to R3-220048 SCG BL CR to TS 38.423 (Ericsson) |
| --- | --- |
| Samsung | The definition of the new IE SCG Activation Request in XnAP spec is a little different with the one in X2AP/F1AP spec. XnAP Spec / TS38.423 / R3-220048 9.2.3.xxx SCG Activation Request The SCG Activation Request IE indicates whether the SCG resources are required to be activated or deactivated. X2AP Spec / TS36.423 / R3-220045 9.2.A2 SCG Activation Request The SCG Activation Request IE indicates whether the SCG resources are needed to be activated. F1AP Spec / TS38.473 / R3-220049 9.3.1.x1 SCG Activation Request This IE indicates whether the SCG resources are needed to be activated. Comment: Maybe it’s better to align all the three definitions, since the IE names are totally same. It’s not critical, just a little suggestion. |

| Company | Comments to R3-220045 SCG BL CR to TS 36.423 (Nokia, Nokia Shanghai Bell) |
| --- | --- |

| Company | Comments to R3-220049 SCG BL CR to TS 38.473 (Samsung) |
| --- | --- |

Question 2: do you have any comment on the CPAC BL CRs? If so, please elabore in the tabluars below:

| Company | Comments to R3-220052 CPAC BL CR to TS 37.340 (Huawei) |
| --- | --- |

| Company | Comments to R3-220020 CPAC BL CR to TS38.401 (ZTE) |
| --- | --- |

| Company | Comments to R3-220041 CPAC BL CR to TS 38.420 (Lenovo, Motorola Mobility) |
| --- | --- |

| Company | Comments to R3-220050 CPAC BL CR to TS 36.420 (China Telecommunications) |
| --- | --- |

| Company | Comments to R3-220053 CPAC BL CR to TS 38.423 (Ericsson) |
| --- | --- |
| Huawei | Need to check whether the similar changes as proposed in [14] for X2AP are applicable for XnAP BL CR or not. And update if needed. |
| Nokia | To avoid unnecessary burden for the rapporteur, if there are no other updates, the corrections from [14] can be included only in the post-meeting update of the XnAP BL CR. |

| Company | Comments to R3-220051 CPAC BL CR to TS 36.423 (Nokia, Nokia Shanghai Bell) |
| --- | --- |

| Company | Comments to R3-220021 CPAC BL CR to TS38.463 (Qualcomm) |
| --- | --- |

| Company | Comments to R3-220022 BLCR to TS 38.473 for Conditional PScell Change/Addition (CATT) |
| --- | --- |

In [14], several aspects are proposed to be corrected:

CPC and CHO indicators

For the purpose of CHO with DC, an indicator to stop early data transmission was defined as the CHO DC Early Data Forwarding Indicator IE. Then, for the purpose of CPC, an indicator that CPC has been started has been added and, a separate one, to stop early data transmission. These indicators are clearly too numerous and can be combined:

- Either the CHO indicator is reused for the CPC purposes (possibly with the change of the IE name, which is backward-compatible), or

- There is only one CPC indicator that is used for both, starting or stopping early data transmission.

And therefore it is proposed in [14]:

Proposal 1: RAN3 shall consider if the CHO indicator for early data transmission can be reused for CPC (with IE name change, which is backward-compatible), or the two CPC indicators are combined. In order to avoid touching existing IEs, the latter may be preferred.

Question 3: do you agree with the proposal above?

| Company | Answer | Comment |
| --- | --- | --- |
| Huawei | Ok | Ok to not touching existing IEs, and update the CPC Indicator to support both starting and supporting early data transmission. |
| Samsung | Ok |  |

“CPAC” vs “Conditional PSCell Addition and Change”.

The abbreviation “CPAC” is resolved in the list of abbreviations to “Conditional PSCell Addition or Change”. However, in many places a very similar term is used: “Conditional PSCell Addition and Change”.

And therefore it is proposed in [14]:

Proposal 2: “CPAC” is resolved to “Conditional PSCell Addition and Change” and it is then used in the text wherever “Conditional PSCell Addition and Change” is currently mentioned.

Question 4: do you agree with the proposal above?

| Company | Answer | Comment |
| --- | --- | --- |
| Huawei | Ok but | Agree to use the abbreviation “CPAC” to replace the “Conditional PSCell Addition or/and Change” in the other part of the specification, but should the CPAC be understood as “Conditional PSCell Addition or Change”? As CPA and CPC will not happen simultaneously. Propose to change the proposal to: “CPAC” is resolved to “Conditional PSCell Addition or Change” and it is then used in the text wherever “Conditional PSCell Addition and/or Change” is currently mentioned. |

PSCell ID vs en-gNB ID

In some places, the en-gNB ID has been used for a IE that is meant to transfer the NR CGI ID.

And therefore it is proposed in [14]:

Proposal 3: NR CGI is referred when the PSCell ID is needed instead of the en-gNB ID.

Question 5: do you agree with the proposal above?

| Company | Answer | Comment |
| --- | --- | --- |
| Huawei | Agree |  |
| Samsung | Agree |  |

Max number of PSCells that can be configured for CPAC in the UE

Currently, RAN3 does not assume anything – the value is marked “FFS”. The decision is up to RAN2. However, currently RAN2 does not discuss this topic and the value inherited from CHO is assumed (max number of conditional configurations is 8, which is to be shared among CHO and CPAC).

And therefore it is proposed in [14]:

Proposal 4: RAN3 replaces the “FFS” for the max number of PSCells that can be prepared for a UE with value 8.

Question 6: do you agree with the proposal above?

| Company | Answer | Comment |
| --- | --- | --- |
| Huawei | ok |  |
| Samsung | Ok but wait for RAN2 | We have same experience deciding the max number for CHO. It was originally decided to 16 at RAN3, changed to 8 after RAN2’s discussion. |
| Nokia | OK | We’re fine to wait for RAN2, if this is preferred. However, according to the information from our delegates there, there is hardly any discussion on this topic going on, so we thought it may be fixed already now. |

XnAP impact

Most of the above corrections apply to the XnAP BL CR, too.

And therefore it is proposed in [14]:

Proposal 5: The above corrections, if agreed, are included in the next revision of the XnAP BL CR.

Question 7: do you agree with the proposal above?

| Company | Answer | Comment |
| --- | --- | --- |
| Huawei | ok | Ok for the changes if applicable for XnAP BL CR. |
| Samsung | ok |  |
| Nokia | ok | To avoid unnecessary burden for the rapporteur, if there are no other updates, the corrections can be included only in the post-meeting update of the XnAP BL CR. |

Based on the analyses in [14], a TP is also provided in section 4 of this paper.

Question 8: any comments for the TP provided in section 4 of R3-220153?

R3-220153 (TP to CPAC BL CR to 36.423, LTE_NR_DC_enh2-Core)  CPAC BL CR rapporteur’s corrections (Nokia, Nokia Shanghai Bell)	other

| Company | Comment |
| --- | --- |
| Huawei | in section 3.3, no need to change “or” to “and” in the CPAC abbreviation in section 9.1.2.43, CPC Indicator IE, “,” is missing before “…”. |

# Conclusion, Recommendations [if needed]

If needed

# References

R3-220020 CPAC BL CR to TS38.401 (ZTE)	CR0174r6, TS 38.401 v16.8.0, Rel-17, Cat. B

R3-220021 CPAC BL CR to TS38.463 (Qualcomm)	CR0641r2, TS 38.463 v16.8.0, Rel-17, Cat. B

R3-220022 BLCR to TS 38.473 for Conditional PScell Change/Addition (CATT)	CR0795r4, TS 38.473 v16.8.0, Rel-17, Cat. B

R3-220041 CPAC BL CR to TS 38.420 (Lenovo, Motorola Mobility)	CR0023r1, TS 38.420 v16.0.0, Rel-17, Cat. B

R3-220045 SCG BL CR to TS 36.423 (Nokia, Nokia Shanghai Bell)	CR1609r5, TS 36.423 v16.8.0, Rel-17, Cat. B

R3-220046 SCG BL CR to TS 37.340 (ZTE)	draftCR

R3-220047 SCG BL CR to TS 38.401 (Huawei)	CR0176r6, TS 38.401 v16.8.0, Rel-17, Cat. B

R3-220048 SCG BL CR to TS 38.423 (Ericsson)	CR0633r5, TS 38.423 v16.8.0, Rel-17, Cat. B

R3-220049 SCG BL CR to TS 38.473 (Samsung)	CR0777r6, TS 38.473 v16.8.0, Rel-17, Cat. B

R3-220050 CPAC BL CR to TS 36.420 (China Telecommunications)	CR0023r5, TS 36.420 v16.0.0, Rel-17, Cat. B

R3-220051 CPAC BL CR to TS 36.423 (Nokia, Nokia Shanghai Bell)	CR1610r5, TS 36.423 v16.8.0, Rel-17, Cat. B

R3-220052 CPAC BL CR to TS 37.340 (Huawei)	draftCR

R3-220053 CPAC BL CR to TS 38.423 (Ericsson)	CR0634r5, TS 38.423 v16.8.0, Rel-17, Cat. B

R3-220153 (TP to CPAC BL CR to 36.423, LTE_NR_DC_enh2-Core)  CPAC BL CR rapporteur’s corrections (Nokia, Nokia Shanghai Bell)	other