3GPP TSG-RAN WG3#114bis			R3-221150

E-Meeting, 17 – 26 January 2022

Title:	LS on Coverage-Based Carrier Selection

Response to:

Release:	Rel-17

Work Item:	NB_IOTenh4_LTE_eMTC6-Core

Source:	RAN3

To:	RAN2

Cc:

Contact Person:

#### Name:	Philippe Godin

Tel. Number:	+33 1 6040 0304

E-mail Address:	philippe.godin@nokia.com

Attachments:

1. Overall Description:

RAN3 has discussed the potential RAN3 impacts related to the recent RAN2 decision to use option 1c alternative 2 for NB-IoT paging carrier selection based on the coverage level.

In this option, it is necessary to convey to the paged gNB whether coverage-based carrier selection is supported and will be used or not by the UE.

RAN3 kindly asks RAN2 to whether the paged eNB is able to get such information via the inter-node RRC containers carried by the NGAP/S1AP PAGING message, i.e. the UERadioPagingInformation-NB and UEPagingCoverageInformation-NB. RAN3 has understood from the previous RAN2 agreements in RAN2#114-e agreements that S1AP/NG-AP impacts are assumed not needed. Therefore, the majority of companies in RAN3 consider that RAN2 will decide to use an existing RAN2 container for this purpose.

2. Actions:

To RAN2 group:

ACTION: 	RAN3 kindly ask RAN2 to inform RAN3 whether it is confirmed to use the inter node RRC container(s) to indicate whether coverage-based carrier selection is supported and will be used or not by the UE.

3. Date of Next TSG-RAN WG3 Meetings:

TSG-RAN WG3#115                       21 February – 3 March 2021				E-meeting