3GPP TSG-RAN WG3 #114bis-e	R3-221043

Online, 17 – 26 Jan, 2022

Agenda Item:	17.3

Source:	ZTE(moderator)

Title:	Summary of Offline Discussion on CB: # RANSlicing3_UESliceMB

Document for:	Approval

# Introduction

This contribution is to kick off the following discussion.

CB: # RANSlicing3_UESliceMBR - Continue the discussion on the open issues - For UE slice MBR, decide the solution over NG, e.g., in PDU Session Resource Setup Request message or DL NAS PDU message. And the impact on F1 and E1. - How to support S-MBR Enforcement? Any standard impact? - How to introduce Target NSSAI over NG interface? Establishing the dual connectivity based on the Target NSSAI is not pursed in Rel-17? - LS to SA2? - Capture agreements and provide TPs/BL CRs if agreeable (ZTE - moderator) Summary of offline disc R3-221043

Please Note: plan to do two rounds of discussion in this meeting.

The first round email discussion plan to be end 2 hour before on-line session  1st week.(Wednesday 11:00 UTC, 2022-1-19)

# For the Chairman’s Notes

Agreement for discussion:

# First Round Discussion

### Impact on RAN slicing of UE slice MBR

### NGAP impact

The following table provide the summary of each impacted message with supported companies.

| Message Company | PDU Session Resource Setup Request | Downlink NAS transport | PATH SWITCH REQUEST ACKNOWLEDGE | CONNECTION ESTABLISHMENT INDICATION | UE Information Transfer | AMF CP RELOCATION INDICATION | REROUTE NAS REQUEST |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Nokia[1] |  |  |  |  |  |  |  |
| Ericsson[4] | Y | Y | Y | Y |  |  |  |
| Huawei[7] | Y |  |  |  |  |  |  |
| ZTE[12] | Y | Y | Y | Y | Y | Y | Y |
| CATT[19] |  | Y |  |  |  |  |  |

Table 1 views on UESliceMBR message impact

For PDU Session Resource Setup Request message, it is observed that UE-AMBR has already been included.As we can see there is no UE-AMBR IE in PDU session level messge, but in 38.413.f30, the UE-AMBR IE was introduced in  PDU Session Resource Setup procedure. The motivation is when UE-AMBR is not provided by AMF in initial context setup messge, there is no way for Core network to control bit rate of the UE via UE-AMBR.  The principal is same for Slice-MBR.  In this way, Core network can provide Slice level rate control after Initial UE context setup toward the UE. Please check the corresponding CR in R3-190971.

For Downlink NAS transport message, it is observed that both Allowed NSSAI and UE-AMBR has already been included. It is straightforward fro AMF to provide UE-Slice-MBR to the RAN in this message.

For other messages e.g. PATH SWITCH REQUEST ACKNOWLEDGE message,CONNECTION ESTABLISHMENT INDICATION messages etc, it is observed that Allowed NSSAI has already been included. It is possible to update the UE-Slice-MBR to RAN in these message.

Based on views from the company, PDU Session Resource Setup Request and  Downlink NAS Transport message got the most support and can be supported for NGAP.

Proposal 1: To carry UE slice MBR information in the following messages of NGAP:

- PDU Session Resource Setup Request

- Downlink NAS Transport

Based on views from the company, at least 1 company to support the following message in NGAP.

Proposal 2: To carry UE slice MBR information in the following messages of NGAP:

- PATH SWITCH REQUEST ACKNOWLEDGE

- CONNECTION ESTABLISHMENT INDICATION

- UE Information Transfer

- AMF CP RELOCATION INDICATION

- REROUTE NAS REQUEST

Q1: Please provide your view on Proposals.

| Company | Do you agree the proposals. | Comment |
| --- | --- | --- |

The following options discussed without achieve consensus at last meeting.

Signaling impact of introduce UE Slice MBR in NGAP takes following options as start point:

Option 1:  AMF provides UE Slice MBR as optional element within the Allowed NSSAI.

Option 2:  AMF provides UE Slice MBR in the way as UE AMBR.

The following table provide the summary of IE design from contribution.

| Option Company | Option 1 | Option 2 |
| --- | --- | --- |
| Nokia[1] | Y |  |
| NEC[3] |  | Y |
| Ericsson[4] |  | Y |
| Huawei[7] |  | Y |
| ZTE[12] |  | Y |
| CATT[19] | Y |  |

Table 2 views on UESliceMBR IE impact

As described in the SA2’s CR[S2-2104908] for TS23.502, it is observed that AMF may update UE-Slice-MBR after initial context setup. Instead of update Allowed NSSAI together , it is possible for AMF to only provide update UE-Slice-MBR to the RAN node.

The AMF takes appropriate action according to the changed subscriber data as follows, e.g.: - initiating an AMF initiated Deregistration procedure if the updated subscription data indicates the UE is not allowed to roam in this network; and - updating UE context stored at AN to modify the UE-AMBR. - updating UE context stored at RAN to modify the UE-Slice-MBR corresponding to an S-NSSAI. - initiating UE Configuration Update procedure as defined in clause 4.2.4.2. - initiating UE Parameters Update via UDM Control Plane Procedure as defined in clause 4.20.

Option 2 provide more flexibility to support the above requirement of SA2. Therefore based on view of companies the following proposals is given:

Proposal 3: UE slice MBR information can be updated without update Allowed NSSAI in NGAP.

Q2: Please provide your view on Proposal.

| Company | Do you agree the proposal. | Comment |
| --- | --- | --- |

### XnAP impact

Three company [7][13][20] support to introduce UE slice MBR into the following messages of XnAP:

- HANDOVER REQUEST

- S-NODE ADDITION REQUEST

- S-NODE MODIFICATION REQUEST

In addition, one company [13] support to introduce UE slice MBR into the following message of the XnAP:

- RETRIEVE UE CONTEXT RESPONSE

Proposal 4: To carry UE slice MBR information in the following messages of XnAP:

- HANDOVER REQUEST

- S-NODE ADDITION REQUEST

- S-NODE MODIFICATION REQUEST

- RETRIEVE UE CONTEXT RESPONSE

Q3: Please provide your view on Proposal.

| Company | Do you agree the proposal. | Comment |
| --- | --- | --- |

### F1AP &E1AP impact

Based contributions, the views impact of messages and IE design can achieve consensus.

Proposal 5: To carry UE slice MBR information in the following messages of F1AP:

- UE CONTEXT SETUP REQUEST

- UE CONTEXT MODIFICATION REQUEST

To carry UE slice MBR information in the following messages of E1AP

- BEARER CONTEXT SETUP REQUEST

- BEARER CONTEXT MODIFICATION REQUEST

Q4: Please provide your view on Proposal.

| Company | Do you agree the proposal. | Comment |
| --- | --- | --- |

### S-MBR Enforcement

-S-MBR Enforcement

--RAN is able to reply to the AMF with information indicating that the S-MBR enforcement is not-supported or not-feasible or supported-and-feasible- Ericsson

--No need to indicate to the CN the support of UE Slice MBR enforcement in RAN node- NEC

-Lack of S-MBR Enforcement seems related to both RAN2 and SA2, there is no issue on from RAN3 perspective-Huawei

-lack of S-MBR enforcement in the NG-RAN can be tackled by one of the two option- Nokia

Q5: Please provide your view on this aspect.

| Company | View on S-MBR Enforcement |
| --- | --- |

### Target NSSAI

### NGAP impact

At last meeting , consensus on NGAP impact list below:

To introduce Target NSSAI IE at least in the following messages for NGAP:

- INITIAL CONTEXT SETUP REQUEST

- DOWNLINK NAS TRANSPORT

In addition, one company in [4] propose to introduce Target NSSAI IE in the following messages for NGAP:UE CONTEXT MODIFICATION REQUEST,PATH SWITCH REQUEST ACKNOWLEDGE,HANDOVER REQUEST.

Proposal 6: To introduce Target NSSAI IE in the following messages for NGAP:

UE CONTEXT MODIFICATION REQUEST

PATH SWITCH REQUEST ACKNOWLEDGE

HANDOVER REQUEST

Q6: Please provide your view on Proposal.

| Company | Do you agree the proposal. | Comment |
| --- | --- | --- |

### XnAP impact

One company in [17] propose to introduce Target NSSAI in HANDOVER REQUEST message and RETRIEVE UE CONTEXT RESPONSE message in TS 38.423.

Q7: Please provide your view on this aspect.

| Company | View on Target NSSAI in XnAP |
| --- | --- |

### Any other issue left

Q7: Please provide your view if anything missing.

| Company | Comments |
| --- | --- |

# Conclusion, Recommendations [if needed]

If needed

# References

R3-220200 (TP for TS 38.413) Support for Slice Maximum Bit Rate (Nokia, Nokia Shanghai Bell)

R3-220201 (TP for TS 38.473 and TS 38.463) Support of Slice Maximum Bit Rate  (Nokia, Nokia Shanghai Bell)

R3-220247 Support of Enhancement of RAN slicing - UE Slice MBR and Target NSSAI (NEC)

R3-220438 Introduction of Target NSSAI and SMBR (Ericsson)

R3-220439 LS on S-MBR and Target NSSAI (Ericsson)

R3-220440 Way forward on S-MBR and Target NSSAI (Ericsson)

R3-220663 (TP for NR_Slice for TS 38.413, TS 38.423, TS 38.463 and TS 38.473) Supporting network slicing enhancement (Huawei)

R3-220664 (TP for NR_Slice BLCR for TS 38.300) Supporting  network slicing enhancement (Huawei)

R3-220725 (TP for SON BL CR for TS 38.463) SA2 impact on RAN (China Unicom)

R3-220726 (TP for SON BL CR for TS 38.473) SA2 impact on RAN slicing (China Unicom)

R3-220764 Impact on RAN slicing of UE slice MBR and Target NSSA (ZTE)

R3-220765 (TP for SON BL CR for TS 38.413) SA2 impact on RAN slicing (ZTE)

R3-220766 (TP for SON BL CR for TS 38.423) SA2 impact on RAN slicing (ZTE)

R3-220811 (TP for SON BL CR for TS 37.340) SA2 impact on RAN slicing (China Telecom,ZTE)

R3-220920 Consideration on Target NSSAI in Dual Connectivity (LG Electronics)

R3-220926 (TP for BL CR TS 38.413) Support of Target NSSAI (Samsung)

R3-220927 (CR for TS38.423) RAN slicing enhancement (Samsung)

R3-220944 Discussion on Supporting for UE-Slice-MBR (CATT)

R3-220945 TP to 38.413 for UE-Slice-MBR (CATT)

R3-220946 TP to 38.423 for UE-Slice-MBR (CATT)