3GPP TSG-RAN WG3 #114bis-e	R3-221141

Online, 17 – 26 Jan, 2022

Agenda Item:	17.3

Source:	ZTE(moderator)

Title:	Summary of Offline Discussion on CB: # RANSlicing3_UESliceMB

Document for:	Approval

# Introduction

This contribution is to kick off the following discussion.

CB: # RANSlicing3_UESliceMBR - Continue the discussion on the open issues - For UE slice MBR, decide the solution over NG, e.g., in PDU Session Resource Setup Request message or DL NAS PDU message. And the impact on F1 and E1. - How to support S-MBR Enforcement? Any standard impact? - How to introduce Target NSSAI over NG interface? Establishing the dual connectivity based on the Target NSSAI is not pursed in Rel-17? - LS to SA2? - Capture agreements and provide TPs/BL CRs if agreeable (ZTE - moderator) Summary of offline disc R3-221043rev in R3-221141

Please Note: plan to do two rounds of discussion in this meeting.

The first round email discussion plan to be end 2 hour before on-line session  1st week.(Wednesday 11:00 UTC, 2022-1-19)

The second round email discussion plan to be end 2 hour before deadline of email discussion 2nd week.(Monday 11:00 UTC, 2022-1-24)

# For the Chairman’s Notes

Agreement for discussion:

UE slice MBR information can be signalled as an IE separate from the Allowed NSSAI.

To carry UE slice MBR information in the following messages of NGAP:

  - PDU Session Resource Setup Request

To carry UE slice MBR information in the following messages of XnAP:

-HANDOVER REQUEST

-S-NODE ADDITION REQUEST

-S-NODE MODIFICATION REQUEST

-RETRIEVE UE CONTEXT RESPONSE

To carry UE slice MBR information in the following messages of F1AP:

-UE CONTEXT SETUP REQUEST

-UE CONTEXT MODIFICATION REQUEST

To carry UE slice MBR information in the following messages of E1AP

-BEARER CONTEXT SETUP REQUEST

-BEARER CONTEXT MODIFICATION REQUEST

Removal of the Target NSSAI/RFSP from the UE context should be discussed and agreed in SA2 first, before RAN3 can take any action.

For 2nd Round:

Whether to signal event from NG-RAN to Core network, i.e. the event that S-MBR cannot be enforced.

Detail IE design and work split of stage 2/3/LS.

# Second round Discussion

### UE slice MBR in NGAP/XnAP/F1AP/E1AP

### NGAP

After check IE design from contributions, the moderator would like to suggest the following IE design and text part:

#### 9.3.1.xx	Slice Maximum Bit Rate Value List

This IE defines the rate limit per UE per slice as specified in 23.501 [9].

| IE/Group Name | Presence | Range | IE type and reference | Semantics description |
| --- | --- | --- | --- | --- |
| Slice Maximum Bit Rate Value Item |  | 1..<maxnoofSMBRValues> |  |  |
| >S-NSSAI | M |  | 9.3.1.24 |  |
| >Slice Maximum Bit Rate Downlink | M |  | Bit Rate 9.3.1.4 | This IE indicates the Slice Maximum Bit Rate as specified in TS 23.501 [9] in the downlink direction. |
| >Slice Maximum Bit Rate Uplink | M |  | Bit Rate 9.3.1.4 | This IE indicates the Slice Maximum Bit Rate as specified in TS 23.501 [9] in the uplink direction. |

| Range bound | Explanation |
| --- | --- |
| maxnoofSMBRValues | Maximum no. of SLICE MAXIMUM BIT RATE values for a UE. Value is 8. |

Text proposal suggestion:

If the UE Slice-Maximum Bit Rate List IE is included in PDU SESSION RESOURCE SETUP REQUEST message, the NG-RAN node shall, if supported, store the received UE Slice-Maximum Bit Rate List in the UE context, and use it to enforce for each S-NSSAI for the concerned UE as specified in TS 23.501 [9].

### UE slice MBR in XnAP

After check IE design from contributions, the moderator would like to suggest the following IE design and text part,take R3-220663 as reference except IE design.

#### 9.3.1.xx	Slice Maximum Bit Rate Value List

This IE defines the rate limit per UE per slice as specified in 23.501 [7].

| IE/Group Name | Presence | Range | IE type and reference | Semantics description |
| --- | --- | --- | --- | --- |
| Slice Maximum Bit Rate Value Item |  | 1..<maxnoofSMBRValues> |  |  |
| >S-NSSAI | M |  | 9.3.1.24 |  |
| >Slice Maximum Bit Rate Downlink | M |  | Bit Rate 9.3.1.4 | This IE indicates the Slice Maximum Bit Rate as specified in TS 23.501 [7] in the downlink direction. |
| >Slice Maximum Bit Rate Uplink | M |  | Bit Rate 9.3.1.4 | This IE indicates the Slice Maximum Bit Rate as specified in TS 23.501 [7] in the uplink direction. |

| Range bound | Explanation |
| --- | --- |
| maxnoofSMBRValues | Maximum no. of SLICE MAXIMUM BIT RATE values for a UE. Value is 8. |

### UE slice MBR in E1AP

After check IE design from contributions, the moderator would like to suggest the following IE design and text part,take R3-220663 as reference except IE design.

#### 9.3.1.xx	Slice Maximum Bit Rate Value List

This IE defines the rate limit per UE per slice as specified in 23.501 [20].

| IE/Group Name | Presence | Range | IE type and reference | Semantics description |
| --- | --- | --- | --- | --- |
| Slice Maximum Bit Rate Value Item |  | 1..<maxnoofSMBRValues> |  |  |
| >S-NSSAI | M |  | 9.3.1.24 |  |
| >Slice Maximum Bit Rate Downlink | M |  | Bit Rate 9.3.1.4 | This IE indicates the Slice Maximum Bit Rate as specified in TS 23.501 [20] in the downlink direction. |

| Range bound | Explanation |
| --- | --- |
| maxnoofSMBRValues | Maximum no. of SLICE MAXIMUM BIT RATE values for a UE. Value is 8. |

### UE slice MBR in F1AP

After check IE design from contributions, the moderator would like to suggest the following IE design and text part,take R3-220663 as reference except IE design.

#### 9.3.1.xx	Slice Maximum Bit Rate Value List

This IE defines the rate limit per UE per slice as specified in 23.501 [21].

| IE/Group Name | Presence | Range | IE type and reference | Semantics description |
| --- | --- | --- | --- | --- |
| Slice Maximum Bit Rate Value Item |  | 1..<maxnoofSMBRValues> |  |  |
| >S-NSSAI | M |  | 9.3.1.24 |  |
| >Slice Maximum Bit Rate Uplink | M |  | Bit Rate 9.3.1.4 | This IE indicates the Slice Maximum Bit Rate as specified in TS 23.501 [21] in the uplink direction. |

| Range bound | Explanation |
| --- | --- |
| maxnoofSMBRValues | Maximum no. of SLICE MAXIMUM BIT RATE values for a UE. Value is 8. |

Proposal 2-1: Taken into above IE design and description in the procedure text part for NGAP/XnAP/E1AP/F1AP.

Q2-1: Please provide your view on Proposal.

| Company | Do you agree the proposals. | Comment |
| --- | --- | --- |
| Huawei | Agree with comments | No strong view, just suggest to have the following updates. The IE name as “UE Slice Maximum Bit Rate List”, at least remove the “value” The range can be the same as “maxnoofAllowedS-NSSAIs” |
| CATT | Agree | Share comments with HW. |
| Ericsson | Agree | Same comments as above |

### 38.300 update

In [8], the company propose the following update:

In downlink, for GBR flows, the gNB guarantees the GFBR and ensures that the MFBR is not exceeded while for non-GBR flows, it ensures that the UE-AMBR is not exceeded (see clause 12). When configured for a GBR flow, the gNB also ensures that the MDBV is not exceeded. The gNB in addition ensures that the UE-Slice-MBR is not exceeded as specified in TS 23.501 [3].

NOTE 3:	Through radio protocol configuration and scheduling, the gNB can guarantee the GFBR(s) and ensure that any of the MFBR(s), the UE-AMBR and the UE-Slice-MBR is not exceeded in uplink (see clause 12).

In addition, an Aggregate Maximum Bit Rate is associated to each PDU session (Session-AMBR), to each UE (UE-AMBR) and to each slice per UE (UE-Slice-MBR). The Session-AMBR limits the aggregate bit rate that can be expected to be provided across all Non-GBR QoS Flows for a specific PDU Session and is ensured by the UPF. The UE-AMBR limits the aggregate bit rate that can be expected to be provided across all Non-GBR QoS Flows of a UE and is ensured by the RAN (see clause 10.5.1). The UE-Slice-MBR limits the aggregate bit rate that can be expected to be provided across all GBR and Non-GBR QoS Flows corresponding to PDU Sessions of the UE for the same slice (S-NSSAI) as specified in TS 23.501 [3] and is ensured by the RAN (see clause 10.5.1).

Proposal 2-2: Taken into above update in TS38.300.

Q2-2: Please provide your view on Proposal

| Company | Do you agree the proposals. | Comment |
| --- | --- | --- |
| Huawei | Yes | At least for the second change in section 12 QoS of TS 38.300, the change is needed which is partly belonging to our RAN3 remit. |
| CATT | Yes | For the NOTE 3: Through radio protocol configuration and scheduling, the gNB can guarantee the GFBR(s) and ensure that any of the MFBR(s), the UE-AMBR and the UE-Slice-MBR is not exceeded in uplink (see clause 12). The UE may not ensure if the UE cannot enforce the SMBR as we are discussing now. May add “(if enforced)” after the UE-Slice-MBR |
| Ericsson | See cmments | The following amendment should be applied> NOTE 3: Through radio protocol configuration and scheduling, the gNB can guarantee the GFBR(s) and ensure that any of the MFBR(s), the UE-AMBR and, if feasible, the UE-Slice-MBR is not exceeded in uplink (see clause 12). |

### 37.340 update

In [14][25], companies propose the following update:

-	The MN decides the DL UE Slice MBR and UL UE Slice MBR limits to be assigned to the SN, and indicates these to the SN:

-	The PDCP entity at the SN applies the received DL UE Slice MBR limit to the set of all bearers for which the SN hosts PDCP for the UE;

-	The MAC entity at the SN applies the received UL UE Slice MBR limit to the scheduled uplink radio traffic at the SN for the UE.

Proposal 2-3: Taken into above update in TS37.340.

Q2-3: Please provide your view on Proposal

| Company | Do you agree the proposals. | Comment |
| --- | --- | --- |
| Huawei | Yes |  |
| CATT | Yes |  |

### Whether to signal event from NG-RAN to Core network, i.e. the event that S-MBR cannot be enforced.

During the first round discussion, there is no consensus on this topic while one company explain many company misunderstand the issue. In this sub section,please provide your view focus on the dynamic part of S-MBR can not be enforced.

Can we agree that signal event from NG-RAN to Core network, i.e. the event that S-MBR cannot be enforced and if the answer is yes, can we agree the update in the TP [4] R3-220438 Introduction of Target NSSAI and SMBR.

Q2-4: Please provide your view.

| Company | Comment |
| --- | --- |
| Huawei | No need to signal the “non-support” or “infeasibility” etc to the CN, as we commented above, unless there is such clear requirements/update from SA2. |
| CATT | NO |
| Ericsson | Yes. The mandate from SA2 is already clear. SA2 specifications state that S/MBR can be enforced in UL only “if feasible”, meaning that enforcement may not be feasible. Can companies explain how would an operator understand that, at some point in time, S/MBR enforcement does not occur because the RAN deemed it not feasible? |

### Target NSSAI in NGAP.

During the first round discussion, there is no consensus on this topic. Then the moderator would like to focus on Path switch message.

Proposal 2-4: To introduce Target NSSAI IE in the following messages for NGAP:

PATH SWITCH REQUEST ACKNOWLEDGE

Q2-5: Please provide your view on Proposal

| Company | Do you agree the proposals. | Comment |
| --- | --- | --- |
| Huawei | Not so far | This can be marked as FFS. |
| CATT | No |  |
| Ericsson | Yes | We see that there are no valid technical objections. TS23.501 states the following: the AMF […] may determine a Target NSSAI to be used by the NG-RAN, in addition to the information the AMF receives, such as the Allowed NSSAI and the RFSP for the Allowed NSSAI, to attempt to redirect the UE to a cell and TA in another frequency band and TA that supports the S-NSSAIs in the Target NSSAI If the frequency band/TA in question is not available at the current serving cell (which is an option contemplated by the SA2´s specs with the “to attempt” text) the RAN cannot redirect the UE. As soon as the target frequency/TA is available (i.e. when it overlaps in coverage with the serving cell) the RAN will redirect the UE. The question is: what happens if the UE hands over to a different RAN node *before* redirection to the target frequency/TA can be performed? The obvious answer is that the Target NSSAI is transferred to the target RAN, so that the Target RAN can in its turn search for the available target frequency/TA and, when available, redirect the UE there. For this reason it is needed that the Target NSSAI is included in the PATH SWITCH REQUEST ACK. If this is objected, then it should be explained how the issue is resolved. |

### LS for SA2

In [5], the company provide an LS for SA2.

Do we need to send LS for SA2 at this meeting ? and  if the answer is yes, can we agree R3-220439 or provide your update comments.

Q2-6: Please provide your view.

| Company | Comment |
| --- | --- |
| Huawei | We don’t see the need. |
| CATT | No need |
| Ericsson | We for sure need to tell SA2 of the progrsss in implementing their own specifications. Do companies want to send an LS at the next meeting? If yes, we are ok with that but we need to send an LS sooner or later. |

### Anything missing

| Company | Comment |
| --- | --- |

# First Round Discussion

### Impact on RAN slicing of UE slice MBR

### NGAP impact

The following table provide the summary of each impacted message with supported companies.

| Message Company | Initial Context Setup Request | Initial Context Modification Request | PDU Session Resource Setup Request | Downlink NAS transport | Handover Request | PATH SWITCH REQUEST ACKNOWLEDGE | CONNECTION ESTABLISHMENT INDICATION | UE Information Transfer | AMF CP RELOCATION INDICATION | REROUTE NAS REQUEST |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Nokia[1] |  |  |  |  |  |  |  |  |  |  |
| Ericsson[4] | Y | Y | Y | Y | Y | Y | Y |  |  |  |
| Huawei[7] | Y | Y | Y | Y | Y | Y |  |  |  |  |
| ZTE[12] |  |  | Y | Y |  | Y | Y | Y | Y | Y |
| CATT[19] |  |  |  | Y |  |  |  |  |  |  |

Table 1 views on UESliceMBR message impact

For PDU Session Resource Setup Request message, it is observed that UE-AMBR has already been included.As we can see there is no UE-AMBR IE in PDU session level messge, but in 38.413.f30, the UE-AMBR IE was introduced in  PDU Session Resource Setup procedure. The motivation is when UE-AMBR is not provided by AMF in initial context setup messge, there is no way for Core network to control bit rate of the UE via UE-AMBR.  The principal is same for Slice-MBR.  In this way, Core network can provide Slice level rate control after Initial UE context setup toward the UE. Please check the corresponding CR in R3-190971.

For Downlink NAS transport message, it is observed that both Allowed NSSAI and UE-AMBR has already been included. It is straightforward fro AMF to provide UE-Slice-MBR to the RAN in this message.

For other messages e.g. PATH SWITCH REQUEST ACKNOWLEDGE message,CONNECTION ESTABLISHMENT INDICATION messages etc, it is observed that Allowed NSSAI has already been included. It is possible to update the UE-Slice-MBR to RAN in these message.

Based on views from the company, PDU Session Resource Setup Request and  Downlink NAS Transport message got the most support and can be supported for NGAP.

Proposal 1: To carry UE slice MBR information in the following messages of NGAP:

- PDU Session Resource Setup Request

- Downlink NAS Transport

Based on views from the company, at least 1 company to support the following message in NGAP.

Proposal 2: To carry UE slice MBR information in the following messages of NGAP:

- PATH SWITCH REQUEST ACKNOWLEDGE

- CONNECTION ESTABLISHMENT INDICATION

- UE Information Transfer

- AMF CP RELOCATION INDICATION

- REROUTE NAS REQUEST

Q1: Please provide your view on Proposals.

| Company | Do you agree the proposals. | Comment |
| --- | --- | --- |
| Ericsson | Agree on Proposal 1, partially agree to Proposal 2 | We agree to include the S-MBR in the following messages: Initial Context Setup Request: This may be the first UE associated message, hence S-MBR is needed here for PDU Sessions to be established Initial Context Modification Request: The S-MBR may be updated and for that it needs to be added in the context modification procedure PDU Session Resource Setup Request: For cases where the S-MBR is signalled or modified at PDU Session setup Downlink NAS transport: This might be the first UE associated message, hence S-MBR may be added here. However, addition here is less important as a DL NAS Transport does not imply that establishment of UP will happen. Handover Request: This is needed to pass the S-MBR to target RAN during NG based HOs PATH SWITCH REQUEST ACKNOWLEDGE: This is needed to pass the S-MBR to target RAN during Xn based HOs CONNECTION ESTABLISHMENT INDICATION: This might be the first UE associated message, hence S-MBR may be added here. However, addition here is less important as a CONNECTION ESTABLISHMENT INDICATION does not imply that establishment of UP will happen. We believe that with the above additions all cases for transfer of S-MBR are covered. |
| Nokia | Partly proposal 1 depending on Q2 NOK proposal 2 | Q1 depends on question Q2! Proposal 1 If S-MBR is added within allowed NSSAI (Q2 option 1) then no additional message is needed compared to those agreed last time. If S-MBR is provided separate from Allowed NSSAI at message level (option 2*), it is also needed also in the PDU Session Setup Request. Proposal 2 Only the Path switch request ack could be relevant but it is proposed below to send instead the S-MBR using the Xn HO Request instead. The rest of messages is not needed. |
| Samsung | Proposal 1 is OK, Proposal 2 is NOK | In our views, the UE-Slice-MBR is one kind of UE context, so the messages including this information should be either the first UE associated message from CN or UE context related messages. Besides the messages in proposal 1, we think below messages can also include UE-Slice-MBR. - INITIAL CONTEXT SETUP REQUEST message - UE CONTEXT MODIFICATION REQUEST message - HANDOVER REQUEST message Based on our understanding, we don’t see the need of the messages in proposal 2 to include the UE-Slice-MBR, if UE-Slice-MBR need to be updated, the UE CONTEXT MODIFICATION REQUEST message can be used. |
| Huawei | OK for proposal 1 partially ok to Proposal 2 | Proposal 2: only the path switch request acknowledge is needed. For the rest messages, we don’t see the need. |
| LGE | OK for Proposal 1 NOK for Proposal 2 | Agree with Samsung. We also think that the S-MBR can be included into the following NGAP messages: INITIAL CONTEXT SETUP REQUEST message UE CONTEXT MODIFICATION REQUEST message HANDOVER REQUEST message We think that the PATH SWITCH REQUEST ACK message can be used instead of the Xn HANDOVER REQUEST message in order to maintain the latest S-MBR at NG-RAN node. |
| ZTE | OK for proposal 1/2 |  |
| CMCC | P1 OK, P2 partially OK | We share view with HW. |
| CATT |  | Depend on the option choice, if we carry it with allowed NSSAI, all the message include allowed NSSAI implicitly include the UE-SMBR and we just add allowed NSSAI in UE CONTEXT MODIFICATION REQUEST. |

The following options discussed without achieve consensus at last meeting.

Signaling impact of introduce UE Slice MBR in NGAP takes following options as start point:

Option 1:  AMF provides UE Slice MBR as optional element within the Allowed NSSAI.

Option 2:  AMF provides UE Slice MBR in the way as UE AMBR.

The following table provide the summary of IE design from contribution.

| Option Company | Option 1 | Option 2 |
| --- | --- | --- |
| Nokia[1] | Y |  |
| NEC[3] |  | Y |
| Ericsson[4] |  | Y |
| Huawei[7] |  | Y |
| ZTE[12] |  | Y |
| CATT[19] | Y |  |

Table 2 views on UESliceMBR IE impact

As described in the SA2’s CR[S2-2104908] for TS23.502, it is observed that AMF may update UE-Slice-MBR after initial context setup. Instead of update Allowed NSSAI together , it is possible for AMF to only provide update UE-Slice-MBR to the RAN node.

The AMF takes appropriate action according to the changed subscriber data as follows, e.g.: - initiating an AMF initiated Deregistration procedure if the updated subscription data indicates the UE is not allowed to roam in this network; and - updating UE context stored at AN to modify the UE-AMBR. - updating UE context stored at RAN to modify the UE-Slice-MBR corresponding to an S-NSSAI. - initiating UE Configuration Update procedure as defined in clause 4.2.4.2. - initiating UE Parameters Update via UDM Control Plane Procedure as defined in clause 4.20.

Option 2 provide more flexibility to support the above requirement of SA2. Therefore based on view of companies the following proposals is given:

Proposal 3: UE slice MBR information can be updated without update Allowed NSSAI in NGAP.

Q2: Please provide your view on Proposal.

| Company | Do you agree the proposal. | Comment |
| --- | --- | --- |
| Ericsson | Yes | We agree that the S-MBR is a totally independent piece of information from the Allowed NSSAI and that nesting the S-MBR inside the Allowed NSSAI creates an unnecessary dependency. Hence we agree with Proposal 3 |
| Nokia | Yes | Both option 1 and option 2 are doable and have pros and cons. We are ok to follow the majority with option 2 if this means that a list of S-MBRs is provided at message level. |
| Samsung | Yes | We think that’s the reason why UE-Slice-MBR can be signaled independent of Allowed NSSAI, so we prefer option 2. |
| Huawei | Yes | Agree after the pros and cons analysis. |
| NEC | Yes |  |
| LGE | Yes | We also agree that the S-MBR can be updated independent of Allowed NSSAI. |
| ZTE | Yes |  |
| CMCC | Yes |  |
| CATT | Yes |  |

### XnAP impact

Three company [7][13][20] support to introduce UE slice MBR into the following messages of XnAP:

- HANDOVER REQUEST

- S-NODE ADDITION REQUEST

- S-NODE MODIFICATION REQUEST

In addition, one company [13] support to introduce UE slice MBR into the following message of the XnAP:

- RETRIEVE UE CONTEXT RESPONSE

Proposal 4: To carry UE slice MBR information in the following messages of XnAP:

- HANDOVER REQUEST

- S-NODE ADDITION REQUEST

- S-NODE MODIFICATION REQUEST

- RETRIEVE UE CONTEXT RESPONSE

Q3: Please provide your view on Proposal.

| Company | Do you agree the proposal. | Comment |
| --- | --- | --- |
| Ericsson | Yes, with comments | It should be specified that for DC related messages the portion of the S-MBR decided by the MN is signalled and not the S-MBR |
| Nokia | Yes | Same comment as Ericsson: we assume that it means that a share of the S-MBR is sent for the DC case. |
| Samsung | Yes, with comments | Same comment as E///, for DC case, it’s the S-NG-RAN node UE Slice Maximum Bit Rate signaled in S-NODE ADDITION REQUEST message and S-NODE MODIFICATION REQUEST message, which had already been agreed in the last meeting, so we proposed the CR for TS 38.423 R3-220927 [17] based on the agreements in the last meeting (please note that the Target NSSAI part in the CR can be FFS) |
| Huawei | Yes | Agree to specify the portion of the UE-Slice-MBR. This is captured in our [R3-0220663] already e.g., in the semantic descriptions in the same way as UE-AMBR. The UE Slice Maximum Bit Rate List is split into M-NG-RAN node UE Slice Maximum Bit Rate List and S-NG-RAN node UE Slice Maximum Bit Rate List which are enforced by M-NG-RAN node and S-NG-RAN node respectively. |
| NEC | Yes |  |
| LGE | Yes | Same view with Ericsson |
| ZTE | Yes |  |
| CMCC | Yes | And agree to send the portion of S-MBR to SN for DC case. |
| CATT | Yes | Should be split SMBR |

### F1AP &E1AP impact

Based contributions, the views impact of messages and IE design can achieve consensus.

Proposal 5: To carry UE slice MBR information in the following messages of F1AP:

- UE CONTEXT SETUP REQUEST

- UE CONTEXT MODIFICATION REQUEST

To carry UE slice MBR information in the following messages of E1AP

- BEARER CONTEXT SETUP REQUEST

- BEARER CONTEXT MODIFICATION REQUEST

Q4: Please provide your view on Proposal.

| Company | Do you agree the proposal. | Comment |
| --- | --- | --- |
| Ericsson | Yes |  |
| Nokia | Yes |  |
| Samsung | Yes |  |
| Huawei | Yes |  |
| NEC | Yes |  |
| LGE | Yes |  |
| ZTE | Yes |  |
| CMCC | Yes |  |
| CATT | Yes |  |

### S-MBR Enforcement

-S-MBR Enforcement

--RAN is able to reply to the AMF with information indicating that the S-MBR enforcement is not-supported or not-feasible or supported-and-feasible- Ericsson

--No need to indicate to the CN the support of UE Slice MBR enforcement in RAN node- NEC

-Lack of S-MBR Enforcement seems related to both RAN2 and SA2, there is no issue on from RAN3 perspective-Huawei

-lack of S-MBR enforcement in the NG-RAN can be tackled by one of the two option- Nokia

Q5: Please provide your view on this aspect.

| Company | View on S-MBR Enforcement |
| --- | --- |
| Ericsson | The fact that S-MBR enforcement may be supported, but not feasible, has been confirmed by both SA2 and RAN2 as in the excerpts reported below: Excerpt from TS23.501 5.7.1.10 UE-Slice-MBR enforcement and rate limitation If a supporting RAN receives for a UE a UE-Slice-MBR (see clause 5.7.2.6) for an S-NSSAI from the AMF, the RAN shall apply this UE-Slice-MBR for all PDU Sessions of that UE corresponding to the S-NSSAI which have an active user plane if feasible. Excerpt from R2-2111400 Support of QoS - NG-RAN supports QoS differentiation within a slice, and per Slice-Maximum Bit Rate may be enforced per UE, if feasible. How NG-RAN enables UE-Slice-MBR enforcement and rate limitation (see TS 23.501 [3]) is up to network implementation. Hence RAN3 shall not re-discuss this very clear point and simply accept that S-MBR enforcement may not be feasible. The problem cannot be solved by limiting the number of slices accessible in parallel by a UE because the problem occurs when a channel group contains DRBs of different slices. DRBs are cropped together in a channel group when they share the same RRM treatment, hence even with few slices supported in parallel, the issue may occur. Therefore, we see at least the need to define a proper indication from RAN to AMF, stating that S-MBR enforcement is not feasible. With this, the operator has visibility over the fact that slice bit rate for a UE is not controlled. The latter can be used for monitoring and billing, for example. Hence we propose that the RAN notifies the AMF at least for the case where S-MBR enforcement is not feasible. |
| Nokia | As explained in tdoc [1] it is always possible for gNB to enforce the S-MBR. If the DU is not able to enforce it, it is still possible for the CU UP to shape the corresponding traffic at DRB level. This would just require CU CP to send the appropriate S-MBR also to the CU UP in case of split architecture. Also, in case DU cannot enforce the UL S-MBR, there is nothing AMF can do except triggering the PCF method dynamically while this coupling was not foreseen by SA2. If this is for monitoring purpose RAN O&M can do it itself towards the operator. |
| Samsung | We’d like to ask does UE-AMBR have the same story? How did RAN3 handle the problem of UE-AMBR before? |
| Huawei | For the NG-RAN node capability of UE-slice-MBR enforcement, we agree with NEC that this is up to the OAM, and there is no need to exchange the NG-RAN node capability. For the feasibility of the UE-slice-MBR enforcement, RAN2 has already specified that this is up to the network implementation. From our perspective, we don’t see the need for the NG-RAN to report the feasibility to the AMF. If anything else is needed, we agree with Nokia that the RAN O&M can be involved. |
| NEC | While it may be “feasible” to have an indication, to be clear enough whether the NG-RAN node will do the enforcement or not, per PDU Session, if not, then the UPF need to do the enhancement. However, this is likely again to discuss whether need to have node capability indication to the peer node, while the proponent is having different wording to say ”feasible” or “not-feasible”. Therefore, think for the moment this can up to OAM. |
| ZTE | Would like prevent the way to provide node capability to Core. |
| CMCC | Our understanding is that it is always feasible for NG-RAN to enforce DL Slice MBR, as analyzed by Nokia. And the controversial part focuses on the enforcement of UL Slice MBR, for which RAN2 provided the running CR indicating that the enforcement is up to network implementation. So it is unclear that why there are cases that the network implementation is not feasible to enforce the UL Slice MBR. For the condition that UL Slice MBR cannot be temporarily enforced due to that QoS flows from different slices can be mapped to the same DRB, our understanding is that the network implementation is able to reconfigure the mapping appropriately to enforce UL Slice MBR. |
| CATT | We share with NEC. If OAM can be involved for this issue solved instead of the indication capability |
| Ericsson Response | We would like to clarify that we do not propose to signal node capabilities to the AMF. An NG-RAN node may be capable to support and enforce the S-MBR. However, as confirmed in SA2 and in RAN2´s specs, such enforcement is only possible when “feasible”. Namely the enforcement is only possible when DRBs of different slices are not mixed in the same channel group. We not that there is no specification stating that a channel group shall contain only DRBs of the same slice… Therefore, what we propose to signal to the AMF is an indication that, at a certain point in time, S-MBR enforcement is not feasible. This is not a capability, but an event. To reply to Samsung´s question: How did RAN3 handle the problem of UE-AMBR before? There is no enforcement problem with the AMBR because the UE-AMBR acts on ALL DRBs and not only on those from a certain slice. Hence the enforcement in UL can take place by policing the UL grants on all channel groups. The S-MBR is different because it is based on policing the UL grants only for DRBs of a certain slice. If a channel group contains DRBs of different slices, UL grants policing does not work anymore. |

Based on majorities view,

Conclusion: No notification from RAN to the AMF for the case where S-MBR enforcement is not feasible.

### Target NSSAI

### NGAP impact

At last meeting , consensus on NGAP impact list below:

To introduce Target NSSAI IE at least in the following messages for NGAP:

- INITIAL CONTEXT SETUP REQUEST

- DOWNLINK NAS TRANSPORT

In addition, one company in [4] propose to introduce Target NSSAI IE in the following messages for NGAP:UE CONTEXT MODIFICATION REQUEST,PATH SWITCH REQUEST ACKNOWLEDGE,HANDOVER REQUEST.

Proposal 6: To introduce Target NSSAI IE in the following messages for NGAP:

UE CONTEXT MODIFICATION REQUEST

PATH SWITCH REQUEST ACKNOWLEDGE

HANDOVER REQUEST

Q6: Please provide your view on Proposal.

| Company | Do you agree the proposal. | Comment |
| --- | --- | --- |
| Ericsson | Yes | Inclusion in the UE CONTEXT MODIFICATION REQUEST is needed to update the Target NSSAI, in case there are changes to it. Inclusion in the PATH SWITCH REQUEST ACKNOWLEDGE and HANDOVER REQUEST is needed to communicate the Target NSSAI to a target RAN after Xn based HO. This is in case the UE was not yet moved to the target frequency/cell where the Target NSSAI can be served. In this case the RAN needs to be informed of the Target NSSAI to try and move the UE to a cell/frequency where it can be served. |
| Nokia | No | In SA2 TS 23.502 the Target NSSAI is provided only at registration time and UCU (UE Configuration Update) which means NGAP Initial Context Setup and DL NAS Transport. See section 4.2.2 and 4.2.4. The proposal in [4] to store the target NSSAI for later reuse is harmful and doesn’t work. The gNB could end up selecting a cell which is outside the RA of the UE which would be very damaging. Even if the cell is within the RA this means that the UE is not handed over the to the best cell which is also detrimental. SA2 has only defined Target NSSAI to be used in relation with immediate “redirection” feature. The proposal in [4] is against SA2 assumption and is harmful. |
| Samsung | Partially yes | In our views, the Target NSSAI is one kind of UE context, so it can be included in UE CONTEXT MODIFICATION REQUEST in case of update, but we don’t see the need to include it in the PATH SWITCH REQUEST ACKNOWLEDGE and HANDOVER REQUEST, we acknowledge the case mentioned by E///, but we think another way is to store the Target NSSAI in the serving gNB, if there’s no proper cell to redirect, and the Target NSSAI can be propagated during mobility, in case the next target gNB can redirect the UE to a proper cell according to the Target NSSAI. |
| Huawei | No | At this stage we share the view from Nokia, unless SA2 has such requirement. Another point is that after the HO, the target NSSAI may be outdated due to the change of the serving RAN node (with different slice support list). To transfer these outdated NSSAI may have detrimental consequences. |
| Samsung2 | Reply to HW | Target NSSAI may include S-NSSAIs in Rejected NSSAI and Allowed NSSAI, if the RA (with the same slice support) is not changed for the UE, we don’t think the Target NSSAI will be outdated. |
| LGE | No | Same view with Nokia and Huawei. We can re-discuss this proposal if there is a new requirement from SA2. |
| ZTE | Yes |  |
| CMCC | Partially yes | It seems that we can agree on that Target NSSAI should be maintained updated, otherwise it would be harmful. For the case without mobility, as commented by Nokia, if Target NSSAI can only be provided to UE upon registration or UCU as specified in 23502, then Initial Context Setup Request and DL NAS Transport would be enough for NG-RAN to understand the most updated Target NSSAI. And no need to add Target NSSAI in UE Context Modification Request. While for the case with mobility, as commented by Samsung, the NAS UCU procedure may not be performed upon NG or Xn based HO, so for the cases that UCU is not performed, the target node has no clue on which cell to redirect the UE without the information of Target NSSAI. So it is needed to add Target NSSAI in Path Switch Request ACK and HO Req. |
| CATT | No | Share with HW |
| Ericsson Reply |  | We do not understand the comment from Nokia “The gNB could end up selecting a cell which is outside the RA of the UE which would be very damaging.” Obviously, the Target NSSAI contains rejected S-NSSAIs, which are most likely not supported/allowed in the current RA. It is therefore obvious that the UE will need to be mover to a different RA for such rejected S-NSSAIs to be accessible. Note that there is no guarantee that the serving RAN will be able to move the UE to a cell/frequency layer where the Target NSSAI is supported. This is the case where we think that forwarding the Target NSSAI is beneficial, because the need for the UE to access the Target NSSAI still exists. |

Conclusion:  No consensus , to be continue.

### XnAP impact

One company in [17] propose to introduce Target NSSAI in HANDOVER REQUEST message and RETRIEVE UE CONTEXT RESPONSE message in TS 38.423.

Q7: Please provide your view on this aspect.

| Company | View on Target NSSAI in XnAP |
| --- | --- |
| Ericsson | In our view this is not needed because signalling of the Target NSSAI shall always be performed by the CN. If the CN has no control over signalling of the Target NSSAI it might occur that there is no more need for the RAN to move the UE where the Target NSSAI is supported but still, the Target NSSAI may be propagated via Xn HO signalling. |
| Nokia | NOK. See also answer to previous question Q6. The Target NSSAI has been defined in relation with the redirection feature. It is not stored in the gNB because of no value after the redirection, and therefore not propagated at Xn handover. |
| Samsung | As we commented in Q6, we see the benefits of storing the Target NSSAI. It is possible that the current serving gNB cannot find the most suitable cell to redirect the UE when receiving the Target NSSAI, if the Target NSSAI is stored and propagated during handover, it is also possible that the target gNB has a neighbor that supports all the slices in Target NSSAI, then it can redirect the UE to the most suitable cell. Besides, we think Target NSSAI can also help the serving gNB to choose the SCG resource in DC scenario if the SCG can be outside of the RA. |
| Huawei | Not OK now, unless there is such requirement from SA2. |
| NEC | Understand that the Target NSSAI is for the redirection purpose at the registration as described in SA2 spec, share the same as above companies views, so for the moment think no need to give the Target NSSAI in Xn Handover. |
| LGE | Same view with Nokia and Huawei. |
| ZTE | Not necessary, Core network can provide the Target NSSAI. |
| CMCC | We share view with Ericsson. If Target NSSAI can be added in PS Req ACK, then there might be no need for introduction of Target NSSAI over Xn. |
| CATT | Not needed |

Based on majorities view:

Conclusion: No XnAP impact of Target NSSAI.

### Any other issue left

Q7: Please provide your view if anything missing.

| Company | Comments |
| --- | --- |
| Ericsson | We have the additional proposal: It is proposed that signaling is introduced for removing the Target NSSAI and Target RFSP value from the UE context. Considering that reception of the Target NSSAI by the RAN constitute a mandate to move the UE to a cell/frequency where the Target NSSAI is served, we see the need to also remove such mandate, in case such need does not exist anymore. Not having an indication of Target NSSAI removal may imply that the RAN constantly tries to move the UE to a cell/frequency where the Target NSSAI is served, even when such mobility is not needed. |
| Nokia | Ericsson proposal above is NOK. It is related to proposal in [4] which is not aligned with SA2 and harmful. See answer to Q6. |
| Samsung | After introducing Target NASSI information in TS 38.413 (according to current BL CR), there are two Index to RAT/Frequency Selection Priority IEs in INITIAL CONTEXT SETUP REQUEST message and DOWNLINK NAS TRANSPORT message in different IE levels. We think clarification on those two IEs is needed. |
| Huawei | 1 on the Ericsson’s proposal, this removal of target NSSAI is not described in SA2. We think this can be hold till SA2 has such update or requirement. 2 we have R3-220664 TP for TS 38.300, it is appreciated to be discussed in the 2nd round. 3 on the Samsung’s proposal, we think these two RFSPs are needed, one is associated with allowed NSSAI, one is associated with target NSSAI. |
| Samsung2 | Reply to HW, thanks for the clarification, it seems two IEs are needed, but we noticed that the statement in current specification may lead misunderstandings, if two RFSP IEs exit in the same message, the NG-RAN node will store both IEs, we can take the descriptions of the INITIAL CONTEXT SETUP REQUEST message below for example Upon receipt of the INITIAL CONTEXT SETUP REQUEST message the NG-RAN node shall - attempt to execute the requested PDU session configuration; - store the received UE Aggregate Maximum Bit Rate in the UE context, and use the received UE Aggregate Maximum Bit Rate for Non-GBR QoS flows for the concerned UE as specified in TS 23.501 [9]; - store the received Mobility Restriction List in the UE context; - store the received UE Radio Capability in the UE context; - store the received Index to RAT/Frequency Selection Priority associated with Allowed NSSAI in the UE context and use it as defined in TS 23.501 [9]; Once these two RFSP IEs are received, the NG-RAN shall store them no matter which IE level they are in, but whether to store Target NSSAI info including the corresponding RFSP is FFS. Another concern is that do we need to state clearly the relationship between RFSP and Allowed NSSAI/Target NSSAI in RAN3 specification. So one possible revision suggestion is to add “associated with Allowed NSSAI” as above. |
| LGE | For Ericsson’s proposal, we also have same view with Nokia and Huawei. In current SA2 specification, there is no requirement for Ericsson’s proposal. |
| CATT | Looks the draftCR for 37.340 is missed which CATT submitted and CT/ZTE also provide the TP with same contents with CATT R3-220943 BLCR to 37.340 for Enhancement of RAN Slicing R3-220811 (TP for SON BL CR for TS 37.340) SA2 impact on RAN slicing |

Stage 2 can be discussed at 2nd round discussion.

# Conclusion, Recommendations [if needed]

If needed

# References

R3-220200 (TP for TS 38.413) Support for Slice Maximum Bit Rate (Nokia, Nokia Shanghai Bell)

R3-220201 (TP for TS 38.473 and TS 38.463) Support of Slice Maximum Bit Rate  (Nokia, Nokia Shanghai Bell)

R3-220247 Support of Enhancement of RAN slicing - UE Slice MBR and Target NSSAI (NEC)

R3-220438 Introduction of Target NSSAI and SMBR (Ericsson)

R3-220439 LS on S-MBR and Target NSSAI (Ericsson)

R3-220440 Way forward on S-MBR and Target NSSAI (Ericsson)

R3-220663 (TP for NR_Slice for TS 38.413, TS 38.423, TS 38.463 and TS 38.473) Supporting network slicing enhancement (Huawei)

R3-220664 (TP for NR_Slice BLCR for TS 38.300) Supporting  network slicing enhancement (Huawei)

R3-220725 (TP for SON BL CR for TS 38.463) SA2 impact on RAN (China Unicom)

R3-220726 (TP for SON BL CR for TS 38.473) SA2 impact on RAN slicing (China Unicom)

R3-220764 Impact on RAN slicing of UE slice MBR and Target NSSA (ZTE)

R3-220765 (TP for SON BL CR for TS 38.413) SA2 impact on RAN slicing (ZTE)

R3-220766 (TP for SON BL CR for TS 38.423) SA2 impact on RAN slicing (ZTE)

R3-220811 (TP for SON BL CR for TS 37.340) SA2 impact on RAN slicing (China Telecom,ZTE)

R3-220920 Consideration on Target NSSAI in Dual Connectivity (LG Electronics)

R3-220926 (TP for BL CR TS 38.413) Support of Target NSSAI (Samsung)

R3-220927 (CR for TS38.423) RAN slicing enhancement (Samsung)

R3-220944 Discussion on Supporting for UE-Slice-MBR (CATT)

R3-220945 TP to 38.413 for UE-Slice-MBR (CATT)

R3-220946 TP to 38.423 for UE-Slice-MBR (CATT)

R3-220943 BLCR to 37.340 for Enhancement of RAN Slicing (CATT)