3GPP TSG-RAN WG3 #114-bis-e						R3-221017

17-26 Jan 2022

Online

Agenda Item:	10.2.1.4

Source:	ZTE (moderator)

Title:	Summary of Offline Discussion on CB: # SONMDT2_UEHistoryInfor

Document for:	Approval

# Introduction

CB: # SONMDT2_UEHistoryInfor

- Continue the discussion on the open issues from last meeting

- Check the details of TPs

- Try to close this topic, capture agreements and update the TPs if agreeable

(ZTE - moderator)

Summary of offline disc R3-221017

It is proposed to divide the discussion into two phases:

-	Phase 1: Identify the issues to be discussed in RAN3

Deadline: Please provide your views by 8:00am UTC Wednesday January 19th

-	Phase 2: Further discussion to capture agreements and open issues

Deadline: TBD pending on the outcome of Phase 1

# For the Chairman’s Notes

[TBD]

# Phase 1 discussion

## Time information for SN UHI

In the last meeting, it is still FFS whether to include time spent without SCG or time stamp in SN UHI to correctly judge SN ping pong error and correlate MN and SN UHI. The reasons for each camp are listed as follows.

Time stamp:

- Time spent without SCG will cause accumulating inaccuracy issue over the duration of DC operation which is not good for the correlation. Timestamp helps avoid this issue [1].

- A rudimentary synchronisation is plenty enough to use timestamp for UHI [1].

- The synchronization between MN and SN can be avoided by sending the timestamp of SN release. MN can then use the timestamps in the SN UHI together with SN release time to achieve the correlation with MN UHI and the current time at MN [9].

- The specification impact is less if the Time Stamp IE is reused in SN UHI. There will be a correlation error due to the time delay between SN sending SN UHI and MN receiving SN UHI if Time spent without SCG and time stay parameters are used to achieve the correlation [12].

Time spent without SCG:

- Using timestamp in SN UHI is more cumbersome as this involves either defining absolute timestamps (e.g., UTC) at the time of PSCell setup/release or relative timestamps from a reference point [3][4].

- Add the time stamps in the SN UHI will increase the specification works [4].

- Time spent without SCG is easy for MN to achieve the correlation. It is complex to extract the time duration without SCG using timestamp [5].

- This information can be used to enhance understanding of previous UE choices in terms of DC [9].

We have already discussed this issue in several meetings and it seems that both camps stay the same position. Moderator would suggest a hybrid scheme including both two parameters as a compromise. An example is given in the following figure to illustrate how to achieve the correlation based on the hybrid scheme. We can design the time stamp as the absolute time when a PSCell is added, thus the MN is aware of the starting time t1, t3, and t5 for each PSCell. Since we have agreed to include time UE stayed in the cell in SN UHI, MN can derive the corresponding leaving time t2, t4, and t6 for each PSCell according to the time stay parameters T1, T2, and T3 for each PSCell. But if the time UE stayed in the cell IE exceeds its limit, e.g. the limit is 4095 but T2 > 4095, then T2 will be set to 4095 and the calculated leaving time t’4 is wrong (PSCell 2 will only be correlated to PCell 1 instead of both PCell 1 and PCell 2 with this wrong information). When the the time UE stayed in the cell IE exceeds its limit, we can use time spent without SCG to calculate the correct leaving time of this PSCell, e.g. using the time spent without PSCell 2 T4 with t5 to derive the correct t4.

Question 1: Companies are kindly asked which option below is preferred.

- Time stamp

- Time spent without SCG

- Hybrid solution including both Time stamp and Time spent without SCG

| Company | Option | Comment |
| --- | --- | --- |
| ZTE | 1) or 3) | UHI does not require strict synchronization, and the time differences among different base stations are very small. Thus the synchronization issue pointed out by the opponents is not critical. A correlation error will be caused if we only use 2) to achieve the correlation as analyzed in [12]. We think only including time stamp is enough, but we can accept 3) as a compromise. |
| CATT | 2) | In our opinion, this issue is about how to correlate MN and SN UHI. There are two solutions, time stamp or time stay in SN UHI. Both solutions can work, but time stamp needs extra work to keep aligned between MN and SN. So, we prefer time stay in SN UHI to time stamp. For time spent without SCG, it is MN to add time spent without SCG in correlated MN and SN UHI when SN is removed. In other words, it is not added in SN UHI by SN, So it is not used by MN to correlate MN and SN UHI. |
| Lenovo and Motorola Mobility | 1) | The issue due to synchronization among gNBs/eNBs is negligible, and Option1 is better for MN to achieve the correlation. Option 3 is acceptable when the time UE stayed in the cell IE exceeds the limit. |
| Nokia | Nothing or 1 | Please note, “time without SCG/PSCell” or the timestamps are relevant only in the inter-MN signalling – as long as the UE stays within the same SN, the MN can measure it itself. However, the motivation for providing them is disputable: once the PSCells are mapped to the PCells and the time stayed in each PSCell is provided, the target SN has all it needs. |
| Samsung | None | For Time information for SN UHI, “time stay in SN UHI” was already agreed. UE history information of secondary node includes: PSCell list, time UE stayed in the cell Time stay in SN UHI from SN to MN is enough for correlating MN and SN UHI in MN. We agree with CATT for this point. SON is based on statistics. The overall mechanism should be easy to be implemented by real products. Ping-Pong detection has been a good feature in legacy SON mechanism. The proposed mechanism so far is too complex to be used. We really doubt companies will implement the correlation as in above Figure. |

## How MN subscribes to PSCell changes from SN

In the last meeting, we have agreed that MN may also subscribe to PSCell changes from SN, thus we need to consider how to achieve the subscription. According to the contributions, there are two options:

Option 1: Add a flag indicating subscription of PSCell changes to the SN addition request and/or SN modification request messages.

Option 2: Use the existing Location Information at S-NODE Reporting and Location Information at S-NODE IE

The reasons for each camp are listed as follows.

Option 1:

- The Location Reporting procedure is originally designed to acquire the UE location related information. It would be better to avoid reusing the same procedure for a different purpose [3][4][12].

- The Location Reporting procedure is initiated by AMF and NG-RAN has no control on the subscription parameters. It would be more straightforward to introduce a new subscription mechanism initiated by NG-RAN without AMF involvement [3][5][12].

- The usage of the Location Information Reporting mechanism may need authorization due to security concerns [12].

Option 2:

- The use of this scheme is not only limited to the location information. MN can record the entry time to the PSCell itself based on the provided new PSCell ID from SN [1][18].

Question 2: Companies are kindly asked which option above is preferred.

| Company | Option | Comment |
| --- | --- | --- |
| ZTE | 1 | Adding a new indicator for subscription initiated by NG-RAN is more straightforward, and it is not a big cost. |
| CATT | 1 | Agree with ZTE |
| Lenovo and Motorola Mobility | 1 | The existing Location Reporting procedure is initiated by AMF, it is better to introduce a separate subscription mechanism initiated by RAN node. |
| Nokia | 2 | The only part reused is the request from the MN to the SN (single IE) – there is no dependency on AMF or MME (location reporting may be initiated by AMF/MME, but the use of the IE is not!). Plenty of IEs are shared among features and it is never a problem. On the contrary, it is recommended not to duplicate the same functionality in multiple IEs! If needed, the existing IE may be enhanced, e.g. more codepoints added. This depends on the actual needs (so far it seems no enhancements are needed). |
| Samsung | 2 | In RAN3, the procedure text is normally from the receiving node side, not from the sending node side. The benefit for this is that one IE is added based on one scenario. It can also be used for other scenarios. In the S-NODE ADDITION REQUEST message, “Location Information at S-NODE reporting” IE is included. The description in TS38.423 is as follow for convenience: If the Location Information at S-NODE Reporting IE set to "pscell" is included in the S-NODE ADDITION REQUEST, the S-NG-RAN node shall, start providing information about the current location of the UE. If the Location Information at S-NODE IE is included in the S-NODE ADDITION REQUEST ACKNOWLEDGE, the M-NG-RAN node shall store the included information so that it may be transferred towards the AMF. There is no description in the specification to say the MN can only include “Location Information at S-NODE reporting” IE when receiving request from the AMF. So if the MN wants to subscriber to PSCell changes from the SN, the MN could include “Location Information at S-NODE reporting” IE in the S-NODE ADDITION REQUEST message based on the current text in TS38.423. No new IE is needed. Pls also note that at last meeting when option 2 was agreed, the main argument is that location reporting request from MN to the SN in TS38.423 is supported already. |

If MN subscribes to PSCell changes, SN needs to inform MN with the information including the Global Cell ID of the new PSCell in case of PSCell changes. According to the contributions, there are three options:

Option 1: Introduce a new optional IE PSCell change information containing Global Cell ID of the new PSCell and/or other available SN UHI content in the SN MODIFICATION REQUIRED message.

Option 2: Introduce a dedicated, mandatory class 2 procedure message PSCELL CHANGE INFORMATION including the Global Cell ID of the new PSCell.

Option 3: Send the full SN UHI during each PSCell change from the SN to the MN. This can be sent through the SN MODIFICATION REQUIRED message which has already been agreed to contain SN UHI leading to reduced specification impact at the cost of extra signalling.

Question 3: Companies are kindly asked which option above is preferred.

| Company | Option | Comment |
| --- | --- | --- |
| ZTE | 3 | Prefer the solution with less spec impact |
| CATT | 3 | Agree with ZTE |
| Lenovo and Motorola Mobility | 3 | The agreed SN MODIFICATION REQUIRED message containing SN UHI can be totally reused. |
| Nokia | 1, but | PSCell Id can be reported already now, and at this moment it seems nothing more needs to be reported in addition to the PSCell ID. So, currently, option 1 means “reuse existing IE with the PSCell ID”. Sending full SCG UHI after every PSCell change (opt. 3) makes no sense at all: the whole idea of “subscription” is based on the assumption that the MN builds the SCG UHI on its own! To get full SCG UHI, the MN uses the MN-initiated modification (e.g. before a HO)! Please note, if the MN “subscribes” to the PSCell changes, the SN may not even collect the full SG UHI, because the MN is supposed to do this! |
| Samsung |  | Agree with Nokia. Once the MN requests the SN reporting PSCell ID in Addition Request or Modification request message, the SN will always notify the PSCell ID to the MN. The MN can also get the time stay in PScell based on the received message. No new IE or no new message is needed. |

## Enhancement on SN modification request message

In the lasting meeting, we have discussed whether to add a new IE, e.g. UE history information query in the SN modification request messages to indicate the retrieving of SN UHI, and [3] believes that there is no need to define a new “query” mechanism by which MN can request for a one-time update of the PSCell information from the SN, in addition to the subscription procedure. However, from moderator’s point of view, we have agreed that MN can initiate SN modification procedures to retrieve SN UHI before handover without delaying HO, MN may also subscribe to PSCell changes from SN. Thus, a new IE needs to be added in the SN modification request message to indicate that MN wants to retrieve the SN UHI through the MN initiated SN modification procedure.

Question 4: Do companies agree to add a new IE, e.g. PSCell history information retrieve in the SN modification request message to indicate the retrieving of SN UHI?

| Company | Yes/No | Comment |
| --- | --- | --- |
| ZTE | Yes | This indicator is needed to reflect the previous agreement “MN can initiate SN modification procedures to retrieve SN UHI before handover without delaying HO” |
| CATT | Yes | To make the SN aware the request of SN UHI from MN, an indication is needed. |
| Lenovo and Motorola Mobility | Yes | It is agreed that MN can initiate SN modification procedure to retrieve SN UHI before handover, a flag in the SN modification request message is needed. |
| Nokia | Yes |  |
| Samsung | No | RAN3 has agreed to include SCG UE History Information in S-NODE MODIFICATION REQUEST ACKNOWLEDGE message. If the MN trigger S-Node Modification procedure e.g. for delta configuration, a Rel-17 SN which supports the feature of PSCell UE history information will include SCG UE History Information in the S-NODE MODIFICATION REQUEST ACKNOWLEDGE message. No new IE in the request message is needed. For legacy SN or Rel-17 SN not supporting this feature, even if the MN includes new retrieve IE in the request message, the SN will ignore it. From above analysis, it could be observed that the MN can get SCG UE History Information from the SN supporting this feature in S-NODE MODIFICATION REQUEST ACKNOWLEDGE message even no new IE in the request message. |

If RAN3 agrees to add a flag indicating subscription of PSCell changes in the SN modification request message, moderator would suggest adding a new IE e.g. PSCell history information retrieve with three codepoints “query, subscription, subscription stop” in the SN modification request message since the query and subscription function can not be used at the same time.

Question 5: Do companies agree to add a new IE, e.g. PSCell history information retrieve with three codepoints “query, subscription, subscription stop” in the SN modification request message if RAN3 agrees to add a flag indicating subscription of PSCell changes in the SN modification request message?

| Company | Yes/No | Comment |
| --- | --- | --- |
| ZTE | Yes | Prefer not to introduce two separate IEs for subscription and query since these two functions cannot be used at the same time |
| CATT |  | We prefer to use different IE to support the function of SN UHI query and subscription of PScell change since they are two different functions. |
| Lenovo and Motorola Mobility |  | Firstly, we need to discuss whether to use SN modification procedure for SN UHI subscription besides SN addition procedure. If yes, a flag indicating subscription of PSCell changes (e.g. an IE for subscription which is separate from another IE for query, or a new IE with three codepoints “query, subscription, subscription stop”) is needed in the SN modification request message. |
| Nokia | No | For the subscription, the existing IE may be reused (possibly with new codepoints, if identified as needed). Once the MN asks for subscription, the SN is not obliged to collect SCG UHI any more (the MN does this). Then, a separate flag is needed to fetch the SCG UHI, if the SN collects is. |
| Samsung |  | The same reasoning as the answer for Q2, the existing modification procedure is enough. |

## RAN3 impact of SN UHI from UE

In the RAN2#115e-meeting, it was agreed that the PSCell transition is part of MHI. Thus, some companies analyzed the RAN3 impact of SN UHI form UE based on this agreement. [16] proposes the following modification in TS38.413.

9.3.1.166	UE History Information from UE

This IE contains information about mobility history report for a UE.

| IE/Group Name | Presence | Range | IE type and reference | Semantics description |
| --- | --- | --- | --- | --- |
| CHOICE UE History Information from UE | M |  |  |  |
| >NR |  |  |  |  |
| >>NR Mobility History Report | M |  | OCTET STRING | VisitedCellInfoList contained in the UEInformationResponse message (TS 38.331 [18]). VisitedPSCellInfoList also contained in the UEInformationResponse message (TS 38.331 [18]). |

- analyzes that the UE History information from the UE IE containing the mobility report will contain PSCell information in Dual-connectivity mode. Once this information is retrieved by the MN, it needs to be forwarded to the SN as RAN2 concluded against sending the mobility report directly to the SN. This requires two solutions depending on when the MN retrieved the mobility report last. The MN can forward the report to the SN in the SN ADDITION REQUEST message if it has already retrieved the report from the UE before the start of DC. If the MN has however not retrieved the report before SN addition, then the same can be forwarded to the SN optionally in the SN MODIFICATION REQUEST message. Thus [9] proposes to add UE history information from the UE IE in the following messages.

- Mandatory IE in the SN ADDITION REQUEST message

- Optional IE in the SN MODIFICATION REQUEST message

From moderator’s point of view, MN may not always have UHI form the UE before the start of DC. Thus, moderator would suggest adding optional UE history information from the UE IE in both SN addition request and SN modification request messages.

Question 6: Do companies agree to 1) modify the semantics description in 9.3.1.166 as above, 2) add optional UE history information from the UE IE in the SN ADDITION REQUEST message, 3) add optional UE history information from the UE IE in the SN MODIFICATION REQUEST message?

| Company | Yes/No | Comment |
| --- | --- | --- |
| ZTE | Yes |  |
| CATT | Yes |  |
| Lenovo and Motorola Mobility | Yes |  |
| Nokia | Yes |  |
| Samsung | Yes |  |

## Corrections to Xn/X2 BL CRs

It is noted that the Last Visited PSCell List IE is appended to the Last Visited Cell Information IE according to 9.2.3.64 and 9.2.38 in the XnAP and X2AP BLCRs respectively. However, this cannot be actually implemented since the current ASN.1 structure of the Last Visited Cell Information IE cannot be extended. Since we have already added the Last Visited PSCell List IE in the NGAP and S1AP BL CRs, moderator would suggest removing the Last Visited PSCell List IE in the XnAP and X2AP BLCRs.

Question 7: Please provide comments if companies do not agree to remove the Last Visited PSCell List IE in the XnAP and X2AP BLCRs.

| Company | Comment |
| --- | --- |

## Transfer of UHI during conditional handovers

[9] states that no discussions have taken place yet on transfer of UHI during conditional handovers (CHO). As HO requests are sent from a source RAN node to multiple target RAN nodes well in advance of the actual HO, the UHI sent to the target RAN nodes will not be up-to date. Thus [9] proposes the following two solutions to prevent this scenario of wrong UHI.

Option 1: Instruct all candidate RAN nodes to start a timer to update UHI upon successful HO.

Option 2: A new message to update UHI after successful HO.

From moderator’s point of view, this is indeed an issue that may need further discussion. However, we still have many issues to solve and there is not enough time left for Rel-17. Thus, moderator would suggest postponing the discussion of this issue to Rel-18.

Question 8: Do companies agree to postpone the discussion of the UHI transfer during CHO to Rel-18?

| Company | Yes/No | Comment |
| --- | --- | --- |
| ZTE | Yes | This issue is worth discussing, but we need to focus on other unsloved issues at this stage. |
| CATT | Yes |  |
| Lenovo and Motorola Mobility | Yes |  |
| Nokia | ? | We are not sure if the issue exists… Isn’t it so that a PSCell change actually deletes any conditional configuration in the UE? So, if there is CHO configured in the UE, PSCell can’t be changed. The only possible issue is with time information, i.e. the time UE stayed in the last PSCell. This can likely be addressed with timestamps though, no need to introduce any extra procedures. But in short, there may be no issue at all and thus no need to discuss it, neither now nor later… |
| Samsung | Yes |  |

# Phase 2 discussion

# Conclusion, Recommendations [if needed]

If needed

# References

R3-220159	[TP to SON BL CR to 38.413, NR_ENDC_SON_MDT_enh]  Completion of the work on the SCG UHI (Nokia, Nokia Shanghai Bell)	other

R3-220160	[TP to SON BL CR to 38.423, NR_ENDC_SON_MDT_enh]  Completion of the work on the SCG UHI (Nokia, Nokia Shanghai Bell)	other

R3-220270	UE History Information in MR-DC (Qualcomm Incorporated)	discussion

R3-220316	(TP for SON BLCR for 38.423, 38.413, 36.413 and 36.423, 37.340, 38.300) UE History Information in MR-DC (Huawei)	other

R3-220389	Consideration on UE history information (China Telecommunication)	other

R3-220517	(TP for 38.300)Enhancement of UE history information in MR-DC scenario (CATT, CMCC)	other

R3-220518	(TP on UE history information for 36.413) Addition of UE history information for SN (CATT, CMCC)	other

R3-220519	(TP on UE history information for 36.423) Addition of UE history information for SN (CATT, CMCC)	other

R3-220575	(TP for SON BL CR for TS 38.423, TS 38.413, TS 36.413) UE History Information for Secondary Node (Ericsson)	other

R3-220876	(TP to SON BLCR TS 38.413)UE history information in MR-DC (CMCC, CATT)	other

R3-220877	(TP to SON BLCR TS 38.423)UE history information in MR-DC (CMCC, CATT)	other

R3-220972	UE History Information in MR-DC (ZTE, Lenovo, Motorola Mobility, China Unicom)	discussion

R3-220973	(TP for SON BL CR for TS 37.340) Introduce UHI in MR-DC (ZTE, Lenovo, Motorola Mobility, China Unicom)	other

R3-220974	(TP for SON BL CR for TS 38.423) Introduce UHI in MR-DC (ZTE, Lenovo, Motorola Mobility, China Unicom)	other

R3-220975	(TP for SON BL CR for TS 36.423) Introduce UHI in MR-DC (ZTE, Lenovo, Motorola Mobility, China Unicom)	other

R3-220976	(TP for SON BL CR for TS 38.413) Introduce UHI in MR-DC (ZTE, Lenovo, Motorola Mobility, China Unicom)	other

R3-220977	(TP for SON BL CR for TS 36.413) Introduce UHI in MR-DC (ZTE, Lenovo, Motorola Mobility, China Unicom)	other

R3-220786	TP for SON BLCR for 38.423: UE History Information in MR-DC (Samsung)	Other

R3-220787	TP for SON BLCR for 36.423: UE History Information in EN-DC (Samsung)	Other

R3-216006	Summary of Offline Discussion on CB: # SONMDT2_UEHistoryInfor

# Comments

PSCell ID can be reported already now, so if nothing else is needed, the existing IE shall not be duplicated.