3GPP TSG-RAN WG3 #115-e	R3-22xxxx

Online, 21 February – 3 March 2022

Agenda Item:	31.3

Source:	Qualcomm Incorporated (moderator)

Title:	Summary of Offline Discussion on Endorsed Rel-17 TEI CRs Review

Document for:	Approval

# Introduction

CB: # 12_R17TEICR_Review - Check details, agree all CRs if no further comments (Qualcomm - moderator) [NWM] Summary of offline disc R3-222401

# For the Chairman’s Notes

Interim outcomes:

Comments captured so far (2022-02-22, 11.59 UTC):

- R3-221636/R3-221637: Minor comment on the cover pages: Other specs Y should be ticked

- R3-221638: Minor comment on the cover page: Other specs Y should be ticked and other 38.46x CRs should be mentioned

Recommend that responsible companies check / address these.

For all others, no comments received, and can further check online.

From online discussion it was requested to open a more detailed discussion on [8,9] motivated by comments online, particularly on the network sharing scenario.

# Discussion for gNB ID aspects [8,9]

For efficiency, the moderator believes this discussion is linked to the related documents in AI32, but will not reference them specifically (also officially they have not been opened).

The formal position as the moderator sees it is:

- CRs in [8,9] were previously endorsed

- In a related development, discussion was triggered at RAN in connection with status of the topic in RAN2, which concluded with the guidance that “issues can be brought up in the corresponding WGs on their own merits and the decision will be made by the group”

- There are objections to approving [8,9]

- The objections are based on the argument that some scenarios are not covered by these CRs, and also that the solution needs to be communicated to SA2.

Further, the objecting companies believe that RAN3 needs to inform RAN2 of these perceived limitations in order to reopen the discussion in RAN2 on a solution that covers such scenarios (over and above RAN guidance).

As per guidance, we will focus on the two main aspects from online discussion (i.e., RAN sharing scenarios and SA2 interaction).

## RAN sharing

The moderator observes, based on online exchanges and documents submitted, that there is no consensus on what the limiting scenario is, or whether it even exists.

With that, the moderator would like to request the companies that see limitations to explain the scenario and problem.

Please note that repetition or paraphrasing of the presentations in existing documents is not encouraged – we need to go further and provide as many specifics as possible.

Q1: Please provide description of the RAN sharing scenario and explanation of why the solution in [8,9] does not address it. Feel free to add diagrams or text outside the table (e.g. add sub-section at 3rd level).

| Company | Comment |
| --- | --- |
| Ericsson | Please find in Section 3.4.1 and 3.4.2 explanations on the shortfalls of solutions in R3-221618 and R3-221619. The following conclusions are drawn: Conclusion 1: The solution in R3-221618 and R3-221619 may work in RAN sharing scenarios where gNB-ID coordination between operators is possible, but it is subject to issues for RAN sharing scenarios where operators do not coordinate gNB-IDs Conclusion 2: The solution in R3-221618 and R3-221619 may work in networks where an operator can flexibly adapt its gNB-ID encoding to the hierarchical encoding proposed in the solution, but it is subject to errors in cases where the gNB-ID encoding schemes used by an operator are well established and not in line with the ones proposed With this analysis we do not want to undermine the value of the solution in R3-221618 and R3-221619, but we want just to highlight that there are scenarios where the solution has limitations and it will generate errors. Yes, one can claim that those scenarios should not exist, but they are real deployment scenarios, unfortunately. If we are looking for a solution that can help in the use of Flexible gNB-ID we should acknowledge the shortfalls of the solution in R3-221618 and R3-221619 and allow for a discussion to take place on how to address the unresolved use cases. |
| Bell Mobility | Thanks Ericsson for the detailed explanation. Bell confirms that the scenario described by Ericsson is a valid scenario for operators sharing the RAN |
| Huawei | I think the scenario in section 3.4.1 below needs further clarification. In order to understand what the errors is for the network solution in network sharing, below is my further illustration on the network sharing scenario as per the scenarios mentioned in section 3.4.1 below : General scenario: MOCN. Assuming following two use cases for NCGI construction: Case 1: independent cell id schemes Then, in SIB1 of cells of operator A’s RAN: PLMN A: cell ID x, gNB ID = PLMN A+ node ID part in cell ID x. PLMN B: cell ID y, gNB ID = PLMN B+ node ID part in cell ID y. In this case, the gNB will represent different gNB Ids to AMFs of operator A and B respectively. Question to clarify: Which cell ID scheme that the Equivalent PLMN x will use? It will decide which NCGI will be used in the UL RAN configuration message transfer for routing. Case 2: operator B uses operator A’s cell Id schemes Then, in SIB 1: PLMN A, PLMN B: cell ID x, gNB ID = PLMN A+ node ID part in cell ID x. In this case, the gNB will use the first PLMN in SIB to produce the gNB Id to AMFs of operator B as per our current spec. Question to clarify: Which cell ID scheme that the Equivalent PLMN x will use? It will decide which NCGI will be used in the UL RAN configuration message transfer for routing. We may further consider where the routing issue is after the two questions above are clarified. |
| ZTE | For RAN sharing scenario（gnb1<>gNB2 in section 3.4.1）, in practical the SIB1 in shared RAN not only broadcast Operator 1’s cell information but also for Operator 2. For RAN node to aware a new unknown CGI can identify differentiate CGI from different Operators by utilizing PLMN information. Based on the information, RAN node can only trigger to AMF when acquires CGI belong to it’s Operator. There is no further requirement for coordination between Operators. For RAN not shared scenario (gNB 1<>gNB3), it is not necessary to setup Xn interface via two gNB belong to different PLMN without cooridnator. |
| Qualcomm | Our understanding is that the detail depends a lot on the question from Huawei i.e. is this assuming single cell or multiple cell ID per physical cell? Either way we believe that the scenario does not cause a problem, once the details are checked. For example, for the single ID case, if there was such a problem, we would already have a clash even in LTE. But this is not the case since there are other discriminants i.e. the PLMN ID in the global gNB ID, and even the TAI (which in that case would need to be coordinated and are unlikely to be the same in the two areas). Anyway, we can wait for further clarification before going to the next level of detail. |

## SA2 aspects

As per online request, the moderator has checked the communication with other groups during the work for ANR with option 3 including also inter-system exchange.

The key LS was in R3-191119 (available at https://www.3gpp.org/ftp/tsg_ran/WG3_Iu/TSGR3_103/Docs/R3-191119.zip). This LS had however two parts, one for CT4 and one for SA2.

At the time, there was a direct dependency on CT4 based on the choice of container described in the LS (and RAN3 had prepared two sets of endorsed CRs while waiting for CT4’s response). For SA2, the action however was “to take this information into account, provide feedback if needed, and update relevant specifications if appropriate”.

Re-reading the LS, the full impacts on the MME were not spelt out in detail, particularly the routing and database impacts at the MME.

With that precedent, the moderator thinks it is reasonable to inform SA2 in a similar manner.

The moderator would therefore propose the following: an LS is sent to SA2 including the two CRs, with some explanatory text and action to “take this information into account, provide feedback if needed, and update relevant specifications if appropriate”. Approval of the CRs does not need to be pending on the LS reply, if any.

Q1: Do you agree with the above proposal?

| Company | Comment |
| --- | --- |
| Ericsson | The example selected by the moderator is not exactly in line with the discussion we are having here. The moderator selected past discussions on Xn TNL Address Discovery, where the only role of the MME is to forward transparent containers with the aim of reaching a target RAN node. Quoting from R3-191119: The agreed solution in RAN3 involves steps similar to those in LTE, whereby a container (“SON Configuration Transfer”) is sent by the initiating eNB towards the MME and is relayed across the S10 interface (if needed), and then sent down to the target eNB, with a response then following the reverse path. The MME does not need to process the container apart from extracting the information required to identify a target eNB (and/or MME in case S10 relaying is required). In EN-DC, the main difference is that one of the RAN endpoints is an en-gNB (i.e. the container is further relayed within RAN), and additional information is provided to the MME to aid routing. Hence there is no processing of the information exchanged in the solution described in R3-191119. The discussion here is substantially different because the AMF is requested to: Decode a transparent container Process its information to achieve the following: Disambiguate and identify a target gNB-ID Forward the Transparent container to the Target RAN Note that with the above, the container signalled for Xn TNL discovery is not transparent anymore because its information needs to be processed by the AMF. This implies also an involvement of CT4 because effectively the AMF needs to deduce the gNB-ID, encode it into the (no more) transparent container and then signal it to a Target AMF over N16. It is clear that RAN3 cannot simply agree to the solution in R3-221618 and R3-221619 and ask SA2 to take that into account. The functionality discussed is totally within the AMF and under SA2´s control. Additionally, the fiunctionality impacts inter AMF interfaces. To make a counter example, we are stopping discussions on Network Slicing in RAN3 on the basis that they need SA2´s opinion for issues with much less impact and relevance. Therefore, the opinion of SA2 is essential to determine if the solution is feasible or not and the solutions in R3-221618 and R3-221619 are not agreeable before receiving a positive LS reply from SA2. |
| Huawei | We cannot agree on the comments above from Ericson. Fortunately, I also followed the EN-DC X2 TNL address discovery topic at that time. So, I know the details very well. Technically, the impact on AMF for the network solution is totally the same as the impact on MME in EN-DC X2 TNL address discovery where it is Ericsson who proposed to let the MME to do the longest LSB match of gNB ID with the gNB IDs reported by the eNBs connecting to the MME. Here the only difference is to use a NCGI to do the longest LSB match to a gNB ID in the AMF. I am afraid that we cannot make any progress if one company has total opposite views to the same function at different point in time. |
| ZTE | Send LS to SA2 is the same story as the topic of TNL address discovery for option 3. At first RAN3 achieve agreement and then send LS to SA2 /CT4 for alignment. |
| Qualcomm | As someone who was personally involved in the option 3 discussion, I share Huawei’s reaction to the attempt to make this look any more complex than option 3. In fact option 3 is arguably more complex, because not only was the target identification algorithm changed, but also further information was being uploaded to the MME which would result in additional database information at the MME. Let’s take the statements made by Ericsson as to why this is different Decode a transparent container: this is a surprising statement given that the additional information is added to the target information which the AMF always has to look at, else it has no idea what to do. This is how it has always worked since rel8. No change. Process its information to achieve the following: Disambiguate and identify a target gNB-ID: that is the only new functionality, which as stated above is comparable to (and maybe even simpler than) option 3 changes Forward the Transparent container to the Target RAN: this is same as legacy, in fact it is the goal of the process since rel8. No change. So to summarize all the words used, this requires a modification of the algorithm for identifying the ultimate target RAN, which is exactly the same change as with ANR for option 3, except simpler. |

## Anything else

Below space is for any other issues, if needed. Please however do not repeat any aspects already presented in documents.

| Company | Comment |
| --- | --- |

## Details on Flexible gNB-ID discussion

## RAN Sharing

Here we present details on why the solution in R3-221618 and R3-221619 is subject to limitations when it comes to RAN sharing.

The most important aspect to be understood is that operators assign gNB-IDs to their RAN nodes independently from each other, on the basis of Operator´s internal gNB-ID structures. There is no coordination between operators when it comes to gNB-ID assignment.

As an example, an operator may decide to configure its gNB-IDs in the following way:

gNB-ID == [4 bits] Region area code, [4 bits] City area code, [4 bits] Node Type (Macro, pico…), [4 to 8 bits] Frequency Identifier, [16 to 12 bits] Local Node Identifier

Other operators may follow a different configuration scheme.

It needs to be appreciated that it is not easy for an operator to change the gNB-ID encoding of choice because such encoding is strictly connected to operation and maintenance processes within the operator´s network (e.g. diagnostics, trouble shooting). A typical example is that of operations processes, where an alarm is triggered for a certain gNB-ID and where analysis of the gNB-Id reveals the location of the node, the type and frequency of the node and even the node´s vendor. Changing such processes has a huge impact.

With the above in mind, the picture below explains the issue affecting the solution in R3-221618 and R3-221619

NCI are overlapping and since you do not know

In the figure above it has been assumed that gNB1, gNB2 and gNB3 are shared gNBs.

It has also been assumed that operators have deployed PLMN X, which is an equivalent PLMN on which the UEs sharing both operators´networks can be served. Therefore, a UE moving between Operator 1 and Operator 2 cells within the shared network will remain connected to PLMN X.

Step 1: A UE connected to gNB3 reports Cell 2-1 as part of ANR measurements.

Step 2: Serving gNB-3 decides to trigger Xn address discovery to establish an Xn interface with gNB 1. For that, gNB 3 signals NG: UPLING CONFIGURATION TRANSFER to AMF1. NG: UPLING CONFIGURATION TRANSFER includes TEI X and CGI 1-2.

Step 3: the AMF needs to disambiguate from CGI 1-2 the gNNB-ID of the gNB with which Xn needs to be established. However, CGI 1-2 contains both gNB ID 1 and gNB ID 2. It is therefore impossible for AMF 1 to derive the right gNB ID form CGI 1-2.

An example similar to the one above can be made by assuming that each gNB serves dedicated PLMNs, namely if there is no “common” PLMN X. Even in this example, the fact that operators assign gNB-IDs independently still creates a problem of lack of gNB-ID coordination, which may lead to the problem of not been able to disambiguate between gNB-IDs.

Conclusion 1: The solution in R3-221618 and R3-221619 may work in RAN sharing scenarios where gNB-ID coordination between operators is possible, but it is subject to issues for RAN sharing scenarios where operators do not coordinate gNB-IDs

### Hierarchical gNB-ID allocation

It has also been pointed out during the online discussion and in documents presented at RAN3-115e that the issue with the Solution in R3-221618 and R3-221619 is also that it imposes a hierarchical structure between gNBs.

As it has been explained above, an operator has ways to encode gNB-IDs that are tightly connected with operation and maintenance processes such as performance and failure monitoring, troubleshooting etc. Such encoding mechanisms are often derived from previous network generations, e.g. LTE, hence they have a strong legacy.

### For this reason, imposing now a solution that implies a very specific, hierarchical way to encode the gNB-ID, is unfeasible as it would mean to totally change well established operation and maintenance processes in an operator´s network.

Conclusion 2: The solution in R3-221618 and R3-221619 may work in networks where an operator can flexibly adapt its gNB-ID encoding to the hierarchical encoding proposed in the solution, but it is subject to issues in cases where the gNB-ID encoding schemes used by an operator are well established and not in line with the ones proposed

# Discussion (please continue using NWM for all other checking)

Introduction:

This offline discussion covers several CRs that have been previously technically endorsed and are now up for review before approval. A full list is provided at the end of this document.

Below we take the CRs grouped by topic and request review comments. Since all of these have been previously endorsed, the assumption is that they will be approved in the absence of comments. If there are comments, then we will need further discussion to resolve these comments.

Unfortunately, we cannot avoid nine questions, but hope this is acceptable due to the special nature of this AI.

## Chapter 10

| [1] R3-221611 | Correction for Chapter 10 (Ericsson, Nokia, Nokia Shanghai-Bell, Huawei) | CR0558r4, TS 38.413 v16.8.0, Rel-17, Cat. F |
| --- | --- | --- |
| [2] R3-221612 | Correction for Chapter 10 (Ericsson, Nokia, Nokia Shanghai-Bell, Huawei) | CR1804r4, TS 36.413 v16.8.0, Rel-17, Cat. F |

Q1: Please provide comments, if any, on the above CRs.

| Company | Comment |
| --- | --- |

## CSI-RS over X2/Xn [CSIRSXn/CSIRSX2]

| [3] R3-221613 | Signalling of Neighbour cell CSI-RS configuration information over Xn [CSIRSXn] (Ericsson, China Telecom) | CR0653r1, TS 38.423 v16.8.0, Rel-17, Cat. B |
| --- | --- | --- |
| [4] R3-221614 | Signalling of Neighbour cell CSI-RS configuration information over X2 [CSIRSX2] (Ericsson, China Telecom) | CR1614r1, TS 36.423 v16.8.0, Rel-17, Cat. B |
| [15] R3-221632 | CSI-RS configuration request Indicator [CSIRSXn] (Ericsson, China telecom, Huawei, ZTE, Nokia, Nokia Shanghai Bell) | CR0700r2, TS 38.423 v16.8.0, Rel-17, Cat. B |
| [23] R3-221862 | CSI-RS configuration request Indicator [CSIRSX2] (Ericsson, China telecom, Huawei, Nokia Shanghai Bell, ZTE) | CR1642r2, TS 36.423 v16.8.0, Rel-17, Cat. B |

Q2: Please provide comments, if any, on the above CRs.

| Company | Comment |
| --- | --- |

## Support of Enhancement of Redundant PDU Sessions [Paired_ID]

| [5] R3-221615 | Support of Enhancement of Redundant PDU Sessions [Paired_ID] (Nokia, Nokia Shanghai Bell, Ericsson, Huawei, LG Electronics, CATT, Samsung) | CR0647r3, TS 38.413 v16.8.0, Rel-17, Cat. B |
| --- | --- | --- |
| [6] R3-221616 | Support of Enhancement of Redundant PDU Sessions [Paired_ID] (Nokia, Nokia Shanghai Bell, Ericsson, LG Electronics, Huawei, CATT, Samsung) | CR0656r3, TS 38.423 v16.8.0, Rel-17, Cat. B |
| [7] R3-221617 | Support of Enhancement of Redundant PDU Sessions [Paired_ID] (Nokia, Nokia Shanghai Bell, Ericsson, Huawei, LG Electronics, CATT, Samsung) | CR0627r3, TS 38.463 v16.8.0, Rel-17, Cat. B |

Q3: Please provide comments, if any, on the above CRs.

| Company | Comment |
| --- | --- |

## Support for handling unknown length of gNB identifier [FLEX_gNB_Len]

| [8] R3-221618 | Support for handling unknown length of gNB identifier [FLEX_gNB_Len] (Qualcomm Incorporated, Huawei) | draftCR |
| --- | --- | --- |
| [9] R3-221619 | Support for handling unknown length of gNB identifier [FLEX_gNB_Len] (Qualcomm Incorporated, Huawei) | CR0571r3, TS 38.413 v16.8.0, Rel-17, Cat. B |

Q4: Please provide comments, if any, on the above CRs.

| Company | Comment |
| --- | --- |

## Removal of ETWS/CMAS restriction in SNPN

| [10] R3-221620 | Removal of ETWS/CMAS restriction in SNPN (Qualcomm Incorporated, Ericsson, Nokia, Nokia Shanghai Bell) | draftCR |
| --- | --- | --- |

Q5: Please provide comments, if any, on the above CRs.

| Company | Comment |
| --- | --- |

## Addition of NR Timing Advance reporting for NR UL E-CID [NRTADV-F1]

| [11] R3-221627 | Addition of NR Timing Advance reporting for NR UL E-CID [NRTADV-F1] (Ericsson, CATT, NTT Docomo, Polaris Wireless, Verizon, China Telecom, FirstNet, Deutsche Telekom, Intel Corporation, Nokia, Nokia Shanghai Bell, Huawei, ZTE) | CR0817r2, TS 38.473 v16.8.0, Rel-17, Cat. B |
| --- | --- | --- |
| [12] R3-221628 | Addition of NR Timing Advance reporting for NR UL E-CID [NRTADV] (Ericsson, NTT Docomo, Polaris Wireless, Verizon, China Telecom, FirstNet, Deutsche Telekom, Intel Corporation, CATT, Nokia, Nokia Shanghai Bell, Huawei, ZTE) | CR0042r2, TS 38.455 v16.6.0, Rel-17, Cat. B |

Q6: Please provide comments, if any, on the above CRs.

| Company | Comment |
| --- | --- |

## Local NG-RAN Node IDs for RRC_INACTIVE [RRCInactive]

| [13] R3-221629 | Introduction of Local NG-RAN Node IDs for RRC_INACTIVE [RRCInactive] (Ericsson, ZTE, Radisys, Reliance JIO, China Telecom, Huawei, Nokia, Nokia Shanghai Bell, Deutsche Telekom) | draftCR |
| --- | --- | --- |
| [14] R3-221631 | Support flexible I-RNTI partitioning [RRCInactive] (ZTE, Radisys, Reliance JIO, China Telecom, Ericsson, Nokia, Nokia Shanghai Bell, Deutsche Telekom, Huawei) | CR0674r3, TS 38.423 v16.8.0, Rel-17, Cat. B |

Q7: Please provide comments, if any, on the above CRs.

| Company | Comment |
| --- | --- |

## Inter MN resume without SN change [InterMNResume]

| [16] R3-221633 | Inter MN resume without SN change [InterMNResume] (Qualcomm Incorporated, Huawei, Ericsson, China Telecom, T-Mobile USA, ZTE, Intel Corporation, Nokia, Nokia Shanghai Bell, Samsung, Radisys, Reliance JIO) | CR0596r6, TS 38.423 v16.8.0, Rel-17, Cat. B |
| --- | --- | --- |
| [17] R3-221634 | Addition of the Retrieve UE Context Confirm procedure [InterMNResume] (Nokia, Nokia Shanghai Bell, Qualcomm Incorporated, Huawei, Ericsson, China Telecom, T-Mobile USA, ZTE, Intel Corporation, Samsung) | CR0025r1, TS 38.420 v16.0.0, Rel-17, Cat. B |
| [18] R3-221635 | Inter-MN RRC Resume without SN change [InterMNResume] (Ericsson, Qualcomm Incorporated, Huawei, Intel Corporation, China Telecom, T-Mobile USA, ZTE, Nokia, Nokia Shanghai Bell, Samsung, RadiSys, Reliance JIO, Google Inc.) | draftCR |

Q8: Please provide comments, if any, on the above CRs.

| Company | Comment |
| --- | --- |

## E1 specification aspects

| [19] R3-221636 | E1 TS 38.460 specification transfer to TS 37.480 (Nokia, Nokia Shanghai Bell) | CR0054r2, TS 38.460 v16.4.0, Rel-17, Cat. F |
| --- | --- | --- |
| [20] R3-221637 | Transfer of E1 interface specification from 38-series to 37-series (Huawei) | CR0018r2, TS 38.462 v16.1.0, Rel-17, Cat. F |
| [21] R3-221638 | Transfer of Rel-17 E1 interface specification from 38.46x series to 37.48x series (Intel Corporation) | CR0003r2, TS 38.461 v16.0.0, Rel-17, Cat. F |
| [22] R3-221639 | E1AP specification transfer to TS 37.483 (Ericsson) | CR0665r2, TS 38.463 v16.8.0, Rel-17, Cat. F |

Q9: Please provide comments, if any, on the above CRs.

| Company | Comment |
| --- | --- |
| Ericsson | R3-221636/R3-221637: Minor comment on the cover pages: Other specs Y should be ticked R3-221638: Minor comment on the cover page: Other specs Y should be ticked and other 38.46x CRs should be mentioned |

# Conclusion, Recommendations [if needed]

If needed

# References

| [1] R3-221611 | Correction for Chapter 10 (Ericsson, Nokia, Nokia Shanghai-Bell, Huawei) | CR0558r4, TS 38.413 v16.8.0, Rel-17, Cat. F |
| --- | --- | --- |
| [2] R3-221612 | Correction for Chapter 10 (Ericsson, Nokia, Nokia Shanghai-Bell, Huawei) | CR1804r4, TS 36.413 v16.8.0, Rel-17, Cat. F |
| [3] R3-221613 | Signalling of Neighbour cell CSI-RS configuration information over Xn [CSIRSXn] (Ericsson, China Telecom) | CR0653r1, TS 38.423 v16.8.0, Rel-17, Cat. B |
| [4] R3-221614 | Signalling of Neighbour cell CSI-RS configuration information over X2 [CSIRSX2] (Ericsson, China Telecom) | CR1614r1, TS 36.423 v16.8.0, Rel-17, Cat. B |
| [5] R3-221615 | Support of Enhancement of Redundant PDU Sessions [Paired_ID] (Nokia, Nokia Shanghai Bell, Ericsson, Huawei, LG Electronics, CATT, Samsung) | CR0647r3, TS 38.413 v16.8.0, Rel-17, Cat. B |
| [6] R3-221616 | Support of Enhancement of Redundant PDU Sessions [Paired_ID] (Nokia, Nokia Shanghai Bell, Ericsson, LG Electronics, Huawei, CATT, Samsung) | CR0656r3, TS 38.423 v16.8.0, Rel-17, Cat. B |
| [7] R3-221617 | Support of Enhancement of Redundant PDU Sessions [Paired_ID] (Nokia, Nokia Shanghai Bell, Ericsson, Huawei, LG Electronics, CATT, Samsung) | CR0627r3, TS 38.463 v16.8.0, Rel-17, Cat. B |
| [8] R3-221618 | Support for handling unknown length of gNB identifier [FLEX_gNB_Len] (Qualcomm Incorporated, Huawei) | draftCR |
| [9] R3-221619 | Support for handling unknown length of gNB identifier [FLEX_gNB_Len] (Qualcomm Incorporated, Huawei) | CR0571r3, TS 38.413 v16.8.0, Rel-17, Cat. B |
| [10] R3-221620 | Removal of ETWS/CMAS restriction in SNPN (Qualcomm Incorporated, Ericsson, Nokia, Nokia Shanghai Bell) | draftCR |
| [11] R3-221627 | Addition of NR Timing Advance reporting for NR UL E-CID [NRTADV-F1] (Ericsson, CATT, NTT Docomo, Polaris Wireless, Verizon, China Telecom, FirstNet, Deutsche Telekom, Intel Corporation, Nokia, Nokia Shanghai Bell, Huawei, ZTE) | CR0817r2, TS 38.473 v16.8.0, Rel-17, Cat. B |
| [12] R3-221628 | Addition of NR Timing Advance reporting for NR UL E-CID [NRTADV] (Ericsson, NTT Docomo, Polaris Wireless, Verizon, China Telecom, FirstNet, Deutsche Telekom, Intel Corporation, CATT, Nokia, Nokia Shanghai Bell, Huawei, ZTE) | CR0042r2, TS 38.455 v16.6.0, Rel-17, Cat. B |
| [13] R3-221629 | Introduction of Local NG-RAN Node IDs for RRC_INACTIVE [RRCInactive] (Ericsson, ZTE, Radisys, Reliance JIO, China Telecom, Huawei, Nokia, Nokia Shanghai Bell, Deutsche Telekom) | draftCR |
| [14] R3-221631 | Support flexible I-RNTI partitioning [RRCInactive] (ZTE, Radisys, Reliance JIO, China Telecom, Ericsson, Nokia, Nokia Shanghai Bell, Deutsche Telekom, Huawei) | CR0674r3, TS 38.423 v16.8.0, Rel-17, Cat. B |
| [15] R3-221632 | CSI-RS configuration request Indicator [CSIRSXn] (Ericsson, China telecom, Huawei, ZTE, Nokia, Nokia Shanghai Bell) | CR0700r2, TS 38.423 v16.8.0, Rel-17, Cat. B |
| [16] R3-221633 | Inter MN resume without SN change [InterMNResume] (Qualcomm Incorporated, Huawei, Ericsson, China Telecom, T-Mobile USA, ZTE, Intel Corporation, Nokia, Nokia Shanghai Bell, Samsung, Radisys, Reliance JIO) | CR0596r6, TS 38.423 v16.8.0, Rel-17, Cat. B |
| [17] R3-221634 | Addition of the Retrieve UE Context Confirm procedure [InterMNResume] (Nokia, Nokia Shanghai Bell, Qualcomm Incorporated, Huawei, Ericsson, China Telecom, T-Mobile USA, ZTE, Intel Corporation, Samsung) | CR0025r1, TS 38.420 v16.0.0, Rel-17, Cat. B |
| [18] R3-221635 | Inter-MN RRC Resume without SN change [InterMNResume] (Ericsson, Qualcomm Incorporated, Huawei, Intel Corporation, China Telecom, T-Mobile USA, ZTE, Nokia, Nokia Shanghai Bell, Samsung, RadiSys, Reliance JIO, Google Inc.) | draftCR |
| [19] R3-221636 | E1 TS 38.460 specification transfer to TS 37.480 (Nokia, Nokia Shanghai Bell) | CR0054r2, TS 38.460 v16.4.0, Rel-17, Cat. F |
| [20] R3-221637 | Transfer of E1 interface specification from 38-series to 37-series (Huawei) | CR0018r2, TS 38.462 v16.1.0, Rel-17, Cat. F |
| [21] R3-221638 | Transfer of Rel-17 E1 interface specification from 38.46x series to 37.48x series (Intel Corporation) | CR0003r2, TS 38.461 v16.0.0, Rel-17, Cat. F |
| [22] R3-221639 | E1AP specification transfer to TS 37.483 (Ericsson) | CR0665r2, TS 38.463 v16.8.0, Rel-17, Cat. F |
| [23] R3-221862 | CSI-RS configuration request Indicator [CSIRSX2] (Ericsson, China telecom, Huawei, Nokia Shanghai Bell, ZTE) | CR1642r2, TS 36.423 v16.8.0, Rel-17, Cat. B |