3GPP TSG-RAN WG3 #115-e						                              	                   R3-22xxxx

21 February – 3 March 2022

Online

Agenda Item:	13.2.3

Source: 	ZTE

Title: 	(TP for IAB BL CR for TS 38.470) Header Rewriting Configuration in IAB

Document for:	Agreement

# Introduction

This TP is used to capture the agreement in RAN3#115-e.

# TP for BL CR for NR_IAB_enh of TS 38.470

-------------------------------------------Change Start------------------------------------------

### 5.2.12	IAB support function

The BAP mapping configuration function allows the IAB-donor-CU to provide BAP mapping which includes the backhaul routing configuration and/or BH RLC channel mapping information for IAB-donor-DU or IAB-DU. This function also allows the IAB-donor-CU to provide BAP header rewriting configuration to an IAB-DU.

-------------------------------------------End of change-------------------------------------------