3GPP TSG-RAN WG3 #115-e							 R3-222410

21 Feb - 3 Mar 2022

Online

Agenda Item:	30.1

Source:	ZTE (moderator)

Title:	Summary_of_offline_disc_CB # 18_IoToverNTN

Document for:	Approval

# Introduction

This contribution is to kick off the following discussion.

CB: # 18_IoToverNTN - Check work plan, reply LS to RAN2 towards R3-221655, any further impact on TAC report? - New cause value needed over S1? - Other potential cleanup if needed - Capture agreements and provide TPs/CRs if agreeable (ZTE - moderator) Summary of offline disc R3-222410

For the first round, we focus on the technical issues of this WI and try to reach some agreements. The deadline is Wednesday, February 23rd, 07:00am UTC.

For the second round, we focus on the left issue in the first round, prepare the reply LS and clean up the BL CRs. The deadline is Tuesday, March 1st, 11:00am UTC.

# For the Chairman’s Notes

<TBD>

# Discussion - Second Round

<TBD>

# Discussion - First Round

## Issue 1: BL CRs and work plan

| R3-221597 | NB-IoT/eMTC support for Non-Terrestrial Networks (ZTE, CATT, Samsung, MediaTek, Nokia, Nokia Shanghai Bell, Ericsson, Qualcomm Incorporated) | draftCR |
| --- | --- | --- |
| R3-221599 | (BL CR for 36.423) IoT over NTN (CATT) | CR1665r2, TS 36.423 v16.8.0, Rel-17, Cat. B |
| R3-221600 | Support of NTN RAT identification and NTN RAT restrictions (Ericsson, Huawei, Qualcomm Incorporated, Nokia, Nokia Shanghai Bell, ZTE, CATT) | CR1853r3, TS 36.413 v16.8.0, Rel-17, Cat. B |
| R3-221601 | NNSF for IoT NTN providing access over multiple countries (Qualcomm Incorporated, Ericsson, Huawei, Nokia, Nokia Shanghai Bell, ZTE, CATT) | CR0028r2, TS 36.410 v16.0.0, Rel-17, Cat. C |
| R3-221701 | Updated Work Plan on NB-IoT and eMTC Support for NTN (ZTE) | discussion |

Question 1: Do you agree to endorse the above BL CRs and note the work plan?

| Company | Agree or Disagree | Comment |
| --- | --- | --- |
| Nokia | Agree |  |
| Ericsson | Agree |  |
| Qualcomm | Agree |  |
| Huawei | Agree |  |

## Issue 2: Incoming LS from RAN2 and potential impact on RAN3

One LS on UE location information for NB-IoT has been received from RAN2 in [1].

As the AS security is not supported for NB-IoT UEs, RAN2 has assumed that sending detailed location over AS cannot be supported. Furthermore, SA3 stated that even sending coarse location unprotected should be avoided. Therefore, RAN2 has assumed that not even coarse location may be reported over AS for NB-IoT. In this case, RAN2 sent the LS to RAN3 to ask the potential impact on RAN3 without the UE location information over AS (e.g. E-UTRAN selecting correct core network, NNSF and constructing the mapped cell ID and any potential ULI) and whether it is feasible that UE provides the location information to the MME via NAS.

Considering the impact on RAN3, in [2], it is proposed that there is no significant negative impact on the lack of location information in early phases of UE network attach. In [3], the lack of UE location over AS may lead to failure of selecting correct core network, NNSF and constructing the mapped Cell ID and any potential ULI. In [4], the lack of UE location over AS has the impact on the mapped cell ID construction and TAC reporting in ULI for the NB-IoT UEs. In [5], the MME should check the UE location via LCS service and do corresponding fallback.

Question 2-1: What’s your opinion on the potential impact on RAN3 based on the LS from RAN2?

| Company | Comment |
| --- | --- |
| Nokia | If no UE location, the eNB may select an incorrect MME, but the MME can ask the UE to detach then re-attach. No UE location info also affect the mapped cell ID determination, but the eNB may use a “special” mapped cell ID corresponding to a very large area or implicitly informing the MME that no UE location, and this “special” mapped cell ID can be configured in both eNB and MME just like other mapped cell IDs. So it seems that SA2 may be the right group to answer whether it is acceptable. |
| Ericsson | As stated in our papers, the lack of such information may indeed reduce the RAN’s capacity to select the appropriate CN node, but if the cell size is appropriate and not too big (realistically comparable in size to a terrestrial network) this will only happen in very extreme cases. But when that happens, the selection will converge to the appropriate node on subsequent UE reattach attempts. The RAN will know the reason for a UE context release by the core network thanks to the cause value we recently introduced in NR NTN (which should be maintained for IoT NTN as proposed in e.g. [4]). |
| Qualcomm | We agree with Nokia’s view, in fact as of last meeting we sent an LS to SA2 asking the same question. It does not seem that we have the full view of the situation in RAN3. Most of our impacts are in services to the AMF (NNSF and ULI), and so although we could comment about impacts, ultimately this is SA2’s area. |
| Huawei | We agree with Nokia and QC that ultimately this is whether SA2 can accept it or not. It seems it will increase the possibility of wrongly selecting the MME. To RAN3, the more direct impact is mapped cell construction, which of course, in the end also impacts SA2. eNB is responsible for constructing mapped cells based on the available UE location knowledge. The finer the UE location the eNB can get, the better (greater granularity) the mapped cell the eNB can construct. Currently it seems no UE location at all, and not like NR NTN where we can refine it after AS security, there will be no UE location at all for all the times, so eNB has no ability to construct good enough mapped cell IDs. |

Considering the feasibility of providing the location information via NAS, in [2] and [3], it is proposed that this issue it outside RAN3 responsibility. While in [4] and [5], it is acceptable from the prospective of RAN3.

Question 2-2: What’s your opinion on the feasibility of providing the location information via NAS for NB-IoT UEs?

| Company | Comment |
| --- | --- |
| Nokia | It is out of RAN3 scope on sending the UE location info via NAS. |
| Ericsson | RAN3 is not the right group to take this discussion, since we do not have responsibility over which use would the MME have for this information. As far as RAN3 is concerned, once the NNSF has selected a CN node (right or wrong), there is no further use for the UE-provided ULI in the RAN. |
| Qualcomm | Indeed this is out of scope for RAN3, and we need not discuss or reply on this point. |
| Huawei | Out of RAN3 scope |

Moderator’s summary:

<TBD>

## Issue 3: TAC reporting in ULI

In last RAN3 meeting, the TAC reporting in ULI was introduced over NG in NR NTN WI. And it is reasonable to introduce the similar functionality in IoT NTN WI.

In [3], [4], [5] and [6], it is proposed that the TAC reporting in ULI should also be supported over S1. While, in [6], in addition to the ULI, the Broadcast TAC List is proposed to be added in the following S1AP messages (Please NOTE, the corresponding NGAP messages use ULI IE).

- eNB CP RELOCATION INDICATION

- HANDOVER NOTIFY

- PATH SWITCH REQUEST

- INITIAL UE MESSAGE

- UPLINK NAS TRANSPORT

- LOCATION REPORT

However, there are some differences between S1AP and NGAP, since the ULI IE was introduced in NGAP in the beginning, while the ULI IE was introduced in S1AP in Rel-12. The S1AP messages introduced before Rel-12 use TAI IE but no ULI IE, for example, the UPLINK NAS TRANSPORT message

#### 9.1.7.3	UPLINK NAS TRANSPORT

This message is sent by the eNB and is used for carrying NAS information over the S1 interface.

Direction: eNB ( MME

| IE/Group Name | Presence | Range | IE type and reference | Semantics description | Criticality | Assigned Criticality |
| --- | --- | --- | --- | --- | --- | --- |
| Message Type | M |  | 9.2.1.1 |  | YES | ignore |
| MME UE S1AP ID | M |  | 9.2.3.3 |  | YES | reject |
| eNB UE S1AP ID | M |  | 9.2.3.4 |  | YES | reject |
| NAS-PDU | M |  | 9.2.3.5 |  | YES | reject |
| E-UTRAN CGI | M |  | 9.2.1.38 |  | YES | ignore |
| TAI | M |  | 9.2.3.16 |  | YES | ignore |
| GW Transport Layer Address | O |  | Transport Layer Address 9.2.2.1 | Indicating GW Transport Layer Address if the GW is collocated with eNB. | YES | ignore |
| … |  |  |  |  |  |  |

For this reason, Contribution [6] propose additional changes to cover the scenario when the TAI is not reported as part of the ULI.

Question 3: What’s your opinion on the TAC reporting in ULI, do you agree to introduce this functionality only in ULI or introduce this functionality in both ULI and other S1AP messages?

| Company | Only ULI/both ULI and other S1AP messages | Comment |
| --- | --- | --- |
| Nokia | Both ULI and other S1AP messages. | Due to the differences on the ULI IE in S1AP and NGAP, we need to consider the scenario when the TAI is not reported as part of the ULI, e.g. INITIAL UE MESSAGE, UPLINK NAS TRANSPORT, etc |
| Ericsson | Only ULI | TAI list reporting for NTN is only needed at UE attach. Once that is done, there is no need to add it to any other messages, and there seems to be no requirement for it. |
| Qualcomm |  | In principle, we think all messages should have similar information as a default – unless proven not to be needed. However we do not agree to having a structure similar to that agreed last time for NTN as this is not stable in our view. |
| Huawei | FFS | The coding of TAI list/TAI in NR NTN is not fully stable in our view. We may revise when we receive SA2 response. So propose to postpone this and no hurry to copy the agreements in NTN-IoT. |

Moderator’s summary:

<TBD>

## Issue 4: Mapped Cell ID

In [8], it is proposed to update the stage 2 BL CR to clarify the mapped cell ID construction is only used for the BL UE or the UE in enhanced coverage.

While, in [6] and [7], in addition to the ULI, the mapped cell ID is reported to core network via E-UTRAN CGI IE in the following S1AP messages which does not have ULI IE (Please NOTE, the corresponding NGAP messages use ULI IE). Therefore, both the stage 2 BL CR and the stage 3 BL CR should be updated.

- eNB CP RELOCATION INDICATION

- HANDOVER NOTIFY

- PATH SWITCH REQUEST

- INITIAL UE MESSAGE

- UPLINK NAS TRANSPORT

- LOCATION REPORT

- CELL TRAFFIC TRACE

Question 4: What’s your opinion on the issue of mapped cell ID? In addition to the stage 2 BL CR, whether the stage 3 BL CR should also be updated?

| Company | Yes or No | Comment |
| --- | --- | --- |
| Nokia | Yes | Due to the differences on the ULI IE in S1AP and NGAP, we need to consider the scenario when the mapped cell ID is not reported as part of the ULI, e.g. INITIAL UE MESSAGE, UPLINK NAS TRANSPORT, etc. |
| Ericsson | No | Same as previous question. This information is only needed at UE attach; once that is done, there’s no need to add it to any other messages. Given that the mapping is configured by OAM in both the RAN and the CN, even if it changes during the lifetime of a UE connection the changes will be consistent, hence there is no need for additional signaling. |
| Qualcomm | Yes for stage 2 Stage 3 FFS | Changes in [6,8] are fine for stage 2 only and could be merged. However stage 3 changes in [7] are not acceptable in their current format as they mirror NTN changes form last meeting which are not stable. |
| Huawei | Yes for stage 2 | We acknowledge the issue, but we prefer only change stage 2. |

## Issue 5: Cause value for country-specific routing

In [7], [8] and [9], it is proposed to introduce a cause value over S1 for the country-specific routing to follow the latest agreement in NR NTN WI, namely “UE not in PLMN serving area”.

Question 5: What’s your opinion on the cause value for country-specific routing, do you agree to introduce it over S1?

| Company | Agree or Disagree | Comment |
| --- | --- | --- |
| Nokia | Agree |  |
| Ericsson | Agree | The cause value is needed to drive NNSF – same use case as for NR NTN (see our answer to question 2-1 above). |
| Qualcomm | Agree |  |
| Huawei | Agree |  |

Moderator’s summary:

<TBD>

## Issue 6: Correction on stage 2 BL CR

In [10], one TP to stage 2 BL CR is provided, i.e. remove the ATG and HAPS related descriptions and specify the UE type that are applicable to NTN access.

Question 6: Do you agree with this TP?

| Company | Agree or Disagree | Comment |
| --- | --- | --- |
| Nokia | Agree |  |
| Ericsson | Agree in principle; consider alternative rewording | Another alternative could be to remove the part about UEs altogether. Then the corresponding sentence in Sec. 4.x would become: “…providing non-terrestrial access by means of an NTN…”. |
| Qualcomm | Agree |  |
| Huawei | Agree | Also fine with Ericsson’s rewording method. |

Moderator’s summary:

<TBD>

## Issue 7: Any other aspect

Question 7: Please add any further aspects that are in scope and were not included in the above.

| Company | Comment |
| --- | --- |

Moderator’s summary:

<TBD>

# Conclusion, Recommendations [if needed]

If needed

# References

R3-221655  LS on UE providing Location Information for NB-IoT   RAN2

R3-221798  UE Location Information and IoT NTN  Ericsson

R3-221923  Dicussion about location report and mapping in NTN-IoT  Huawei

R3-222043  Further Discussion on NB-IoT and eMTC Support for NTN  ZTE

R3-222376  (TP for IoT NTN BL CRs) TAC Reporting in ULI  CATT

R3-221905  (TP for TS36.300 BL CR) Discussion on the mapped cell ID and TAC reporting in S1AP  Nokia, Nokia Shanghai Bell

R3-221906  (TP for TS36.413 BL CR) Update for the mapped cell ID and TAC reporting in S1AP  Nokia, Nokia Shanghai Bell

R3-222044  (TP for IoT NTN BL CR 36.300, 36.410 and 36.413) NB-IoT and eMTC Support for NTN  ZTE

R3-222375	(TP for IoT NTN BL CRs) Cause Value and for Cross-country Scenario  CATT

R3-221924	TP to stage 2 BL CR  Huawei, China Unicom, CMCC