3GPP TSG-RAN WG3 Meeting #115-e													draft R3-222436

Electronic Meeting, February 21 – March 3, 2022

Agenda item:	19.2.5

Source: 	Qualcomm Incorporated (Moderator)

Title: 	Summary of offline: Multipath and NLOS Mitigation

Document for:		Discussion

# 1.	Introduction

This contribution summarizes the following email discussion:

CB: # 1905_Pos_Multipath_NLOS - Should a new request for RSRP measurements for additional paths be signalled form LMF to TRP? - Removal of editor´s note in “LoS/NLoS Information”? Updating semantics? (Qualcomm - moderator) Summary of offline disc R3-222436

The following contributions were submitted for Agenda Item 19.2.5:

[1] R3-221748, "(TP for NRPPa baseline) Path Power for Additional Paths", Qualcomm Incorporated.

[2]	R3-221883, "(TP for POS BL CR for TS 38.455, TS 38.473) correction Multipath and NLOS",  Huawei.

# 2.	For the Chair's Notes

Conclusions for RSRP of additional paths:

-	TBD

Conclusions for IE LoS/NLoS Information:

-	TBD

# 3	Discussion (Phase 1)

Please provide your Phase 1 views (5 questions) by XX UTC xx.

## 3.1	RSRP of additional paths

Background – RAN1 agreements (highlights made by the moderator):

RAN1#106bis-e:

Agreement:

Support reporting the path RSRP for the first path and for additional paths as part of DL-TDOA, UL-TDOA, and multi-RTT reporting enhancements.

- FFS: Support introducing a request from the LMF to the UE/TRP when the path-RSRP for additional paths is desired to be reported.

- FFS: Support of path RSRP for additional paths as part of DL-AoD.

RAN1#107-e:

Agreement

- Support the LMF to request DL PRS-RSRPP together with timing measurement as part of DL-TDOA and multi-RTT reporting enhancements

  - Note: This applies to the first path and also to additional paths.

- Support the LMF to request UL SRS-RSRPP together with timing measurement as part of UL-TDOA and multi-RTT reporting enhancements

  - Note: This applies to the first path and also to additional paths.

Contribution[1] proposes adding the additional path RSRP to the new IE Extended Additional Path List (9.2.x12), as shown in yellow highlight below:

### 9.2.x12	Extended Additional Path List

This IE contains the extended additional path results of time measurement.

| IE/Group Name | Presence | Range | IE Type and Reference | Semantics Description |
| --- | --- | --- | --- | --- |
| Additional Path Item |  | 1..<maxnoExtPath> |  |  |
| >CHOICE Relative Path Delay | M |  |  |  |
| >>k0 | M |  | INTEGER(0..16351) |  |
| >>k1 | M |  | INTEGER(0..8176) |  |
| >>k2 | M |  | INTEGER(0..4088) |  |
| >>k3 | M |  | INTEGER(0..2044) |  |
| >>k4 | M |  | INTEGER(0..1022) |  |
| >>k5 | M |  | INTEGER(0..511) |  |
| >Path Quality | O |  | Measurement Quality 9.2.43 |  |
| >Multiple UL-AoA | O |  | 9.2.x9 |  |
| >Path Power | O |  | INTEGER(FFS) | FFS RAN4 |

The encoding of the Path Power is FFS and should probably be the same as for the UL SRS-RSRPP in 9.2.x10 of the current baseline.

Question 1: Do you agree that the IE Extended Additional Path List should include the "Path Power" for each reported additional path as an optional field?

| Company | Yes/No | Comments |
| --- | --- | --- |

Contribution[1] also proposes adding a request for the additional path RSRP to the MEASUREMENT REQUEST message as shown by the yellow highlight below:

| IE/Group Name | Presence | Range | IE type and reference | Semantics description | Criticality | Assigned Criticality |
| --- | --- | --- | --- | --- | --- | --- |
| Message Type | M |  | 9.2.3 |  | YES | reject |
| NRPPa Transaction ID | M |  | 9.2.4 |  | - |  |
| LMF Measurement ID | M |  | INTEGER (1..65536, …) |  | YES | reject |
| TRP Measurement Request List |  | 1 |  |  | YES | reject |
| >TRP Measurement Request Item |  | 1..<maxnoofMeasTRPs> |  |  | EACH | reject |
| >>TRP ID | M |  | 9.2.24 |  | - |  |
| >>Search Window Information | O |  | 9.2.26 |  | - |  |
| >>Cell ID | O |  | NR CGI 9.2.9 | The Cell ID of the TRP identified by the TRP ID IE. | YES | ignore |
| >>AoA Search Window Information | O |  | UL-AoA Assistance Information 9.2.x4 |  | YES | ignore |
| >>Number of TRP Rx TEGs | O |  | ENUMERATED (2, 3, 4, 6, 8) |  | YES | ignore |
| >>Number of TRP RxTx TEGs | O |  | ENUMERATED (2, 3, 4, 6, 8) |  | YES | ignore |
| Report Characteristics | M |  | ENUMERATED (OnDemand, Periodic, ...) |  | YES | reject |
| Measurement Periodicity | C-ifReportCharacteristicsPeriodic |  | ENUMERATED (120ms, 240ms, 480ms, 640ms, 1024ms, 2048ms, 5120ms, 10240ms, 1min, 6min, 12min, 30min, 60min,…, 20480ms, 40960ms) | The codepoint 60min is not applicable | YES | reject |
| TRP Measurement Quantities |  | 1 |  |  | YES | reject |
| >TRP Measurement Quantities Item |  | 1 .. <maxnoPosMeas> |  |  | EACH | reject |
| >TRP Measurement Type | M |  | ENUMERATED (gNB-RxTxTimeDiff, UL-SRS-RSRP, UL-AoA, UL-RTOA,…, Multiple UL-AoA, UL SRS-RSRPP) |  | - |  |
| >Timing Reporting Granularity Factor | O |  | INTEGER (0..5) | Value (0..5) corresponds to (k0..k5) TS 38.133 [16] | - |  |
| SFN initialisation Time | O |  | Relative Time 1900 9.2.36 | If this IE is not present, the TRP may assume that the value is same as its own SFN initialisation time. | YES | ignore |
| SRS Configuration | O |  | 9.2.28 |  | YES | ignore |
| Measurement Beam Information Request | O |  | ENUMERATED (true,...) |  | YES | ignore |
| System Frame Number | O |  | INTEGER(0..1023) |  | YES | ignore |
| Slot Number | O |  | INTEGER(0..79) |  | YES | ignore |
| Response Time | O |  | 9.2.x6 |  | YES | ignore |
| Extended Additional Path List Request | O |  | ENUMERATED (true, …) |  | YES | ignore |
| Additional Path Power Request | O |  | ENUMERATED (true, …) |  | YES | ignore |
| Multiple UL AoA of Additional Path Request | O |  | ENUMERATED (true, …) |  | YES | ignore |
| LoS/NLoS Information Request | O |  | ENUMERATED (true, …) |  | YES | ignore |

Question 2: Do you agree that the MEASUREMENT REQUEST message should include a request from the LMF to the TRP when the path power for additional paths is desired to be reported?

| Company | Yes/No | Comments |
| --- | --- | --- |

Question 3: If your responses to Questions 2/3 were at least partially positive, please provide any comments regarding the related TP in [1].

| Company | Comments |
| --- | --- |

## 3.2	LoS/NLoS Information

Background – RAN1 agreements (highlights made by the moderator):

Agreement Confirm the working assumption on UE-based LoS/NloS indicators option 1 with the following revision: Option 1: LMF associates UE-based LoS/NloS indicators with each DL PRS resource for each TRP, provided the LMF can give different values for Los/NLos indicators of different DL PRS resource of one TRP. Agreement Support the following two options of values for LoS/NLoS indicator reporting from UE/TRP: Soft values: [0, 0.1, …, 0.9, 1] (in steps of 0.1) Hard values: [0, 1] The values correspond to the likelihood of LoS, with a value of 1 corresponding to LoS and a value of 0 corresponding to NLoS

The current IE LoS/NLoS Information in 9.2.x15 contains an Editor' Note that the details of this IE may be further refined:

### 9.2.x15	LoS/NLoS Information

This IE contains the LoS/NLoS information for UL measurement.

| IE/Group Name | Presence | Range | IE type and reference | Semantics description |
| --- | --- | --- | --- | --- |
| CHOICE LoS/NLoS Indicator | M |  |  |  |
| >Soft Indicator |  |  |  |  |
| >>LoS/NLoS Indicator Soft | M |  | INTEGER (0..10) | Values ordered in increasing likelihood of LoS, i.e. 10 corresponding to LoS and 0 corresponding to NLoS. |
| >Hard Indicator |  |  |  |  |
| >>LoS/NLoS Indicator Hard | M |  | ENUMERATED (NLoS, LoS) |  |

Editor’s Note: The details of this IE may be further refined.

Contribution [2] proposes to update the semantics description as shown below and to remove the Editor's Note:

| >>LoS/NLoS Indicator Soft | M |  | INTEGER (0..10) | Values represents the likelihood of LoS in the increasing order with steps of 0.1, i.e. 10 corresponding to LoS and 0 corresponding to NLoS. |
| --- | --- | --- | --- | --- |

Question 4: Do you agree that semantics description for the "LoS/NLoS Indicator Soft" field in IE LoS/NLoS Information should be updated as shown above, and if so, that the Editor’s Note can then be removed?

| Company | Yes/No | Comments |
| --- | --- | --- |

Question 5: If your response to Question 4 was at least partially positive, please provide any comments regarding the related TP in [2].

| Company | Comments |
| --- | --- |

# 4	Discussion (Phase 2), if needed

TBD

# 5	Conclusions, Recommendations

TBD