3GPP TSG-RAN WG3 Meeting #115-e													draft R3-222436

Electronic Meeting, February 21 – March 3, 2022

Agenda item:	19.2.5

Source: 	Qualcomm Incorporated (Moderator)

Title: 	Summary of offline: Multipath and NLOS Mitigation

Document for:		Discussion

# 1.	Introduction

This contribution summarizes the following email discussion:

CB: # 1905_Pos_Multipath_NLOS - Should a new request for RSRP measurements for additional paths be signalled form LMF to TRP? - Removal of editor´s note in “LoS/NLoS Information”? Updating semantics? (Qualcomm - moderator) Summary of offline disc R3-222436

The following contributions were submitted for Agenda Item 19.2.5:

[1] R3-221748, "(TP for NRPPa baseline) Path Power for Additional Paths", Qualcomm Incorporated.

[2]	R3-221883, "(TP for POS BL CR for TS 38.455, TS 38.473) correction Multipath and NLOS",  Huawei.

# 2.	For the Chair's Notes

Conclusions for RSRP of additional paths:

-	TBD

Conclusions for IE LoS/NLoS Information:

-	TBD

# 3	Discussion (Phase 1)

Please provide your Phase 1 views (5 questions) by XX UTC xx.

## 3.1	RSRP of additional paths

Background – RAN1 agreements (highlights made by the moderator):

RAN1#106bis-e:

Agreement:

Support reporting the path RSRP for the first path and for additional paths as part of DL-TDOA, UL-TDOA, and multi-RTT reporting enhancements.

- FFS: Support introducing a request from the LMF to the UE/TRP when the path-RSRP for additional paths is desired to be reported.

- FFS: Support of path RSRP for additional paths as part of DL-AoD.

RAN1#107-e:

Agreement

- Support the LMF to request DL PRS-RSRPP together with timing measurement as part of DL-TDOA and multi-RTT reporting enhancements

  - Note: This applies to the first path and also to additional paths.

- Support the LMF to request UL SRS-RSRPP together with timing measurement as part of UL-TDOA and multi-RTT reporting enhancements

  - Note: This applies to the first path and also to additional paths.

Contribution[1] proposes adding the additional path RSRP to the new IE Extended Additional Path List (9.2.x12), as shown in yellow highlight below:

### 9.2.x12	Extended Additional Path List

This IE contains the extended additional path results of time measurement.

| IE/Group Name | Presence | Range | IE Type and Reference | Semantics Description |
| --- | --- | --- | --- | --- |
| Additional Path Item |  | 1..<maxnoExtPath> |  |  |
| >CHOICE Relative Path Delay | M |  |  |  |
| >>k0 | M |  | INTEGER(0..16351) |  |
| >>k1 | M |  | INTEGER(0..8176) |  |
| >>k2 | M |  | INTEGER(0..4088) |  |
| >>k3 | M |  | INTEGER(0..2044) |  |
| >>k4 | M |  | INTEGER(0..1022) |  |
| >>k5 | M |  | INTEGER(0..511) |  |
| >Path Quality | O |  | Measurement Quality 9.2.43 |  |
| >Multiple UL-AoA | O |  | 9.2.x9 |  |
| >Path Power | O |  | INTEGER(FFS) | FFS RAN4 |

The encoding of the Path Power is FFS and should probably be the same as for the UL SRS-RSRPP in 9.2.x10 of the current baseline.

Question 1: Do you agree that the IE Extended Additional Path List should include the "Path Power" for each reported additional path as an optional field?

| Company | Yes/No | Comments |
| --- | --- | --- |
| HW | No | The RSRPP has already provide the RSRP information per path. There would be no need to include additional information in each measurement of DL-TDOA, UL-TDOA, and multi-RTT. |
| Qualcomm | Yes (proponent) | The SRS-RSRPP provides the RSRP of the first detected path. However, for UL timing measurements (UL-RTOA, gNB Rx-Tx Time Difference Measurement), the TRP can report path timing of additional detected paths. In Rel-17 – per RAN1 agreement – a TRP can report not only the path timing of the additional paths, but also the path power of each detected path. We think this TP reflects the RAN1 agreements. |

Contribution[1] also proposes adding a request for the additional path RSRP to the MEASUREMENT REQUEST message as shown by the yellow highlight below:

| IE/Group Name | Presence | Range | IE type and reference | Semantics description | Criticality | Assigned Criticality |
| --- | --- | --- | --- | --- | --- | --- |
| Message Type | M |  | 9.2.3 |  | YES | reject |
| NRPPa Transaction ID | M |  | 9.2.4 |  | - |  |
| LMF Measurement ID | M |  | INTEGER (1..65536, …) |  | YES | reject |
| TRP Measurement Request List |  | 1 |  |  | YES | reject |
| >TRP Measurement Request Item |  | 1..<maxnoofMeasTRPs> |  |  | EACH | reject |
| >>TRP ID | M |  | 9.2.24 |  | - |  |
| >>Search Window Information | O |  | 9.2.26 |  | - |  |
| >>Cell ID | O |  | NR CGI 9.2.9 | The Cell ID of the TRP identified by the TRP ID IE. | YES | ignore |
| >>AoA Search Window Information | O |  | UL-AoA Assistance Information 9.2.x4 |  | YES | ignore |
| >>Number of TRP Rx TEGs | O |  | ENUMERATED (2, 3, 4, 6, 8) |  | YES | ignore |
| >>Number of TRP RxTx TEGs | O |  | ENUMERATED (2, 3, 4, 6, 8) |  | YES | ignore |
| Report Characteristics | M |  | ENUMERATED (OnDemand, Periodic, ...) |  | YES | reject |
| Measurement Periodicity | C-ifReportCharacteristicsPeriodic |  | ENUMERATED (120ms, 240ms, 480ms, 640ms, 1024ms, 2048ms, 5120ms, 10240ms, 1min, 6min, 12min, 30min, 60min,…, 20480ms, 40960ms) | The codepoint 60min is not applicable | YES | reject |
| TRP Measurement Quantities |  | 1 |  |  | YES | reject |
| >TRP Measurement Quantities Item |  | 1 .. <maxnoPosMeas> |  |  | EACH | reject |
| >TRP Measurement Type | M |  | ENUMERATED (gNB-RxTxTimeDiff, UL-SRS-RSRP, UL-AoA, UL-RTOA,…, Multiple UL-AoA, UL SRS-RSRPP) |  | - |  |
| >Timing Reporting Granularity Factor | O |  | INTEGER (0..5) | Value (0..5) corresponds to (k0..k5) TS 38.133 [16] | - |  |
| SFN initialisation Time | O |  | Relative Time 1900 9.2.36 | If this IE is not present, the TRP may assume that the value is same as its own SFN initialisation time. | YES | ignore |
| SRS Configuration | O |  | 9.2.28 |  | YES | ignore |
| Measurement Beam Information Request | O |  | ENUMERATED (true,...) |  | YES | ignore |
| System Frame Number | O |  | INTEGER(0..1023) |  | YES | ignore |
| Slot Number | O |  | INTEGER(0..79) |  | YES | ignore |
| Response Time | O |  | 9.2.x6 |  | YES | ignore |
| Extended Additional Path List Request | O |  | ENUMERATED (true, …) |  | YES | ignore |
| Additional Path Power Request | O |  | ENUMERATED (true, …) |  | YES | ignore |
| Multiple UL AoA of Additional Path Request | O |  | ENUMERATED (true, …) |  | YES | ignore |
| LoS/NLoS Information Request | O |  | ENUMERATED (true, …) |  | YES | ignore |

Question 2: Do you agree that the MEASUREMENT REQUEST message should include a request from the LMF to the TRP when the path power for additional paths is desired to be reported?

| Company | Yes/No | Comments |
| --- | --- | --- |
| HW | No | See Q1 |
| Qualcomm | Yes (proponent) | We think this reflects the RAN1 agreement. A TRP should need to report the RSRPP of the additional paths only when requested (and supported). |

Question 3: If your responses to Questions 2/3 were at least partially positive, please provide any comments regarding the related TP in [1].

| Company | Comments |
| --- | --- |
| HW | Probably need to clarify more ragarding why this is needed in addition to RSRPP. Also, current RAN1 agreements are mainly for RSRPP. More RAN1/4 information would be needed to justify this. |
| Qualcomm | Because the UL SRS-RSRPP is the power corresponding to the first detected path. The additional paths are reported in the IE Extended Additional Path List and there is currently no SRS RSRPP reported for the i-th path delay. |

## 3.2	LoS/NLoS Information

Background – RAN1 agreements (highlights made by the moderator):

Agreement Confirm the working assumption on UE-based LoS/NloS indicators option 1 with the following revision: Option 1: LMF associates UE-based LoS/NloS indicators with each DL PRS resource for each TRP, provided the LMF can give different values for Los/NLos indicators of different DL PRS resource of one TRP. Agreement Support the following two options of values for LoS/NLoS indicator reporting from UE/TRP: Soft values: [0, 0.1, …, 0.9, 1] (in steps of 0.1) Hard values: [0, 1] The values correspond to the likelihood of LoS, with a value of 1 corresponding to LoS and a value of 0 corresponding to NLoS

The current IE LoS/NLoS Information in 9.2.x15 contains an Editor' Note that the details of this IE may be further refined:

### 9.2.x15	LoS/NLoS Information

This IE contains the LoS/NLoS information for UL measurement.

| IE/Group Name | Presence | Range | IE type and reference | Semantics description |
| --- | --- | --- | --- | --- |
| CHOICE LoS/NLoS Indicator | M |  |  |  |
| >Soft Indicator |  |  |  |  |
| >>LoS/NLoS Indicator Soft | M |  | INTEGER (0..10) | Values ordered in increasing likelihood of LoS, i.e. 10 corresponding to LoS and 0 corresponding to NLoS. |
| >Hard Indicator |  |  |  |  |
| >>LoS/NLoS Indicator Hard | M |  | ENUMERATED (NLoS, LoS) |  |

Editor’s Note: The details of this IE may be further refined.

Contribution [2] proposes to update the semantics description as shown below and to remove the Editor's Note:

| >>LoS/NLoS Indicator Soft | M |  | INTEGER (0..10) | Values represents the likelihood of LoS in the increasing order with steps of 0.1, i.e. 10 corresponding to LoS and 0 corresponding to NLoS. |
| --- | --- | --- | --- | --- |

Question 4: Do you agree that semantics description for the "LoS/NLoS Indicator Soft" field in IE LoS/NLoS Information should be updated as shown above, and if so, that the Editor’s Note can then be removed?

| Company | Yes/No | Comments |
| --- | --- | --- |
| HW | Yes | The step information of 0.1 of the likelihood needs to be added. |
| Qualcomm | Yes | O.K. with the clarification. |

Question 5: If your response to Question 4 was at least partially positive, please provide any comments regarding the related TP in [2].

| Company | Comments |
| --- | --- |
| Qualcomm | Text could be improved, since a probability is between 0 and 1. E.g., "Provides the likelihood of a LOS propagation path in the range between 0 and 1 with 0.1 steps resolution. Value '0' indicates NLOS and value '1' indicates LOS. |

# 4	Discussion (Phase 2), if needed

TBD

# 5	Conclusions, Recommendations

TBD