3GPP TSG-RAN WG3 #115-e	R3-222391

Online, 21 February – 3 March 2022

Agenda Item:	8.3.1

Source:	Qualcomm Incorporated (moderator)

Title:	Summary of Offline Discussion on UE Security Capabilities

Document for:	Approval

# Introduction

CB: # 2_UESecurity_Capability - Check previously endorsed R17 CRs - Revise endorsed CRs for Xn/X2/NGAP at RAN3#115 aligning approach with S1AP - Reply LS to SA3 with full CR set (Qualcomm - moderator) Summary of offline disc R3-222391

# For the Chairman’s Notes

Propose the following:

R3-20xxxa, R3-20xxxc merged

R3-20xxxc rev [in xxxg] – agreed

R3-20xxxd rev [in xxxh] – agreed

R3-20xxxe rev [in xxxi] – agreed

R3-20xxxf rev [in xxxj] – endorsed

Propose to capture the following:

Agreement text…

Agreement text…

WA: carefully crafted text…

Issue 1: no consensus

Issue 2: issue is acknowledged; need to further check the impact on xxx. May be possible to address with a pure st2 change. To be continued…

# Discussion

Introduction:

RAN3 received an LS from SA3 in RAN3#114 [1], requesting that UE security capabilities be passed without manipulation across all the RAN interfaces (and also those sent from the CN to RAN to be the same as those in NAS), irrespective of whether the CN or RAN node understands the specific capability.

In RAN3#114, CRs were endorsed for a range of specifications i.e., 38.300, 36.300, 37.340, 38.413, 38.423, 36.413, 36.423.

It was also requested that RAN3 further considers making support even more future proof by ensuring that, within RAN, the full bitmap is preserved (i.e. 16-bit including bits that cannot even have equivalent in NAS today).

At this meeting, we have a number of CRs for review, as well as some TPs. The full background and status of the CRs is provided in ref [9]. We use the table in this paper below:

| Specification | Document number | Revision of | Comment |
| --- | --- | --- | --- |
| 36.300 | R3-221625 [6] | R3-216056 | No change from endorsed version at RAN3#114 |
| 38.300 | R3-221626 [7] | R3-216057 | No change from endorsed version at RAN3#114 |
| 37.340 | R3-221630 [8] | R3-216095 | No change from endorsed version at RAN3#114 |
| 38.413 | R3-221621 [2] | R3-216047 | Changed from endorsed version at RAN3#114 (**) |
| 36.413 | R3-221622 [3] | R3-221278 | No change from endorsed version at RAN3#114bis |
| 38.423 | R3-221623 [4] | R3-216049 | Changed from endorsed version at RAN3#114 (**) |
| 36.423 | R3-221624 [5] | R3-216050 | Changed from endorsed version at RAN3#114 (**) |

The changes marked (**) are those already discussed in RAN3#114bis but not implemented as discussed above, and they consist of adding some text to the IE explanation, aligning with the endorsed version of S1AP in [3]. In addition, for Xn, since the bitmap is shifted, this is explicitly stated in a note (i.e., need to do a 1-bit shift between NGAP and XnAP on the 16-bit bitmap) so that the retention of the “complete bitmap” is possible.

## Stage 2 draft CRs

As stated above, the draft CRs for stage 2 are in [6,7,8] and are as per the previous endorsed versions at RAN3#114.

Q1: Are the stage 2 CRs ready for approval?  Please provide comments, if any, on the stage 2 CRs.

| Company | Comment |
| --- | --- |
| Huawei | For our stage 2 draft CR for TS 37.340 [8], first we need to update the title with the suffix “[UE_Sec_Caps]” (thanks Young lk for pointing out this). Second, about the following change, since the MN may perform mapping from E-UTRA security bits to NR security bits, we are wondering whether to have this further update (see the highlighted) from: In EN-DC, the UE supports the NR security algorithms corresponding to the E-UTRA security algorithms signalled at NAS level and the UE NR AS Security capability is not signalled to the MN over RRC. Mapping from E-UTRA security algorithms to the corresponding NR security algorithms, where necessary, is performed at the MN. The MN sends the complete UE security capabilities including all security capability bits previously received to the SN. to: In EN-DC, the UE supports the NR security algorithms corresponding to the E-UTRA security algorithms signalled at NAS level and the UE NR AS Security capability is not signalled to the MN over RRC. Mapping from E-UTRA security algorithms to the corresponding NR security algorithms, where necessary, is performed at the MN. The MN sends the complete UE security capabilities including all security capability bits previously received (after mapping, where necessary) to the SN. No strong view, but it seems more clear have this addition. |

## Stage 3 CRs

As stated above, the current CRs for stage 3 are in [2,3,4,5].

In addition, also as stated above

- The 36.413 CR [3] is as endorsed at RAN3#114bis

- The other CRs are modified from their previously endorsed versions at RAN3#114, taking into account the agreement on the S1AP modification and related discussions at RAN3#114bis

Meanwhile there are also TPs [11,12,13] which also propose related changes.

In the moderator’s understanding, the TPs take into account changes discussed (but not implemented) at RAN3#114bis and align the cover page. However, it is the moderator’s understanding that the revisions provided also tried to do the same.

If this understanding is correct, then the TPs can be understood to be implicitly merged into the revised CRs.

Therefore, the moderator would like to check that

- The proposals in the TPs [11,12,13] are contained in the revised CRs

- As such, whether the CRs in [2,3,4,5] can be agreed

Q2: Are the stage 3 CRs [2,3,4,5] ready for approval? Can the TPs be considered implicitly merged, or do you see any missing aspects, or other details to be further checked?

| Company | Comment |
| --- | --- |
| Huawei | Agree. |

## Reply LS

For now the moderator would just like to confirm that companies are agreeable to send a reply LS at this meeting, assuming that a full set of CRs can be agreed, and also if there are any immediate comments on the draft in [10]. Details can be considered later.

Q3: Do you agree to send a reply LS at this meeting, assuming that a full set of CRs can be agreed? Do you have any immediate comments on the draft in [10]?

| Company | Comment |
| --- | --- |
| Huawei | Agree. It seems the date of RAN3#116-e should be updated in the draft LS. |

## Other issues

Please feel free to add any issues or aspects missing from the above.

| Company | Comment |
| --- | --- |

# Conclusion, Recommendations [if needed]

If needed

# References

R3-214714, “LS on User Plane Integrity Protection for eUTRA connected to EPC”, source SA3, SA3#104-e, August 2021.

R3-221621, “Support for mapping complete security capabilities from NAS [UE_Sec_Caps] (Qualcomm Incorporated, Ericsson, Huawei, Nokia, Nokia Shanghai Bell)	CR0669r2, TS 38.413 v16.8.0, Rel-17, Cat. C

R3-221622, “Support for mapping complete security capabilities from NAS [UE_Sec_Caps] (Qualcomm Incorporated, Huawei, Ericsson, Nokia, Nokia Shanghai Bell)	CR1835r4, TS 36.413 v16.8.0, Rel-17, Cat. C

R3-221623, “Support for mapping complete security capabilities from NAS [UE_Sec_Caps] (Qualcomm Incorporated, Ericsson, Huawei, Nokia, Nokia Shanghai Bell)	CR0676r2, TS 38.423 v16.8.0, Rel-17, Cat. C

R3-221624, “Support for mapping complete security capabilities from NAS [UE_Sec_Caps] (Qualcomm Incorporated, Ericsson, Huawei, Nokia, Nokia Shanghai Bell)	CR1624r2, TS 36.423 v16.8.0, Rel-17, Cat. C

R3-221625, “UE Security Capabilities signaling in E-UTRAN [UE_Sec_Caps] (Ericsson, Qualcomm Incorporated, Huawei)	 draftCR

R3-221626, “UE Security Capabilities signaling in NG-RAN [UE_Sec_Caps] (Ericsson, Qualcomm Incorporated, Huawei)	 draftCR

R3-221630, “On UE security capability to address SA3 request [UE_Sec_Caps] (Huawei, Ericsson, Qualcomm Incorporated) draftCR

R3-221736, “Presentation of CRs on Handling of UE Security Capabilities (Qualcomm Incorporated) discussion

R3-221737, “[DRAFT] Reply LS on User Plane Integrity Protection for eUTRA connected to EPC (Qualcomm Incorporated)	LS out To: SA3 CC: RAN2, CT1, CT4, SA2

R3-222183, “(TP for TS 36.423) X2AP Handling of UE Security Capabilities (ZTE), other

R3-222184, “(TP for TS 38.413) NGAP Handling of UE Security Capabilities (ZTE), other

R3-222185 (TP for TS 38.423) XnAP Handling of UE Security Capabilities (ZTE),	other