# 3GPP TSG-RAN WG3 #115-e	R3-222449

# Electronic Meeting, Feb. 21st - Mar. 3rd, 2022

# Agenda Item:	18.4.1

# Source:	ZTE (moderator)

# Title:	Summary of CB: # AIRAN3_ES

# Document for:	Approval

# Introduction

CB: # AIRAN3_ES

- Discuss the left issues input/output/feedback, and standard impacts

- Update the solutions, flowcharts if needed

- Capture the conclusion for ES if agreeable

- Capture agreements and clean up FFS, provide conclusion on ES, and TP if agreeable

(ZTE - moderator)

Summary of offline disc R3-222449

Two phases of this email discussion:

- Phase 1 Deadline: 18:00 UTC, Friday, 25th Feb.

- Phase 2 Deadline : 08:00 UTC, Tuesday, 1st Mar, we will try to come up with agreeable TP in the 2nd phase discussion before online session.

# For the Chairman’s Notes

Propose to capture the following:

xxx

# Discussion

## Solutions and flowcharts

Regarding the corrections to the solutions and flowcharts, following are proposed by companies:

| ID | Corrections to the solutions and flowcharts | Proponent |
| --- | --- | --- |
| 1 | In both section 5.1.2.2 and 5.1.2.3, Rename the box in the message flow chart in step 2 to “Measurement(s)”, and modify the description of step 2 as The UE collects the indicated measurement(s), e.g., UE measurements related to RSRP, RSRQ, SINR of serving cell and neighbouring cells. Likewise in step 3 and step 7/8 the reports can be plural, thus the sentence should be modified as “The UE sends the measurement report message(s) to NG-RAN node 1.” | [1] |
| 2 | In section 5.1.2.2, Modify the description of step 5 as: “Step 5: Model Training at OAM. Required measurements and input data from other NG-RAN nodes are leveraged to train AI/ML models for network energy saving.” | [1] |
| 3 | In Figure 5.1.2.1-1: Split step 4 into two steps | [4] |
| 4 | In both Figure 5.1.2.1-1 and Figure 5.1.2.2-1: Rename the step “energy saving predictions/decisions (Model Inference)” into “Model Inference” | [4] |
| 5 | In both Figure 5.1.2.1-1 and Figure 5.1.2.2-1: Add a new step for action: network energy saving strategy before the step “Handover” | [4] |
| 6 | Adjust the text in the descriptions under Figure 5.1.2.1-1 and Figure 5.1.2.2-1. “If NG-RAN node 2 executes the AI/ML model, the input data for Model Training can include the corresponding inference result from NG-RAN node 2.” | [8] |
| 7 | Add the step0 description for optional AI/ML model at NG-RAN node 2. | [4][5][8] |
| 8 | Use the dashed line box for AI/ML Model (Optional) in NG-RAN node 2. | [5] |
| 9 | “Handover” could be changed to “Energy Saving Action” to be consistent with 5.2 and 5.3. | [5] |
| 10 | Add gNB-CU to the gNB node block of the existing signaling flowchart to complete the description of all AI/ML-based energy-saving solutions. | [13] |
| 11 | Text corrections in the use case description | [5] |
| 12 | Clean the Editor Note | [10] |

Question 1: Companies are invited to provide the comments on whether these corrections to the use case description, solutions and flowcharts could be agreed, and reflected into the TP?

| Company | Which could be agreed?(1~12) | Comments |
| --- | --- | --- |
| Ericsson | Support: 1, 2, 3, 4, 5, 7, 8, 9, 12 | Concerning 6, we do not see the need for this sentence as it does not add new information Concerning 10, we do not see the benefits of this addition |

## Input

In the previous RAN3#114bis-e meeting, following is the open issue related to input for AI/ML-based network energy saving:

- FFS Accept/reject of offloading plan to transfer a certain number of UEs to a neighboring RAN node for energy saving reasons

Following inputs are proposed by contributions:

| ID | Input information | Support/Objection |
| --- | --- | --- |
| 1 | Accept/reject of offloading plan to transfer a certain number of UEs to a neighboring RAN node for energy saving reasons | Support: [1],[2],[7], [11] Not support: [3],[4], [6](up to implementation), [8], [9], [10], [13] Move the input information as feedback information [1] Move the input information as standard impacts instead of input information [12] |
| 2 | Predicted energy state | To align with predicted energy efficiency/resource status,, should be straightforward. [5] |

Question 2: Companies are invited to provide your comments on whether the input information above for AI/ML based Network Energy Saving could be agreed to capture into the TR?

| Company | Which could be agreed?(1~2) | Comments |
| --- | --- | --- |
| Ericsson | Support: 1, 2 | We feel we need to clarify the use case concerning “Accept/reject of offloading plan”. We acknowledge the comments from companies stating that handovers can be failed by the HO target node. However, this mechanism is not sufficient in the Energy Saving use case. An NG-RAN node may infer that if e.g. 10 UEs are offloaded to a target neighbour cell, its energy efficiency will improve. Note, only if all the 10 UEs are offloaded such improvement will take place. If we rely on HO failures, the source NG-RAN may offload 5 UEs successfully and get HO failures for the remaining 5. This event may not improve energy efficiency at source while it may degrade energy efficiency at target and for that it should be avoided. For this reason, we find it beneficial for source to indicate to target that 10 UEs need to be handed over. If target can accept this action, then the inferred action will take place, otherwise another action will be chosen. This concept can also be extended to predict energy efficiency at target RAN, but we leave these aspects to normative phase. |

In addition, [2] believes it would be beneficial for source RAN node and target RAN node to negotiate regarding number of UEs/traffic to be offloaded for the energy saving reasons. Such negotiations may be in a form of offloading plan accept/reject on in another form. It is proposed to add the following Note to step 11 of 5.1.2.2 and step 9 of 5.1.2.3:

“Note: NG-RAN node 1 and NG-RAN node 2 may perform negotiations related to UE HO / traffic offloading before HO execution to prevent service interruptions and excessive signaling and for faster traffic offloading.”

Question 3: Companies are invited to provide your comments on whether to capture the Note regarding negotiations between NG-RAN node 1 and NG-RAN node 2 above?

| Company | Yes/No | Comments |
| --- | --- | --- |
| Ericsson | We tend to support this | We see this proposal as fitting in the previous concept of “Accept/reject of offloading plan”, so maybe it could be part of that concept and taken as a whole. |

## Output

## 3.3.1 Validity time

In the previous RAN3#114bis-e meeting, following is the open issue related to output for AI/ML-based network energy saving:

- FFS Validity time of the predicted energy saving decisions

Upon the contributions, [4][6][11][12][13] propose to introduce the validity time of the predicted energy saving decisions, and provide the benefits and definition of the validity time, while [9][10] think there is no need to introduce the validity time, because received information are valid till a new version of such information is received, and the output information would be reported periodically, which implicitly indicate the validity time.

And [1] proposes to replace FFS with Validity time (internal node use only). [7][8] propose to discuss the validity time in the normative Rel-18 phase.

Moderator tries to conclude the options below regarding left issue on the validity time:

A. Remove Validity time as output information, and further discuss the validity time in the normative R18 work.

B. Remove FFS and keep it as an output information

C. Replace FFS with “Validity time (internal node use only)”.

D. Replace FFS with “Validity time use outside the internal node will be discussed during the work item phase”.

Question 4: Companies are invited to provide their views on which options could be agreed regarding validity time.

| Company | Which options could be agreed?(A~D) | Comments |
| --- | --- | --- |
| Ericsson | Support: A, C, D | We see validity time to apply to limited outputs, i.e. to quantifiable outputs such as predicted metrics rather than predicted actions. We would be ok to state that validity time is a node internal output. If we want to signal this output, then we need to discuss in normative phase to what output exactly the validity time applies. If the group cannot converge, we would be also fine with removing the validity time parameter. |

3.3.2 Other Outputs

Following outputs are proposed by contributions [3][7].

| ID | Proposed Outputs | Supporting Reason |
| --- | --- | --- |
| 1 | Finer granularity of on/off in time, frequency and space domain, coverage modification, resource coordination | [3] An active cell can support finer granularity of on/off, and the finer granularity on/off may have impact to F1/E1 interface because the inference is supported in the gNB-CU. |
| 2 | Offloading plan | [7] Handover strategy can comprise of one or more offloading proposal plans, and should be added as an ML-model output |

Question 5: Companies are invited to provide your views on whether the outputs above for AI/ML based Network Energy Saving above could be agreed to capture into the TR?

| Company | Which could be agreed?(1~2) | Comments |
| --- | --- | --- |
| Ericsson | Support: 2 | Regarding 1, we do not see the benefit of signalling over the interfaces inference outputs concerning actions with granularity higher than cell level. As an example, such actions do not impact mobility Regarding 2) we believe it would be good to allow the exchange of offloading plans that target RAN nodes may check and support, or reject. We believe however that if an NG RAN node decides to switch off a cell, this should not be communicated to neighbours necessarily. So the offloading plan can be signalled only when multiple plans are possible and the optimal one needs to be selected |

## Standard impacts

- proposes to add NG interface impact for information exchange via core network. The same information exchange should be supported over NG for the scenario where Xn is not available.

- Same information exchange as Xn above between NG-RAN nodes via core network.

- proposes to extend the standard impacts to include the output information impacts and extend feedback information impacts, which are listed as follows:

-New signalling procedure or enhanced existing procedure to provide the output data information

- Predicted energy efficiency between neighboring NG-RAN nodes and source NG-RAN node

- Predicted energy state (e.g., active, high, low, inactive) between neighboring NG-RAN nodes and source NG-RAN node

- Validity time of the predicted energy saving decisions

-New signalling procedure or enhanced existing procedure to retrieve feedback information

- UE performance information between neighboring NG-RAN nodes and source NG-RAN node

- System KPIs between neighboring NG-RAN nodes and source NG-RAN node

- considers the current MDT mechanism should be enhanced in order to support consecutive AI/ML data collection. The standard impacts of Network Energy Saving should be extended to include MDT enhancement:

- MDT signaling enhancement to retrieve consecutive AI/ML input information from UE.

- [12] proposes to add following related to “Accept/reject of offloading plan” to the standards impact for the feedback information:

- Accept/reject of offloading plan to transfer a certain number of UEs to a neighboring RAN node for energy saving reasons from neighboring NG-RAN node to a NG-RAN node.

[12] also proposes the Xn impacts that is predicted energy saving decision from a NG-RAN node to neighbor NG-RAN node.

Upon the contributions, moderator concludes the standard impacts for AI/ML based energy saving, and invites companies to provide your views on these standard impacts below.

Potential Uu impacts:

- MDT signaling enhancement to retrieve consecutive AI/ML input information from UE.

Potential Xn impacts:

New signalling procedure or enhanced existing procedure to provide the output data information

2. Predicted energy efficiency between neighboring NG-RAN nodes and source NG-RAN node

3. Predicted energy state (e.g., active, high, low, inactive) between neighboring NG-RAN nodes and source NG-RAN node

4. Validity time of the predicted energy saving decisions

- Predicted energy saving decision from a NG-RAN node to neighbor NG-RAN node

New signalling procedure or enhanced existing procedure to retrieve feedback information

6. UE performance information between neighboring NG-RAN nodes and source NG-RAN node

7. System KPIs between neighboring NG-RAN nodes and source NG-RAN node

8. Accept/reject of offloading plan to transfer a certain number of UEs to a neighboring RAN node for energy saving reasons from neighboring NG-RAN node to a NG-RAN node.

Potential NG impacts:

9. Same information exchange as Xn above between NG-RAN nodes via core network.

Question 6: Companies are invited to provide your views on whether the standard impacts for AI/ML based Network Energy Saving above could be agreed to capture into the TR?

| Company | Which could be agreed?(1~9) | Comments |
| --- | --- | --- |
| Ericsson | Not needed | In our view, “standard impacts” should be a high level description of how the standard may be affected. We foresee that normative work should be based on the use case descriptions, so what is in those descriptions should be taken into account. We see that many of the proposals above just repeat the content of the use case description and for that they are not needed (and not that the proposals above also include use cases that we do support). Some further comments: we have not at all discussed signalling of AI/ML information over NG, hence this cannot be added to the TR. The topic of signalling frequent and high volume information via the CN needs a dedicated discussion. MDT enhancements will be taken during normative phase. For now, we have captured that these are potential changes If we ensure that the “Accept/reject of offloading plan” is added to the inputs/outputs, there is no need to add it to the standard impacts |

## Conclusion

- [10] both propose to add the sub-section to include the conclusion to the AI/ML based Network Energy Saving use case. And [11] suggests to Consider AI based Energy saving use case as baseline for normative work.

Following are the proposed conclusion for the R18 normative work:

- The Network Energy Saving use case description and “solutions and standard impacts” should be taken as baseline for normative phase. [7]

- RAN3 has analyzed the descriptions and potential solutions, expected inputs, expected outputs, and expected feedback information of AI/ML based Network Energy Saving, and RAN3 is recommended to specify the potential solutions and potential standard impacts in the above clauses in the Rel.18 WI. [10]

Question 7: Companies are invited to provide the comments on whether to add the sub-section to include the conclusion to the AI/ML based Network Energy Saving for the R18 normative work?

| Company | If yes, Conclusion1 or Conclusion2 | Comments |
| --- | --- | --- |
| Ericsson | Need to be taken in CB: #1 | We of course support the content of both proposals 1 and 2, but there is a discussion ongoing in CB: # 1 on an overall conclusion for the study. We suggest to focus on that discussion and to add the content from 1. And 2. To the overall conclusion |

## Others

[8] proposes to discuss and make a decision in RAN3 on the preferred way forward between the following 2 options with respect to slicing information in the AI/ML Rel.17 study/Rel.18 work:

1.Include in the scope of the study predictions of existing metrics that may be made on a per slice granularity and in this way introduce slicing aspects into the energy saving use case.

2.Exclude slicing aspects completely from the study and revisit those under a new use case covering slicing enhancements for a possible Rel.18 SI.

Question 8: Companies are invited to provide the comments on which options above is preferred?

| Company | Option1/Option2 | Comments |
| --- | --- | --- |
| Ericsson | Neither of them | Network slicing is implicitly supported in the 5G system in the sense that per slice information is already exchanged within the RAN, e.g. resource status information per slice. For that we do not see the need to focus on slicing explicitly. Besides that, we have not studied and we cannot think of any energy saving action that is made per slice. Hence we believe nothing specific needs to be done for the slicing use case, but slicing will be implicitly supported. |

# Conclusion, Recommendations [if needed]

If needed

# References

R3-221695	Closing open issues in AI/ML Energy Savings use case  (InterDigital Finland Oy)	other

R3-221780	Proposed updates to Energy Saving Solutions and Standard Impact (NEC)	other

R3-221848	Network energy saving (Qualcomm Incorporated)	pCR

R3-221942	AI/ML based network energy saving (Intel Corporation)	discussion

R3-221986	(TP to TR 37.817) On Network Energy Saving (Lenovo, Motorola Mobility)	other

R3-222018	(TP for TR 37.817)Discussion on Standards Impact on energy saving (CATT)	other

R3-222101	(TP for BL CR for TR 37.817) Network Energy Saving (Ericsson)	other

R3-222121	(TP for TR 37.817) A few final aspects on AI/ML Energy Saving (Nokia, Nokia Shanghai Bell)	other

R3-222228	Further discussions on energy saving (Huawei)	other

R3-222244	Further discussion on solution to AI based Network Energy Saving (ZTE Corporation)	other

R3-222274	On Remaining issues for AI based Energy Saving (CMCC)	other

R3-222309	Discussion on Standard Impact for AI/ML based Network Energy Saving (Samsung)	other

R3-222328	Further discussion for AI-based network energy saving (China Telecom Corporation Ltd.)	discussion