# 3GPP TSG-RAN WG3 #115-e	R3-222449

# Electronic Meeting, Feb. 21st - Mar. 3rd, 2022

# Agenda Item:	18.4.1

# Source:	ZTE (moderator)

# Title:	Summary of CB: # AIRAN3_ES

# Document for:	Approval

# Introduction

CB: # AIRAN3_ES

- Discuss the left issues input/output/feedback, and standard impacts

- Update the solutions, flowcharts if needed

- Capture the conclusion for ES if agreeable

- Capture agreements and clean up FFS, provide conclusion on ES, and TP if agreeable

(ZTE - moderator)

Summary of offline disc R3-222449

Two phases of this email discussion:

- Phase 1 Deadline: 18:00 UTC, Friday, 25th Feb.

- Phase 2 Deadline : 08:00 UTC, Tuesday, 1st Mar, we will try to come up with agreeable TP in the 2nd phase discussion before online session.

# For the Chairman’s Notes

Propose to capture the following:

xxx

# Discussion

## Solutions and flowcharts

Regarding the corrections to the solutions and flowcharts, following are proposed by companies:

| ID | Corrections to the solutions and flowcharts | Proponent |
| --- | --- | --- |
| 1 | In both section 5.1.2.2 and 5.1.2.3, Rename the box in the message flow chart in step 2 to “Measurement(s)”, and modify the description of step 2 as The UE collects the indicated measurement(s), e.g., UE measurements related to RSRP, RSRQ, SINR of serving cell and neighbouring cells. Likewise in step 3 and step 7/8 the reports can be plural, thus the sentence should be modified as “The UE sends the measurement report message(s) to NG-RAN node 1.” | [1] |
| 2 | In section 5.1.2.2, Modify the description of step 5 as: “Step 5: Model Training at OAM. Required measurements and input data from other NG-RAN nodes are leveraged to train AI/ML models for network energy saving.” | [1] |
| 3 | In Figure 5.1.2.1-1: Split step 4 into two steps | [4] |
| 4 | In both Figure 5.1.2.1-1 and Figure 5.1.2.2-1: Rename the step “energy saving predictions/decisions (Model Inference)” into “Model Inference” | [4] |
| 5 | In both Figure 5.1.2.1-1 and Figure 5.1.2.2-1: Add a new step for action: network energy saving strategy before the step “Handover” | [4] |
| 6 | Adjust the text in the descriptions under Figure 5.1.2.1-1 and Figure 5.1.2.2-1. “If NG-RAN node 2 executes the AI/ML model, the input data for Model Training can include the corresponding inference result from NG-RAN node 2.” | [8] |
| 7 | Add the step0 description for optional AI/ML model at NG-RAN node 2. | [4][5][8] |
| 8 | Use the dashed line box for AI/ML Model (Optional) in NG-RAN node 2. | [5] |
| 9 | “Handover” could be changed to “Energy Saving Action” to be consistent with 5.2 and 5.3. | [5] |
| 10 | Add gNB-CU to the gNB node block of the existing signaling flowchart to complete the description of all AI/ML-based energy-saving solutions. | [13] |
| 11 | Text corrections in the use case description | [5] |
| 12 | Clean the Editor Note | [10] |

Question 1: Companies are invited to provide the comments on whether these corrections to the use case description, solutions and flowcharts could be agreed, and reflected into the TP?

| Company | Which could be agreed?(1~12) | Comments |
| --- | --- | --- |
| Ericsson | Support: 1, 2, 3, 4, 5, 7, 8, 9, 12 | Concerning 6, we do not see the need for this sentence as it does not add new information Concerning 10, we do not see the benefits of this addition |
| Nokia | 1,2, 3,4,5,6,7,8, 9 with a comment, 10, 12 | Regarding 6, in step 4 we have only captured that an NG-RAN node 2 has an ML Model available. This doesn’t necessarily mean that the NG-RAN node 2 executes inference. For input data from NG-RAN node 2 to also comprise predictions, NG-RAN node 2 needs to run model inference, not just having an ML Model available. Regarding 9, this could be changed to Energy Saving Action but an Action may be a local decision at a node and may not have impacts on a neighbour. Therefore, representing this generalization in the figure may be more complex. Regarding 10, it is ok to add gNB-CU to the gNB node block. Irrespective of the way forward, this should be aligned among the use cases (currently CU is mentioned in the node block in the Load Balancing use case). |
| Samsung | Support 1, 2, 3, 4, 6, 7, 8, 9, 10, 12 | For 4, as the model in node 2 is optional, it is better to add such description. For 5, the handover needs to be done before switch-off. So the action step is not before the HO. |
| Intel | 1, 2, 3, 4, 5, 7, 8, 9, 10, 12 | For 6, we think it may not be needed as we have captured the required information for training/inference explicitly in following sections. For 9, step 11 should also be updated, as NG-RAN node may also not perform handover, but act on other energy saving strategies. Step 11 then should be updated as “NG-RAN node 1 executes network energy saving actions. NG-RAN node 1 may select the most appropriate target cell for each UE before it performs handover, if the output is handover strategy” |
| Lenovo, Motorola Mobility | 1, 2, 3, 4, 7, 8, 9, 11, 12 | 4, to be consistent among different use case diagrams, either use “Model Inference” or use “xxxxx predictions/decisions” 5, we proposed in [5] to replace “Handover” with “Energy saving action” 6, we have text describing different kinds of input in the other subclause, we don’t need to repeat here. |
| InterDigital | 1, 2, 3, 4, 5, 7, 8, 9, 10, 12 |  |
| Qualcomm | All except 6 | 6 introduces confusion on recursive training. |
| CATT | 1,2, 3,4,5,6,7,8, 9 | for 10, we are not sure all the message in the flow chart are connected only with CU. For example, step 12 and 13 feedback may also be provided from DU to OAM. But it is needed to consider split gNB case in flow chart. |
| CMCC | 1,2,3,4,5,7,8,9,10,12 | For 6, it is duplicated information. |
| Huawei | Yes: 1,2,3,4,5,7,8,9,12 No: 6,10,11 | Regarding 6, the current text shows the NG-RAN node 2 sends input data for model training to OAM. It means the NG-RAN 2 could sends the inference result as the input data to OAM. We do not see any new information. Regarding 10, we do not see the benefits. Regarding 11, no sure about the purpose. |

## Input

In the previous RAN3#114bis-e meeting, following is the open issue related to input for AI/ML-based network energy saving:

- FFS Accept/reject of offloading plan to transfer a certain number of UEs to a neighboring RAN node for energy saving reasons

Following inputs are proposed by contributions:

| ID | Input information | Support/Objection |
| --- | --- | --- |
| 1 | Accept/reject of offloading plan to transfer a certain number of UEs to a neighboring RAN node for energy saving reasons | Support: [1],[2],[7], [11] Not support: [3],[4], [6](up to implementation), [8], [9], [10], [13] Move the input information as feedback information [1] Move the input information as standard impacts instead of input information [12] |
| 2 | Predicted energy state | To align with predicted energy efficiency/resource status,, should be straightforward. [5] |

Question 2: Companies are invited to provide your comments on whether the input information above for AI/ML based Network Energy Saving could be agreed to capture into the TR?

| Company | Which could be agreed?(1~2) | Comments |
| --- | --- | --- |
| Ericsson | Support: 1, 2 | We feel we need to clarify the use case concerning “Accept/reject of offloading plan”. We acknowledge the comments from companies stating that handovers can be failed by the HO target node. However, this mechanism is not sufficient in the Energy Saving use case. An NG-RAN node may infer that if e.g. 10 UEs are offloaded to a target neighbour cell, its energy efficiency will improve. Note, only if all the 10 UEs are offloaded such improvement will take place. If we rely on HO failures, the source NG-RAN may offload 5 UEs successfully and get HO failures for the remaining 5. This event may not improve energy efficiency at source while it may degrade energy efficiency at target and for that it should be avoided. For this reason, we find it beneficial for source to indicate to target that 10 UEs need to be handed over. If target can accept this action, then the inferred action will take place, otherwise another action will be chosen. This concept can also be extended to predict energy efficiency at target RAN, but we leave these aspects to normative phase. |
| Nokia | 2 | About 1, we think that the source node, utilizing AI/ML, should be in position to take “good” actions. The source, using AI/ML intelligence, should be able to determine how many UEs it is realistic to offload and to which neighbour(s) for energy efficiency. If the source takes a suboptimal decision, then it can use retraining of its Model until its decisions lead to the best energy efficiency performance, which the target would have no incentive to reject. |
| Samsung | Support 1 | For 1, negotiation of offloading plan helps to realize globe optimization by successful offloading. If the target node can not accept the offloading plan, the source node can select other candidate plan. The ES decision is set based on the status of node and its neighbors. But maybe there are several offloading plans from several nodes to one node. For example, node A and node C are the neighbors for node B, but node A and node C are not the neighbor for each other. Due to not-heavy load in node B, node A sets the decision to offload n UEs to node B at time T1, and at the same time, node C also sets the decision to offload m UEs to node B at time T1. At this situation, without negotiation in advance, node B needs to reject the multiple HO request at time T1, which leads to heavy signaling overhead. And node A and node C may needs to re-design the ES strategy, which delays the ES action such as switch-off. For 2 (energy state), we are fine for active and inactive. But the high/low energy state is confused. So suggest to add the description about what is high/low energy state. |
| Intel | Support 2 | For 1, if we understand E///’s comment correctly, the purpose is still objecting the action plan from the source NG-RAN node. During last meeting, it was explained that the source NG-RAN node can decide its own action based on inference result. Additionally, the negative impact on neighbouring NG-RAN node is already taken into account during source NG-RAN node’s model training. OAM and source NG-RAN node can avoid negative performance impact on neighbouring NG-RAN node by collecting input from neighbouring NG-RAN node for model training. |
| Lenovo, Motorola Mobility | 2 |  |
| InterDigital | Support 1,2 | While we feel that 1 is actually feedback instead of input (and some of the comments above both pro and con support this) we are ok keeping it as input if majority supports. |
| Qualcomm | 2 | Existing handover preparation procedure can be used for #1. |
| CATT | None | For 1), Whether UE can be accepted or rejected by a neighbouring RAN node is part of handover procedures. After source NG-RAN is informed of this information, it can select another target cell to finish handover or no suitable target cell can be founded temporarily. It is up to implementation. For 2), we think energy state is current state. It is not needed to align again. |
| NEC | Yes | We believe that negotiations between neighbor NG-RAN nodes regarding NG-RAN nodes for ES is beneficial. |
| CMCC | Support 1 | Share the view with Samsung that negotiation of offloading plan helps to realize globe optimization by successful offloading. If the target node can not accept the offloading plan, the source node can select other candidate plan. |
| Huawei | No to 1, not sure about the purpose of 2 | For 1, as we already indicated, existing mechanism allows the acceptation/rejection of an incoming request, not sure what else needed; For 2, now it seems we introduced predicted energy state, predicted energy efficiency, predicted energy resource status, not sure if we need so many predicted info which seem to be similar. |

In addition, [2] believes it would be beneficial for source RAN node and target RAN node to negotiate regarding number of UEs/traffic to be offloaded for the energy saving reasons. Such negotiations may be in a form of offloading plan accept/reject on in another form. It is proposed to add the following Note to step 11 of 5.1.2.2 and step 9 of 5.1.2.3:

“Note: NG-RAN node 1 and NG-RAN node 2 may perform negotiations related to UE HO / traffic offloading before HO execution to prevent service interruptions and excessive signaling and for faster traffic offloading.”

Question 3: Companies are invited to provide your comments on whether to capture the Note regarding negotiations between NG-RAN node 1 and NG-RAN node 2 above?

| Company | Yes/No | Comments |
| --- | --- | --- |
| Ericsson | We tend to support this | We see this proposal as fitting in the previous concept of “Accept/reject of offloading plan”, so maybe it could be part of that concept and taken as a whole. |
| Nokia | No | AI/ML can be used on top of existing mechanisms to make them better. We don’t see the need to introduce a new mechanism of negotiations. |
| Samsung | OK | Same reason as question2 |
| Intel | No | As explained above, impact on neighbouring NG-RAN node is already taken into account during source NG-RAN node’s model training. OAM and source NG-RAN node can avoid negative performance impact on neighbouring NG-RAN node by collecting input from neighbouring NG-RAN node for model training. Therefore, it’s not needed to negotiate for the predicted action, which will increase delays. |
| Lenovo, Motorola Mobility | Maybe no | Agree with other companies, let’s focus on basic use of AI/ML first before negotiation between different AI/ML algorithms. |
| InterDigital | OK |  |
| Qualcomm | No | Let’s use handover preparation procedure for this purpose. No need to introduce a new mechanism. |
| CATT | None | For 1), Whether UE can be accepted or rejected by a neighbouring RAN node is part of handover procedures. After source NG-RAN is informed of this information, it can select another target cell to finish handover or no suitable target cell can be founded temporarily. It is up to implementation. For 2), we think energy state is current state. It is not needed to align again. |
| CATT | No | We do not think negotiation is benefit as if NG-RAN1 informs NG-RAN2 offloading plan, NG-RAN2 has to reserve resource in advance for offloaded UE which may waste NG-RAN resource. On the contrary, Source RAN node has considered the neighbor RAN load and state and then makes decision. Neighbor NG-RAN can accept/reject UE based on current state which can use NG-RAN resource effectively. So, it is not needed to negotiate. |
| NEC | Yes | We believe that negotiations between neighbor NG-RAN nodes regarding NG-RAN nodes for ES is beneficial. |
| CMCC | Yes |  |
| Huawei | No | We think the decision/strategy from AI/ML model already take the situation/status of neighbor node into consideration, to introduce negotiation mechanism just makes things complicated without extra benefits. Of course, any request could be rejected, this is business as usual. |

## Output

## 3.3.1 Validity time

In the previous RAN3#114bis-e meeting, following is the open issue related to output for AI/ML-based network energy saving:

- FFS Validity time of the predicted energy saving decisions

Upon the contributions, [4][6][11][12][13] propose to introduce the validity time of the predicted energy saving decisions, and provide the benefits and definition of the validity time, while [9][10] think there is no need to introduce the validity time, because received information are valid till a new version of such information is received, and the output information would be reported periodically, which implicitly indicate the validity time.

And [1] proposes to replace FFS with Validity time (internal node use only). [7] propose to discuss the validity time in the normative Rel-18 phase. [8] proposes to discuss model output validity in normative work.

Moderator tries to conclude the options below regarding left issue on the validity time:

A. Remove Validity time as output information, and further discuss the validity time in the normative R18 work.

B. Remove FFS and keep it as an output information

C. Replace FFS with “Validity time (internal node use only)”.

D. Replace FFS with “Validity time use outside the internal node will be discussed during the work item phase”.

Question 4: Companies are invited to provide their views on which options could be agreed regarding validity time.

| Company | Which options could be agreed?(A~D) | Comments |
| --- | --- | --- |
| Ericsson | Support: A, C, D | We see validity time to apply to limited outputs, i.e. to quantifiable outputs such as predicted metrics rather than predicted actions. We would be ok to state that validity time is a node internal output. If we want to signal this output, then we need to discuss in normative phase to what output exactly the validity time applies. If the group cannot converge, we would be also fine with removing the validity time parameter. |
| Nokia | Support: A with a note | We have hard time to understand how exactly validity time will be defined. It seems to be a model specific parameter related to how long a prediction is valid. However, how to define it exactly seems to depend on the model output. E.g., in certain cases it can be a time window during which a prediction is valid and in other examples it is a time instant. It is not clear why is it better if the node running inference indicates for how long the action will be valid as opposed to just sending a new action when the action becomes invalid. But even further, in our view model output validity may not depend only on time. So we could be open to discuss in Rel.18 model output validity that may not necessarily be a time-dependent quantity. |
| Samsung | Prefer B | The validity time is to indicate the applicative time for the results obtained from AI/ML model. We need to know when the predicted value is for. Without such information, the results may not benefit to the RAN if applying it to a misplaced time. The validity time might be a time period or time point for predicted energy saving decision. Only when the decision would be done in the determined time, the function is valuable. For example, it may lead to a disaster to execute in advance such as connection lost for UEs or local overload. So it is better to set the validity time as additional information along with the predicted energy saving decision. |
| Intel | Prefer B | The Validity time can be defined as a time period of an active and valid model inference result, indicating the start time and stop time of the predicted energy saving strategy. The target NG-RAN node should only perform the received inference action during validity time. When validity time expires, the inference action should be dropped. As a compromise, we are fine to capture “validity time as output information will be discussed during normative R18 work”. |
| Lenovo, Motorola Mobility | B or D |  |
| InterDigital | Prefer C then D | We would support A or B if and only if it is aligned with other use cases. |
| Qualcomm | D preferred, then A |  |
| CATT | D | In our understanding, validity time is useful for neighboring RAN node to know the valid time period for exchanged information. For exchanged predicted energy saving strategies and energy state, only valid time period is clarified, neighboring RAN node can know how to use these information and then make its own prediction. |
| NEC | A, B, D |  |
| CMCC | B or D | We see benefits of validity time for both internal and neighboring nodes. |
| Huawei | A | We think the received information are valid till a new version of such information is received. Secondly, the output information can be reported to the subscribed node with a given periodicity, which is just like the existing mechanism where on entity could raise request of load status to another entity with a given periodicity, this mechanism could be reused. In addition, |

3.3.2 Other Outputs

Following outputs are proposed by contributions [3][7].

| ID | Proposed Outputs | Supporting Reason |
| --- | --- | --- |
| 1 | Finer granularity of on/off in time, frequency and space domain, coverage modification, resource coordination | [3] An active cell can support finer granularity of on/off, and the finer granularity on/off may have impact to F1/E1 interface because the inference is supported in the gNB-CU. |
| 2 | Offloading plan | [7] Handover strategy can comprise of one or more offloading proposal plans, and should be added as an ML-model output |

Question 5: Companies are invited to provide your views on whether the outputs above for AI/ML based Network Energy Saving above could be agreed to capture into the TR?

| Company | Which could be agreed?(1~2) | Comments |
| --- | --- | --- |
| Ericsson | Support: 2 | Regarding 1, we do not see the benefit of signalling over the interfaces inference outputs concerning actions with granularity higher than cell level. As an example, such actions do not impact mobility Regarding 2) we believe it would be good to allow the exchange of offloading plans that target RAN nodes may check and support, or reject. We believe however that if an NG RAN node decides to switch off a cell, this should not be communicated to neighbours necessarily. So the offloading plan can be signalled only when multiple plans are possible and the optimal one needs to be selected |
| Nokia | None | Regarding 1, we do not need to capture finer granularity in the output. Those can be left to implementation. Regarding 2, we are not sure why the introduction of AI/ML necessitates the introduction of an offloading plan in the output. On the contrary, AI/ML should help a source node to identify the best strategy/offloading plan out of a set of options. Once the best strategy is selected, the need for rejection by the target node vanishes. |
| Samsung | Support 2 | For 1, it is up on implementation. For 2, offloading plan is fine for us. Negotiation of offloading plan is beneficial for globe optimization by successful offloading. If the target node can not accept the offloading plan, the source node can select other candidate plan. The details can be discussed in normative phase. |
| Intel | No | Same as Q2/Q3. |
| Lenovo, Motorola Mobility | None |  |
| InterDigital | Support 2 | This is tied to support in Q2/Q3 |
| Qualcomm | 1 | #1 was almost agreed in last meeting. But, it was removed from the TR because some companies think it can be up to implementation. Actually, it is not true. The finer granularity on/off may have impact to F1/E1 for inference input and output enforcement. |
| CATT | None | For 1, we think it is up to implementation. For 2, AI/ML module can make decision any time, it is not needed for AI/ML module to follow a previous plan as current NG-RAN state may change rapidly. So, plan may be not beneficial while mislead neighbor NG-RAN. |
| NEC | 2 |  |
| CMCC | Support 2 |  |
| Huawei | None | For 1, we understand the intention that finer granularity of on/off could be considered, but we are not see the benefit of signaling such outputs over the interfaces. This is up to implementation. For 2, we understand the intention, yet this offloading plan is also overlapped with use case on load balancing, but firstly we should be clear on what here more offloading plans mean. |

## Standard impacts

- proposes to add NG interface impact for information exchange via core network. The same information exchange should be supported over NG for the scenario where Xn is not available.

- Same information exchange as Xn above between NG-RAN nodes via core network.

- proposes to extend the standard impacts to include the output information impacts and extend feedback information impacts, which are listed as follows:

-New signalling procedure or enhanced existing procedure to provide the output data information

- Predicted energy efficiency between neighboring NG-RAN nodes and source NG-RAN node

- Predicted energy state (e.g., active, high, low, inactive) between neighboring NG-RAN nodes and source NG-RAN node

- Validity time of the predicted energy saving decisions

-New signalling procedure or enhanced existing procedure to retrieve feedback information

- UE performance information between neighboring NG-RAN nodes and source NG-RAN node

- System KPIs between neighboring NG-RAN nodes and source NG-RAN node

- considers the current MDT mechanism should be enhanced in order to support consecutive AI/ML data collection. The standard impacts of Network Energy Saving should be extended to include MDT enhancement:

- MDT signaling enhancement to retrieve consecutive AI/ML input information from UE.

- [12] proposes to add following related to “Accept/reject of offloading plan” to the standards impact for the feedback information:

- Accept/reject of offloading plan to transfer a certain number of UEs to a neighboring RAN node for energy saving reasons from neighboring NG-RAN node to a NG-RAN node.

[12] also proposes the Xn impacts that is predicted energy saving decision from a NG-RAN node to neighbor NG-RAN node.

Upon the contributions, moderator concludes the standard impacts for AI/ML based energy saving, and invites companies to provide your views on these standard impacts below.

Potential Uu impacts:

- MDT signaling enhancement to retrieve consecutive AI/ML input information from UE.

Potential Xn impacts:

New signalling procedure or enhanced existing procedure to provide the output data information

2. Predicted energy efficiency between neighboring NG-RAN nodes and source NG-RAN node

3. Predicted energy state (e.g., active, high, low, inactive) between neighboring NG-RAN nodes and source NG-RAN node

4. Validity time of the predicted energy saving decisions

- Predicted energy saving decision from a NG-RAN node to neighbor NG-RAN node

New signalling procedure or enhanced existing procedure to retrieve feedback information

6. UE performance information between neighboring NG-RAN nodes and source NG-RAN node

7. System KPIs between neighboring NG-RAN nodes and source NG-RAN node

8. Accept/reject of offloading plan to transfer a certain number of UEs to a neighboring RAN node for energy saving reasons from neighboring NG-RAN node to a NG-RAN node.

Potential NG impacts:

9. Same information exchange as Xn above between NG-RAN nodes via core network.

Question 6: Companies are invited to provide your views on whether the standard impacts for AI/ML based Network Energy Saving above could be agreed to capture into the TR?

| Company | Which could be agreed?(1~9) | Comments |
| --- | --- | --- |
| Ericsson | Not needed | In our view, “standard impacts” should be a high level description of how the standard may be affected. We foresee that normative work should be based on the use case descriptions, so what is in those descriptions should be taken into account. We see that many of the proposals above just repeat the content of the use case description and for that they are not needed (and not that the proposals above also include use cases that we do support). Some further comments: we have not at all discussed signalling of AI/ML information over NG, hence this cannot be added to the TR. The topic of signalling frequent and high volume information via the CN needs a dedicated discussion. MDT enhancements will be taken during normative phase. For now, we have captured that these are potential changes If we ensure that the “Accept/reject of offloading plan” is added to the inputs/outputs, there is no need to add it to the standard impacts |
| Nokia | Not needed | Relevant standards impacts have been captured already in the TR. Possible NG impacts haven’t really been discussed during the study and in our view considering AI/ML over a scenario where Xn is not available would be very complex and should not be prioritized. |
| Samsung | 2 is already captured. Support 4,5,6,8 | For 1, how to get location information has not discussed. So it is better not to limit UU impact to MDT. For 2, it is already captured in the TR. For 3, it is still not clear about what is high/low energy state. More clarification is needed. For 4 and 5, OK. Exchanging predicted ES decision informs the neighbor nodes when it will switch-off/on in advance, which helps neighbor nodes to do SON decision (such as ES, LB, MO) to avoid local overload and HO ping-pong. Validity time is to show when the switch-off/on will take place. It is important for neighbor node to know this information. For 6, UE performance information exchange after ES action can help to set the suitable ES decision without UE performance downgrading. For 7, still have concern about system KPI, as it is effected by multiple factors incl. number of UE, channel condition, services, etc. It can not reflect the impact of ES directly. For 8, negotiation of offloading plan is beneficial for globe optimization as commented in previous questions. For 9, not very clear about NG impact for energy saving. More clarification is needed. |
| Intel | 2, 3, 4, 6, 7 |  |
| InterDigital | Probably not needed but in general support 6,7, 8 | In line with the Ericsson comments above and our comments in the other use case discussions. In general, most of these proposals are just adding the inputs/outputs/feedback to the standards impact when need to be sent over the Xn interface. It is clear if we agree on a parameter as input/output/feedback and it is not in a usable existing message and needs to get from one NG-RAN node to another it is a standard impact. |
| Qualcomm | 1: disagree 2,3: already in TR 4: No, wait for normative phase 5, 6, 7, 9: OK | In current standard, features are equally supported on Xn and NG based handover. So, for AI/ML, we can do the same. All the existing information exchange identified for Xn should be applicable to NG as well. I don’t see any technical difficulty. At least the information can be included in transparent container over NG. |
| CATT | Not needed for NG impact, others is OK | We have not discussed AMF impact during the study. |
| CMCC | 4,5,6,8 |  |
| Huawei | Not needed | Standard impacts have been captured in the TR, and it should be a high level description. Some further comments: For 4, see comments to 3.3.1; For 9, we are just not sure for the moment, since NG interface has not been discussed, and it could not just simple copy what has been agreed for Xn, maybe we could discuss this case by case during normative phase. For 5, it is not clear “predicted energy saving decision”, we think decision is decision, which is to be executed, not sure what prediction means here. |

## Conclusion

- [10] both propose to add the sub-section to include the conclusion to the AI/ML based Network Energy Saving use case. And [11] suggests to Consider AI based Energy saving use case as baseline for normative work.

Following are the proposed conclusion for the R18 normative work:

- The Network Energy Saving use case description and “solutions and standard impacts” should be taken as baseline for normative phase. [7]

- RAN3 has analyzed the descriptions and potential solutions, expected inputs, expected outputs, and expected feedback information of AI/ML based Network Energy Saving, and RAN3 is recommended to specify the potential solutions and potential standard impacts in the above clauses in the Rel.18 WI. [10]

Question 7: Companies are invited to provide the comments on whether to add the sub-section to include the conclusion to the AI/ML based Network Energy Saving for the R18 normative work?

| Company | If yes, Conclusion1 or Conclusion2 | Comments |
| --- | --- | --- |
| Ericsson | Need to be taken in CB: #1 | We of course support the content of both proposals 1 and 2, but there is a discussion ongoing in CB: # 1 on an overall conclusion for the study. We suggest to focus on that discussion and to add the content from 1. And 2. To the overall conclusion |
| Nokia | Both conclusions are ok but… | We agree with E/// that this topic should be discussed in CB: # AIRAN1_General. |
| Samsung | OK but prefer a general conclusion instead of individual ones for each use case | We prefer to have a conclusion for the whole TR instead of separate conclusions for each use case. It seems nothing special in conclusion for each separate use case. A general one makes TR clear and clean. |
| Intel | Prefer to be discussed in CB: # AIRAN1 |  |
| InterDigital | Prefer to do in CB #1 | We support the content of both proposal 1 and 2, but should be a general conclusion. |
| Qualcomm | Covered by CB#1 |  |
| CATT | Need to be taken in CB: #1 | Agree with Eric |
| NEC | Prefer to be discussed in CB: # AIRAN1 |  |
| CMCC | Prefer to do in CB #1 |  |
| Huawei | See comments | We think the rapporteur is also leading a discussion on how to conclude, we could reach conclusion there. |

## Others

[8] proposes to discuss and make a decision in RAN3 on the preferred way forward between the following 2 options with respect to slicing information in the AI/ML Rel.17 study/Rel.18 work:

1.Include in the scope of the study predictions of existing metrics that may be made on a per slice granularity and in this way introduce slicing aspects into the energy saving use case.

2.Exclude slicing aspects completely from the study and revisit those under a new use case covering slicing enhancements for a possible Rel.18 SI.

Question 8: Companies are invited to provide the comments on which options above is preferred?

| Company | Option1/Option2 | Comments |
| --- | --- | --- |
| Ericsson | Neither of them | Network slicing is implicitly supported in the 5G system in the sense that per slice information is already exchanged within the RAN, e.g. resource status information per slice. For that we do not see the need to focus on slicing explicitly. Besides that, we have not studied and we cannot think of any energy saving action that is made per slice. Hence we believe nothing specific needs to be done for the slicing use case, but slicing will be implicitly supported. |
| Nokia | 1 | Even though slicing is implicitly supported in current mechanisms, it hasn’t been explicitly discussed during the study. In our view, it needs to be taken into account when going forward with normative work in Rel.18 and we propose to capture it explicitly to avoid any confusion e.g., “Impact of Slicing for AI/ML Energy Saving to be considered in normative phase”. |
| Samsung | Case by case | It needs to be studied case by case. If the objective is for ES and it is just to consider slicing granularity, it is fine to study in R18 WI. If the objective is not relevant to ES, it is better to study in R18 SI (but it still depends on whether to agree slicing as a new use case). |
| Intel | None for now | Agree with Ericsson. It’s too early to discuss Rel-18 SI scope. |
| InterDigital | None for now | Agree with Ericsson, as per their example slicing aspects can be included intrinsically, too early to discuss other slice specific enhancements for R18 SI. |
| Qualcomm | No for now | This is last meeting. We didn’t study this topic before. Let’s discuss in normative phase. |
| CATT | No for now | As we do not have any conclusion on slice, we propose not to mention it at this time. |
| NEC | None for now |  |
| CMCC | None for now | It’s too early to discuss Rel-18 SI scope. |
| Huawei | Not sure | Since we have not discussed slicing related issues, but agreements reached so far should anyway be linked with slicing more or less, e.g. energy saving decision should apply to all slice, and why should we introduce per slice energy saving policy? We could discuss this during normative phase. |

# Conclusion, Recommendations [if needed]

If needed

# References

R3-221695	Closing open issues in AI/ML Energy Savings use case  (InterDigital Finland Oy)	other

R3-221780	Proposed updates to Energy Saving Solutions and Standard Impact (NEC)	other

R3-221848	Network energy saving (Qualcomm Incorporated)	pCR

R3-221942	AI/ML based network energy saving (Intel Corporation)	discussion

R3-221986	(TP to TR 37.817) On Network Energy Saving (Lenovo, Motorola Mobility)	other

R3-222018	(TP for TR 37.817)Discussion on Standards Impact on energy saving (CATT)	other

R3-222101	(TP for BL CR for TR 37.817) Network Energy Saving (Ericsson)	other

R3-222121	(TP for TR 37.817) A few final aspects on AI/ML Energy Saving (Nokia, Nokia Shanghai Bell)	other

R3-222228	Further discussions on energy saving (Huawei)	other

R3-222244	Further discussion on solution to AI based Network Energy Saving (ZTE Corporation)	other

R3-222274	On Remaining issues for AI based Energy Saving (CMCC)	other

R3-222309	Discussion on Standard Impact for AI/ML based Network Energy Saving (Samsung)	other

R3-222328	Further discussion for AI-based network energy saving (China Telecom Corporation Ltd.)	discussion