3GPP TSG-RAN WG3 #115-e	R3-222728

E-meeting, 21st February – 3rd March 2022

Source:	CATT

Title:	(TP for TS 38.300) Lossless handover for multicast service

Agenda Item:	22.3.1

Document for:	Discussion and decision

# Introduction

This document provides TP on session management

# TP

////////////////////////////////////////////////////////////////////////skip unrelated text////////////////////////////////////////////////////////////////////////

### 16.x.5	Multicast Handling

#### 16.x.5.1	Session Management

There are two delivery modes as specified in TS 23.247[X].

-	5GC Shared MBS traffic delivery

-	5GC Individual MBS traffic delivery

As specified in TS23.247[X],if the gNB node supports MBS,the network shall use the 5GC Shared MBS traffic delivery,in which case aMBS Session Resource context for a multicast session is setup in the gNB when the first UE joins the multicast session.

For MBS shared delivery mode, shared NG-U resources are used to provide MBS user data to the gNB. The gNB node initiates the Multicast Distribution Establishment procedure towards the 5GC, to allocate shared NG-U resources for a multicast session. In case multiple MBS session areas are associated with the MBS session for location dependent MBS services, multiple NG-U shared resources are established for the same multicast session per MBS Area Session ID served by the gNB.

A shared NG-U resource applies one of the following transport options:

-	unicast transport.

-	multicast transport.

For 5GC Shared MBS traffic delivery an MBS Session Resource comprises one or several MRBs. If minimisation of data loss is applied for a given MRB, synchronisation of allocation of PDCP SNs is applied by either or a combination of the following methods:

-	derivation of the PDCP SNs by means of a DL MBS QFI Sequence Number provided on NG-U

-	deployment of a Shared NG-U Termination at NG-RAN, shared among gNBs, which comprises a common entity for assignment of PDCP SNs.

Synchronisation in terms of MBS QoS flow to MRB mapping among gNBs is achieved by means of network implementation.

If PDCP SNs are derived from a DL MBS QFI Sequence Number provided on NG-U and

-	only one QoS Flow is mapped to an MRB, the gNB shall set the PDCP SN of PDCP PDU to the value of the DL MBS QFI Sequence Number provided with the received packet over NG-U.

-	multiple QoS Flows are mapped to an MRB,  the gNB may derive the PDCP SN of the PDCP PDU from the sum of the DL MBS QFI Sequence Numbers of the QoS Flows mapped to this MRB.

NOTE:	Synchronisation of PDCP SNs in case user data for MBS QoS flows mapped to the same MRB arrive over NG-U at different gNBs in different order or in case of loss of data over NG-U, and related handling of minimisation of data loss is left to implementation.

////////////////////////////////////////////////////////////////////////end////////////////////////////////////////////////////////////////////////