3GPP TSG-RAN WG3 #115	R3-222445

21 February - 03 March 2022

Online

Agenda Item:	17.2

Source:	Nokia, Nokia Shanghai Bell - Moderator

Title:	Summary of Offline Discussion – Slicing Service Continuity

Document for:	Approval

# Introduction

This is the summary document for the following come back:

CB: # RANSlicing2_Service_Continuity

- Complete Leftover issues for service continuity in case of slice overload at target gNB

- Turn WA of ‘Slice pre-emption’ into agreement?

- Solution for time critical handover?

- Leftover issues to support slice based cell reselection and RACH?

- Capture agreements and provide TPs if agreeable

(Nok - moderator)

Summary of offline disc R3-222445

# For the Chairman’s Notes

Propose the following:

Agree TP … .

# First Round

In this summary let us take the following abbreviations:

MCRS: Multi-Carrier Resource Sharing

CBRP: Configuration Based Resource repartitioning

Editor’s notes

There is an ongoing open point under checking by SA2 on whether the gNB should know the RA of the UE to possibly avoid (based on operator policy) adding SCG resources for a PDU session of an allowed slice outside the RA. There is a corresponding editor’s note in TS 38.300:

Editor’s Note: whether the “new cell” can be outside the RA of the UE is FFS.

Tdoc R3-221964 says that only the MRL (Mobility Restriction List) needs to be checked and if the SCG resources are OK for the MRL then they can be added (provided that the slice is supported in the SCG cell of course) regardless of whether the SCG is inside or outside the RA.

Q1: Do you think that MRL also accounts for slice restrictions?

| Company | Comment |
| --- | --- |
| Nokia | No. Of course, MRL must be taken into account when adding SCG. However, MRL doesn’t account for slicing aspects. Therefore, once MRL check is passed, there is still the question of the validity of the Allowed NSSAI which is assumed to be valid only “within the RA”. Therefore, adding SCG outside the RA for a slice of the Allowed NSSAI is still questionable even when MRL is ok and even when the SCG cell supports the slice. In short, MRL doesn’t account for slicing aspects in our view. |
| Ericsson | Yes. We share the same opinion as R3-221964 in our paper R3-221966. It needs to be noted that the Allowed NSSAI is calculated on the basis of the cell where the primary UE connection is established, namely the PCell or to be totally clear, the cell terminating NAS signalling. The allowed MNSSAI therefore does not apply to the SCG. Note that we have a very similar case of SCG addition management in non slicing cases. Namely, a service may be accessible by a UE in PLMN A but not in PLMN B. Still, if an SCG in PLMN B is not forbidden by the MRL, the SCG can be added and the service can be consumed by the UE even via SCG resources. Also note that TS38.413 states the following: 9.3.1.85 Mobility Restriction List This IE defines roaming or access restrictions for subsequent mobility action for which the NG-RAN provides information about the target of the mobility action towards the UE, e.g., handover, or for SCG selection during dual connectivity operation or for assigning proper RNAs. NG-RAN behaviour upon receiving this IE is specified in TS 23.501 [9]. In 5G, slicing is a feature added since the very beginning, so the above text from TS38.413 takes also slicing into account (as slicing was already supported at the time the text was agreed). |
| Samsung | Technically, we agree with R3-221964 that the SCG selection is based on MRL. But we don’t think we should confuse the SCG selection principle with the slice restriction to make things complicated. Here we’re talking about the solution to solve the resource shortage issue, SCG can be used to solve the issue, and whether the cell can be selected is based on current mechanism and specification, regardless of the cell is outside of RA or not. So we prefer to keep current description as below and remove the editor note. “In Multi-Carrier Resource Sharing the RAN node can setup the dual connectivity or carrier aggregation with different frequency and overlapping coverage where the same slice is available” |
| Deutsche Telekom | From our perspective, in case of resource shortage a SCG could be added under the assumption that there is no restriction in MRL and the SCG is also supporting the related slice(s). This should be feasible even if the SCG is out of UE’s RA as the PCell of the MN is the relevant CP anchor. Therefore, we are fine with removal of the editor’s note. |
| CATT | I don’t think we need mix the SCG selection and slice selection |
| Huawei | Agree with DT and Ericsson. As discussed in R3-221964 (same view as R3-222093), as long as the MRL allows, and slice in the Allowed NSSAI is supported by the SCG, then the SCG can be setup to ensure the slice continuity. In other words, the NG-RAN can use the MRL to select the proper SCG accordingly, no matter the new cell is within the RA or outside of the RA to ensure the slice continuity. |

There is a second editor’s note in 38.300 dealing with the

Measurements of RRM policy utilization according to resource types defined in TS 28.451 are reported from RAN nodes to O&M and may lead O&M to update the Slice RRM policies/restrictions configuration (FFS).

Editor’s Note: the above FFS sentence is pending confirmation from SA5.

Tdoc R3-221964 states that the editor’s note can be removed without waiting the answer from SA5 because the following table in TS 28.541 already shows that O&M should be able to update the RRM policies/restrictions configuration.

| Attribute name | S | isReadable | isWritable | isInvariant | isNotifyable |
| --- | --- | --- | --- | --- | --- |
| rRMPolicyMaxRatio | M | T | T | F | T |
| rRMPolicyMinRatio | M | T | T | F | T |
| rRMPolicyDedicatedRatio | O | T | T | F | T |

We have the following possible options:

- option 1: wait SA5 reply.

- option 2: remove editor’s note and let the text in BL CR TS 38.300 as it is.

- option 3: remove the editor’s note but changing the text into: may lead O&M to update the Slice RRM policies/restrictions configuration at least statically  (see tdoc R3-222283).

Q2: which one is your preferred option?

| Company | Comment |
| --- | --- |
| Nokia | Option 1 In RAN3 LS sent to SA5 in R3-216238, RAN3 did not only ask whether the solution was feasible but also “with which frequency can the modification to slice resource re-partitioning be performed” therefore it would be better to wait for SA5 answer. O&M to update “statically” sounds really strange so we prefer SA5 reply. |
| Ericsson | Option 2. RAN3 needs to close the WI on slicing at this meeting. The SA5 specifications already state that RRM policies can be updated by the OAM. It is obvious that the maximum frequency of such updates is implementation dependent, hence we do not see it is critical to wait for SA5´s reply. Obviously, if SA5 replied negatively to our assumption we could correct the text. We agree that O&M to update “statically” seems a little contradictory. |
| Samsung | We prefer option 1 or 3, the intension of option 3 is to not include the “dynamic update” case which hasn’t been confirmed by SA5. Any rewording of option 3 to reflect the intension is also OK for us. Regarding the dynamic update RRM policy, we still have doubt on it, as the traffics in the gNB change quite frequently, we don’t think the OAM deployed as a central node can make a proper adjustment to satisfy the real-time traffic requirements in the local gNB. |
| Deutsche Telekom | To go with Option 2 is ok for us, as the feasibility for RRM policy updates by OAM is a fact. Nevertheless, dependent on outstanding feedback from SA5 there might be the need in a later step for an addition to clarify the dynamics of possible changes. From our operator’s view, we don’t expect frequent changes as the RRM policy is strongly related to SLAs with customers where a proper RAN configuration is expected from the beginning of introducing a slice to fulfil those SLAs. Option 3 is not a suitable alternative for us as it is unclear what is meant by ”statically”. |
| CATT | Option 2. In SA5 spec, the updating of RRM policy is already supported. In RAN3 spec, we don’t need specify how the updating performs because it is out of RAN3 scope. |
| Huawei | Option 2, considering this is the last meeting to freeze the functions. And about the update frequency “at least statically”, our view is that there is no need to specify it in RAN spec since this is implementation dependent, and beyond RAN3 scope. |

Moderator’s summary:

Majority of companies think …

Proposal 2: TP...

Pre-emption

RAN3#114bis achieved the following Working Assumptions:

WA: Pre-emption in the shared pool can rely on existing QoS flow ARP based mechanism. Nothing additional is needed.

WA: For prioritized pool, RAN assumes that SA5 statement on prioritized resource of the Slice member list prevails over QoS ARP of non Slice member list. Nothing additional is needed.

Tdocs R3-222283 and R3-221813 propose to turn these into agreements and a TP is proposed as follows:

Pre-emption in the shared pool can rely on existing QoS flow ARP. In the prioritized pool, prioritized resource of the slice member list prevails over the QoS ARP of non-slice member list.

Q3: can we turn these working assumptions into agreements and agree the TP above for the BL CR 38.300? please update text if needed.

| Company | Comment |
| --- | --- |
| Nokia | OK for us. |
| Ericsson | We think we can turn those WA into agreements. We do not see the need to add statements in 38.300 as these principles are already explained clearly in the SA5 specifications. Adding double descriptions implies that multiple specs need to be maintained and that there is ambiguity on which spec takes precedence. |
| Samsung | OK to turn WA into agreements, no strong view on whether to capture them in the spec. |
| Deutsche Telekom | Turning the WAs into agreements is fine for us. If the majority of companies think it is useful to capture them via the proposed TP we are not against it, but based on availability of SA5 specs there is no strong need for it. |
| CATT | Agree to turn the WA to agreement. We also don’t think we need capture it in RAN3 spec. if companies would like to capture something, we may just state like as “the Pre-emption mechanism of slice resource specified in 28.541….” |
| Huawei | Yes to turning the above into agreements. But we also don’t see the need to capture them into RAN spec since RAN made these two proposals just based on the SA5 spec. Nothing new is introduced. |

“Resource Change” Reporting from Target

Tdoc R3-222283 proposes that the target gNB informs the source gNB after performing resource repartitioning due to the slice resource shortage at least for one service type defined in RRM policy. The source gNB can then make a proper decision for the upcoming handover UEs to avoid service interruption, as in some cases, if pre-emption happens, there will always be service interruption for some UEs.

(e.g. the source gNB may not select the gNB with slice resource change indication as a candidate for the UE), or the source gNB can consider this change to make better handover decision for the following handover decision (e.g. the source gNB may not select the gNB with slice resource change indication as a target for the following handover UEs).

An alternative would be to rely on Xn resource status exchange but if the slice resource shortage is due to lack of RRC Connected users and/or DRB, there’s no corresponding slice related resource status exchange over Xn.

Q4: what is your view on reporting slice resource change indication by target gNB in the handover request acknowledge?

| Company | Comment |
| --- | --- |
| Nokia | We are not convinced that this indication can help avoiding pre-emption. If resources of another slice happens to be used, this is most probably in the shared pool and therefore should be OK with a very low risk of being pre-empted. Also O&M reporting and long term adjustment is assumed to kick in to adjust the quota which would be better on longer term than starting to influence/biaise the handover decision criteria. |
| Ericsson | We are not convinced such changes are needed. It is already possible for RAN nodes to exchange the Slice Available Capacity IE, which gives at least an indication of maximum amount of resources available per slice. Note that the Slice Available Capacity IE may also take the maximum number of UEs and DRBs per slice into account. We believe that the main reason of pre-emption or HO failure is for lack of resources, hence the existing Slice Available Capacity IE is sufficient. |
| Samsung | We support to have this indication to avoid bad handover decisions like let the UE hands over to a cell with slice resource (i.e. UE/DRB) limitation. Regarding the Slice Available Capacity IE, it only can reflect the per slice PRB resources, it cannot reflect the per-slice UEs and DRBs resources, so this indication can make the handover decision or load balance decision more comprehensive and efficient. |
| Deutsche Telekom | We are not convinced about the benefits of such indication with respect to resource shortage. If we are missing any slice-related information exchange between nodes for HO or other purposes, we should address that in the SON/MDT WI. |
| CATT | We are not convinced. Share with above. |
| Huawei | We also not convinced, and consider this is more like optimization. Agree with the above “not convinced” camp. |

Moderator’s summary:

Majority of companies think …

Proposal 2: TP...

Resource Shortage in mobility scenarios: time to add DC

For using the MCRS at target, Tdoc R3-221813 proposes that source gNB indicates to the target gNB whether it estimates that the target gNB has time to add the secondary “other cell” during the handover preparation (“MCRS possible by target”) if that would be necessary to serve the slice (i.e. slice is in shortage at target gNB but target gNB could add another cell using DC to serve it). The source gNB estimates whether target could do DC addition during the handover preparation based on the quality of radio link at source cell. Therefore, this proposal is not related to the PDB or whether the application is delay critical.

Q5: what is your view on this proposal?

| Company | Comment |
| --- | --- |
| Nokia | Could be OK. Alternatively, the target could fail the PDU session as of today and indicate back that the PDU session could have been served using DC. Then source could send a second Handover Request using CHO update. But this alternative would make two steps. So we prefer this proposal that source indicates proactively if there is time for target to setup DC (“MCRS possible by target”) during the handover preparation. |
| Ericsson | We do not see the benefits of this proposal. The time needed to add an SCG is highly depending on the radio conditions at the SN and it is rather unlikely that source RAN can estimate such conditions well enough. Also, nothing prevents an implementation to serve a UE in MN first for a short time window, until the SCG is added. In this case a decision not to handover the UE to the target RAN only because of presumed delays in SCG addition would not be reasonable. |
| Samsung | We have doubt on this proposal, as it seems that the source gNB estimates whether the handover is time critical based on the radio conditions, but the radio conditions will be sent to the target gNB via Handover Request message in forms of measurement report, why additional estimation is needed in the source gNB? |
| Deutsche Telkom | We don’t the benefits as it is up to the target node to find the best conditions for supporting the UE’s demand. The information provided by source node should be sufficient. |
| CATT | We don’t see the benefits. The target node has all the information include application type, radio quality of the qualified cell. The target node may decide whether add the DC for slice based on these information |
| Huawei | We think this is a handover related optimization. And we don’t fully understand why addition information is needed from the source since the current QoS parameters, and slice configurations can be used to determine how to ensure the handover performance. This can be left to Handover enhancement WI or other topics for further discussion. |

Moderator’s summary:

Majority of companies think …

Proposal 2: TP...

Slice Grouping

Abbreviations: SGM: Slice Group Mapping i.e. mapping of Slice to Slice Group.

Tdoc R3-221966 proposes that the SGM should be configured within the remit of RAN and that the gNB sends it to the AMF in the NG setup request/RAN Configuration Update messages.

Alternatively, tdoc R3-222193 says that CN can learn by O&M the SGM because it is static.

Q6: what is your view on these two proposals?

| Company | Comment |
| --- | --- |
| Nokia | We support the proposal in R3-221966 to send the SGM in NG Setup Request because the list of slices is already sent per TA. If we would follow the reasoning of R3-222193 then also the list of Slices per TA would not be present today in the NG setup Request message! |
| Ericsson | We cannot decide on this topic as recent discussions in SA2 concluded by noting all proposals on slice grouping, hence it is not clear if there will be any progress on the topic. The proposal we can make to try to simplify the issue and by that converge to an agreement, is to have a slice group granularity per PLMN. That means that NG-RAN nodes in different Tas can still support different RAN groups, but the Slice Group ID would be unique within the PLMN. Even this proposal, however, needs to wait until decisions are taken in SA2 and RAN2. |
| Samsung | The slice group granularity is per TA, which had already been agreed in RAN2. Regarding the SGM, we think it should be decided by SA2 first, as one possible solution is the SGM is determined by CN, and it will be sent to UE via NAS, and sent to NG-RAN node via NGAP. So we cannot tell the RAN3 impact if there’s no conclusion in SA2. |
| Deutsche Telekom | In principle we are fine with the proposal in R3-221966, but as there is still no conclusion in SA2 which may also impact RAN2’s view we should wait for final decisions in both WGs. |
| CATT | We should wait for SA2 output for this topic. Even RAN2 agree support SGM per TA, the SA2 may object it and change it to per PLMN. If SGM is per PLMN, RAN does not need send anything CN |
| Huawei | About the slice group granularity (PLMN level or TA level), RAN3 can be pending on other groups, since RAN2 just makes a working assumption, and SA2 will not provide the reply LS this meeting. But no matter the answer is, we think there is need to send SGM in the NG setup request message, following the same logic when the NG-RAN reports its slices to the CN. |

Tdoc R3-221966 proposes also that SGM is exchanged across NG-RAN nodes in the Xn Setup/NG-RN configuration update procedures.

This is because RAN2 agreed that “RAN2 assumes that for purpose of UE checking supported slices on the highest ranked cell at TA/RA boundary, gNB can provide in SIB the slice group that supported by these neighbour cells. If this conflicts with SA2, RAN2 will align with SA2”.

Q7: what is your view on the proposal to exchange the SGM across NG-RAN nodes in Xn setup/gNB configuration update?

| Company | Comment |
| --- | --- |
| Nokia | This seems OK. Peharps could be added with editor’s note to be confirmed by SA2, or alternatively we specify this at next RAN3 if WI is extended. |
| Ericsson | As mentioned above, these discussions need to b eput on hold until SA2 and RAN2 take firm agreements. |
| Samsung | If it’s CN that determines the SGM, we don’t see the need to exchange SGM over Xn. This discussion depends on SA2’s conclusion. |
| Deutsche Telekom | We prefer to wait for SA2’s decisions and possible consequences from RAN2. |
| CATT | We should wait for SA2 output for the SGM granularity and the RAN2 solution for supporting of the neighbor TA slice mapping |
| Huawei | As the proponent company, we are fine to wait for RAN2 further progress to tackle with the issue “gNB can provide in SIB the slice group that supported by these neighbour cells”. |

Tdoc R3-222193 and R3-222262 address the issue of how can a UE located in a TA translates the slice group information received in SIB message into slice correctly, if the neighbouring TA and the serving TA/RA have different mapping relationship between Slice Group and Slice?

Tdoc R3-222193 proposes a deployment solution so that the Slice group ID configured by one TA would not be reused by other surrounding TAs. Tdoc R3-222262 proposes instead that UE uses the mapping relationship in the served TA/RA (and not the mapping relationship of the neighboring TA) to broadcast the slice group(s) supported by the neighboring TA

Q8: what is your view on these two proposals?

| Company | Comment |
| --- | --- |
| Nokia | First, we think that the RAN2 assumption that SGM is homogeneous in the RA is not suitable because AMF should not build RA based on SGM concept. Then, assuming that SA2 decides that SMG is sent over NAS per TA, the UE could translate easily using the neighbor TA received information. If this is confirmed, we don’t need the two above proposals. |
| Ericsson | Again, these are very fine details on which RAN3 cannot deliberate until firm agreements are taken in other WGs. However, it is clear that the topic is rather complex and it could be greatly simplified if the Slice Group ID was unique within the PLMN. In that case there would not be the need to broadcast any neighbour TA slice group info |
| Samsung | Similar view as Nokia. If it’s CN that determines the SGM and send to UE via NAS, the UE can perform the translation of neighboring TA, thus there will no impact on RAN3. So this discussion also depends on SA2’s conclusion. |
| Deutsche Telekom | We prefer to wait for SA2’s decision(s). |
| CATT | We need wait for SA2 and RAN2 output |
| Huawei | These issues can be pending on the other group progress. |

Moderator’s summary:

Majority of companies think …

Proposal 2: TP...

# Second Round

Moderator’s summary:

Majority of companies think …

Proposal 2: TP...

# Conclusion

The following is proposed:

Proposal 1: TP...

# References

- RP-193254, “Study on Enhancement of RAN Slicing”

- TR 38.832, Technical Specification Group RAN; NR; Study on Enhancement of RAN Slicing, v17.0.0,