3GPP TSG-RAN WG3 #115-e	R3-222408

Online, 21 February-3 March 2022

Agenda Item:	11.2

Source:	NEC (moderator)

Title:	Summary of Offline Discussion on Support for RedCap Capability Exchange

Document for:	Approval

# Introduction

CB: # RedCap2_UECapability

- Add cause value “RedCap UE is temporarily barred” is introduced in XnAP as well as in NGAP?

- Update the Redcap cell support via NGAP Target to Source NGAP Container when no Xn is available?

- Update for TS38.401?

- Capture agreements and provide stage2/3 TPs if agreeable

(NEC - moderator)

Summary of offline disc

The 1st round of discussion is set to deadline on 24th Feb (Thursday) 11:59 UTC.

The 2nd round of discussion (if needed) is set to deadline on e.g. 28th Fed  (Monday) 11:59 UTC.

# For the Chairman’s Notes

Propose the following:

R3-20xxxa, R3-20xxxc merged

R3-20xxxc rev [in xxxg] – agreed

R3-20xxxd rev [in xxxh] – agreed

R3-20xxxe rev [in xxxi] – agreed

R3-20xxxf rev [in xxxj] – endorsed

Propose to capture the following:

Agreement text…

Agreement text…

WA: carefully crafted text…

Issue 1: no consensus

Issue 2: issue is acknowledged; need to further check the impact on xxx. May be possible to address with a pure st2 change. To be continued…

# Discussion (1st round)

RAN3#114bis meeting has reached the following status;

For coordination of RedCap access/mobility restrictions:

- OAM is not precluded (may be sufficient in some deployments)

- Support the exchange of RedCap access configuration via Xn Setup/Configuration Update (solution 2)

Support sending RedCap access configuration over F1AP

For mobility between nodes without Xn, assume OAM, but allow to revisit next meeting also taking into account RACS discussion if applicable)

Not discussed and to be continued: cause values.

This RAN3#115e meeting we see some contributions that discuss and propose the related mobility with Xn and without Xn interface, with mainly regards to the target gNB that is temporarily barring / return to not barring the RedCap UEs.

This offline discussion then categorize the discussion into three parts:

- Mobility without Xn interface

- Mobility with Xn interface

- other (TP to 38.401)

## Mobility without Xn interface i.e. NG Handover

One paper [3] discuss  and propose to exchange the support of RedCap cell within the Target to Source container and the Target to Source  Failure Container when no Xn is available i.e. NG handover. The reason for such solution, is explained that to consider a scenario that neighbour cell change the barring status would be more frequent, OAM solution might not good enough.

Q1: Please state if you consider solution  proposed by [3] is feasible and agreeable i.e. include support of RedCap cell  within the Target To Source Transparent Container and the Target to Source Failure Transparent Container. Please also give comment why you think such.

| Company | Comment |
| --- | --- |
| NEC | The propose way in [3] is a way to do. No strong view. |
| Ericsson | First, we wonder why should we consider the scenario of NG-based handover at all, where neither source RAN nor target RAN in a neighbouring “network portion” hasn’t been upgraded at all to support the RedCap feature? A minimum support of features is necessary to be able to rely on a certain automatism in the network. If that is not given, OAM is still an option as agreed in last e-meeting. Please note that 3GPP did not consider it necessary to enhance S1AP for the S1-based handover of BL CE UEs in LTE. Then on the solution in [3], we disagree. This was already extensively discussed in previous e-meeting (see CB R3-221142 sections 3.4 and 4.1) and the solution was considered flawed by all companies (and it seems that even the proponents themselves highlight its flaws in [3]). |

[5] propose for the mobility without Xn, a potential way forward  to introduce a new IE with criticality set to “Reject” in the Source to Target Transparent Container to the inform the target gNB about the handover of RedCap UEs. As stated in the paper [5] this propose way forward is related with the TEI17 RACS support discussion (agenda 31.2.4 Support exchange of protocol support at target RAN node for NG handover ) .

Q2: Please state if you consider the proposed way forward to introduce a new IE with criticality “reject” in the Source to Target Transparent Container to inform the target gNB about the handover of RedCap UEs.

or if you would consider this proposed way forward to be discussed later when after the discussion in agenda 31.2.4 is concluded?

| Company | Comment |
| --- | --- |
| NEC | It would be good to follow the result of the RACS discussion in agenda 31.2.4, therefore this proposed way forward from Huawei can be pending. |
| Ericsson | As agreed previously, OAM is a solution. Then, if Criticality Diagnostics information is going to be added in the Target NG-RAN Node to Source NG-RAN Node Transparent Container – pending on RACS discussion –, there is no need for a separate RedCap IE, as RedCap UE can be identified from UE Radio Capability in the RRC container. |

[1] [2] and [6] propose to include a cause value in NGAP for the handover failure related with the Redcap UE mobility. The reason that the source NG-RAN node when trigger the Xn handover may not be aware of the dynamic change of the no-barring to barring in the target cell.

For the cause value, [1] propose “RedCap UE is temporarily barred”, [4] propose  “RedCap broadcast information changed”, [6] propose “RedCap UE Not Supported”.

Q3: Please state if you consider to include cause value in NGAP for the handover failure related with Redcap UE mobility is agreeable.

If it is agreeable, which/what cause value is agreeable. (“RedCap UE is temporarily barred”[1], “RedCap broadcast information changed”[4], “RedCap UE Not Supported”[6] or other)?

| Company | Comment |
| --- | --- |
| NEC | Yes it is agreeable, we propose to introduce new cause value “RedCap UE is temporarily barred” |
| Ericsson | We understand the motivation for when the RedCap barring status is changing very fast, and the cause value can cover this corner-case scenario. However, we prefer to wait, since there is an on-going discussion in RAN2 where a RedCap UE may always need to check SIB1 of the target during the HO procedure to understand if the cell doesn’t support RedCap and thus not HO to such cell (for e.g. if it is legacy gNB). |

## Mobility with Xn interface i.e. Xn Handover

With the already agreed signaling solution  in Xn “Support the exchange of RedCap access configuration via Xn Setup/Configuration Update”, two paper [1] [4] propose to introduce a cause value (“RedCap UE is temporarily barred”[1], “RedCap broadcast information changed” [4]) in XnAP handover failure.

The reason for introduce such cause value for handover failure is explained that the source NG-RAN node when trigger the Xn handover may not be aware of the dynamic change of the no-barring to barring in the target cell.

However  one paper [6] see no need for introduce any cause value for such case.

Q4: Please provide your view whether need to introduce cause value to show for the Xn handover failure related with the RedCap UE.

If it is agreeable, which/what cause value is agreeable. (“RedCap UE is temporarily barred”[1], or “RedCap broadcast information changed” [4] o other)?).

| Company | Comment |
| --- | --- |
| NEC | It would be good to follow the result of the RACS discussion in agenda 31.2.4, therefore this proposed way forward from Huawei can be pending. |
| Ericsson | Prefer not to add anything. There are some dependencies with RAN2 discussion on target RAN and UE’s behaviors during HO. |

## Other (Text Propose to TS38.401)

[5] found it needs to introduce text in 38.401 with related to the RedCap in F1 and propose a TP into baseline CR 38.401.

Q5: Please state if you agree with the TP proposed by [5] into the baseline CR 38.401 for the F1 related.

| Company | Comment |
| --- | --- |
| NEC | OK, no comment. |
| Ericsson | OK for the addition in section 8.7. Not OK for the addition in section 8.5. (Not sure why we even have that sentence for the NPN cell information in step 1) TS 38.470 is the place where this text should be captured, if not already captured before… Otherwise, if we have to capture all the cell info that gNB-DU provides in the Served Cell Information NR IE during the F1 SETUP, then we will produce quite the cumbersome text and it creates a bad habit for TS 38.401 maintenance. |

## Other (if any)

If any more proposal in any submitted contribution that was overlooked by the moderator, please add here and please add reference of the contribution.

Also, please add any issues or aspects missing from the above.

| Company | Comment |
| --- | --- |

# Discussion (2nd round, if needed)

# Conclusion, Recommendations [if needed]

If needed

# References

[1] R3-221772, (TP for XnAP BL CR on RedCap)  RedCap Mobility Handling and Cause Value (NEC)

[2] R3-221773, (TP for NGAP BL CR on RedCap)  RedCap Mobility Handling and Cause Value (NEC)

[3] R3-221809, (TP for TS 38.413) Coordination of Redcap Capability across gNBs with no Xn (Nokia, Nokia Shanghai Bell)

[4] R3-221914, (TP for TS38.423 and TS38.413) Support of RedCap UE mobility (CATT)

[5] R3-221918, RedCap leftover issues (Huawei)

[6] R3-221932, 	(TP for TS 38.413 on RedCap UE Support) Cause values for Xn and NG mobility failure for RedCap Ues (Radisys, Reliance JIO)