3GPP TSG-RAN WG3 Meeting #116-e 	R3-223751

# E-Meeting, May 9-19, 2022

Agenda item:	8.1

Source:	Nokia (moderator)

Title:	CB: # 55_PriorityCall - Summary of Offline Discussion

Document for:	Decision

# 1	Introduction

CB: # 55_PriorityCall

- Clarify the issue

- Take R3-223676 into account

(Nok - moderator)

Summary of offline disc R3-223751

##

It is proposed to have the deadline for discussions as follows

- 17/May (Tue) 11:59:58 UTC

# 2	For the Chair’s Notes

To be updated after discussion

# 3	Discussion

PROBLEM DISCUSSION

Contribution in R3-223600 highlights an issue in regard to treatment of a mobile terminated access request triggered dur to a priority paging procedure and, discusses alternatives to ensure the response to the paging event is also treated with an appropriate priority in line with that used in the paging event.

The scenario under discussion consists on two parts

- (a) Priority Paging Event

- (b) Mobile Terminated Access Event

(A) Priority Paging Event

The specifications allow for operator to configure different priority levels for treatment of calls (PrioLevel1, PrioLevel2, PrioLevel3, PrioLevel4, PrioLevel5, PrioLevel6, PrioLevel7, PrioLevel8), where the lower the value, the higher the prioritization that is expected to be applicable for the call.

In case of a network initiated paging event, the configured priority is signaled both via AMF to gNB-CU over NG interface, and subsequently to gNB-DU via the F1 interface. The gNB-DU then takes into account this information and prioritizes the paging for the call over other ones.

(B) Mobile Terminated Access Event

When the UE responds to the paging event, it will attempt a RRC Connection Setup Request and indicate an Establishment Cause (EC). The existing ECs defined in RRC specification TS 38.331 are shown in the excerpt below.

RRCSetupRequest message

-- ASN1START

-- TAG-RRCSETUPREQUEST-START

RRCSetupRequest ::=                 SEQUENCE {

rrcSetupRequest                     RRCSetupRequest-IEs

}

RRCSetupRequest-IEs ::=             SEQUENCE {

ue-Identity                         InitialUE-Identity,

establishmentCause                  EstablishmentCause,

spare                               BIT STRING (SIZE (1))

}

InitialUE-Identity ::=              CHOICE {

ng-5G-S-TMSI-Part1                  BIT STRING (SIZE (39)),

randomValue                         BIT STRING (SIZE (39))

}

EstablishmentCause ::=              ENUMERATED {

emergency, highPriorityAccess, mt-Access, mo-Signalling,

mo-Data, mo-VoiceCall, mo-VideoCall, mo-SMS, mps-PriorityAccess, mcs-PriorityAccess,

spare6, spare5, spare4, spare3, spare2, spare1}

-- TAG-RRCSETUPREQUEST-STOP

-- ASN1STOP

From the encoding we can see that the ECs when responding to the paging would be:

- “emergency”

- “highPriorityAccess”

- “mps-PriorityAccess”

- “mcs-PriorityAccess”

- “mt-access”

That is, the priority set by the operator and accounted for the paging event is not represented in the treatment of the responding call, as these would all be treated equally as “mt-access”, even though the operator has configured certain calls to be prioritized over others.

One way to identify that the call is due to a prioritized paging, is via comparison of the 5G-S-TMSI value received from the UE request. This is possible at the gNB-DU and gNB-CU based on implementation and can be taken into account when carrying out admission control. Further, if the gNB-DU has already identify that the call is due to priority paging, it could convey this information via F1 to gNB-CU and avoid doing the same processing again at gNB-CU.

Online Discussion

During the online discussion some of the following points were raised

- One view is that if a UE is paged with priority, the UE could change the EC to mps/mcsPriorityAccess EC rather than “mt-access”.

- Another view was that identification of whether the call is in response of a priority call could be limited to gNB-CU with gNB-DU intervention and avoid check of the Establishment Cause or 5G-S-TMSI at the gNB-DU.

- Another view was that prioritization of only the paging event could be sufficient and that no further prioritization between answering of the priority call is needed.

- Another view is that the proposed changes are beneficial as there may be a very large number of calls originating with the same EC (i.e. “mt-access”), and hence the gNB would not be able to determine which are to be treated with priority. In situations of e.g., disaster events, this situation can also worsen.

- Another view was that for MPS priority access services, a similar functionality in which the gNB-DU determines whether the incoming call needs special treatment and takes the Establishment Cause into consideration for admission control and expedited processing is proposed in R3-223676.

QUESTIONS FOR DISCUSSION

Q1: Is there is a need to further separately prioritize the signalling and treatment of incoming calls with EC=”mt-access” responding to a priority paging event?

| Company | Comment |
| --- | --- |

Q2: Provide your view in regard to signaling over F1AP from gNB-DU to gNB-CU whether an incoming UE request is due to a response to a priority paging event?

| Company | Comment |
| --- | --- |

Q3: Provide your view regarding whether the gNB-DU should rely on the establishment cause within the RRC Setup Request message to carry out prioritization of processing of the message over other requests.

| Company | Comment |
| --- | --- |

Q4: Provide your view in regard to signaling over F1AP from gNB-DU to gNB-CU whether an incoming UE request is due to a MPS Priority Access request?

| Company | Comment |
| --- | --- |

Q5: Any other comments/remarks.

| Company | Comment |
| --- | --- |

# 4	Conclusions

To be updated after discussion

# 5	References

| R3-223600 | Discussion on Priority Call-back (Nokia, Nokia Shanghai Bell) | Discussion |
| --- | --- | --- |
| R3-223609 | Priority Call-back Indication (Nokia, Nokia Shanghai Bell) | CR0955r, TS 38.473 v17.0.0, Rel-17, Cat. F |
| R3-223676 | Clarification of DU Early Identification capability for MPS (Peraton Labs, CISA ECD, AT&T) | Discussion Late contribution Move to 9.3.9 noted |