3GPP TSG-RAN WG3 #116-e			R3-22xxxx

Electronic Meeting, 9 May – 19 May, 2022

Title:	[DRAFT] Reply LS on the user consent for trace reporting

Response to:	(S3-211338 - R3-211464) Reply LS on the user consent for trace reporting

Release:	Rel-16

Source:	Apple [to become RAN3]

To:	SA3, RAN2, SA5

Cc:

Contact Person:

#### Name:	Sasha Sirotkin

E-mail Address:	ssirotkin@apple.com

Send any reply LS to:	3GPP Liaisons Coordinator, 3GPPLiaison@etsi.org

1. Overall Description:

RAN3 thanks SA3 for their LS on user consent, in which SA3 clarified that there should be a possibility for an operator to collect and handle user consent for location information in RLF/CEF cases. From RAN3's perspective these cases correspond to scenarios where the NG-RAN reports accessibility measurements to the OAM (Trace Collection Entity - TCE).

RAN3 have discussed the issue, and would like to clarify that location information reporting from the NG-RAN to OAM (TCE) is enabled as part of the MDT functionality with stage 2 specification under responsibility of SA5 and RAN2. The NG-RAN is informed about PLMNs allowed for MDT (i.e. information resulting from the operators' collection and handling of user consent) via NGAP signalling introduced in Rel-16. RAN3 believes that this mechanism also applies for accessibility measurements (RLF/CEF) reported to the TCE, including location information contained therein.

2. Actions:

To SA3, RAN2, and CT3 groups.

ACTION: 	RAN3 asks SA3, RAN2, and SA5 to take the above into account.

3. Date of Next TSG-RAN3 Meetings:

TSG-RAN3 Meeting #117-e	15-25 August 2022				Online

# Comments

"location information in RLF/CEF" is unclear, and could e.g. refer to reporting over the Uu interface which is not in RAN3's realm. SA3 used the term "RLF/CEF cases", hence referring to the scenario and not to specific interface.

Is the last part of the sentence intended to address the Uu interface (RRC)? The Uu interface is not under RAN3's responsibility.

From our side we challenge the need to support new user consent signaling for location information contained in accessibility measurements (RLF/CEF) reported to the TCE (i.e. MDT or "trace reporting" to align with SA3's term).