3GPP TSG-RAN WG3 #108-e	R3-20xxxx

Online, 1-11 June 2020

Agenda Item:	9.1.6.1.1

Source:	Huawei (moderator)

Title:	Summary of Offline Discussion on MBS1_General_Architecture

Document for:	Approval

# Introduction

CB: # MBS1_General_Architecture

- Whether and how to introduce RAN triggered Broadcast Session Release procedure

- affected spec: 413/410

- ref tdoc: R3-223072 R3-223073 (HW) / R3-223605 (ZTE) /R3-223650 R3-223651 (CMCC) / R3-223379 R3-223380 R3-223381 (Ericsson)

- Clarification on resource model, e.g., whether setup DRB for PDU session that only includes MBS QoS flows

- affected spec: 38300

- ref tdoc: R3-223535 (HW etc)

- PDCP SN/COUNT derivation from NG-U correction

- affected spec: 38300

- ref tdoc: R3-223452 (Nokia)

- PDCP SN length sync among gNBs for service continuity

- affected spec: 38300

- ref tdoc: R3-223604 (ZTE)

- Initial value of HFN and reference SN over E1AP

- affected spec: E1AP

- ref tdoc: R3-223302/R3-223303 (Lenovo)

- User Inactivity Monitoring and Reporting for Multicast

- affected spec: E1AP, F1AP, NG-C

- appeared in paper: R3-223300 R3-223301 (Lenovo)

- Impacts from RAN2 decision on RRC Structure (e.g., F1AP impacts on PTP only tunnel, Re-tx tunnel)

- affected spec: mainly F1AP

- ref tdoc: R3-223304 (lenovo) / R3-223074 (HW) / R3-223650 (CMCC )

- F1AP alignment with RAN2 progress (e.g., MRB ID space, MRB type indication, SIB 20 and 21 handling)

- affected spec: F1AP/E1AP

- R3-223074 R3-223075 R3-223076 (HW) / R3-223379 (Ericsson)

- Other issues

- affected spec: 38.300 and others

- R3-223379 (Ericsson) / R3-223535 (HW)

- Clean-up work on following spec

- 38401 38410 38420 38460 38470

- ref tdoc: R3-223459 (LG, 460), etc.

- LS out if needed (e.g., to RAN2/SA2)

- LS to SA2 (R3-223533, CATT)

- Capture agreements and provide CRs if agreeable, split work

(HW - moderator)

Summary of offline disc R3-223690

# For the Chairman’s Notes

//to be added.

# Discussion

## Broadcast

### RAN initiated Broadcast Session Release Require

In previous meetings, RAN3 asked a question [R3-221468] to SA2 on the RAN initiated BC Session Release procedure, and got the following feedback:

Furthermore, majority companies in RAN3 think that it is beneficial to introduce a RAN initiated Broadcast Session Release Require procedure, to trigger the CN to initiate Broadcast Session Release procedure. To be used in case RAN is not able to provide the service over radio, due to e.g. lack of radio resources. RAN3 kindly ask SA2 to provide feedback on this. [Answer]: SA2 shares the view of RAN3 that it is beneficial for NG-RAN to notify CN if a broadcast session cannot be provided by a NG-RAN node. SA2 respectfully asks RAN3 to proceed with the work. SA2 intends to agree necessary related changes at a future meeting.

Based on the response LS from SA2 [S2-2201315] and agreed CR for TS 23.247 [S2-2202143], and the submitted papers [R3-223072], [R3-223605], [R3-223650/51], it is straight forward to get the following proposal:

Proposal: introduce a non-UE associated class2 NGAP: Broadcast Session Release Require procedure, with a non-UE associated NGAP message: BROADCAST SESSION RELEASE REQUIRE message including MBS Session ID and cause.

| Company | Agree/Disagree | Comment |
| --- | --- | --- |
| Huawei | Agree |  |
| Nokia | Agree | BROADCAST SESSION RELEASE REQUIRED |

### Modification of Shared NG-U termination

In [R3-223379], it is proposed to discuss for both, multicast and broadcast, whether and how Rel-17 should support the possibility to modify both, RAN and CN side terminations of the shared NG-U bearer, for both, multicast and unicast transport.

For Multicast,

-	the NG-RAN has the possibility to release and setup resources in the right order for "emulating" a modification of the DL shared NG-U transport termination. The MB-SMF should handle such requests from NG-RAN in a transparent manner and not relate those requests to each other.

-	there is however no current means available for the CN to change the termination point. one might argue that the applications foreseen for Rel-17 for multicast wouldn’t require that, but it should be at least discussed in general before declaring Rel-17 to be finalised.

For Broadcast,

-	however, there is currently no means available for NG-RAN to change the DL termination, which is from our point of view really missing, given the expectation that broadcast sessions my last rather long.

Question1: For Multicast, if and how to enable the CN to modify the IP multicast address?

Question2: For Broadcast, if and how to enable RAN node to change the DL termination?

| Company | View | Comment |
| --- | --- | --- |
| Huawei | FFS | For 1, it is not clear whether there is requirement to enable CN to update the IP Multicast address for MC. For 2, no strong view, currently the RAN node is able to modify the DL termination in BC session modification response. |
| Nokia | OK but covered in tdoc R3-223453 (see CB MBS#3) | For 1/ there is the scenario agreed in CT4 of MB UPF restart which is addressed in tdoc R3-223453 (proposal 2, add multicast address in session update). For 2/ the NG-RAN node can send a Broadcast release required and provide in the broadcat release response the new TNL address. This is covered also in tdoc R3-223453 proposal 8 (based on SA2 Tdoc S2-2202143). |

### SIB20 SIB21 handling

As discussed in [R3-223074], SIB20 and SIB21 were introduced by RAN2 in TS 38.331, SIB 20 contains the information required to acquire the MCCH configuration for MBS broadcast, SIB21 contains the mapping between frequency and MBS services.

- For SIB20, based on previous discussion for broadcast bearer management over F1AP, it is straight forward for the gNB-DU to be responsible for the encoding of SIB20.

- For SIB21, as the gNB-DU has already reported its supported FSA ID list to the gNB-CU of each cell, the gNB-CU can generate the SIB21 based on the information received from gNB-DUs and other gNBs, it is straight forward for the gNB-CU to be responsible for the encoding of SIB21.

Proposal: The gNB-CU is responsible for the encoding of SIB21, the gNB-DU is responsible for the encoding of SIB20, include SIB20 in gNB-DU System Information IE.

| Company | Agree/Disagree | Comment |
| --- | --- | --- |
| Huawei | Agree |  |
| Nokia | Agree |  |

## Multicast

### MRB ID related

It is considered in [R3-223074] that as RAN2 agreed to extend MRB ID space beyond current 32 limit and up to 512, in case there are limited MBS services within a cell or a DU, the same MRB ID can be used for all the UEs for the same MBS service, note that during HO, the UE may need to be re-configured to change the MRB ID used in the new cell.

But on the other hand, in [R3-223379], it is proposed to liaise to RAN2 that RAN3 will keep the MRB ID value range on NG-RAN network interfaces 32 as the proposal from RAN2 doesn’t provided the aimed 1:1 mapping between MRB IDs used on NG-RAN interfaces and MRB IDs used on RRC and leave it up to RAN2 to consider further changes.

As we in RAN3 should respect the agreement/outcome achieved by other working groups, it is proposed to update the MRB ID range as RAN2 agreed.

Proposal: update the MRB ID from INTEGER (1.. 32, ...) to INTEGER (1.. 512, ...) in F1AP, E1AP, XnAP specifications.

| Company | Agree/Disagree | Comment |
| --- | --- | --- |
| Huawei | Agree |  |
| Nokia | Agree |  |

It is considered in [R3-223074] about per MBS session MRB ID or per UE MRB ID design, based on the feedback from RAN2 there is no per MBS Session MRB ID, the per UE MRB ID is extended to 512, but, once the MBS services increasing, e.g. more than 512 MBS sessions within a cell or a DU, even if the gNB configures only one MRB for one MBS session, the MRB ID still not able to be configured in a per cell or per DU granularity.

From RAN3 point of view, in order to have a unified per MBS session MRB ID in the non UE associated F1/E1 signalling, it is needed for the gNB-CU-CP to assign a “unified per MBS session MRB ID” to be used as the reference over F1 and E1 non UE associated MBS signalling, note that this “unified per MBS Session MRB ID” is only applicable over F1 and E1 interfaces, and the mapping relationship between the “per UE MRB ID” and the “unified per MBS session MRB ID” will be informed to the gNB-DU.

We would like to highlight that with this “unified per MBS Session MRB ID”, there will be no need for RAN2 to introduce MRB ID modification related procedure.

Proposal: Besides per UE MRB ID, the gNB-CU-CP assigns {unified per MBS Session MRB ID} to be used as the reference over F1AP and E1AP non-UE associated MBS signalling.

| Company | Agree/Disagree | Comment |
| --- | --- | --- |
| Huawei | Strongly recommended | This is quite helpful for the network, and will only impact F1AP E1AP specification, no impact to UE. In case RAN3 adopt this solution, RAN2 does not need to consider/discuss the MRB ID modification which is quite complex. |
| Nokia | NOK | Not needed. |

### MRB context from CU to DU

In last meeting, the following agreements was achieved:

- F1/E1 MC MBS Session resource control in MBS-associated procedures only (revisit if RAN2 prohibit RAN3 to do so), UE specific MBS configuration is transferred via UE associated procedures.

As RAN2 decided to not support the Common lower layer configuration, the only way RAN3 can use is the per UE lower layer configuration, therefore, it is straight forward to reuse the existing F1AP UE Context Management messages to support Multicast Bearer Management.

In [R3-223304], it is considered that according to RAN2’s agreements and as specified in TS 38.300, the MRB type includes split MRB, PTP only MRB and PTM only MRB:

-	For a multicast session, gNB provides one or more of the following multicast MRB configuration(s) to the UE via dedicated RRC signalling:

-	Multicast MRB with  DL only RLC-UM or bidirectional RLC-UM configuration for PTP transmission;

-	Multicast MRB with RLC-AM entity configuration for PTP transmission;

-	Multicast MRB with DL only RLC-UM entity for PTM transmission;

-	Multicast MRB with two RLC-UM entities, one DL only RLC-UM entity for PTP transmission and the other DL only RLC-UM entity for PTM transmission;

-	Multicast MRB with three RLC-UM entities, one DL RLC-UM entity and one UL RLC-UM entity for PTP transmission and the other DL only RLC-UM entity for PTM transmission;

-	Multicast MRB with two RLC entities, one RLC-AM entity for PTP transmission and the other DL only RLC-UM entity for PTM transmission.

-	For a multicast session, gNB may change the MRB type using RRC signalling.

Since the MRB type is configured by RRC signalling, it is straight forwards that the gNB-CU makes the decision. When gNB-CU decides to change the MRB bearer type, the gNB-CU needs to indicate the requested MRB bearer type to the gNB-DU so that the gNB-DU can provide corresponding L2/L1 configuration parameters. Since the MRB type configuration is per UE basis, the gNB-CU needs to indicate the requested MRB bearer type to the gNB-DU in UE associated signalling i.e. UE Context Management related messages.

Similar view can be found also in [R3-223074/75], and besides the MRB Type, it is further proposed to provide MRB ID, RLC mode of PTP leg in the existing F1APUE Context Management related messages.

Proposal: Introduce MRB related context in existing F1AP: UE Context Management related messages:

- MRB ID

- MRB Type (PTP only MRB, PTM only MRB, or split MRB)

- RLC mode of the PTP leg

Do you agree with the Proposal? Any comment?

| Company | Agree/Disagree | Comment |
| --- | --- | --- |
| Huawei | Agree all |  |
| Nokia | Agree all |  |

### F1-U tunnel related

In [R3-223304], it is considered that, for the shared F1-U tunnels setup, using the MBS service associated signalling MULTICAST DISTRIBUTION SETUP REQUEST message is a good method. However, for the per PTP MRB, the method is inefficient, because for each PTP MRB and PTP retransmission per UE, the gNB-DU needs initialize an MBS service associated Multicast Distribution Setup procedure in both F1AP and E1AP, which is inefficient and unnecessary.

As RAN2 decided not to support the Common RRC signalling, the only way RAN3 can use is the per UE lower layer configuration, therefore, it is straight forward to reuse the existing F1AP UE Context Management messages for MRB management. Taking this into account, it is also beneficial to reuse the F1AP UE Context Management and E1AP Bearer Context Management related messages for providing the PTP only F1-U tunnel.

For retransmission PTP F1-U tunnel, the gNB-DU has no idea that whether it is needed or not. It is not reasonable that the gNB-DU decides to trigger the PTP retransmission F1 tunnel establishment. One way is the gNB-CU provides an indication to request the PTP retransmission F1 tunnel e.g. when receives the PDCP SR from UE after handover. Another solution is the PTP retransmission F1 tunnel can always been provided by the UE associated signalling i.e., UE Context/Bearer Management related messages.

Proposals:

- Reuse the UE associated signalling i.e., UE Context/Bearer Management related messages for providing the PTP only F1-U tunnel.

- RAN3 to discuss how to decide PTP retransmission F1 tunnel establishment:

Option 1: gNB-CU provides an indication to request the PTP retransmission F1 tunnel e.g. when receives the PDCP SR from UE after handover;

Option 2: the gNB-DU provides the PTP retransmission F1 tunnel info by default in the UE associated signalling i.e., UE Context Management related messages

Do you agree with the Proposals? Any comment?

| Company | Agree/Disagree | Comment |
| --- | --- | --- |
| Huawei | Agree a) Agree b option1) | For b, option 1 is more efficient on the consumption of backhaul resources. |
| Nokia | Agree a) Agree b option 1) | Default option is not clear. |

### E1AP: Initial value of HFN and reference SN

In order to avoid PDCP HFN desynchronization, RAN2 agreed that a reference SN together with the initial value of HFN can be configured by the gNB by RRC. In [R3-223302], it is proposed that the gNB-CU-UP needs to provide the initial value of HFN and reference SN of an MRB to the gNB-CU-CP for RRC configuration. And to achieve this, provide the detail solution over E1AP:

Proposals:

- The gNB-CU-UP provides the initial HFN and reference SN of an MRB in the MC BEARER CONTEXT SETUP RESPONSE message.

- The gNB-CU-CP can trigger a MC Bearer Context Modification procedure to request the initial HFN and reference SN of an MRB. The gNB-CU-UP sends the initial HFN and reference SN in the MC BEARER CONTEXT MODIFICATION RESPONSE message.

Do you agree with above Proposals? Any comment?

| Company | Agree/Disagree | Comment |
| --- | --- | --- |
| Huawei | Agree a) and b) | Support gNB-CU-CP needs to get the initial value of HFN and reference SN, although there will be latency for the gNB-CU-CP to configure MRB until the CU-UP receive the first packet during the multicast session establishment. |
| Nokia | Partly Agree | Agree to send a reference HFN and SN values. However, the exact interpretation of those is pending RAN2 decision on how to handle this initial value (i.e. in connection with the issue of the negative RXlev). |

### User Inactivity Monitoring and Reporting for Multicast

In [R3-223300], it is pointed that a cause value ‘user inactive’ in NG interface is used to indicate the request of release of NG interface is due to user inactivity on all PDU sessions. So, the multicast session should also be considered when setting the cause value ‘user inactivity’, as follows:

Proposal: include multicast sessions for setting the cause value ‘user inactivity’ in NGAP?

| Company | Agree/Disagree | Comment |
| --- | --- | --- |
| Huawei | No strong view | For multicast, there is Session activation and deactivation procedures over NGAP, therefore may be not essential to have this solution. |
| Nokia | NOK | The inactivity of MBS sessions is managed through the Session Activate/deactivate. No relation with this traffic detection. |

In current E1AP specification, the gNB-CU-CP may send BEARER CONTEXT SETUP REQUEST message with UE/PDU session/DRB level inactivity timer. The gNB-CU-UP sends BEARER CONTEXT INACTIVITY NOTIFICATION message with inactivity monitoring results. The gNB-CU-CP may determine that the UE should enter RRC-inactive (e.g., after receiving Bearer Context Inactivity Notification procedure).

In current F1AP specification, if the Inactivity Monitoring Request IE is contained in the UE CONTEXT MODIFICATION REQUEST message, gNB-DU may consider that the gNB-CU has requested the gNB-DU to perform UE inactivity monitoring. The gNB-DU provides per DRB activity results to the gNB-CU in the UE INACTIVITY NOTIFICATION message.

In [R3-223300], it is proposed that for multicast sessions or multicast MRBs there are two ways to support multicast inactivity notification over E1AP and F1AP:

- Solution 1: Reusing the UE associated BEARER CONTEXT INACTIVITY NOTIFICATION(E1AP)/ UE INACTIVITY NOTIFICATION(F1AP) message for multicast inactivity notification.

- Solution 2: Introduce a new MBS associated MC BEARER CONTEXT INACTIVITY NOTIFICATION(E1AP)/ MULTICAST INACTIVITY NOTIFICATION(F1AP) message for multicast inactivity notification.

Question: which solution do you prefer for multicast inactivity notification over E1AP and F1AP?

| Company | Agree/Disagree | Comment |
| --- | --- | --- |
| Huawei | No strong view | Slightly support for solution1, since this procedure is to determine the RRC status for each UE. |
| Nokia | NOK | The inactivity of MBS sessions is managed through the Session Activate/deactivate. No relation with this traffic detection. |

### Admission control failure case

In [R3-223533], two questions are mentioned to ask SA2:

- For Multicast session update failure and Multicast session activation failure cases, should the NG-RAN node trigger Distribution Release procedure to release NG-U resources for the failed MBS session or just wait for the signalling from 5GC?

- In case the NG-RAN node could not provide resources for active MBS service, should the NG-RAN node directly initiate a Distribution Release procedure to release the NG-U resources for the MBS service or initiate a new procedure to inform MB-SMF and wait for further signalling from 5GC?

The above question also applies to the case that NG-RAN node could not admit all QoS flows for one MBS session when it receives Distribution Setup Response which indicates the MBS session is ACTIVE.

Based on the LS [S2-2203049], this will not be specified in this release:

Based on the feedback from SA2, we may not need to consider this topic in this release.

Any view for this topic?

| Company | View | Comment |
| --- | --- | --- |
| Huawei | noted |  |
| Nokia | Noted. | Agree with Huawei. We disagree with proposed changes. |

### S-NSSAI for a Multicast Session

In [R3-223379], it is proposed to:

- Include the S-NSSAI for the MC MBS Session within the Distribution Setup Response message (top message level) over NGAP.

- Include the S-NSSAI for the MC MBS Session within the MBS Session Information Source to Target List IE over NGAP.

- Include the S-NSSAI within the MBS Session Information List IE over XnAP.

Question: any view for these proposals?

| Company | View | Comment |
| --- | --- | --- |
| Huawei | Not needed | The S-NSSAI of a multicast session shall be the same with the associated PDU session, as in the non-MBS supporting node, the service will be provided via the associated PDU session. |
| Nokia | NOK | Agree with Huawei. This is clearly specified in TS 23.247 section 7.2.1.2: NOTE 1: The DNN and S-NSSAI are used to establish the PDU session which can carry the operations related to multicast session(s), i.e. session join/leave, and can be associated with multicast MBS session(s). |

# CR Revision

## TS 38.300 CR Revision

### draftCR on PDU session without DRB establishment

| R3-223535 | Correction on NR MBS (Huawei, CBN, China Unicom, Nokia, Nokia Shanghai Bell) | draftCR |
| --- | --- | --- |

In [R3-223535], it is proposed that the NG-RAN establishes at least one DRB together with a PDU session in 38.300, but in case the PDU session only includes MBS related QoS flows, the MBS capable gNB will not setup DRB, only MRBs will be established, it is needed to update the 38.300 description to introduce exception for MBS only case to not establish DRB for the PDU session:

Section 12.1, update the 38.300 description to introduce exception for MBS only case to not establish DRB for the PDU session.

Section 16.10.2.1, update “MB QoS Flow” to “MBS QoS Flow”.

Section 16.10.5.1, update the procedure name to “Multicast Distribution Setup” to align with stage3.

Section 16.10.5.2, change the multicast session “start” to “activated”, as session start is not applicable for multicast.

Section 16.10.5.3.3, clarify that for NG HO, the SMF provides MBS Session IDs to the target gNB via NGAP HO Request, which is not the same way as Xn HO, i.e PDU session modify after HO.

Other editorial updates.

Question: any comments on the changes proposed in this draftCR?

| Company | Agree/Disagree | Comment |
| --- | --- | --- |
| Huawei | Agree |  |
| Nokia | NOK | Sorry for the misunderstanding on first change but there is at least one DRB for the UE. Other changes are ok. |

### draftCR on PDCP SN length sync

| R3-223604 | Correction on NR MBS mobility for 38300 (ZTE Corporation) | draftCR |
| --- | --- | --- |

The following change is proposed to section 16.10.5.1 in this paper: (note that the HO related part is up to MBS2 discussion)

Question: any comments on the above change proposed in this draftCR?

| Company | Agree/Disagree | Comment |
| --- | --- | --- |
| Huawei | Agree |  |
| Nokia | OK |  |

### draftCR on PDCP COUNT/SN

| R3-223452 | Correction of MBS Data Forwarding (Nokia, Nokia Shanghai Bell, Huawei) | draftCR |
| --- | --- | --- |

The following change is proposed to section 16.10.5.1 in this paper: (note that the HO related part is up to MBS2 discussion)

Question: any comments on the above change proposed in this draftCR?

| Company | Agree/Disagree | Comment |
| --- | --- | --- |
| Huawei | Agree |  |
| Nokia | OK |  |

## TS 38.410 CR Revision

| R3-223073 | Correction on NR MBS for 38410 (Huawei, CBN, China Unicom) | CR0040r, TS 38.410 v17.0.0, Rel-17, Cat. F |
| --- | --- | --- |

- Add NG-RAN triggered release procedure for BC.

- Add the missed Multicast Session Update procedure in the list of NR MBS Session Management Procedures.

- Remove all the Editor’s notes.

- Update Figure 7.2-1 to be applicable for both PDU Session and MBS Session.

- Remove Figure 7.2-2.

Question: any comments on the changes proposed in this CR?

| Company | Agree/Disagree | Comment |
| --- | --- | --- |
| Huawei | Agree |  |
| Nokia | OK | Would be happy to cosign this one. |

## TS 38.413 CR Revision

### CR on BC Session Release Require

On BC Session Release Require, there are three NGAP CRs submitted:

| R3-223072 | Introduction of RAN triggered Broadcast Session Release procedure (Huawei, CBN, China Unicom, Qualcomm Incorporated, Lenovo, Motorola Mobility) | CR0767r, TS 38.413 v17.0.0, Rel-17, Cat. F |
| --- | --- | --- |
| R3-223605 | Correction on NR MBS for 38413 (ZTE Corporation) | CR0837r, TS 38.413 v17.0.0, Rel-17, Cat. F |
| R3-223651 | CR to TS38.413 for introduction of broadcast session release required procedure (CMCC) | CR0843r, TS 38.413 v17.0.0, Rel-17, Cat. F |

Comparing with these NGAP CRs, considering of the CR quality and to share load, it is proposed to further proceed on [R3-223651].

Do you have any comments on [R3-223651] NGAP CR on BC Session Required?

| Company | Comments |
| --- | --- |
| Huawei | Message Type should be “ignore” in the tabular. |
| Nokia | OK |

### CR on User Inactivity for Multicast Session

On User Inactivity for Multicast Session, there is one NGAP CR submitted:

| R3-223301 | Correction on User Inactivity for Multicast Session (Lenovo) | CR0796r, TS 38.413 v17.0.0, Rel-17, Cat. F |
| --- | --- | --- |

Do you have any comments on [R3-223303] NGAP CR on User Inactivity?

| Company | Comments |
| --- | --- |
| Nokia | NOK. Disagre with this change. See comment before. |

## TS 38.420 CR Revision

| R3-223096 | Alignment with rel-17 changes in XnAP (Qualcomm Incorporated) | CR0028r, TS 38.420 v17.0.0, Rel-17, Cat. F |
| --- | --- | --- |

A new “MBS management support function” is added to the function list, with explanatory text.

It is proposed to add the function in section 5.2 in a way that aligns with section 6.2 (procedure list). This implies moving the numbering of other sections.

Question: any comments on the changes proposed in this CR?

| Company | Agree/Disagree | Comment |
| --- | --- | --- |
| Huawei | Agree | But why MBS has to use 5.2.11? It can be added as 5.2.13, to avoid impact to SDT and QMC sections. |
| Nokia | OK | Same comment as Huawei: should be placed at the end of section 5. Would be happy to cosign this one. |

## TS 38.470 CR Revision

| R3-223076 | Corrections on NR MBS in 38470 (Huawei, CBN, Nokia, Nokia Shanghai Bell) | CR0088r, TS 38.470 v17.0.0, Rel-17, Cat. F |
| --- | --- | --- |

In section 4.3, clarify that F1 interface supports to manage radio bearers for MBS sessions;

In section 5.2.2, clarify that DU is responsible for the encoding of SIB20;

In section 5.2.3, clarify that the UE Context Management function also mange multicast MRBs for the UE.

In section 5.2.13, update the NR MBS function section to not only mention multicast group paging.

In section 6.1.13, clarify the different NR MBS related release procedures.

Question: any comments on the changes proposed in this CR?

| Company | Agree/Disagree | Comment |
| --- | --- | --- |
| Huawei | Agree |  |
| Nokia | OK |  |

## TS 38.473 CR Revision

| R3-223075 | Corrections on NR MBS in F1AP (Huawei, CBN, Nokia, Nokia Shanghai Bell) | CR0865r, TS 38.473 v17.0.0, Rel-17, Cat. F |
| --- | --- | --- |

- Update the MRB ID from INTEGER (1.. 32, ...) to INTEGER (1.. 512, ...) in F1AP, E1AP, XnAP specifications.

- Introduce DL PDCP SN length IE in the MULTICAST CONTEXT SETUP/MODIFICATION REQUEST messages for each MRB.

- Remove the MBS CU to DU RRC Information IE in the MULTICAST CONTEXT SETUP/MODIFICATION REQUEST messages.

- Introduce Multicast MRB related information {MRB ID, MRB Type (PTP only MRB, PTM only MRB, or split MRB), and the RLC mode of the PTP leg} in exiting F1AP: UE Context Management related messages.

- In Section 9.2.14.7, add the missing MBS Service Area IE

- In Section 9.2.14.10, add the presence of the Multicast F1-U Context To Be Setup List IE as mandatory

- Remove the MBS Multicast F1-U Context Descriptor IE in the MULTICAST DISTRIBUTION SETUP RESPONSE, MULTICAST DISTRIBUTION SETUP FAILURE, MULTICAST DISTRIBUTION RELEASE COMMAND and MULTICAST DISTRIBUTION RELEASE COMPLETE messages.

- Update the procedural texts from “may include Supported MBS FSA ID List IE in the xxx message” to “may include Supported MBS FSA ID List IE in the Served Cell Information IE in the xxx message”.

- In Section 9.3.2.7, for location dependent case, move the MBS F1-U Information IE to the same level as MBS Area Session ID IE.

- In Section 9.2.14.11, move MRB F1-U TNL Info at CU IE to the same level of MRB ID IE.

- In Section 9.3.1.221, change the maximum value of the MBS Area Session ID IE to 65535.

- In Section 9.3.1.222 and 9.3.1.223, remove Editor’s Note about the values. And change the value of maxnoofMBSServiceAreaInformation from 512 to 256 to align with NGAP specification.

- Include SIB20 in the gNB-DU System Information IE.

Do you have any comments on [R3-223075] F1AP CR?

| Company | Comments |
| --- | --- |
| Huawei | Support. Note: need to avoid overlapping part with the F1AP changes in MBS3, to be updated accordingly based on the discussion. |
| Nokia | OK except “change the value of maxnoofMBSServiceAreaInformation from 512 to 256 to align with NGAP specification” which should be covered in CB MBS#3. |

## TS 38.460 CR Revision

| R3-223459 | Corrections on E1 bearer context management function for NR MBS (LG Electronics) | CR0058r, TS 38.460 v17.0.0, Rel-17, Cat. F |
| --- | --- | --- |

In section 5.1.x, all of Editor’s Notes are removed and the sentence related to header compression is added.

Question: any comments on the changes proposed in this CR?

| Company | Agree/Disagree | Comment |
| --- | --- | --- |
| Huawei | Agree | Note that in case it is agreed, E1AP update is needed, i.e. to provide the MRB header compression parameters from CP to UP. |
| Nokia | OK |  |

## TS 37.483 CR Revision

| R3-223303 | Correction on configuration of initial value of HFN and reference SN (Lenovo, Huawei) | CR0007r, TS 37.483 v17.0.0, Rel-17, Cat. F Move to 9.1.6.1.1 |
| --- | --- | --- |

Do you have any comments on [R3-223303] E1AP CR?

| Company | Comments |
| --- | --- |
| Nokia | Pending outcome of RAN2 discussions on initial HFN value. |

# References

| R3-223072 | Introduction of RAN triggered Broadcast Session Release procedure (Huawei, CBN, China Unicom, Qualcomm Incorporated, Lenovo, Motorola Mobility) | CR0767r, TS 38.413 v17.0.0, Rel-17, Cat. F |
| --- | --- | --- |
| R3-223073 | Correction on NR MBS for 38410 (Huawei, CBN, China Unicom) | CR0040r, TS 38.410 v17.0.0, Rel-17, Cat. F |
| R3-223074 | Correction on Multicast MRB Management and other F1AP aspects (Huawei, CBN) | discussion |
| R3-223075 | Corrections on NR MBS in F1AP (Huawei, CBN, Nokia, Nokia Shanghai Bell) | CR0865r, TS 38.473 v17.0.0, Rel-17, Cat. F |
| R3-223076 | Corrections on NR MBS in 38470 (Huawei, CBN, Nokia, Nokia Shanghai Bell) | CR0088r, TS 38.470 v17.0.0, Rel-17, Cat. F |
| R3-223096 | Alignment with rel-17 changes in XnAP (Qualcomm Incorporated) | CR0028r, TS 38.420 v17.0.0, Rel-17, Cat. F |
| R3-223282 | Discussion the editor’s notes related to consent (Samsung) | discussion |
| R3-223283 | Remove the editor’s notes related to consent information (Samsung) | CR0214r, TS 38.401 v17.0.0, Rel-17, Cat. F |
| R3-223284 | Remove the editor’s notes related to consent information (Samsung) | CR0006r, TS 37.483 v17.0.0, Rel-17, Cat. F |
| R3-223300 | User Inactivity Monitoring and Reporting for Multicast (Lenovo) | discussion |
| R3-223301 | Correction on User Inactivity for Multicast Session (Lenovo) | CR0796r, TS 38.413 v17.0.0, Rel-17, Cat. F |
| R3-223452 | Correction of MBS Data Forwarding (Nokia, Nokia Shanghai Bell, Huawei) | draftCR |
| R3-223459 | Corrections on E1 bearer context management function for NR MBS (LG Electronics) | CR0058r, TS 38.460 v17.0.0, Rel-17, Cat. F |
| R3-223533 | [Draft]LS on left-over issues on Rel-17 MBS (CATT) | LS out To: SA2 CC: |
| R3-223535 | Correction on NR MBS (Huawei, CBN, China Unicom, Nokia, Nokia Shanghai Bell) | draftCR |
| R3-223604 | Correction on NR MBS mobility for 38300 (ZTE Corporation) | draftCR |
| R3-223605 | Correction on NR MBS for 38413 (ZTE Corporation) | CR0837r, TS 38.413 v17.0.0, Rel-17, Cat. F |
| R3-223627 | Consent information exchange between E1 interface (Huawei) | discussion |
| R3-223628 | Correction on the FFS consent information (Huawei) | CR0226r, TS 38.401 v17.0.0, Rel-17, Cat. F |
| R3-223629 | Correction on the FFS consent information (Huawei) | CR0018r, TS 37.483 v17.0.0, Rel-17, Cat. F |
| R3-223650 | Remaining Issues for Stage2 details (CMCC) | discussion |
| R3-223651 | CR to TS38.413 for introduction of broadcast session release required procedure (CMCC) | CR0843r, TS 38.413 v17.0.0, Rel-17, Cat. F |
| R3-223379 | Rel-17 MBS Corrections (Ericsson) | Other Move to 9.1.6.1.1 |
| R3-223380 | MBS NGAP Corrections (Ericsson) | CR0801r, TS 38.413 v17.0.0, Rel-17, Cat. F Move to 9.1.6.1.1 |
| R3-223381 | MBS XnAP Corrections (Ericsson) | CR0807r, TS 38.423 v17.0.0, Rel-17, Cat. F Move to 9.1.6.1.1 |
| R3-223382 | MBS F1AP Corrections (Ericsson) | CR0909r, TS 38.473 v17.0.0, Rel-17, Cat. F Move to 9.1.6.1.1 |
| R3-223383 | MBS E1AP Corrections (Ericsson) | CR0009r, TS 37.483 v17.0.0, Rel-17, Cat. F Move to 9.1.6.1.1 |
| R3-223672 | Corrections to E1AP for NR MBS (ZTE) | CR0022r, TS 37.483 v17.0.0, Rel-17, Cat. F Move to 9.1.6.1.1 |
| R3-223077 | MBS Session Status during Xn HO preparation (Huawei, CBN, China Unicom, Lenovo, Motorola Mobility) | CR0773r, TS 38.423 v17.0.0, Rel-17, Cat. F Move to 9.1.6.1.1 |
| R3-223078 | MBS Session Status during NG HO preparation (Huawei, CBN, China Unicom, Lenovo, Motorola Mobility) | CR0768r, TS 38.413 v17.0.0, Rel-17, Cat. F Move to 9.1.6.1.1 |
| R3-223185 | Indication for inactive MBS session (NEC) | Discussion Move to 9.1.6.1.1 |
| R3-223187 | MBS Session Status indication in NGAP interface (NEC) | CR0789r, TS 38.413 v17.0.0, Rel-17, Cat. F Move to 9.1.6.1.1 |
| R3-223188 | MBS Session Status indication in Xn interface (NEC) | CR0787r, TS 38.423 v17.0.0, Rel-17, Cat. F Move to 9.1.6.1.1 |
| R3-223302 | Configuration of initial value of HFN and reference SN over E1AP (Lenovo, Huawei) | Discussion Move to 9.1.6.1.1 |
| R3-223303 | Correction on configuration of initial value of HFN and reference SN (Lenovo, Huawei) | CR0007r, TS 37.483 v17.0.0, Rel-17, Cat. F Move to 9.1.6.1.1 |
| R3-223304 | F1-U tunnels related issues (Lenovo) | Discussion Move to 9.1.6.1.1 |