3GPP TSG-RAN WG3 #108-e	R3-223816

Online, 1-11 June 2020

Agenda Item:	9.1.6.1.1

Source:	Huawei (moderator)

Title:	Summary of Offline Discussion on MBS1_General_Architecture

Document for:	Approval

# Introduction

CB: # MBS1_General_Architecture

- Whether and how to introduce RAN triggered Broadcast Session Release procedure

- affected spec: 413/410

- ref tdoc: R3-223072 R3-223073 (HW) / R3-223605 (ZTE) /R3-223650 R3-223651 (CMCC) / R3-223379 R3-223380 R3-223381 (Ericsson)

- Clarification on resource model, e.g., whether setup DRB for PDU session that only includes MBS QoS flows

- affected spec: 38300

- ref tdoc: R3-223535 (HW etc)

- PDCP SN/COUNT derivation from NG-U correction

- affected spec: 38300

- ref tdoc: R3-223452 (Nokia)

- PDCP SN length sync among gNBs for service continuity

- affected spec: 38300

- ref tdoc: R3-223604 (ZTE)

- Initial value of HFN and reference SN over E1AP

- affected spec: E1AP

- ref tdoc: R3-223302/R3-223303 (Lenovo)

- User Inactivity Monitoring and Reporting for Multicast

- affected spec: E1AP, F1AP, NG-C

- appeared in paper: R3-223300 R3-223301 (Lenovo)

- Impacts from RAN2 decision on RRC Structure (e.g., F1AP impacts on PTP only tunnel, Re-tx tunnel)

- affected spec: mainly F1AP

- ref tdoc: R3-223304 (lenovo) / R3-223074 (HW) / R3-223650 (CMCC )

- F1AP alignment with RAN2 progress (e.g., MRB ID space, MRB type indication, SIB 20 and 21 handling)

- affected spec: F1AP/E1AP

- R3-223074 R3-223075 R3-223076 (HW) / R3-223379 (Ericsson)

- Other issues

- affected spec: 38.300 and others

- R3-223379 (Ericsson) / R3-223535 (HW)

- Clean-up work on following spec

- 38401 38410 38420 38460 38470

- ref tdoc: R3-223459 (LG, 460), etc.

- LS out if needed (e.g., to RAN2/SA2)

- LS to SA2 (R3-223533, CATT)

- Capture agreements and provide CRs if agreeable, split work

(HW - moderator)

Summary of offline disc R3-223690

# For the Chairman’s Notes

//to be added.

# Round2_Discussion

## Leftover issues to be discussed second round

### MRB Type and RLC mode from CU to DU in UE specific signalling.

During the previous discussion, most companies think that it should be the gNB-CU to make decision on the MRB type, as making such decision need to take many factors into account, e.g. measurement results, Qos profiles, UE characteristic, etc.

And in current DRB setup related IE, the RLC mode is a mandatory IE provided from the gNB-CU to the gNB-DU, and it is a mandatory IE provided from the gNB-CU-CP to the gNB-CU-UP.

It is noticed that currently for MBS, the RLC mode is also mandatorily provided from the gNB-CU-CP to the gNB-CU-UP via the MBS PDCP Configuration IE.

Proposal: provide MRB type and RLC mode from CU to DU in UE specific signalling.

| Company | View | Comment |
| --- | --- | --- |
| Huawei | Support | MRB type should be decided by the gNB-CU, and it is better to align with DRB design, i.e. provide RLC mode from CU to DU. [Ericsson: the general mood to align, for a ptm service, with DRB, i.e. is one of the uncurable ailments of Rel-17 MBS. There is still hope that some aspects are reasonably designed. As we have explained during the online discussion, DC was the reason for determining the RLC mode at the CU. But this is not needed for MBS/MRBs.] If we do not support this, then the gNB-DU will need to inform the MRB type and RLC mode to the gNB-CU [Ericsson: if this is really needed, well we have to do it, but don’t see the need so far]. |
| Nokia | Support | When the UE joins, the CU CP must tell the DU the bearer type so that the DU can build the corresponding CG-config with the proper MBS parameters. The CU already provides the RLC mode to the DU for unicast. |
| CATT | Support |  |
| Ericsson | not needed and against fundamental architectural principles. | We still don’t understand why RLC and MRB type, which are by definition are lower layer properties have to be decided by the CU which is not responsible for lower layer configuration. DRB DC bearer type (i.e. the location of SDAP/PDCP and the decision whether split bearer is to configured) is fundamentally different from the MRB bearer type and therefore any kind of comparison/alignment is not appropriate, as the MRB bearer type is not related to SDAP/PDCP at all. The DU will inform the CU anyhow which bearer type is configured, but this information is - from an RRC configuration point of view - transparent to the CU, as the DU is responsible for assembling RRC configuration information regarding lower layer properties. From an F1-U bearer point of view, we have already decided that the CU will inform the DU by means of UE associated signalling means on F1-C for ptp retransmission, but the reason for that is that this is a higher layer (PDCP) decision. Also, any kind of lower layer (also PHY) related properties is not part for CU to decide, whatever acronym you will throw into the discussion, it is not CU’s business. |
| Lenovo | Support | Currently, how DU triggers bearer type change is not clear. There is no signaling to support DU triggered bearer type change. |
| ZTE | Support but | how about a compromise, - CU initiate the MRB type during setup for one UE. - DU is able to modify it in later stage? // it is assumed CU is not always right. // I assume in unicast the RLC mode indication is there mostly for flow control? |
| LGE | Support | As Huawei mentioned, it is a good approach to align with DRB design, where the gNB-CU provides the gNB-DU with the RLC mode. |
| CMCC | Support | Agree with comments from Huawei. |
| Samsung | Support | Agree with comments from Huawei. |

### Establishment of the F1-U tunnel for PTP only MRB

In case the MRB type is decided by the gNB-CU, there are two options to establish the F1-U tunnel for PTP only MRB:

Option 1: the gNB-CU indicate the need on the F1-U tunnel for PTP only MRB, then the gNB-DU trigger to establish the tunnel. (same solution with PTP retransmission F1-U tunnel agreed in 1st round)

Option 2: established via the UE specific signallings.

Question: In case MRB type is decided by the gNB-CU, which option do you prefer to establish the F1-U tunnel for PTP only MRB?

| Company | View | Comment |
| --- | --- | --- |
| Huawei | Slightly prefer Option 2 | Both works, and option 2 is more efficient than option1 in case MRB type is decided by the gNB-CU. |
| Nokia | Option 2 | Same view as Huawei. |
| Ericsson |  | There is only an indication from CU needed for the ptp retransmission bearer, as PDCP level retransmission is a higher layer decision. and there is no reason to deviate from the decision to use DU triggered procedures for setup of F1-U bearers for multicast. If a ptp bearer type is decided by the DU, then it will establish it by means of the Distribution Setup procedure and if it decided to put the UE on ptm again, it will reconfigure the UE (DU triggered UE Context modification) and remove the ptp F1-U bearer. this all works fine and no need to consider UE context signalling. On E1, UE context signalling wouldn’t work anyhow, as the gNB-CU-UP serving the MBS context is not necessarily serving any bearer context for the UE. |
| Lenovo | Option 2 | Even for MRB type is decided by the gNB-CU, using UE associated signaling also has benefits/ |
| ZTE | Option 1 | both work. prefer 1 as a more consistent solution. one question here: for one PTP only MRB, is it always a separate tunnel, or is it optional? |
| LGE | Option 2 | Considering the efficiency of signaling, we prefer Option 2. |
| CMCC | Slightly prefer Option 1 | It is better to align with the solution for establishing PTP retransmission F1-U tunnel. gNB-CU indicates its need to gNB-DU for PTP retransmission F1-U tunnel establishment or PTP only F1-U tunnel. |
| Samsung | Option 2 |  |

### Providing the HFN and reference SN from CU-UP to CU-CP

during the online discussion, the following agreements are achieved:

  - The gNB-CU-UP provides the HFN and reference SN of an MRB in the MC BEARER CONTEXT SETUP RESPONSE message.

  - The gNB-CU-CP can trigger a MC Bearer Context Modification procedure to request the HFN and reference SN of an MRB. The gNB-CU-UP sends the HFN and reference SN in the MC BEARER CONTEXT MODIFICATION RESPONSE message.

And in the meanwhile, it is still open on whether the gNB-CU-UP can trigger a MC Bearer Context Modification Required procedure to provide the HFN and reference SN. And it was clarified by the proponent that in some cases, when the real data package may arrive later than the establishment of the CP, and based on SA2 spec, such scenario is allowed.

Question: Do you agree to enable the gNB-CU-UP to trigger a MC Bearer Context Modification Required procedure to provide the HFN and reference SN? Please clarify the reason, if any.

| Company | View | Comment |
| --- | --- | --- |
| Huawei | Ok | No strong view so far from our side. |
| Nokia | Peharps | It would be good to clarify the scenario: is it a case of UE joining an inactive MBS session? |
| CATT | OK | It seems the scenario that there is no immediate user plane data when UE join the MBS session exists |
| Ericsson |  | isn’t that equivalent to the retrieval of information necessary for the SN STATUS TRANFER? |
| Lenovo | OK | The UP data may come later than the MC Bearer Context Setup procedure. |
| ZTE | OK | // to Nokia: it has to be an active session such that there is context on CU-UP. For the activated session, it is just that the corresponding activation operation is earlier than the data arriving. |
| CMCC | OK |  |
| Samsung | OK |  |

### Handling in case gNB is not able to provide a MC service

In R3-223533 there were two questions raised, and it was clarified that the first question should be noted based on SA2/CT4 progress. And the proponent considers that the second question is not related to the SA2/CT4 LS, and therefore has not been answered yet.

The second question is:

In case the NG-RAN node could not provide resources for active MBS service, should the NG-RAN node directly initiate a Distribution Release procedure to release the NG-U resources for the MBS service or initiate a new procedure to inform MB-SMF and wait for further signalling from 5GC?

This question related to two scenarios, one is the case in which the gNB is not able to continue proving the ongoing service, e.g. due to lack of resources, another is the case in which the session is newly established, but when the gNB gets the indication of session activated in the Distribution Setup Response, the RAN node is not able to provide the service due to e.g. lack of resources.

Note currently we only have MC activation failure and MC update failure, there seems no clear way to indicate the problem in the cases above.

Question: Do you agree with the problem? Any suggestion/solution to go?

| Company | View | Comment |
| --- | --- | --- |
| Huawei | Agree | In the gNB side, we do have the chance to do the admission control in case of MC update and MC activation, but it is indeed not clear if and how to do the admission control in the mentioned scenarios. From our view, one potential way is to find a way to report the failure in there two scenarios, i.e. failure for ongoing active session, failure after Distribution Setup Response with session activated status. |
| Nokia | Disagree | Whether NG-RAN node initiate a Distribution Release message should remain implementation dependent. We don’t agree to specify it. |
| CATT | Agree | Currently, for MBS Session Activation procedure, it is a class 1 procedure which allows the NG-RAN node to provide the activation result to 5GC. However, for a newly established MBS session, there is no way for NG-RAN node to provide the activation result to 5GC.It should be aligned for the two activation mechanism. |
| Ericsson | Agree | but obviously not part of Rel-17 it is evident, that the NG-U resources should be kept, in order to keep C- and U-plane resources active and the “distribution tree” setup, otherwise you may lose the possibility to communicate with NG-RAN. suggestion is to close discussions on it in Rel-17 |
| Lenovo | Agree |  |
| ZTE | Agree, but | We do think this issue exist. And RAN3 needs to discuss this topic by different scenarios, but not now? As we mentioned in round 1, we do not think RAN3 has enough time on discussing this in the remaining period of Rel-17. How to solve this issue(e.g., by implementation, specific definition, or add new procedures ) can be discussed in Rel-18. |
| LGE | Agree, but | RAN3 may discuss this issue, but it does not have much time in Rel-17. So, as ZTE’s suggestion, it can be discussed in Rel-18. |
| CMCC | Agree, but | The motivation for introducing the RAN initiated Multicast Session release procedure is clear. The two solutions corresponding to two potential scenarios need fully investigated. However, considered this is the last meeting in Rel-17, we prefer to leave this issue in Rel-18. |
| Samsung | Agree, but | Agree with ZTE. |

## Second round CR review

Based on the online discussion, it is planned to agree the revisions of the following CRs/draftCRs, please companies upload a revised version to the CR review folder.

https://www.3gpp.org/ftp/tsg_ran/WG3_Iu/TSGR3_116-e/Inbox/Drafts/CB%20%23%20MBS1_General_Architecture/MBS1%20CR%20Review

Please provide your further comments on the updated version of the CR/draftCR, if any.

38.300 draftCRs:

- R3-223824 revised from R3-223535 (Huawei, CBN, CUC, Nokia), remove the change on without DRB setup part.

| Company | Comments |
| --- | --- |

- R3-223825 revised from R3-223604 (ZTE), agree the PDCP SN sync part, remove the HO related part.

| Company | Comments |
| --- | --- |
| Ericsson | if we agree on including this, then please move the two sentences to where they belong: to the “derivation of the PDCP SNs by means of a DL MBS QFI Sequence Number provided on NG-U” bullet |

- R3-223826 revised from 3-223452 (Nokia, Huawei), agree the PDCP count part, remove the HO related part

| Company | Comments |
| --- | --- |
| Ericsson | cover page corrections (second change should be removed) |

38.410 CR:

- R3-223827 revised from R3-223073 (Huawei, CBN, CUC, Nokia, Nokia Shanghai Bell, ZTE)

| Company | Comments |
| --- | --- |

38.413 CRs:

- R3-223828 revised from R3-223651(CMCC, Huawei), revise at least on the procedure criticality which is not aligned in asn1 and tabular

| Company | Comments |
| --- | --- |
| Ericsson | please define the procedure level criticality “reject” |

38.470 CR:

- R3-223829 revised from R3-223076 (Huawei, CBN, Nokia), revision based on comments received in first round.

| Company | Comments |
| --- | --- |
| Ericsson | included info related to CATT/3532 about join info being part of UE context. |

38.473 CR:

- R3-223830 revised from R3-223075 (Huawei, CBN, Nokia), to be updated based on comments received in first round, remove overlapping part with MBS3 discussion, and capture the agreements achieved during this meeting.

| Company | Comments |
| --- | --- |
| Ericsson | apart from corrections, e.g. to remove “successful” lists from the UE Context … response messages, we have included the important correction from CATT/3532 to provide join info in those messages. ASN.1 was not touched in our revision. |

37.480 CR:

- R3-223831 revised from R3-223459 (LGE), only remove Editor’s Notes without adding additional text.

| Company | Comments |
| --- | --- |

37.483 CR:

- R3-223832 revised from R3-223303 (Lenovo, Huawei), to be updated based on the agreements achieved during this meeting.

| Company | Comments |
| --- | --- |

Further:
Ericsson: please consider our corrections for the F1-U descriptor for E1AP and F1AP

# Round1_For the Chairman’s Notes

Proposed Agreements:

- Introduce a non-UE associated class2 NGAP: Broadcast Session Release Required procedure, with a non-UE associated NGAP message: BROADCAST SESSION RELEASE REQUIRED message including MBS Session ID and cause.

- The gNB-CU is responsible for the encoding of SIB21, the gNB-DU is responsible for the encoding of SIB20, include SIB20 in gNB-DU System Information IE.

- Introduce MRB related context in existing F1AP: UE Context Management related messages:

  - MRB ID (9 agree)

  - MRB Type (PTP only MRB, PTM only MRB, or split MRB) (8 agree, 1 no)

  - RLC mode of the PTP leg (8 agree, 1 no)

- Update the MRB ID from INTEGER (1.. 32, ...) to INTEGER (1.. 512, ...) in F1AP, E1AP, XnAP specifications. (7 agree, 2 no)

  - Besides per UE MRB ID, the gNB-CU-CP assigns {unified per MBS Session MRB ID} to be used as the reference over F1AP and E1AP non-UE associated MBS signaling. (2 agree, 6 no, moderator strongly recommend)

- On PTP F1-U tunnel management:

  - For PTP Retransmission F1-U tunnel establishment, gNB-CU provides an indication on the need of the PTP retransmission F1 tunnel via F1AP UE Context Management related messages; (9 agree, 1 neutral)

  - For PTP only F1-U tunnel establishment, use the UE associated signalling i.e., F1AP UE Context/E1AP Bearer Management related messages for providing the PTP only F1-U tunnel. (8 agree, 1 disagree)

- On HFN and Reference SN from CU-UP to CU-CP

  - The gNB-CU-UP provides the HFN and reference SN of an MRB in the MC BEARER CONTEXT SETUP RESPONSE message. (10 agree, 2 thinks the need to monitor RAN2)

  - The gNB-CU-CP can trigger a MC Bearer Context Modification procedure to request the HFN and reference SN of an MRB. The gNB-CU-UP sends the HFN and reference SN in the MC BEARER CONTEXT MODIFICATION RESPONSE message. (10 agree, 2 thinks the need to monitor RAN2)

  - The gNB-CU-UP can trigger a MC Bearer Context Modification Required procedure to provide the HFN and reference SN. (new proposal)

- The parameters for header compression is sent from the gNB-CU-CP to the gNB-CU-UP. (8 agree, 1 no)

- Note the User Inactivity Monitoring and Reporting for MC related proposals in R3-223300.

- Note the MC failure cases related proposals in R3-223533.

- Note the S-NSSAI MC related proposals in R3-223379.

To be further discussed in MBS2/3 (overlapped):

- For Multicast, CN modifies the IP multicast address via MC update procedure (6 agree, 3 FFS, pending to CT4 progress)

- For Broadcast, if and how to enable RAN node to change the DL termination? (6 agree, 3 FFS)

CR Revision in second round, to be agreed at the end of the meeting:

38.300 draftCRs:

- R3-223535 (Huawei, CBN, CUC, Nokia), remove the first change, agree on the other changes included.

- R3-223604 (ZTE), agree the PDCP SN sync part, revision may be needed to remove/update the HO related part, pending to MBS2 discussion.

- R3-223452 (Nokia, Huawei), agree the PDCP count part, revision may be needed to remove/update the HO related part, pending to MBS2 discussion.

38.410 CR:

- R3-223073 (Huawei, CBN, CUC), revision needed to add Nokia and ZTE as co-source companies

38.413 CRs:

- R3-223651(CMCC), revise at least on the procedure criticality which is not aligned in asn1 and tabular, and add Huawei as co-source company.

38.420 CR:

- R3-223096 (QCOM), revise to place the MBS part after current other sections. (overlap with MBS2)

38.470 CR:

- R3-223076 (Huawei, CBN, Nokia), revision based on comments received.

38.473 CR:

- R3-223075 (Huawei, CBN, Nokia), to be updated based on comments received, and the agreements achieved during this meeting.

38.460 CR:

- R3-223459 (LGE), agree to remove Editor’s Notes, further check the additional text in second round.

38.463 CR:

- R3-223303 (Lenovo, Huawei), to be updated based on the agreements achieved during this meeting.

# Round1_Discussion

## Broadcast

### RAN initiated Broadcast Session Release Require

In previous meetings, RAN3 asked a question [R3-221468] to SA2 on the RAN initiated BC Session Release procedure, and got the following feedback:

Furthermore, majority companies in RAN3 think that it is beneficial to introduce a RAN initiated Broadcast Session Release Require procedure, to trigger the CN to initiate Broadcast Session Release procedure. To be used in case RAN is not able to provide the service over radio, due to e.g. lack of radio resources. RAN3 kindly ask SA2 to provide feedback on this. [Answer]: SA2 shares the view of RAN3 that it is beneficial for NG-RAN to notify CN if a broadcast session cannot be provided by a NG-RAN node. SA2 respectfully asks RAN3 to proceed with the work. SA2 intends to agree necessary related changes at a future meeting.

Based on the response LS from SA2 [S2-2201315] and agreed CR for TS 23.247 [S2-2202143], and the submitted papers [R3-223072], [R3-223605], [R3-223650/51], it is straight forward to get the following proposal:

Proposal: introduce a non-UE associated class2 NGAP: Broadcast Session Release Require procedure, with a non-UE associated NGAP message: BROADCAST SESSION RELEASE REQUIRE message including MBS Session ID and cause.

| Company | Agree/Disagree | Comment |
| --- | --- | --- |
| Huawei | Agree |  |
| Nokia | Agree | BROADCAST SESSION RELEASE REQUIRED |
| CATT | Agree |  |
| Samsung | Agree |  |
| Ericsson | Agree | same comment on name as Nokia |
| LGE | Agree |  |
| CMCC | Agree | Same view with Nokia. |
| Lenovo | Agree |  |
| ZTE | agree |  |
| Qualcomm | Agree |  |

### Modification of Shared NG-U termination

In [R3-223379], it is proposed to discuss for both, multicast and broadcast, whether and how Rel-17 should support the possibility to modify both, RAN and CN side terminations of the shared NG-U bearer, for both, multicast and unicast transport.

For Multicast,

-	the NG-RAN has the possibility to release and setup resources in the right order for "emulating" a modification of the DL shared NG-U transport termination. The MB-SMF should handle such requests from NG-RAN in a transparent manner and not relate those requests to each other.

-	there is however no current means available for the CN to change the termination point. one might argue that the applications foreseen for Rel-17 for multicast wouldn’t require that, but it should be at least discussed in general before declaring Rel-17 to be finalised.

For Broadcast,

-	however, there is currently no means available for NG-RAN to change the DL termination, which is from our point of view really missing, given the expectation that broadcast sessions my last rather long.

Question1: For Multicast, if and how to enable the CN to modify the IP multicast address?

Question2: For Broadcast, if and how to enable RAN node to change the DL termination?

| Company | View | Comment |
| --- | --- | --- |
| Huawei | FFS | For 1, it is not clear whether there is requirement to enable CN to update the IP Multicast address for MC. For 2, no strong view, currently the RAN node is able to modify the DL termination in BC session modification response. |
| Nokia | OK but covered in tdoc R3-223453 (see CB MBS#3) | For 1/ there is the scenario agreed in CT4 of MB UPF restart which is addressed in tdoc R3-223453 (proposal 2, add multicast address in session update). For 2/ the NG-RAN node can send a Broadcast release required and provide in the broadcat release response the new TNL address. This is covered also in tdoc R3-223453 proposal 8 (based on SA2 Tdoc S2-2202143). |
| CATT | Both yes | We are open with details. |
| Samsung |  | For 1, we share the view that CN can use MC update procedure to modify the IP multicast address. For 2, in this release, the RAN can modify DL in the modification response message. |
| Ericsson | OK | no strong opinion via which CB this is introduced |
| CMCC | No strong view. | For 1, the benefit of enabling the CN to modify the IP multicast address needs clarification. For 2, we think that Nokia’s suggestion is acceptable. |
| Lenovo | Yes for both | For 1, same view as Nokia and Samsung that MC update procedure can be used for IP multicast address update. For 2: Nokia’s proposal is acceptable. |
| ZTE | FFS for #1 Fine for #2 | We are generally fine for both functions. But we do not think MC new function shall be introduced in the last R17 meeting. We prefer to discuss this part in R18. |
| Qualcomm | OK for both | Nokia proposals are fine. |

### SIB20 SIB21 handling

As discussed in [R3-223074], SIB20 and SIB21 were introduced by RAN2 in TS 38.331, SIB 20 contains the information required to acquire the MCCH configuration for MBS broadcast, SIB21 contains the mapping between frequency and MBS services.

- For SIB20, based on previous discussion for broadcast bearer management over F1AP, it is straight forward for the gNB-DU to be responsible for the encoding of SIB20.

- For SIB21, as the gNB-DU has already reported its supported FSA ID list to the gNB-CU of each cell, the gNB-CU can generate the SIB21 based on the information received from gNB-DUs and other gNBs, it is straight forward for the gNB-CU to be responsible for the encoding of SIB21.

Proposal: The gNB-CU is responsible for the encoding of SIB21, the gNB-DU is responsible for the encoding of SIB20, include SIB20 in gNB-DU System Information IE.

| Company | Agree/Disagree | Comment |
| --- | --- | --- |
| Huawei | Agree |  |
| Nokia | Agree |  |
| CATT | Agree |  |
| Samsung | Agree |  |
| Ericsson | ok |  |
| LGE | Agree |  |
| CMCC | Agree |  |
| Lenovo | Agree |  |
| ZTE | Agree |  |
| Qualcomm | Agree |  |

## Multicast

### MRB ID related

It is considered in [R3-223074] that as RAN2 agreed to extend MRB ID space beyond current 32 limit and up to 512, in case there are limited MBS services within a cell or a DU, the same MRB ID can be used for all the UEs for the same MBS service, note that during HO, the UE may need to be re-configured to change the MRB ID used in the new cell.

But on the other hand, in [R3-223379], it is proposed to liaise to RAN2 that RAN3 will keep the MRB ID value range on NG-RAN network interfaces 32 as the proposal from RAN2 doesn’t provided the aimed 1:1 mapping between MRB IDs used on NG-RAN interfaces and MRB IDs used on RRC and leave it up to RAN2 to consider further changes.

As we in RAN3 should respect the agreement/outcome achieved by other working groups, it is proposed to update the MRB ID range as RAN2 agreed.

Proposal: update the MRB ID from INTEGER (1.. 32, ...) to INTEGER (1.. 512, ...) in F1AP, E1AP, XnAP specifications.

| Company | Agree/Disagree | Comment |
| --- | --- | --- |
| Huawei | Agree |  |
| Nokia | Agree |  |
| CATT | Agree |  |
| Samsung | Agree |  |
| Ericsson |  | Not sure RAN2 really understood the aim of network-wide uniqueness of an MRB ID, which can only be achieved by associating the MRB ID with the Session ID. Even if we reduce the scope of the MRB ID to a cell or a DU, there is still the chance that you have to put quite some effort to achieve uniqueness given the potential multitude of concurrent active session. Also the effort of re-arranging MRB IDs with UE specific signaling plays again into one of our main concerns throughout Rel-17 MBS discussions: avoid UE dedicated signaling, where possible, by all means. This is really our main concern. We have two approaches at hand: a) RAN2 reverts its decision (RRC would only need to be changed in a way that the MRB Release is associated with the Session ID, all other procedures already include the TMGI and allow such association) b) whatever the MRB ID range is finally decided, we go for the Huawei approach: we define a "network" MRB ID and a "UE" MRB ID, and have to provide the mapping in UE signaling on F1 and I guess we need to clarify the nature of the MRB ID at indicated at inter-gNB HO (NG/Xn) (don’t think a mapping is necessary if we clarify that the MRB ID is the one communicated to the UE via RRC). But also in this case, there is no need to extend the range, neither in RRC nor in network signaling. This could be indicated to RAN2. |
| CMCC | Agree |  |
| Lenovo | Agree |  |
| ZTE | disagree | TMGI together with 1-32 will be sufficient. this is related to the next question. |
| Qualcomm | OK |  |

It is considered in [R3-223074] about per MBS session MRB ID or per UE MRB ID design, based on the feedback from RAN2 there is no per MBS Session MRB ID, the per UE MRB ID is extended to 512, but, once the MBS services increasing, e.g. more than 512 MBS sessions within a cell or a DU, even if the gNB configures only one MRB for one MBS session, the MRB ID still not able to be configured in a per cell or per DU granularity.

From RAN3 point of view, in order to have a unified per MBS session MRB ID in the non UE associated F1/E1 signalling, it is needed for the gNB-CU-CP to assign a “unified per MBS session MRB ID” to be used as the reference over F1 and E1 non UE associated MBS ignaling, note that this “unified per MBS Session MRB ID” is only applicable over F1 and E1 interfaces, and the mapping relationship between the “per UE MRB ID” and the “unified per MBS session MRB ID” will be informed to the gNB-DU.

We would like to highlight that with this “unified per MBS Session MRB ID”, there will be no need for RAN2 to introduce MRB ID modification related procedure.

Proposal: Besides per UE MRB ID, the gNB-CU-CP assigns {unified per MBS Session MRB ID} to be used as the reference over F1AP and E1AP non-UE associated MBS ignaling.

| Company | Agree/Disagree | Comment |
| --- | --- | --- |
| Huawei | Strongly recommended | This is quite helpful for the network, and will only impact F1AP E1AP specification, no impact to UE. In case RAN3 adopt this solution, RAN2 does not need to consider/discuss the MRB ID modification which is quite complex. |
| Nokia | NOK | Not needed. |
| CATT | No | In our understanding the MRB ID used in RAN is already a “unified” one. No need to add an extra. |
| Samsung | No |  |
| Ericsson | agree with the concerns from Huawei | see also above. and if we would be allowed to put something on our wish-list, an RRC solution would be really preferred. The cost for it is not tremendous. |
| Lenovo | No | If 512 is not sufficient, we can define a large number such as 2048. RAN2 already agreed MRB ID modification which is not complex if we see the proposals to update the RRC CR. |
| ZTE |  | why not a unified solution for both Uu and F1AP. |
| Qualcomm | No | If MRB-ID space is extended, we can use same MRB-ID in both UE associated and non-UE associated signaling. |

### MRB context from CU to DU

In last meeting, the following agreements was achieved:

- F1/E1 MC MBS Session resource control in MBS-associated procedures only (revisit if RAN2 prohibit RAN3 to do so), UE specific MBS configuration is transferred via UE associated procedures.

As RAN2 decided to not support the Common lower layer configuration, the only way RAN3 can use is the per UE lower layer configuration, therefore, it is straight forward to reuse the existing F1AP UE Context Management messages to support Multicast Bearer Management.

In [R3-223304], it is considered that according to RAN2’s agreements and as specified in TS 38.300, the MRB type includes split MRB, PTP only MRB and PTM only MRB:

-	For a multicast session, gNB provides one or more of the following multicast MRB configuration(s) to the UE via dedicated RRC signalling:

-	Multicast MRB with  DL only RLC-UM or bidirectional RLC-UM configuration for PTP transmission;

-	Multicast MRB with RLC-AM entity configuration for PTP transmission;

-	Multicast MRB with DL only RLC-UM entity for PTM transmission;

-	Multicast MRB with two RLC-UM entities, one DL only RLC-UM entity for PTP transmission and the other DL only RLC-UM entity for PTM transmission;

-	Multicast MRB with three RLC-UM entities, one DL RLC-UM entity and one UL RLC-UM entity for PTP transmission and the other DL only RLC-UM entity for PTM transmission;

-	Multicast MRB with two RLC entities, one RLC-AM entity for PTP transmission and the other DL only RLC-UM entity for PTM transmission.

-	For a multicast session, gNB may change the MRB type using RRC signalling.

Since the MRB type is configured by RRC ignaling, it is straight forwards that the gNB-CU makes the decision. When gNB-CU decides to change the MRB bearer type, the gNB-CU needs to indicate the requested MRB bearer type to the gNB-DU so that the gNB-DU can provide corresponding L2/L1 configuration parameters. Since the MRB type configuration is per UE basis, the gNB-CU needs to indicate the requested MRB bearer type to the gNB-DU in UE associated ignaling i.e. UE Context Management related messages.

Similar view can be found also in [R3-223074/75], and besides the MRB Type, it is further proposed to provide MRB ID, RLC mode of PTP leg in the existing F1APUE Context Management related messages.

Proposal: Introduce MRB related context in existing F1AP: UE Context Management related messages:

- MRB ID

- MRB Type (PTP only MRB, PTM only MRB, or split MRB)

- RLC mode of the PTP leg

Do you agree with the Proposal? Any comment?

| Company | Agree/Disagree | Comment |
| --- | --- | --- |
| Huawei | Agree all |  |
| Nokia | Agree all |  |
| CATT | Agree all |  |
| Samsung | Agree all |  |
| Ericsson | no agreement for b) c), but a bit of a) may be necessary | We would like to know why the proponent of the above solution so easily throw away Rel-15 architectural principles, architectural principles we subscribed to keep for MBS, where lower layer configuration and decisions are a function of the DU. If we go for the Huawei proposal, because RAN2 did not change their mind in terms of associating MRB IDs with the Session ID, there will be the need of some MRB ID mapping information on F1 and probably other interfaces (i.e., a) in same way needs to be provided), but b) and c) is against the NG-RAN (internal) architecture and functional split and not agreeable from a basic principle point of view. |
| LGE | Agree all |  |
| CMCC | Agree all |  |
| Lenovo | Agree all |  |
| ZTE |  | one alternative would be to enhance the MBS Multicast F1-U Context Descriptor to include the RLC mode /bearer type info for each concerned UE. Huawei: this alternative does not work, as this Descriptor IE is generated by the DU, how can the DU generate it without the above information from CU? |
| Qualcomm | Agree all |  |

### F1-U tunnel related

In [R3-223304], it is considered that, for the shared F1-U tunnels setup, using the MBS service associated signalling MULTICAST DISTRIBUTION SETUP REQUEST message is a good method. However, for the per PTP MRB, the method is inefficient, because for each PTP MRB and PTP retransmission per UE, the gNB-DU needs initialize an MBS service associated Multicast Distribution Setup procedure in both F1AP and E1AP, which is inefficient and unnecessary.

As RAN2 decided not to support the Common RRC signalling, the only way RAN3 can use is the per UE lower layer configuration, therefore, it is straight forward to reuse the existing F1AP UE Context Management messages for MRB management. Taking this into account, it is also beneficial to reuse the F1AP UE Context Management and E1AP Bearer Context Management related messages for providing the PTP only F1-U tunnel.

For retransmission PTP F1-U tunnel, the gNB-DU has no idea that whether it is needed or not. It is not reasonable that the gNB-DU decides to trigger the PTP retransmission F1 tunnel establishment. One way is the gNB-CU provides an indication to request the PTP retransmission F1 tunnel e.g. when receives the PDCP SR from UE after handover. Another solution is the PTP retransmission F1 tunnel can always been provided by the UE associated signalling i.e., UE Context/Bearer Management related messages.

Proposals:

- Reuse the UE associated signalling i.e., UE Context/Bearer Management related messages for providing the PTP only F1-U tunnel.

- RAN3 to discuss how to decide PTP retransmission F1 tunnel establishment:

Option 1: gNB-CU provides an indication to request the PTP retransmission F1 tunnel e.g. when receives the PDCP SR from UE after handover;

Option 2: the gNB-DU provides the PTP retransmission F1 tunnel info by default in the UE associated signalling i.e., UE Context Management related messages

Do you agree with the Proposals? Any comment?

| Company | Agree/Disagree | Comment |
| --- | --- | --- |
| Huawei | Agree a) Agree b option1) | For b, option 1 is more efficient on the consumption of backhaul resources. |
| Nokia | Agree a) Agree b option 1) | Default option is not clear. |
| CATT | Agree a) Neutral on b) |  |
| Samsung | Agree a) Agree b option 1) | If the proposals are agreed, the MBS Multicast F1-U Context Descriptor in the F1- MULTICAST DISTRIBUTION SETUP REQUEST should be modified. i.e. This descriptor can not be set for ptp retransmission, or ptp-only MRB. |
| Ericsson |  | We don’t share the argument of inefficiency and non-necessity. 1) Using UE associate signaling would mean that the UE context has knowledge about the MBS Session Resources and knows how to contact CU UP resources (independent from whether E1 is implemented). Currently the “link” to those MBS UP resources is provide via the DU which is responsible for F1-U MBS bearer establishment. we would like to keep this principle, also for the special case of re-transmission ptp MBS F1-U bearers. 2) (comment to option b1) the ptp retransmission F1-U bearer needs to be established at HO preparation (i.e. before the SR is received). 3) don’t understand the meaning of the term "default" in b2 either 4) a possible solution, to comply with existing principles outlined in 1) would be to indicate at F1 UE Context Establishment the need for a ptp retransmission F1-U bearer. This would keep the DU in the role of controlling F1-U bearers by means of the MC Distribution procedures. 5) releasing the F1-U bearers could be done based on timer. if you don’t like it, let's discuss to allow the CU(-UP) to send some "end info" inband. |
| LGE | Agree a) Agree b option 1) | Similar comment as Nokia. |
| CMCC | Agree a) Agree b option1) |  |
| Lenovo | Agree a) Agree b option1) | In b option 2, the term ‘default’ means that the ptp retransmission F1-U tunnel is always established regardless whether there is ptp retransmission. |
| ZTE | agree with b) option 1) |  |
| Qualcomm | Agree a) OK with b1) | In b option 2, resource cost is not a problem. Keeping a tunnel without data transmission just cost memory. Option 1 introduces extra delay. I am fine to follow majority. |

### E1AP: Initial value of HFN and reference SN

In order to avoid PDCP HFN desynchronization, RAN2 agreed that a reference SN together with the initial value of HFN can be configured by the gNB by RRC. In [R3-223302], it is proposed that the gNB-CU-UP needs to provide the initial value of HFN and reference SN of an MRB to the gNB-CU-CP for RRC configuration. And to achieve this, provide the detail solution over E1AP:

Proposals:

- The gNB-CU-UP provides the initial HFN and reference SN of an MRB in the MC BEARER CONTEXT SETUP RESPONSE message.

- The gNB-CU-CP can trigger a MC Bearer Context Modification procedure to request the initial HFN and reference SN of an MRB. The gNB-CU-UP sends the initial HFN and reference SN in the MC BEARER CONTEXT MODIFICATION RESPONSE message.

Do you agree with above Proposals? Any comment?

| Company | Agree/Disagree | Comment |
| --- | --- | --- |
| Huawei | Agree a) and b) | Support gNB-CU-CP needs to get the initial value of HFN and reference SN, although there will be latency for the gNB-CU-CP to configure MRB until the CU-UP receive the first packet during the multicast session establishment. |
| Nokia | Partly Agree | Agree to send a reference HFN and SN values. However, the exact interpretation of those is pending RAN2 decision on how to handle this initial value (i.e. in connection with the issue of the negative RXlev). |
| CATT | Both agree |  |
| Samsung | Agree | But from CP, UP point of view, it is not initial value. Therefore, IE name could be general. E.g. remove the “initial”. |
| Ericsson |  | would be interested on the (final) outcome of RAN2 decisions as well. We understand that the scenario is like UE is the first to enter the gNB and the NG-U is not yet setup at HO execution. |
| LGE | Agree a) and b) |  |
| CMCC | Both agree |  |
| Lenovo | Agree both | Anyway the initial value HFN and ref SN is needed from signaling point of view. How to interpret it is pure UE issue and no impact on RAN3 spec. |
| ZTE | Partly Agree | UP might get the multicast data later, therefore UP might be able to provide the initial HFN and reference SN in a MC Bearer Context Modification (gNB-CU-UP initiated) too. |
| Qualcomm | Agree both |  |

### User Inactivity Monitoring and Reporting for Multicast

In [R3-223300], it is pointed that a cause value ‘user inactive’ in NG interface is used to indicate the request of release of NG interface is due to user inactivity on all PDU sessions. So, the multicast session should also be considered when setting the cause value ‘user inactivity’, as follows:

Proposal: include multicast sessions for setting the cause value ‘user inactivity’ in NGAP?

| Company | Agree/Disagree | Comment |
| --- | --- | --- |
| Huawei | No strong view | For multicast, there is Session activation and deactivation procedures over NGAP, therefore may be not essential to have this solution. |
| Nokia | NOK | The inactivity of MBS sessions is managed through the Session Activate/deactivate. No relation with this traffic detection. |
| CATT | Slightly prefer no |  |
| Samsung | OK |  |
| Ericsson | not ok | we should not require to change PDU Session related activity related functions for MBS. |
| LGE | No strong view | Share the view with Huawei. |
| CMCC | NOK | Session Activation/Deactivation is irrelevant to user activity. |
| Lenovo | OK | Not strong position. |
| ZTE | No strong view | Same view with HW. |
| Qualcomm | NOK | The MBS inactivity is monitored by 5GC. Session deactivation is invoked by 5GC in case of inactivity. |

In current E1AP specification, the gNB-CU-CP may send BEARER CONTEXT SETUP REQUEST message with UE/PDU session/DRB level inactivity timer. The gNB-CU-UP sends BEARER CONTEXT INACTIVITY NOTIFICATION message with inactivity monitoring results. The gNB-CU-CP may determine that the UE should enter RRC-inactive (e.g., after receiving Bearer Context Inactivity Notification procedure).

In current F1AP specification, if the Inactivity Monitoring Request IE is contained in the UE CONTEXT MODIFICATION REQUEST message, gNB-DU may consider that the gNB-CU has requested the gNB-DU to perform UE inactivity monitoring. The gNB-DU provides per DRB activity results to the gNB-CU in the UE INACTIVITY NOTIFICATION message.

In [R3-223300], it is proposed that for multicast sessions or multicast MRBs there are two ways to support multicast inactivity notification over E1AP and F1AP:

- Solution 1: Reusing the UE associated BEARER CONTEXT INACTIVITY NOTIFICATION(E1AP)/ UE INACTIVITY NOTIFICATION(F1AP) message for multicast inactivity notification.

- Solution 2: Introduce a new MBS associated MC BEARER CONTEXT INACTIVITY NOTIFICATION(E1AP)/ MULTICAST INACTIVITY NOTIFICATION(F1AP) message for multicast inactivity notification.

Question: which solution do you prefer for multicast inactivity notification over E1AP and F1AP?

| Company | Agree/Disagree | Comment |
| --- | --- | --- |
| Huawei | No strong view | Slightly support for solution1, since this procedure is to determine the RRC status for each UE. |
| Nokia | NOK | The inactivity of MBS sessions is managed through the Session Activate/deactivate. No relation with this traffic detection. |
| Samsung | No strong view |  |
| Ericsson | not ok | Solution 1 does not work in general, as the CU-UP serving MBS Sessions a UE has joined is not necessarily the same as the CU-UP serving PDU Sessions of that UE. Further, inactivity handling and assumptions for MBS Sessions are quite different from those for PDU Sessions: We do not agree to introduce functions for MBS Sessions with which you could e.g. release MBS Session radio resources, this should be only done at MBS Session Deactivation or in case of pre-emption/resource shortage. |
| LGE | No strong view |  |
| CMCC | No strong view |  |
| Lenovo | OK | No strong view. |
| ZTE | slightly prefer 1. | option 1 brings no spec impacts, i.e., reuse the per (associated) PDU session level monitoring/notification. |
| Qualcomm | NOK | Same reason as last question |

### Admission control failure case

In [R3-223533], two questions are mentioned to ask SA2:

- For Multicast session update failure and Multicast session activation failure cases, should the NG-RAN node trigger Distribution Release procedure to release NG-U resources for the failed MBS session or just wait for the signalling from 5GC?

- In case the NG-RAN node could not provide resources for active MBS service, should the NG-RAN node directly initiate a Distribution Release procedure to release the NG-U resources for the MBS service or initiate a new procedure to inform MB-SMF and wait for further signalling from 5GC?

The above question also applies to the case that NG-RAN node could not admit all QoS flows for one MBS session when it receives Distribution Setup Response which indicates the MBS session is ACTIVE.

Based on the LS [S2-2203049], this will not be specified in this release:

Based on the feedback from SA2, we may not need to consider this topic in this release.

Any view for this topic?

| Company | View | Comment |
| --- | --- | --- |
| Huawei | noted |  |
| Nokia | Noted. | Agree with Huawei. We disagree with proposed changes. |
| CATT | Clarification on this situation is needed | For activation failure and update failure, currently,it is not clear whether the release of NG-U and radio resources for multicast should be triggered by NG-RAN node or CN. We do not know how it works without specification on it. Furthermore, if the status of multicast is included in Distribute setup response message and the status is active, there is no way for the NG-RAN node to provide the activation result to CN,it should be fixed. |
| Samsung | noted | Agree with Huawei. |
| Ericsson | right | it seems, only Rel-18 will provide a good basis for implementation |
| LGE | Noted | Agree with Huawei. |
| CMCC | noted | Agree with Huawei. |
| Lenovo | Noted |  |
| ZTE | Noted | We also do not prefer to discuss this in this meeting. For #1, this can be further discussed by RAN3 in Rel-18. We prefer to avoid introducing new function in the last R17 meeting and try to complete this WI in time. For #2, we are fine for this one. But we think this topic shall be discussed by different scenarios and be contribution driven. In addition, similar reason mentioned in #1, this can also be discussed in Rel-18. |
| Qualcomm | Noted |  |

### S-NSSAI for a Multicast Session

In [R3-223379], it is proposed to:

- Include the S-NSSAI for the MC MBS Session within the Distribution Setup Response message (top message level) over NGAP.

- Include the S-NSSAI for the MC MBS Session within the MBS Session Information Source to Target List IE over NGAP.

- Include the S-NSSAI within the MBS Session Information List IE over XnAP.

Question: any view for these proposals?

| Company | View | Comment |
| --- | --- | --- |
| Huawei | Not needed | The S-NSSAI of a multicast session shall be the same with the associated PDU session, as in the non-MBS supporting node, the service will be provided via the associated PDU session. |
| Nokia | NOK | Agree with Huawei. This is clearly specified in TS 23.247 section 7.2.1.2: NOTE 1: The DNN and S-NSSAI are used to establish the PDU session which can carry the operations related to multicast session(s), i.e. session join/leave, and can be associated with multicast MBS session(s). |
| Samsung | Not needed | Agree with Huawei and Nokia. |
| Ericsson | this is ok | we do not see the general case specified in any normative or informative text in TS 23.247, therefore this info is really needed. |
| CMCC | NOK | Agree with Huawei and Nokia. |
| Lenovo | Nok | Agree with Huawei and Nokia. |
| ZTE | disagree | We share the same view with HW and Nokia. |
| Qualcomm | NOK | This proposal conflicts with SA2 decision. |

# Round1_CR Revision

## TS 38.300 CR Revision

### draftCR on PDU session without DRB establishment

| R3-223535 | Correction on NR MBS (Huawei, CBN, China Unicom, Nokia, Nokia Shanghai Bell) | draftCR |
| --- | --- | --- |

In [R3-223535], it is proposed that the NG-RAN establishes at least one DRB together with a PDU session in 38.300, but in case the PDU session only includes MBS related QoS flows, the MBS capable gNB will not setup DRB, only MRBs will be established, it is needed to update the 38.300 description to introduce exception for MBS only case to not establish DRB for the PDU session:

Section 12.1, update the 38.300 description to introduce exception for MBS only case to not establish DRB for the PDU session.

Section 16.10.2.1, update “MB QoS Flow” to “MBS QoS Flow”.

Section 16.10.5.1, update the procedure name to “Multicast Distribution Setup” to align with stage3.

Section 16.10.5.2, change the multicast session “start” to “activated”, as session start is not applicable for multicast.

Section 16.10.5.3.3, clarify that for NG HO, the SMF provides MBS Session IDs to the target gNB via NGAP HO Request, which is not the same way as Xn HO, i.e PDU session modify after HO.

Other editorial updates.

Question: any comments on the changes proposed in this draftCR?

| Company | Agree/Disagree | Comment |
| --- | --- | --- |
| Huawei | Agree |  |
| Nokia | NOK | Sorry for the misunderstanding on first change but there is at least one DRB for the UE. Other changes are ok. |
| CATT | OK |  |
| Samsung | Ok |  |
| Ericsson | not ok | there is at least one DRB per established PDU Session Resources. the proposed change is not compliant with that principle. |
| CMCC | Agree |  |
| Lenovo | NOK | Same view with Nokia and Ericsson. |
| ZTE | disagree | we dont see the case for one UE that is only consuming multicast services but without any DRB established. if needed we can check with SA2. in SA2 it is stated that there is always a default QoS flow for one PDU session. |

### draftCR on PDCP SN length sync

| R3-223604 | Correction on NR MBS mobility for 38300 (ZTE Corporation) | draftCR |
| --- | --- | --- |

The following change is proposed to section 16.10.5.1 in this paper: (note that the HO related part is up to MBS2 discussion)

Question: any comments on the above change proposed in this draftCR?

| Company | Agree/Disagree | Comment |
| --- | --- | --- |
| Huawei | Agree |  |
| Nokia | OK |  |
| CATT | Agree |  |
| Samsung | Ok |  |
| Ericsson | Not ok | I guess we should honestly look back in which context the sentence before the highlighted one was agreed. We propose to make this clear with the following approach: "For 5GC Shared MBS traffic delivery an MBS Session Resource comprises one or several MRBs. If minimisation of data loss is applied for a given MRB, synchronisation of allocation of PDCP SNs is applied by either or a combination of the following methods: - derivation of the PDCP SNs by means of a DL MBS QFI Sequence Number provided on NG-U; Synchronisation in terms of MBS QoS flow to MRB mapping among gNBs is achieved by means of network implementation. PDCP SN length of the corresponding MRB will be identical among gNBs by means of network implementation - deployment of a Shared NG-U Termination at NG-RAN, shared among gNBs, which comprises a common entity for assignment of PDCP SNs. " Huawei: Disagree with this new approach, as the previous agreement on the sync in terms of mapping covers both cases, not only the first bullets, that is also the reason why it was listed below two bullets. |
| CMCC | OK |  |
| Lenovo | OK | Ericsson ‘s proposal is also fine. |
| ZTE | agree | proponent. |

### draftCR on PDCP COUNT/SN

| R3-223452 | Correction of MBS Data Forwarding (Nokia, Nokia Shanghai Bell, Huawei) | draftCR |
| --- | --- | --- |

The following change is proposed to section 16.10.5.1 in this paper: (note that the HO related part is up to MBS2 discussion)

Question: any comments on the above change proposed in this draftCR?

| Company | Agree/Disagree | Comment |
| --- | --- | --- |
| Huawei | Agree |  |
| Nokia | OK |  |
| CATT | Agree |  |
| Ericsson | whatever |  |
| CMCC | Agree |  |
| Lenovo | Agree |  |
| ZTE | agree |  |

## TS 38.410 CR Revision

| R3-223073 | Correction on NR MBS for 38410 (Huawei, CBN, China Unicom) | CR0040r, TS 38.410 v17.0.0, Rel-17, Cat. F |
| --- | --- | --- |

- Add NG-RAN triggered release procedure for BC.

- Add the missed Multicast Session Update procedure in the list of NR MBS Session Management Procedures.

- Remove all the Editor’s notes.

- Update Figure 7.2-1 to be applicable for both PDU Session and MBS Session.

- Remove Figure 7.2-2.

Question: any comments on the changes proposed in this CR?

| Company | Agree/Disagree | Comment |
| --- | --- | --- |
| Huawei | Agree |  |
| Nokia | OK | Would be happy to cosign this one. |
| CATT | Agree |  |
| Ericsson | OK |  |
| LGE | OK |  |
| CMCC | OK |  |
| Lenovo | OK |  |
| ZTE | Agree | Happy to cosign this one. |

## TS 38.413 CR Revision

### CR on BC Session Release Require

On BC Session Release Require, there are three NGAP CRs submitted:

| R3-223072 | Introduction of RAN triggered Broadcast Session Release procedure (Huawei, CBN, China Unicom, Qualcomm Incorporated, Lenovo, Motorola Mobility) | CR0767r, TS 38.413 v17.0.0, Rel-17, Cat. F |
| --- | --- | --- |
| R3-223605 | Correction on NR MBS for 38413 (ZTE Corporation) | CR0837r, TS 38.413 v17.0.0, Rel-17, Cat. F |
| R3-223651 | CR to TS38.413 for introduction of broadcast session release required procedure (CMCC) | CR0843r, TS 38.413 v17.0.0, Rel-17, Cat. F |

Comparing with these NGAP CRs, considering of the CR quality and to share load, it is proposed to further proceed on [R3-223651].

Do you have any comments on [R3-223651] NGAP CR on BC Session Required?

| Company | Comments |
| --- | --- |
| Huawei | Message Type should be “ignore” in the tabular. |
| Nokia | OK |
| CATT | OK |
| Ericsson | OK, about the criticality we can discuss, but "reject" gives you the possibility to deduce the support of a procedure of the peer node. |
| LGE | OK |
| CMCC | OK, we only need to consider the criticality of message type. |
| Lenovo | OK |
| ZTE | Fine. |

### CR on User Inactivity for Multicast Session

On User Inactivity for Multicast Session, there is one NGAP CR submitted:

| R3-223301 | Correction on User Inactivity for Multicast Session (Lenovo) | CR0796r, TS 38.413 v17.0.0, Rel-17, Cat. F |
| --- | --- | --- |

Do you have any comments on [R3-223303] NGAP CR on User Inactivity?

| Company | Comments |
| --- | --- |
| Nokia | NOK. Disagre with this change. See comment before. |
| Samsung | We are fine to the NGAP CR. |
| Ericsson | not ok, see above |
| CMCC | Depend on the discussion above. |
| Lenovo | OK for sure. |
| ZTE | we come back to this after issue in 3.2.5 is done. |

## TS 38.420 CR Revision

| R3-223096 | Alignment with rel-17 changes in XnAP (Qualcomm Incorporated) | CR0028r, TS 38.420 v17.0.0, Rel-17, Cat. F |
| --- | --- | --- |

A new “MBS management support function” is added to the function list, with explanatory text.

It is proposed to add the function in section 5.2 in a way that aligns with section 6.2 (procedure list). This implies moving the numbering of other sections.

Question: any comments on the changes proposed in this CR?

| Company | Agree/Disagree | Comment |
| --- | --- | --- |
| Huawei | Agree | But why MBS has to use 5.2.11? It can be added as 5.2.13, to avoid impact to SDT and QMC sections. |
| Nokia | OK | Same comment as Huawei: should be placed at the end of section 5. Would be happy to cosign this one. |
| Samsung | OK |  |
| Ericsson |  | wasn’t that part of CB MBS2? |
| Lenovo | OK |  |
| ZTE | OK | would be happy to cosign. |

## TS 38.470 CR Revision

| R3-223076 | Corrections on NR MBS in 38470 (Huawei, CBN, Nokia, Nokia Shanghai Bell) | CR0088r, TS 38.470 v17.0.0, Rel-17, Cat. F |
| --- | --- | --- |

In section 4.3, clarify that F1 interface supports to manage radio bearers for MBS sessions;

In section 5.2.2, clarify that DU is responsible for the encoding of SIB20;

In section 5.2.3, clarify that the UE Context Management function also mange multicast MRBs for the UE.

In section 5.2.13, update the NR MBS function section to not only mention multicast group paging.

In section 6.1.13, clarify the different NR MBS related release procedures.

Question: any comments on the changes proposed in this CR?

| Company | Agree/Disagree | Comment |
| --- | --- | --- |
| Huawei | Agree |  |
| Nokia | OK |  |
| CATT | OK |  |
| Samsung | OK |  |
| Ericsson | partly ok | 5.2.3: UE context management function doesn’t "manage MRBs". The proposed wording is suggesting the wrong thing. A possible specification text could start with "This function is also used to manage a UE's configuration with multicast resources". And, what it seems, we have dropped over time during discussion, is the joining status of UEs as part of UE context, so it would be good to include this important information as well (CATT introduces it in R3-223532). 5.2.13: why "involved"? |
| LGE | OK |  |
| CMCC | OK |  |
| Lenovo | OK |  |
| ZTE | partly ok | 5.2.3 depends on the discussion result of 3.2.2. |

## TS 38.473 CR Revision

| R3-223075 | Corrections on NR MBS in F1AP (Huawei, CBN, Nokia, Nokia Shanghai Bell) | CR0865r, TS 38.473 v17.0.0, Rel-17, Cat. F |
| --- | --- | --- |

- Update the MRB ID from INTEGER (1.. 32, ...) to INTEGER (1.. 512, ...) in F1AP, E1AP, XnAP specifications.

- Introduce DL PDCP SN length IE in the MULTICAST CONTEXT SETUP/MODIFICATION REQUEST messages for each MRB.

- Remove the MBS CU to DU RRC Information IE in the MULTICAST CONTEXT SETUP/MODIFICATION REQUEST messages.

- Introduce Multicast MRB related information {MRB ID, MRB Type (PTP only MRB, PTM only MRB, or split MRB), and the RLC mode of the PTP leg} in exiting F1AP: UE Context Management related messages.

- In Section 9.2.14.7, add the missing MBS Service Area IE

- In Section 9.2.14.10, add the presence of the Multicast F1-U Context To Be Setup List IE as mandatory

- Remove the MBS Multicast F1-U Context Descriptor IE in the MULTICAST DISTRIBUTION SETUP RESPONSE, MULTICAST DISTRIBUTION SETUP FAILURE, MULTICAST DISTRIBUTION RELEASE COMMAND and MULTICAST DISTRIBUTION RELEASE COMPLETE messages.

- Update the procedural texts from “may include Supported MBS FSA ID List IE in the xxx message” to “may include Supported MBS FSA ID List IE in the Served Cell Information IE in the xxx message”.

- In Section 9.3.2.7, for location dependent case, move the MBS F1-U Information IE to the same level as MBS Area Session ID IE.

- In Section 9.2.14.11, move MRB F1-U TNL Info at CU IE to the same level of MRB ID IE.

- In Section 9.3.1.221, change the maximum value of the MBS Area Session ID IE to 65535.

- In Section 9.3.1.222 and 9.3.1.223, remove Editor’s Note about the values. And change the value of maxnoofMBSServiceAreaInformation from 512 to 256 to align with NGAP specification.

- Include SIB20 in the gNB-DU System Information IE.

Do you have any comments on [R3-223075] F1AP CR?

| Company | Comments |
| --- | --- |
| Huawei | Support. Note: need to avoid overlapping part with the F1AP changes in MBS3, to be updated accordingly based on the discussion. |
| Nokia | OK except “change the value of maxnoofMBSServiceAreaInformation from 512 to 256 to align with NGAP specification” which should be covered in CB MBS#3. |
| CATT | Mostly agree, except the bullets overlap with CB#3. |
| Samsung | In general it is fine. But could further check the detail in the next round. |
| Ericsson | - MRB ID depends on the discussions above - what would the DU do with the PDCP SN length? - no need to introduce MRB mode and RLC mode in UE context signalling - F1-U MC context descriptor: long story: we definitely need a bearer context reference in all MC Distribution messages, otherwise the different instances of the MC Distribution procedures cannot be distinguished within the MBS associated signaling connection. But in our opinion, and we apologize for that mistake, the content of the Context Descriptor is partly wrong and partly unnecessary: What we need in that descriptor is just a "neutral" reference (e.g. 3bytes) and a reference to the "content" delivered in the F1-U bearer in case of location dependent services. That is all. This reference should/could be re-used on E1. But allocating a cell-specific reference would require changing the context descriptor in case of intra-DU/inter-cell mobility, which was simply a nasty failure on our side. So the context descriptor should be a sequence of a mandatory (e.g. 3byte) reference plus an optional MBS Areas Session ID. Addition: we should also discuss (see also further above) whether the CU-UP needs to know that a F1-U bearer is established for re-transmissions. probably there is a need for an additional indication. - we would strongly recommend to reconsider the size of lists, especially on F1 (where e.g. the argumentation that 8192 cells is way too much should be rather easy to follow/understand) |
| LGE | Share the view with Samsung. |
| CMCC | Share same view with Samsung. |
| Lenovo | Share same view with Samsung. |
| ZTE | we can come back to this after section 3 is done, as some stage 2 discussion is still on, e.g., - Introduce Multicast MRB related information {MRB ID, MRB Type (PTP only MRB, PTM only MRB, or split MRB), and the RLC mode of the PTP leg} in exiting F1AP: UE Context Management related messages. - Remove the MBS Multicast F1-U Context Descriptor IE in the MULTICAST DISTRIBUTION SETUP RESPONSE, MULTICAST DISTRIBUTION SETUP FAILURE, MULTICAST DISTRIBUTION RELEASE COMMAND and MULTICAST DISTRIBUTION RELEASE COMPLETE messages. |

## TS 38.460 CR Revision

| R3-223459 | Corrections on E1 bearer context management function for NR MBS (LG Electronics) | CR0058r, TS 38.460 v17.0.0, Rel-17, Cat. F |
| --- | --- | --- |

In section 5.1.x, all of Editor’s Notes are removed and the sentence related to header compression is added.

Question: any comments on the changes proposed in this CR?

| Company | Agree/Disagree | Comment |
| --- | --- | --- |
| Huawei | Agree | Note that in case it is agreed, E1AP update is needed, i.e. to provide the MRB header compression parameters from CP to UP. |
| Nokia | OK |  |
| CATT | Agree |  |
| Samsung | Ok |  |
| Ericsson |  | we would just remove the ENs, w/o additional text. |
| LGE | OK |  |
| CMCC | Agree |  |
| Lenovo | OK |  |
| ZTE | OK |  |

## TS 37.483 CR Revision

| R3-223303 | Correction on configuration of initial value of HFN and reference SN (Lenovo, Huawei) | CR0007r, TS 37.483 v17.0.0, Rel-17, Cat. F Move to 9.1.6.1.1 |
| --- | --- | --- |

Do you have any comments on [R3-223303] E1AP CR?

| Company | Comments |
| --- | --- |
| Nokia | Pending outcome of RAN2 discussions on initial HFN value. |
| CATT | Agree |
| Samsung | As commented before, from CP, UP point of view, it is not initial value. IE name could be general. E.g. remove the “initial”. |
| Ericsson | probably we have to wait for RAN2, but my assumption would have been that the scenarios would have been that the UE enters as the first one in a target gNB and the target doesn’t have means to deduce the COUNT value at HO execution yet and relies on forwarded data (at least this was what proponents of data forwarding claimed to be necessary). |
| Lenovo | It is not related to RAN2’s discussion anyway . |
| ZTE | pending on discussion of 3.2.4, we can wait. |

# References

| R3-223072 | Introduction of RAN triggered Broadcast Session Release procedure (Huawei, CBN, China Unicom, Qualcomm Incorporated, Lenovo, Motorola Mobility) | CR0767r, TS 38.413 v17.0.0, Rel-17, Cat. F |
| --- | --- | --- |
| R3-223073 | Correction on NR MBS for 38410 (Huawei, CBN, China Unicom) | CR0040r, TS 38.410 v17.0.0, Rel-17, Cat. F |
| R3-223074 | Correction on Multicast MRB Management and other F1AP aspects (Huawei, CBN) | discussion |
| R3-223075 | Corrections on NR MBS in F1AP (Huawei, CBN, Nokia, Nokia Shanghai Bell) | CR0865r, TS 38.473 v17.0.0, Rel-17, Cat. F |
| R3-223076 | Corrections on NR MBS in 38470 (Huawei, CBN, Nokia, Nokia Shanghai Bell) | CR0088r, TS 38.470 v17.0.0, Rel-17, Cat. F |
| R3-223096 | Alignment with rel-17 changes in XnAP (Qualcomm Incorporated) | CR0028r, TS 38.420 v17.0.0, Rel-17, Cat. F |
| R3-223282 | Discussion the editor’s notes related to consent (Samsung) | discussion |
| R3-223283 | Remove the editor’s notes related to consent information (Samsung) | CR0214r, TS 38.401 v17.0.0, Rel-17, Cat. F |
| R3-223284 | Remove the editor’s notes related to consent information (Samsung) | CR0006r, TS 37.483 v17.0.0, Rel-17, Cat. F |
| R3-223300 | User Inactivity Monitoring and Reporting for Multicast (Lenovo) | discussion |
| R3-223301 | Correction on User Inactivity for Multicast Session (Lenovo) | CR0796r, TS 38.413 v17.0.0, Rel-17, Cat. F |
| R3-223452 | Correction of MBS Data Forwarding (Nokia, Nokia Shanghai Bell, Huawei) | draftCR |
| R3-223459 | Corrections on E1 bearer context management function for NR MBS (LG Electronics) | CR0058r, TS 38.460 v17.0.0, Rel-17, Cat. F |
| R3-223533 | [Draft]LS on left-over issues on Rel-17 MBS (CATT) | LS out To: SA2 CC: |
| R3-223535 | Correction on NR MBS (Huawei, CBN, China Unicom, Nokia, Nokia Shanghai Bell) | draftCR |
| R3-223604 | Correction on NR MBS mobility for 38300 (ZTE Corporation) | draftCR |
| R3-223605 | Correction on NR MBS for 38413 (ZTE Corporation) | CR0837r, TS 38.413 v17.0.0, Rel-17, Cat. F |
| R3-223627 | Consent information exchange between E1 interface (Huawei) | discussion |
| R3-223628 | Correction on the FFS consent information (Huawei) | CR0226r, TS 38.401 v17.0.0, Rel-17, Cat. F |
| R3-223629 | Correction on the FFS consent information (Huawei) | CR0018r, TS 37.483 v17.0.0, Rel-17, Cat. F |
| R3-223650 | Remaining Issues for Stage2 details (CMCC) | discussion |
| R3-223651 | CR to TS38.413 for introduction of broadcast session release required procedure (CMCC) | CR0843r, TS 38.413 v17.0.0, Rel-17, Cat. F |
| R3-223379 | Rel-17 MBS Corrections (Ericsson) | Other Move to 9.1.6.1.1 |
| R3-223380 | MBS NGAP Corrections (Ericsson) | CR0801r, TS 38.413 v17.0.0, Rel-17, Cat. F Move to 9.1.6.1.1 |
| R3-223381 | MBS XnAP Corrections (Ericsson) | CR0807r, TS 38.423 v17.0.0, Rel-17, Cat. F Move to 9.1.6.1.1 |
| R3-223382 | MBS F1AP Corrections (Ericsson) | CR0909r, TS 38.473 v17.0.0, Rel-17, Cat. F Move to 9.1.6.1.1 |
| R3-223383 | MBS E1AP Corrections (Ericsson) | CR0009r, TS 37.483 v17.0.0, Rel-17, Cat. F Move to 9.1.6.1.1 |
| R3-223672 | Corrections to E1AP for NR MBS (ZTE) | CR0022r, TS 37.483 v17.0.0, Rel-17, Cat. F Move to 9.1.6.1.1 |
| R3-223077 | MBS Session Status during Xn HO preparation (Huawei, CBN, China Unicom, Lenovo, Motorola Mobility) | CR0773r, TS 38.423 v17.0.0, Rel-17, Cat. F Move to 9.1.6.1.1 |
| R3-223078 | MBS Session Status during NG HO preparation (Huawei, CBN, China Unicom, Lenovo, Motorola Mobility) | CR0768r, TS 38.413 v17.0.0, Rel-17, Cat. F Move to 9.1.6.1.1 |
| R3-223185 | Indication for inactive MBS session (NEC) | Discussion Move to 9.1.6.1.1 |
| R3-223187 | MBS Session Status indication in NGAP interface (NEC) | CR0789r, TS 38.413 v17.0.0, Rel-17, Cat. F Move to 9.1.6.1.1 |
| R3-223188 | MBS Session Status indication in Xn interface (NEC) | CR0787r, TS 38.423 v17.0.0, Rel-17, Cat. F Move to 9.1.6.1.1 |
| R3-223302 | Configuration of initial value of HFN and reference SN over E1AP (Lenovo, Huawei) | Discussion Move to 9.1.6.1.1 |
| R3-223303 | Correction on configuration of initial value of HFN and reference SN (Lenovo, Huawei) | CR0007r, TS 37.483 v17.0.0, Rel-17, Cat. F Move to 9.1.6.1.1 |
| R3-223304 | F1-U tunnels related issues (Lenovo) | Discussion Move to 9.1.6.1.1 |

# Comments

Already agreed in MBS2 discussion.