3GPP TSG-RAN WG3 #116-e							 R3-223688

9 - 19 May 2022

Online

Agenda Item:	9.1.7.1

Source:	ZTE (moderator)

Title:	Summary_of_offline_disc_CB # NTN2_IoToverNTN

Document for:	Approval

# Introduction

This contribution is to kick off the following discussion.

CB: # NTN2_IoToverNTN - Check incoming LSs - Remove LTE-M Satellite Indication? - Stage 2 alignment with NR NTN? Any additional clarification on NB-IoT UE? - Reply LS to RAN2 and SA2? - Capture agreements and approve the CRs if agreeable (ZTE - moderator) Summary of offline disc R3-223688

For the first round, we focus on the technical issues and try to reach some agreements. The deadline is Friday, May 13th, 07:00am UTC.

For the second round, we focus on the left issue in the first round, prepare the reply LS and clean up the CRs. The deadline is Wednesday, May 18th, 07:00am UTC.

# For the Chairman’s Notes

<TBD>

# Discussion - Second Round

<TBD>

# Discussion - First Round

## Issue 1: Incoming LS from RAN2 and SA2

The reply LS on open issues for IoT NTN from RAN2 and SA2 have been received in [1] and [2] respectively.

In [1], RAN2 confirms that LTE-M NTN capable UE indicates category M1 or M2 in its UE Radio capability and also IoT-NTN support as separate capability indication. While in [2], SA2 believes that there is no need to have a separate new indication (LTE-M Satellite Indication) in UE CAPABILITY INFO INDICATION message.

In addition, SA2 does not see any issue with providing coarse-grained location for UE using only CP CIoT EPS optimisation because MME has anyway the ability to trigger LCS procedure to retrieve a more fine grained location if needed.

Question 1: What’s your opinion on the potential impact on RAN3 based on the LS from RAN2 and SA2?

| Company | Comment |
| --- | --- |
| ZTE | To align with the agreement from SA2, the LTE-M Satellite Indication should be removed over S1. And RAN3 should reply the LS from RAN2 and SA2 to indicate RAN3’s decision. While, for the coarse-grained location for UE using only CP CIoT EPS optimisation issue, as there is no explicit impact on RAN3, the corresponding reply from RAN3 is not needed. |
| Nokia | Agree to remove the LTE-M Satellite Indication. For coarse-grained location for UE, there is no impact to RAN3. |
| Qualcomm | The only new element is the fact that SA2 has removed the LTE-M Satellite Indication (from the requirements on NGAP), and we should react to that. |
| Huawei | We simply remove the LTE-M satellite indication based on SA2’s LS. |
| CATT | Remove the LTE-M Satellite Indication. |
| Ericsson | Agree to remove the unnecessary LTE-M Satellite Indication IE. It also seems beneficial to reply as per our 3342. |
| Samsung | Agree to remove the LTE-M Satellite Indication. |

Moderator’s summary:

<TBD>

## Issue 2: Removal of LTE-M Satellite Indication

In [3], [7], [11] and [15], it is proposed to remove the LTE-M Satellite Indication over S1, and it seems to be a common understanding on the removal.

Question 2: Do you agree to remove the LTE-M Satellite Indication over S1?

| Company | Yes or No | Comment |
| --- | --- | --- |
| ZTE | Yes | As indicated by SA2, this indication over S1 is not needed anymore. |
| Nokia | Yes |  |
| Qualcomm | Yes | SA2 took a look at this and changed their requirements (our own stage 3 was based on the text that they have now changed) |
| Huawei | Yes |  |
| CATT | Yes |  |
| Ericsson | Yes | It’s good that SA2 rectified their stage 2 and corrected their mistake. Once we fix our spec, it will be aligned. |
| Samsung | Yes |  |

Moderator’s summary:

<TBD>

## Issue 3: Stage 2 alignment with NR NTN

In last RAN3#115-e meeting, some stage 2 correction has been introduced in NR NTN WI to clarify the issues related to UE location information, and the details are provided as below.

Agree Text proposal below for stg2 BL CR: “The gNB is responsible for constructing the Mapped Cell ID based on the UE location info received from the UE, if available.” And “The mapping between Cell Identities and geographical areas is configured in the RAN and Core Network. NOTE 2: A specific geographical location may be mapped to multiple Mapped Cell ID(s), and such Mapped Cell IDs may be configured to indicate differerent geographical areas (e.g. overlapping and/or with different dimensions). “

It is obvious that the similar stage 2 correction is beneficial to clarify the UE location info issues in IoT NTN. And these correction should be introduced in TS36.300. In [4], [10] and [14], the corresponding alignment has been introduced.

Question 3: Do you agree on the Stage 2 alignment with NR NTN?

| Company | Yes or No | Comment |
| --- | --- | --- |
| ZTE | Yes | IoT NTN should reuse the agreements in NR NTN, if reasonable. |
| Nokia | Yes |  |
| Qualcomm | Yes | This seems to apply also, so ideally the text can be mirrored |
| Huawei | Yes |  |
| CATT | Yes |  |
| Ericsson | Yes | [4] and [10] are agreeable; [14] is not – its cover page indicates that it is a CR to S1AP: it can’t be. |
| Samsung | Yes |  |

## Issue 4: Stage 2 Clarification on NB-IoT UEs

In [5] and [14], it is proposed to specify the different types of NB-IoT UEs, i.e., a NB-IoT UE that supports S1-U data transfer or User Plane CIoT EPS optimisation and a NB-IoT UE that only supports Control Plane CIoT EPS optimisation.

Question 4: Do you agree to introduce the Stage 2 clarification to support NB-IoT UEs?

| Company | Agree or Disagree | Comment |
| --- | --- | --- |
| ZTE | Neutral | The necessity should be further discussed. |
| Nokia | Agree | The Stage-2 clarification is not to introduce the different types of NB-IOT UEs, since these types of UEs are already captured in 36.300 Section 7.1. (so I updated the question) The Stage-2 clarification is to add the support for those NB-IOT UEs that can support AS security and can provide the UE location after AS security. |
| Qualcomm | Detail to be checked | The change in [5,14] introducing “if available” means potentially that it applies to all UEs (in some cases available sometimes, other cases never). Perhaps “if available” is enough without mentioning UE types. |
| Huawei | Agree | Agree with Nokia |
| CATT | Agree | We prefer specifying the type of UE if possible to avoid ambiguity, only using “if available” may cause different understanding for different person. |
| Ericsson | Agree in principle but CRs need revising | [5]: OK with most changes except moving the existing sentence “The mapping may be pre-configured…”, which should stay where it is. [14] seems to be a CR to S1AP, which can’t be. |
| Samsung | Agree |  |

Moderator’s summary:

<TBD>

## Issue 5: Tabular correction based on ASN.1

In [16], one CR to stage 2 BL CR is provided, i.e. full in the columns of “Criticality” and “Assigned Criticality” to align with the ASN.1.

Question 5: Do you agree with this CR?

| Company | Agree or Disagree | Comment |
| --- | --- | --- |
| ZTE | Agree | As “IE Extensions” for RAT-RestrictionsItem has been introduced in ASN.1, it is fine to full in the columns of “Criticality” and “Assigned Criticality” in IE tabular. |
| Nokia | Agree |  |
| Qualcomm | Agree | Yes, this is needed |
| Huawei | Agree |  |
| CATT | Agree |  |
| Ericsson | Agree |  |
| Samsung | Agree |  |

Moderator’s summary:

<TBD>

## Issue 6: Reply LS to RAN2 and SA2

In [8], [12] and [13], it is proposed that RAN3 should reply the LS to RAN2 and SA2 to indicate RAN3’s decision to remove the LTE-M Satellite Indication.

Question 6: In addition to the removal of LTE-M Satellite Indication, it there any other issue to be included in the reply LS to RAN2 and SA2?

| Company | Comment |
| --- | --- |
| ZTE | Only the removal of LTE-M Satellite Indication needs to be mentioned in the reply LS. |
| Nokia | Not needed. The SA2 LS is actually a reply LS to RAN3 LS which asked SA2 to confirm the LTE-M satellite Indication. Since this is a confirmation from SA2, there is no need to send another reply LS to tell SA2 “you are right”. 😊 |
| Qualcomm | Not clear that any reply is absolutely needed, even for LTE-M (unless we decided against the change). |
| Huawei | Don’t see strong need for reply LS. We only need to remove the LTE-M satellite indication as required. |
| CATT | Agree with ZTE, at least should send LS to RAN2 for clarify the modification of LTE-M Satellite Indication. Maybe we can send LS to RAN2 and CC SA2? |
| Ericsson | In their original LS, RAN2 said they assumed the UE would send its indication to the eNB so it could populate the LTE-M Satellite Indication, so it basically looked OK to them. Now that we are removing that IE from S1AP, it seems beneficial to notify RAN2 as a simple warning (as per our proposed text in [8]). |
| Samsung | Agree with Huawei and Nokia. |

Moderator’s summary:

<TBD>

## Issue 7: Any other aspect

Question 7: Please add any further aspects that are in scope and were not included in the above:

| Company | Comment |
| --- | --- |

Moderator’s summary:

<TBD>

# Conclusion, Recommendations [if needed]

If needed

# References

R3-223015  Reply LS on opens issues for NB-IoT and eMTC support for NTN  RAN2

R3-223030  Reply LS on opens issues for NB-IoT and eMTC support for NTN  SA2

R3-223098  Remove unnecessary LTE-M Satellite Indication  Qualcomm, Huawei

R3-223235  Correction to NTN-IoT  Huawei, Qualcomm, DT

R3-223255  Clarifications for NB-IOT UE  Nokia, Nokia Shanghai Bell, Huawei

R3-223340  LTE-M Capability Indication for NTN  Ericsson

R3-223341  Removing the unnecessary LTE-M satellite indication Ericsson

R3-223342  [DRAFT] Reply LS on open issues for NB-IoT and eMTC support for NTN  Ericsson

R3-223398  Left Issues on NB-IoT and eMTC Support for NTN  ZTE

R3-223399  Stage 2 Correction on NB-IoT and eMTC Support for NTN  ZTE

R3- 223400  Removal of LTE-M Satellite Indication over S1  ZTE

R3-223401  [DRAFT] Reply LS on open issues for NB-IoT and eMTC support for NTN  ZTE

R3-223614  Discussion on reply LS to RAN2 and SA2  CATT

R3-223616  Correction on stage2 for IoT over NTN   CATT

R3-223615  Correction on 36.413 for IoT over NTN  CATT

R3-223344  Correction to NTN tabular mistake  Huawei