3GPP TSG-RAN WG3 #116-e	R3-223679

E-Meeting, 9th – 19th May 2022

Agenda Item:	9.1.1.1

Source:	Ericsson (moderator)

Title:	SoD on NR-U corrections: CB# SONMDT3_NRU

Document for:	Approval

# Introduction

CB: # SONMDT3_NRU

- The Channel Occupancy Time Percentage, Energy Detection Threshold and NR-U ARFCN IEs lack clarity? Introduce Energy Detection Threshold UL over Xn, Channel occupancy time percentage UL, Radio Resource Status (per NR-U Channel) and Composite Available Capacity Group (per NR-U Channel) in F1AP/XnAP? (Ericsson, Deutsche Telekom, Qualcomm Incorporated)

- Update the value of maxnoofNR-UChannelIDs from 4 to 16? Channel Occupancy By Neighbour Cells is a good option to transmit the NR-U resource status of neighbour cells for NR-U? (Samsung)

- Capture agreements and provide CRs if agreeable, split the work if needed

(E/// - moderator)

Summary of offline discussion R3-223679.

# For the Chairman’s Notes

Propose the following:

R3-22xxxa, R3-20xxxc merged

R3-22xxxc rev [in xxxg] – agreed

R3-22xxxd rev [in xxxh] – agreed

R3-22xxxe rev [in xxxi] – agreed

R3-22xxxf rev [in xxxj] – endorsed

Propose to capture the following:

Agreement text…

Agreement text…

WA: carefully crafted text…

Issue 1: no consensus

Issue 2: issue is acknowledged; need to further check the impact on xxx. May be possible to address with a pure st2 change. To be continued…

# Discussion (1st round)

At RAN3-115e the following was captured:

RAN3 enables NR-U channel index for reporting NR-U load.

The solution is complete from RAN3 perspective. However, RAN3 will review the use of the NR-U Channel Index and the LBT reporting at the next meeting.

For this meeting, the presented proposals are grouped as follows:

- Clarifications on agreed IEs for NR-U:

  - Channel Occupancy Time Percentage (in [1], [2], [7])

  - Energy Detection Threshold (in [1], [2])

  - NR-U ARFCN IE (in [1], [2])

- Updated range for maxnoofNR-UChannelIDs (in [4])

- Addition of Channel Occupancy of Neighbor cells (in [4])

- Addition of NR-U Channel metrics in UL (in [3])

- Addition of NR-U Channel metrics in DL (in [3]).

## Clarifications on agreed IEs for NR-U

In [1] and [2] it is proposed to:

- rename “Channel Occupancy Time Percentage” as “Channel Occupancy Time Percentage DL” to clarify in the name that the IE refers to DL

- rename “Energy Detection Threshold” as “Energy Detection Threshold DL” to clarify in the name that the IE refers to DL

- update the semantic descriptions for “Channel Occupancy Time Percentage” and “Energy Detection Threshold” to indicate that the IEs refers to DL

- update the semantic description for “NR-U ARFCN” with references to tables in TS 38.101-1 containing allowed values for NR-U ARFCN.

In [1], [2], [7] is it proposed to:

- align the ASN.1 encoding of “Channel Occupancy Time Percentage” with the tabular, including the value 0 in the range of values.

Q1. Companies are invited to provide their preferences for the clarifications proposed in 1) – 5).

| Company | Comment |
| --- | --- |
| Ericsson | We agree to all the proposed clarifications. |
| Nokia | Adding ‘DL’ to channel occupancy is all right and logical (in both, the name and, possibly, in the semantics). However, in case of the detection threshold it will create issues: after all, the threshold detects energy received at the base station, so kind of “uplink” energy. I would leave it as is. Semantics can be formulated to explain it, but without indication what is uplink or downlink. Perhaps “ET at the node”? |
| ZTE | Fine with 3), 4) and 5). For 1) and 2), it is not necessary to rename the two IEs, and we prefer to keep the original name, changing the corresponding semantics description as given in 3) is enough. |

## Updated range for maxnoofNR-UChannelIDs

In [4] it is proposed to increase the value of maxnoofNR-UChannelIDs from 4 to 16 to uniquely identify one NR-U Channel ID (a chunk of 20 MHz) in the case of multiple bandwidths in one cell, with a maximum bandwidth of 320 MHz.

Q2. Companies are invited to indicate their preference w.r.t the proposal to update the range of maxnoofNR-UChannelIDs

| Company | Comment |
| --- | --- |
| Ericsson | We agree that in case of multiple bandwidth in one cell, using one NR-U Channel ID in a range 1..4 in the RESOURCE STATUS UPDATE message does not suffice to uniquely identify one chunk of 20 MHz. However, we would prefer to solve the issue using a different approach, which we think is cleaner and more future proof. That is, keep the current range for NR-U Channel ID as it is and instead add a NR-U Channel Bandwidth IE to the RESOURCE STATUS UPDATE message. |
| Nokia | neutral |
| ZTE | No strong view, the more future-proof way provided by Ericsson could be considered. |

## Addition of Channel Occupancy of Neighbor cells

In [4] it is proposed to transmit the Channel Occupancy (CO) of neighbor cells for NR-U. In moderator’s understanding, with the proposed addition, one node (Node 1) would obtain from a neighbor node (Node 2) the COs of Node 2’s neighbors (Node 3 and Node 4), where Node 3 and Node 4 do not have an Xn connection to Node 1.

Q3. Companies are invited to indicate their view w.r.t to adding Channel Occupancy of Neighbor cells as NR-U load metric (in DL).

| Company | Comment |
| --- | --- |
| Ericsson | The addition does not seem needed, and it can be misleading. We think that if a node (as Node 1 in [4]) has no Xn connection towards other nodes (Node 3 and Node 4 in [4]), it is expected that Node 3 and Node 4 are not neighboring Node 1, and Node1 will not trigger load balancing actions towards them. Given that Node 1 is not neighbouring Node 3 and Node 4, it is misleading to signal to Node 1 the CO of Node 3 and Node 4. Such occupancy may not affect Node 1 at all. Instead, a Node 2, with an Xn connection towards Node 1, Node 3 and Node 4 is likely a potential target for load balancing from Node 1. In a possible implementation, if Node 2 NR-U is affected by Node 3 and Node 4, Node 2 can report to Node 1 a CO value which takes into account the COs of Node 3 and Node 4. |
| Nokia | We do not quite understand the motivation, as explained in [4]… However, when checking the CRs, it seems that the neighbours’ CO is aggregated in a single percentage value. This may create a risk of multiple including the same information: Node 2 will signal it not only to Node 1, but also to Node 3, which will then include it in information sent to Node 2 etc – it will be a loop. So, we would prefer to have it discussed further as Rel.17 enhancement. |
| ZTE | Not needed. |

## Addition of NR-U metrics in UL

R3-223431 ([3]) proposes to add:

- Channel Occupancy (CO) time percentage UL, in F1AP and in XnAP,

- Energy Detection Threshold in UL in XnAP

as NR-U load metrics readily available at a gNB, to complement the agreed metrics in DL (“CO time percentage DL” and “EDT in DL”) to consider NR-U load in both directions when assessing potential targets for load balancing.

Q4. Companies are invited to provide their view concerning the proposed additions 1) and 2).

| Company | Comment |
| --- | --- |
| Ericsson | We support addition of 1) and 2). If the gNB-CU of a node could receive these metrics, it would be in a better position to judge how a UE handed over to the reporting node would be served by that node. In fact, unless the UE traffic is unidirectional in DL, there is always at least a portion of it in UL. Therefore, we think that knowledge of load metric in UL is important. Regarding the CO time percentage UL, this is known at DU (a DU is aware of NR-U channel usage in UL), while the EDT in UL is known at gNB-CU (which uses it to configure UE accordingly). The load balancing decisions are taken at the gNB-CU (of a neighbor node). To reach the gNB-CU of the neighbor node, the “CO time percentage UL” needs to be added as NR-U load metric both in F1AP and XnAP, while the only impact required for “EDT in UL” is in XnAP. |
| Nokia | But UL requires support from RAN2, which was not offered, right? Wasn’t it why we did not include it in the signalling at the last meeting? How this information can be obtained then? If it is indeed independent from UE input, we’re fine with the proposals – except of the naming for the ET: it would be better to call it “at UE”. |
| ZTE | We think only the NR-U metrics in DL are needed in Rel-17, the UL related metrics could be discussed in next release. |

## Addition of NR-U Channel metrics in DL

R3-223431 ([3]) proposes to add the following NR-U load metrics in F1AP and XnAP:

- Radio Resource Status per NR-U Channel

- Composite Available Capacity per NR-U Channel

For unlicensed cells with more than one NR-U channels, the reported load can be evaluated with the same granularity (NR-U Channel) with which a UE using NR-U can be served.

Q5. Companies are invited to provide their view concerning the proposed addition of 1) and 2).

| Company | Comment |
| --- | --- |
| Ericsson | We support addition of 1) and 2). With current reporting, a node receives the Radio Resource Status and the Composite Available Capacity for one cell. If one unlicensed cell contains more than one NR-U channels the “cell” level reporting provides an average of the resources across the NR-U Channels defined for the cell. The actual levels of resources for each one of the NR-U Channels defined in the cell can be quite different compared to the average “cell” level. And in our understanding, this is more and more likely as the number of NR-U Channel per cell increases. Unless we restrict the scenario for NR-U to cells with only one NR-U Channel, we think the proposed additions are needed to report the load situation according to the granularity requested by NR-U. |
| Nokia | No. This is has never been discussed in Rel.16, so it is not a correction, but an enhancement. We shall review the proposals properly for the current release. |
| ZTE | No, as mentioned by Nokia, these load metrics has not been discussed in Rel-17, they should be considered in next release, if needed. |

# Conclusion, Recommendations [if needed]

If needed

# References

- R3-223429 – Ericsson, Deutsche Telekom, Qualcomm Incorporated - F1AP corrections for NR-U

- R3-223430 – Ericsson, Deutsche Telekom, Qualcomm Incorporated - XnAP corrections for NR-U

- R3-223431 – Ericsson - Load metrics for NR-U

- R3-223561 – Samsung - Discussion on SON for NR-U

- R3-223562 – Samsung - Correction of SON for NR-U (CR0831r for 38.423)

- R3-223563 – Samsung - Correction of SON for NR-U (CR0944r for 38.473)

- R3-223312 – Lenovo - Correction on SON feature enhancements - XnAP

# Comments

Should be Rel-17?