3GPP TSG-RAN Meeting # 116-e	R3-22xxxx

# 9th – 19th May 2022

# online

Title:	Reply LS on PEI and UE Subgrouping

Response to:	R2-2204240/R3-223018

Release:	Rel-17

Work Item:	NR_UE_pow_sav_enh-Core

Source:	RAN3

To:	RAN2

Cc:	SA2, CT1

Contact Person:	chen jiajun

E-mail Address:	chen.jiajun1@zte.com.cn

1. Overall Description:

RAN3 thanks RAN2 for LS on the PEI and UE Subgrouping.

RAN3 would like to provide the following feedback for RAN2's questions.

Question 1: Whether the mismatched understanding about the ‘last used cell’ between UE and NW still exists in NR, if so, whether the LTE method (i.e. to introduce ‘no last cell update’ indication in RRCRelease Message) can be reused?

RAN3's answer: RAN3 thinks the mismatched understanding about the ‘last used cell’ between UE and NW also exists in NR. From RAN3 perspective, the mentioned LTE method can be reused for NR, However, it is up to RAN2. Furthermore, RAN3 agrees that "the PEI-capable gNB always reporting the last used cell information to AMF in the UE CONTEXT RELEASE COMPLETE message". The corresponding CR is attached.

Question 2: Whether this problematic scenario can be avoided or needs to be resolved through signaling?  (In this scenario, assuming that the anchor gNB does not support CN assigned subgrouping).

RAN3's answer: From RAN3 perspective, the problematic scenario can be avoided by implementation ,e.g., CN-assigned subgrouping support is uniform in a certain area e.g., RNA or TA. RAN3 has not a solution other than to assume deployment coordination. RAN3's understanding is that, RAN2 can decide whether a signaling-based solution is needed, as well as the exact solution.

2. Actions:

To RAN2 group.

ACTION: 	RAN3 kindly asks RAN2 to take the above information into consideration.

3. Date of Next RAN3 Meetings:

TSG RAN WG3 Meeting #117		22nd – 26th August 2022			Toulouse, FR

TSG RAN WG3 Meeting #117bis-e		10th – 18th Oct 2022			online