3GPP TSG-RAN Meeting # 116-e	R3-22xxxx

# 9th – 19th May 2022

# online

Title:	Reply LS on PEI and UE Subgrouping

Response to:	R2-2204240/R3-223018

Release:	Rel-17

Work Item:	NR_UE_pow_sav_enh-Core

Source:	RAN3

To:	RAN2

Cc:	SA2, CT1

Contact Person:	chen jiajun

E-mail Address:	chen.jiajun1@zte.com.cn

1. Overall Description:

RAN3 thanks RAN2 for their LS on the PEI and UE Subgrouping.

RAN3 would like to provide the following feedback for RAN2's questions.

Question 1: Whether the mismatched understanding about the ‘last used cell’ between UE and NW still exists in NR, if so, whether the LTE method (i.e. to introduce ‘no last cell update’ indication in RRCRelease Message) can be reused?

RAN3's answer: RAN3 thinks that the mismatched understanding about the ‘last used cell’ between UE and NW also exists in NR. From RAN3 perspective, the mentioned LTE method can be reused for NR, however, the final decision is up to RAN2. Furthermore, RAN3 agrees that "the PEI-capable gNB always report the last used cell information to AMF in the UE CONTEXT RELEASE COMPLETE message". The corresponding CR is attached.

Question 2: Whether this problematic scenario can be avoided or needs to be resolved through signaling?  (In this scenario, assuming that the anchor gNB does not support CN assigned subgrouping).

RAN3's answer: From RAN3 perspective, the problematic scenario can be avoided by implementation, e.g., CN-assigned subgrouping support is uniform in a certain area e.g., RNA or TAs. RAN3 has no solution other than to assume deployment coordination.

2. Actions:

To RAN2 group.

ACTION: 	RAN3 kindly asks RAN2 to take the above information into consideration.

3. Date of Next RAN3 Meetings:

The upcoming RAN3 meetings can be found in the RAN3 Meetings calendar