3GPP TSG-RAN WG3 #117-e	R3-224984

15 - 24 August 2022

Online

Agenda Item:	8.1

Source:	Nokia, Nokia Shanghai Bell - Moderator

Title:	Summary of Offline Discussion – CB#1 – Redcap PTW Length

Document for:	Approval

# Introduction

This is the summary document for the following come back:

CB: # 1_PTW_Length

- RAN3 updates the maximum PTW length of IDLE eDRX to 40.96 seconds or asks RAN WG2 to reconsider their decision?

- Provide CRs if agreeable

(Nok - moderator)

Summary of offline disc R3-224984

# For the Chairman’s Notes

Propose the following:

Agree:

R3-225091 (Nokia, NGAP CR revision of R3-224555).

R3-225109 (Huawei, XnAP CR revision of R3-224585).

R3-225108 (Ericsson, F1AP CR revision of R3-224812).

# Second Round

Q1: Please indicate if any remaining issue with R3-22xxxx (NGAP CR revision of 4555)?

| Company | Comment |
| --- | --- |

Q2: Please indicate if any remaining issue with R3-22xxxx (NGAP CR revision of 4585)?

| Company | Comment |
| --- | --- |

Q3: Please indicate if any remaining issue with R3-22xxxx (NGAP CR revision of 4812)?

| Company | Comment |
| --- | --- |

Moderator’s summary:

Majority of companies think …

Proposal 2: TP...

# First Round

RAN3 Specifications impacted

RAN2 has agreed at RAN2#117 the PTW length and granularity as follows:

- The maximum PTW length is 40.96s when IDLE eDRX cycle is longer than 10.24s.

- The minimum PTW length is 1.28s and the step length/granularity of PTW length is 1.28 when IDLE eDRX cycle is longer than 10.24s.

This is however not aligned with RAN3 specifications for the PTW length which is currently limited to 20.48s:

RAN2 therefore has sent an LS to RAN3 in R3-224211 to ask for alignment at this RAN3#117 meeting.

However, there is a misalignment on the maximum PTW length between RAN2 and RAN3/CT1 current specification. According to the current XnAP and F1AP singalling, the maximum length of NR Paging Time Window is defined as 20.48 seconds.

| IE/Group Name | Presence | Range | IE type and reference | Semantics description |
| --- | --- | --- | --- | --- |
| NR Paging eDRX Cycle Idle | M |  | ENUMERATED(hfquarter, hfhalf, hf1, hf2, hf4, hf8, hf16, hf32, hf64, hf128, hf256, hf512, hf1024, …) | TeDRX,CN defined in TS 38.304 [24]. Unit: [number of hyperframes]. |
| NR Paging Time Window | O |  | ENUMERATED(s1, s2, s3, s4, s5, s6, s7, s8, s9, s10, s11, s12, s13, s14, s15, s16, …) | Unit: [1.28 second]. |

Q1: do you agree that RAN3 should align their specifications to RAN2 decision?

| Company | Comment |
| --- | --- |
| Nokia | Yes. RAN2 is the group with the relevant competence. |
| Ericsson | Yes. Even though the LS is recent, the agreement/requirement was made by RAN2 a year ago (RAN2#115). It was RAN3/CT1 that failed to align in time their specifications |
| Huawei | Yes. Misalignment with RAN2 should be avoided |
| CATT | Yes |
| Qualcomm | No. We understand it is RAN2 to make final decision. PTW length of 20.48sec was carefully chosen to balance between UE power consumption and reliability. We do not think usage of long DRX values coupled with eDRX is beneficial for UE power consumption. CT1 is also discussing the same and they also do not have enough codepoints and their spec also frozen. We would like to better understand what motivation for longer PTW in RAN2 before implementing changes in various interfaces and send reply LS asking for additional info on motivation. |
| Deutsche Telekom | Yes. RAN3 should align with RAN2. |
| ZTE | Yes |
| Samsung | Yes |

The next question is which RAN3 specification(s) should be impacted.

RAN2 LS mentions XnAP and F1AP only.

Q2: do you agree that RAN2 decision impacts at least the NR Paging eDRX Information IE in XnAP and F1AP?

| Company | Comment |
| --- | --- |
| Nokia | Yes. As proposed in R3-224556/57. |
| Ericsson | Yes. As proposed in R3-224812/14. |
| Huawei | Yes. As proposed in R3-224585/86 or R3-224556/57 or R3-224812/14. The three sets of contributions are identical. |
| CATT | Yes |
| Deutsche Telekom | Yes |
| ZTE | Yes |
| Samsung | Yes |

Actually, the NR Paging eDRX Information IE value sent over Xn, F1 is sent from the CN. NG seems also impacted.

Therefore, it seems that the Paging Time Window length should be increased in all NG, Xn, F1 interfaces.

Q3: do you agree that RAN3 should also update the NR Paging eDRX Information IE in NGAP?

| Company | Comment |
| --- | --- |
| Nokia | Yes. As proposed in R3-224555. |
| Ericsson | Yes. As proposed in R3-224813. |
| Huawei | Yes. As proposed in R3-224584/555/4813, the three sets of contributions are identical |
| CATT | Yes |
| Deutsche Telekom | Yes |
| ZTE | Yes |
| Samsung | Yes |

Moderator’s summary:

All companies except one agree to proceed with the change. The moderator additionally thinks that it is better to have all specifications aligned. The company challenging this RAN2 agreement should explain the concern in RAN2 and once/if RAN2 reverse their decision, RAN3 will then reverse again to keep alignment with RAN2. This is the normal process.

Proposal 1: agree to align maximum PTW length to RAN2 decision at 40.96 seconds.

Which impact?

Different flavours are proposed for the change.

- Option 1: Tdocs (R3-224455/56/57) (R3-224584/85/86) and (R3-224812/13/14) propose to extend adding 16 values corresponding to PTW length ranging from 20.48s to 40.96s by steps of 1.28 second

s17,s18,s19,s20,s21,s22,s23,s24,s25,s26,s27,s28,s29,s30,s31,s32

- Option 2: Tdocs (R3-224721/22/23) propose to extend adding only the value 40.96 seconds.

- s32

Q4: which option do you think is aligned with RAN2?

| Company | Comment |
| --- | --- |
| Nokia | We support option 1. The RAN2 LS has the following hint: “and the step length/granularity of PTW length is 1.28 when IDLE eDRX cycle is longer than 10.24s”. |
| Ericsson | Option 1. Agree with the hint from Nokia, it should also align with CT1. |
| Huawei | Option 1. Agree the above |
| CATT | Option 1 |
| Deutsche Telekom | Option 1 as this is triggered by RAN2’s LS. |
| ZTE | Option 1 |
| Samsung | Option 1. Agree with Nokia |

Moderator’s summary:

All companies agree that RAN2 asked for a step of 1.28 second.

Proposal 2: agree to extend the PTW length with a step of 1.28 second.

LS out?

Some companies have proposed a reply LS to RAN2 just to inform and send the agreed CRs in case the answer to Q1 is “yes”:

- In 4592:

RAN3 thanks to RAN2 for the LS on the maximum PTW length of IDLE eDRX. RAN3 has discussed the issue raised by RAN2, and made the following agreements:

- The maximum PTW length for idle eDRX is updated to 40.96s with the 1.28s granularity.

The agreed CRs can be found in the attached documents.

- In 4724

RAN3 would like to inform RAN2 that RAN3 has approved R17 CRs for the misalignment on the maximum PTW length, and the maximum length of NR Paging Time Window in F1AP, XnAP and NGAP is updated to 40.96s.

Some other company has proposed a reply LS in case the answer to Q1 is “no”:

- In 4243

RAN3 asks RAN WG2 to reconsider their decision to set the maximum PTW length of IDLE eDRX to 40.96 seconds

In their incoming LS the actions from RAN2 to RAN3 were as follows:

- Actions

To RAN3/CT1 group:

ACTION: 	RAN2 respectfully asks RAN3/CT1 to consider the RAN2 agreements on maximum PTW length (as 40.96 seconds) and update the PTW length in their related protocols, and to provide feedback if needed.

So RAN2 is asking feedback “only if needed”.

We therefore need to evaluate this “need”. There are 3 possible options:

- Option 1: Send an LS back if answer to Q1 is “yes”

- Option 2: Send an LS back only if answer to Q1 is “no”

- Option 3: No LS back is needed, regardless answer to Q1 is “yes” or “no”.

Q5: what is your view for sending an LS back between these 3 options?

| Company | Comment |
| --- | --- |
| Nokia | Option 2. An LS back seems justified only if RAN3 would agree to challenge RAN2. |
| Ericsson | Option 2 – business as usual |
| Huawei | Option 1, but no strong view. |
| CATT | Option 2. Q1 is agreeable. We just update our spec. based on the RAN2’s agreement. A reply LS is not needed. |
| Qualcomm | Option 2 – we propose to send reply LS asking for details of motivation before implementing CRs. It is not about challenging or not challenging and is more about asking rationale for such change and re-evaluate need. |
| Deutsche Telekom | Option 2 - no need for a Reply LS. |
| ZTE | Option 1, but no strong view. |
| Samsung | Option 1, but no strong view. |

Moderator’s summary:

Given the answer to Q1 as “yes” we have 3 companies for sending the LS , and 4 companies against.

Proposal 3: no LS sent back.

# Conclusion

The following is proposed:

Proposal 4: it is proposed to merge the 3 CRs aligned with RAN2 view and agree the following CRs:

Agree:

R3-22xxxx (revision of 4555) adding “0” before CR number and Huawei/Ericsson cosign.

R3-22xxxx (revision of 4585) adding Nokia/Ericsson cosign

R3-22xxxx (revision of 4812) adding Nokia/Huawei cosign.

# References

- RP-172109, Revised Work Item on New Radio (NR) Access Technology, NTT DOCOMO, Inc.