## Slide 1: Requirements Information
Addition of IMSI_IMEI
R3-110929

## Slide 2
“The SAS does not receive information that identifies the UE involved in the procedure, nor can it derive the identity by any other existing means, and thus, the SAS cannot maintain any context between subsequent request for an UE.”
“Currently, the only crude way positioning requests/results can be correlated with the originating/targetted UEs is on time-scale. However, for driving-test scenario, and especially, under conditions of higher request rates, multiple UEs, network delays, and faster driving, this method based on time-scale becomes less and less accurate. “
1) Testing
2) Support for Hybrid LCS

## Slide 3: Overview of Emergency Service Compliance Testing

## Slide 4
General Requirements are laid out in FCC Office of Engineering and Technology (OET) Bulletin-71
Specifics delegated to Emergency Services Interconnect Forum (ESIF)
  End-to-end System Testing
    Done at System Turn-up
    Requires assistance of Public Safety Answering Point (PSAP)
      911/112 operators
  System Compliance/Maintenance Testing
    Biannual Performance Testing
    Automated Testing
      Uses UE based test eq (e.g. differential WAAS GPS, etc.)
      Compares ground truth from TEST EQ with location from SAS for accuracy
      This is what Requires IMSI_IMEI
Emergency Service
Compliance and Testing

## Slide 5
Emergency Service
Compliance and Testing
FCC Testing and Compliance Guidelines
Office of Engineering and Technology (OET)
Initial Testing Guidelines OET-Bulletin 71
  Establishes Network- and Handset-based Accuracy Requirements
    67% and 95% accuracy benchmarks
  Measures are based on Statistical Considerations
    A very high number of test calls are required for statistical validity (automated test setup)
  Details on Testing are left to ESIF
    Validation testing was proposed, “A biannual validation of accuracy should ordinarily be sufficient.”

## Slide 6
Compliance and Testing
ESIF Subcommittee G
Emergency Services Interconnect Forum (ESIF)
Membership
  NENA, APCO, Carriers, Individual PSAP organizations, Location Vendors
ESIF has been given the authority of developing test guidelines by the FCC
Specific Testing Guidelines for Carriers
Issue Paper 30 – “High Level Requirements for End-to-End Functional Testing”
Issue Paper 33 – “Maintenance Testing”
  Non end-to-end testing (no participation from PSAP)
  Results from SMLC (SAS) to be compared to benchmark from Test Equipment (at UE)

## Slide 7: ESIF suggested testing architecture (e.g. GSM Networks)
Testing is a comparison of location from these 2 points…requires IMSI_IMEI to accurately correlate test calls

## Slide 8: Status and Background on Hybrid LCS

## Slide 9: Hybrid-Technology references Responses to FCC FNPRM (FCC 10-177)
Wireless E911 Location Accuracy Requirements, Further Notice of Proposed Rulemaking and Notice of Inquiry, 75 FCC Rcd 67321 (2010) (“FNPRM” and “NOI”).
  The Commission seeks comment in the FNPRM on whether carriers can employ hybrid solutions to improve location accuracy
Association of Public-Safety Communications Officials-International, Inc. (“APCO”)
  World's largest organization of public safety communications professionals
  Oldest Public Safety Organization (established 1935)
  “We also believe that hybrid technology approaches need to be considered as no single technology appears (at least to date) to be ideal in all types of locations.”
Many Other Commenter's Support and/or Propose Hybrid Solutions
  Verizon Wireless
    Verizon Wireless has both a hybrid technology (handset and network location finding ability) and can operate in a hybrid
  also: Qualcomm, True Position, Polaris Wireless, etc.

## Slide 10: Hybrid-Technology references Responses to FCC FNPRM PS Docket No. 07-114; FCC 10-176
Sect.38 “…APCO, NENA, and … propose…the development of hybrid network--A-GPS technologies”
From Filed Comments “For example, we specifically ask about the use of hybrid technologies that employ both network-based and handset-based location solutions.”
Hybrid Location Technology Availability
Vendor Claims
Currently Developed and Available (this is not a “future” requirement):
  ALU, Qualcomm, True Position, Polaris Wireless, Thales Alenia, etc.

## Slide 11: Appendix B.2 of TS 36.305 (e.g. LTE Hybrid Architecture Example)
Hybrid LCS will require correlation between SAS and SPC (using IMSI_IMEI)
RNC
Iub
Iupc
SAS
UP (UE-Based)
CP (Network-Based)