## Slide 1: Draft summary of RAN3 discussion status concerning NR on the topics for joint session with SA2 and RAN2
NTT DOCOMO, INC.
3GPP TSG RAN WG2 meeting #92
Nanjing, China 23-27, May 2016
Agenda Item: 10.5
Document for: Discussion and decision
R3-161284

## Slide 2: Introduction
A joint session with SA2 and RAN2 will be held for NR / NextGen with the following agenda
  RAN-CN functions
  RAN-CN interconnection variant
  Slicing
This document provides the draft rapporteur’s summary of RAN3 discussion status on the above topics (with some suggestions from the rapporteur), to be provided to the joint session
The intention is to update this document taking into account RAN3 discussions before the joint meeting, and to provide the updated version to the joint session
  In case no agreement can be reached in RAN3 on an updated version for input to the joint session, it is suggested to fallback to this current version
1

## Slide 3: RAN-CN functions
RAN3 agreed to capture a list of NR RAN functions as follows
  Functions similar to E-UTRAN [TS 36.401] (see Table-1 below)
  Additional functions which may be supported (see Table-2 below)
  NOTE 1: The further detail of the functionalities needs further study
  NOTE 2: NR RAN refers to a RAN supporting NR. It may only consist of NR (standalone NR operation) or it may consist of NR and LTE (tight interworking) or it may consist of NR, LTE and WLAN (tight interworking).
Table-1: Functions similar to E-UTRAN [TS 36.401]
Transfer of user data
Radio channel ciphering and deciphering
Integrity protection
Header compression
Mobility control functions: Handover
Inter-cell interference coordination
Connection setup and release
Load balancing
Distributed function for NAS messages
NAS node selection function
Synchronization
Radio access network sharing
Paging
Positioning
Table-2: NR RAN may also include other functions | 
UE operational mode during periods of no traffic | For instance, upon reception of DL data, RAN could notify the UE
Network Slice support | This function provides the capability for NR RAN to support network slicing
Direct services support | This function provides communication whereby UEs can communicate with each other directly
Interworking with LTE | This function provides tight interaction (e.g. DC) between NR and LTE in non-standalone scenario
Multi-connectivity | This function provides means for connectivity between an NR node and multiple NR nodes
Interworking with non-3GPP systems | This function provides interworking betweeen NR and Non-3GPP RAT (e.g. WLAN)
Should we highlight those functions from the above requiring special attention during the joint session? (e.g. “UE operational mode during periods of no traffic”, “Network Slice support”)
2

## Slide 4: RAN-CN interconnection variant
RAN3 agreed to capture the following
  The following scenarios for connectivity between a RAN consisting of evolved LTE (eLTE) and NR and a CN consisting of a 5G CN and an (evolved) EPC should be considered in the discussions on RAN-CN interface definition for the 5G RAN.
  Whether the RAN-CN interfaces in the figures below consist of CP, UP or both it is FFS
Scenario C-1
Scenario C-2
Scenario C-3
Scenario C-4
Scenario C-5
Can we clarify the scenarios:
Clarify “eLTE eNB”
Show cases for standalone and tight interworking separately
Clarify CP/UP taking into account RAN2 email discussion
3

## Slide 5: Slicing
RAN3 agreed to capture the following key principles for support of Network Slicing in RAN
Key principle | Description (red text shows FFSes)
RAN awareness of slices | RAN shall support a differentiated handling of different network slices which have been pre-configured by the operator How RAN supports the slice enabling in terms of RAN functions (i.e. the set of network functions that comprise each slice) is implementation dependent It is still FFS if 3GPP will still additionally want to standardize a few basic slices and the network functions that comprise them (e.g. eMBB, MassiveMTC).
Network slice selection | RAN shall support the selection of the RAN part of the network slice by an index of ID provided by the UE which unambiguously identifies one of the pre-configured network slices in the PLMN How the UE gets this unambiguous index of ID is FFS and to be decided with SA2. The index or ID could be sent to the UE by the CN after the CN has selected the slice (e.g. similar to eDECOR feature) or it should be pre-configured in the UE. It is FFS how the RAN verifies that the UE is authorized to select the slice and when this verification happens It is FFS if the RAN may also select the slice based on specific resources accessed by the UE
Resource management between slices | RAN shall support policy enforcement between slices as per service level agreements How RAN handles the requirements coming from the service level agreements is to be discussed with SA2
Support of QoS | RAN shall support QoS differentiation within a slice It is FFS if RAN shall additionally support QoS enforcement independently per slice
RAN selection of CN entity (FFS) | RAN shall support initial selection of the CN entity for initial routing of uplink messages based on received slice index and a mapping in the RAN node (CN entity, slices supported) Need to discuss whether an NNSF-like function is needed that uses the slice index as input for initial selection of a CN entity that supports this slice
Resource isolation between slices (FFS) | RAN shall support resource isolation between slices Resource isolation needs to be clarified: It is unclear if resource isolation would imply that multiple slices cannot share control plane (respectively user plane) resources or processing resources in common. Its is unclear if resource isolation would imply that cryptographic means should be used to isolate CP and UP traffic between slices.
4