## Slide 1: Draft summary of RAN3 discussion status concerning NR on the topics for joint session with SA2 and RAN2
NTT DOCOMO, INC.
3GPP TSG RAN WG2 meeting #92
Nanjing, China 23-27, May 2016
Agenda Item: 10.5
Document for: Discussion and decision
R3-161455

## Slide 2: Introduction
A joint session with SA2 and RAN2 will be held for NR / NextGen with the following agenda
  RAN-CN functions
  RAN-CN interconnection variant
  Slicing
This document provides the draft rapporteur’s summary of RAN3 discussion status on the above topics, to be provided to the joint session
R3-161284 was updated to reflect RAN3 discussions during RAN3#92
1

## Slide 3: RAN-CN functions
RAN3 agreed to capture a list of NR RAN functions as follows
  Functions similar to E-UTRAN [TS 36.401] (see Table-1 in next slide)
  Additional functions that are agreed to be supported (see Table-2 in next slide)
  Additional functions which may be supported (see Table-3 in next slide)
  NOTE 1: The further detail of the functionalities needs further study
  NOTE 2: NR RAN refers to a RAN supporting NR. It may only consist of NR (standalone NR operation) or it may consist of NR and LTE (tight interworking) or it may consist of NR, LTE and WLAN (tight interworking).
2

## Slide 4: RAN-CN functions
Table-1: Functions similar to E-UTRAN [TS 36.401]
Transfer of user data
Radio channel ciphering and deciphering
Integrity protection
Header compression
Mobility control functions: Handover
Inter-cell interference coordination
Connection setup and release
Load balancing
Distributed function for NAS messages
NAS node selection function
Synchronization
Radio access network sharing
Paging
Positioning
Table-3: Additional functions which may be supported (red text shows coordination pt with SA2) | 
UE operational mode during periods of no traffic | For instance, upon reception of DL data, RAN could notify the UE
NR location area management | This function provides the capability for NR RAN to manage location areas. It is FFS whether location area management needs to be coordinated with LTE.
RAN3 needs response from RAN2 and SA2 on the above two functions (e.g. New state introduction? How many states?) in order to progress on RAN3 functions … like RAN paging, context fetch/mobility … | 
Direct services support | This function provides communication whereby UEs can communicate with each other directly
Interworking with non-3GPP systems | This function provides interworking betweeen NR and Non-3GPP RAT (e.g. WLAN)
LTE-NR handover through CN | This function provides means for LTE-NR handover via the CN.
2
Table-2: Additional functions that are agreed to be supported (red text shows coordination pt with SA2) | 
Network Slice support | This function provides the capability for NR RAN to support network slicing
Interworking with LTE | This function provides tight interaction (e.g. DC) between NR and LTE in non-standalone scenario
Multi-connectivity | This function provides means for connectivity between an NR node and multiple NR nodes
LTE-NR handover through LTE-NR interface | This function provides means for LTE-NR handover via the direct interface between LTE and NR.

## Slide 5: RAN-CN interconnection variant
RAN3 agreed to capture the following
  The following scenarios for connectivity between a RAN consisting of eLTE eNB and NR BS, and a CN consisting of a 5G CN and an (evolved) EPC should be considered in the discussions on RAN-CN interface definition for the 5G RAN.
  The eLTE eNB is the evolution of eNB that supports connectivity to EPC and NG-Core
3
Scenario1
Scenario2
Scenario3
Scenario4
Does SA2 see the connection of NR BS to EPC (i.e. Scenario 1&3) to be part of SA2 work?

## Slide 6: Slicing
RAN3 agreed to capture the following key principles for support of Network Slicing in RAN
Key principle | Description (red text shows FFSes)
RAN awareness of slices | RAN shall support a differentiated handling of different network slices which have been pre-configured by the operator How RAN supports the slice enabling in terms of RAN functions (i.e. the set of network functions that comprise each slice) is implementation dependent It is still FFS if 3GPP will still additionally want to standardize a few basic slices and the network functions that comprise them (e.g. eMBB, MassiveMTC).
Network slice selection | RAN shall support the selection of the RAN part of the network slice by an index of ID provided by the UE which unambiguously identifies one of the pre-configured network slices in the PLMN How the UE gets this unambiguous index of ID is FFS and to be decided with SA2. The index or ID could be sent to the UE by the CN after the CN has selected the slice (e.g. similar to eDECOR feature) or it should be pre-configured in the UE. It is FFS how the RAN verifies that the UE is authorized to select the slice and when this verification happens It is FFS if the RAN may also select the slice based on specific resources accessed by the UE
Resource management between slices | RAN shall support policy enforcement between slices as per service level agreements How RAN handles the requirements coming from the service level agreements is to be discussed with SA2
Support of QoS | RAN shall support QoS differentiation within a slice It is FFS if RAN shall additionally support QoS enforcement independently per slice
RAN selection of CN entity (FFS) | RAN shall support initial selection of the CN entity for initial routing of uplink messages based on received slice index and a mapping in the RAN node (CN entity, slices supported) Need to discuss whether an NNSF-like function is needed that uses the slice index as input for initial selection of a CN entity that supports this slice
Resource isolation between slices (FFS) | RAN shall support resource isolation between slices Resource isolation needs to be clarified: It is unclear if resource isolation would imply that multiple slices cannot share control plane (respectively user plane) resources or processing resources in common. Its is unclear if resource isolation would imply that cryptographic means should be used to isolate CP and UP traffic between slices.
4