3GPP TSG-RAN WG4 Meeting #100-e	R4-2115748

# Electronic Meeting, August 16th – 27th, 2021

Title: 	Way forward for FR1 PUSCH 256QAM performance requirements

Source: 	Huawei, HiSilicon

Agenda item:	9.12.3.1

Document for:	Approval

# Background

This way forward captures the agreements reached during RAN4#100-e meeting based on the discussions happened in previous meetings:

- R4-2106120 Way forward for PUSCH 256QAM performance requirements, Huawei, HiSilicon, RAN4#98bis-e

- R4-2108667 Way forward for PUSCH 256QAM performance requirements, Huawei, HiSilicon, RAN4#99-e

# Test parameters

- MCS

  - MCS 20

- Tx EVM: No explicit Tx EVM modelling

  - Option 1: Consider 3.5% Tx EVM impact in the impairment results submitted by companies.

  - Option 2: Not consider 3.5% Tx EVM impact (Ericsson)

- Propagation condition

  - TDLA30-10 Low

- SCS and Bandwidth combination

  - Option 1:

    - 15kHz SCS: 5MHz and 10MHz

    - 30kHz SCS: 10MHz and 40MHz

  - Option 2: (CMCC)

    - 15kHz SCS: 5MHz, 10MHz and 20MHz

    - 30kHz SCS: 10MHz, 20MHz, 40MHz and 100MHz.

# Simulation assumptions

| Parameter | Value |
| --- | --- |
| Transform precoding | Disabled |
| CP | Normal CP |
| Number of Tx | 1 |
| Number of Rx | 2, 4, 8 |
| Number of layers | 1 |
| TDD pattern | 15kHz SCS: 3D1S1U, S=10D:2G:2U 30kHz SCS: 7D1S2U, S=6D:4G:4U |
| DM-RS sequence generation | NID=0, nSCID=0 |
| DMRS type | Type 1 with single-symbol DM-RS |
| Number of DMRS symbols | 1+1 |
| Number of DM-RS CDM groups without data | 2 |
| Ratio of PUSCH EPRE to DM-RS EPRE | -3dB |
| symbols length | 14 |
| start symbol index | 0 |
| Time domain resource allocation type | type A and B |
| Frequency domain resource | Full applicable test bandwidth |
| MCS index | 20 |
| Carrier frequency (GHz) | 4 |
| Propagation condition | TDLA30-10 Low |
| SCS and BW | 15kHz: 5MHz, 10MHz; 30kHz: 10MHz, 40MHz |
| SRS, PT-RS | Not configured |
| Phase noise modelling | No explicit PN modelling (Note 1) |
| Tx EVM | No explicit 3.5% Tx EVM modelling (Note 2) |
| Timing offset, Frequency offset | 0, 0 |
| Code block group, Frequency hopping, Limited buffer rate matching | Disabled |
| Number of HARQ transmissions and RV sequence | 4, {0,2,3,1} |
| Testing metric | SNR @70% of maximum throughput |
| Note 1: The phase noise impact can be included in the impairment results, but it is left up to companies Note 2: Consider 3.5% Tx EVM impact in the impaired results, but it is left up to companies. |

# Reference

- R4-2115801  Email discussion summary for [100-e][329] NR_perf_enh2_Demod_Part3_NWM, RAN4#100-e, Moderator (Huawei)

- R4-2108698  Email discussion summary for [99-e][332] NR_perf_enh2_Demod_Part3_NWM, RAN4#99-e, Moderator (Huawei)

- R4-2106155  Email discussion summary for [98-bis-e][324] NR_perf_enh2_Demod_Part2_NWM, RAN4#98bis-e, Moderator (Huawei)