## Slide 1: 3GPP TSG-RAN WG4 Meeting #100-e Electronic Meeting, 16-27 Aug, 2021
Intel
WF on NR Positioning Performance Requirements
R4-2115307

## Slide 2
Agreements in the 1st round/GTW
open for 2nd round discussion
Still open after 1st round discussion
Agreements in the 2nd round

## Slide 3: Measurement Accuracy Requirements for RSTD(1)
Group delay calibration margin for the RSTD accuracy requirements is FFS
  Different values for the group delay calibration margin for the RSTD accuracy requirements can be defined depending on PRS parameters combination
    FR(frequency range)
    PRS BW (absolute BW)
    Number of PFLs and whether reference/neighbor cells belong to same PFL
  Companies are encouraged to bring analysis for dependency of margin on these parameters
The frequency drift margin in RSTD accuracy is FFS
  Frequency drift margin will be derived on the maximum time offsets between the two PRS resources instance from the reference cell and neighbor cells which will be used to a single RSTD measurement.
    The maximum time offset for margin definition can be FFS
  A single fixed margin will be used for requirements definition

## Slide 4: Measurement Accuracy Requirements for RSTD(2)
The requirements for the case of “FR1, PRS BW≥ [24], SCS=30kHz.” can be agreed as:
Table 1-1: RSTD accuracy for AWGN in FR1
Table 2-1: RSTD accuracy for fading channels in FR1
Accuracy, Tc+ | PRS BW, PRB | PRS SCS, kHz | Repetition factor (
[132 + margin] | ≥ [24] | 15 | ≥4
[98 + margin] | ≥ [52] |  | All
[42 + margin] | ≥ [104] |  | All
[75 + margin] | ≥ [24] | 30 | ≥4
[48 + margin] | ≥ [48] |  | All
[24 + margin] | ≥ [132] |  | All
[50 + margin] | ≥ [24] | 60 | ≥4
[24+ margin] | ≥ [64] |  | All
[10+ margin] | ≥ [132] |  | All
Note 1: Margin value is FFS |  |  | 
Accuracy, Tc+ | PRS BW, PRB | PRS SCS, kHz | 
[132 + margin] | ≥ [24] | 15 | ≥4
[98 + margin] | ≥ [52] |  | All
[42 + margin] | ≥ [104] |  | All
[75 + margin] | ≥ [24] | 30 | ≥4
[48 + margin] | ≥ [48] |  | All
[24 + margin] | ≥ [132] |  | All
[50 + margin] | ≥ [24] | 60 | ≥4
[24+ margin] | ≥ [64] |  | All
[10+ margin] | ≥ [132] |  | All
Note 1: Margin value is FFS |  |  | 
Accuracy, Tc | PRS BW, PRB | PRS SCS, kHz | Repetition factor (
[247 + margin] | ≥ [24] | 15 | ≥4
[140 + margin] | ≥ [52] |  | All
[86 + margin] | ≥ [104] |  | All
[118 + margin] | ≥ [24] | 30 | ≥4
[109 + margin] | ≥ [48] |  | All
[28 + margin] | ≥ [132] |  | All
[147 + margin] | ≥ [24] | 60 | ≥4
[27+ margin] | ≥ [64] |  | All
[21+ margin] | ≥ [132] |  | All
Note 1: Margin value is FFS Note 2: The requirements above are based on the simulation results under the TDL-A [TS38.101-4] |  |  | 
Accuracy, Tc | PRS BW, PRB | PRS SCS, kHz | 
[247 + margin] | ≥ [24] | 15 | ≥4
[140 + margin] | ≥ [52] |  | All
[86 + margin] | ≥ [104] |  | All
[118 + margin] | ≥ [24] | 30 | ≥4
[109 + margin] | ≥ [48] |  | All
[28 + margin] | ≥ [132] |  | All
[147 + margin] | ≥ [24] | 60 | ≥4
[27+ margin] | ≥ [64] |  | All
[21+ margin] | ≥ [132] |  | All
Note 1: Margin value is FFS Note 2: The requirements above are based on the simulation results under the TDL-A [TS38.101-4] |  |  | 

## Slide 5: Measurement Accuracy Requirements for PRS RSRP(1)
RSRP requirements under the extreme condition
  Option 1: FFS on the PRS RSRP measurement requirements in extreme condition are X dB larger than that in normal condition, and X is:
    3dB for absolute accuracy for FR1.
    3dB for absolute accuracy for FR2.
    1dB for relative accuracy for FR1.
    3dB for relative accuracy for FR2
  Option 2: No need to define PRS RSRP accuracy requirements with the extreme conditions
RF calibration margin for FR1 PRS RSRP relative accuracy requirements can be [2dB]

## Slide 6: Measurement Accuracy Requirements for UE Rx-Tx time difference(1)
Applicability of accuracy requirements under TA adjustment if the uplink transmission timing changes during the UE Rx-Tx measurement period due to autonomous adjustment :
  Option 2: UE Rx-Tx measurement accuracy requirements shall apply if the uplink transmission timing changes during the UE Rx-Tx measurement period due to autonomous adjustment
  Option 3:
    If SRS is transmitted on a cell where UE Rx-Tx measurement is performed then the UE Rx-Tx measurement accuracy requirements shall apply even if the uplink transmission timing changes during the UE Rx-Tx measurement period due to autonomous adjustment.
    If SRS is transmitted on a cell different than the cell where UE Rx-Tx measurement is performed then the UE Rx-Tx measurement accuracy requirements shall not apply if the uplink transmission timing changes during the UE Rx-Tx measurement period due to autonomous adjustment
  Option 4:
    UE Rx-Tx measurement accuracy requirements shall apply for a serving cell even if the uplink transmission timing changes during the UE Rx-Tx measurement period due to autonomous adjustment.
    the UE Rx-Tx measurement accuracy requirements shall not apply for a neighbor cell if the uplink transmission timing changes during the UE Rx-Tx measurement period due to autonomous adjustment

## Slide 7: Measurement Accuracy Requirements for UE Rx-Tx time difference(2)
Group delay calibration margin for the UE Rx-Tx time difference accuracy requirements is FFS
  Different values for the group delay calibration margin for the RSTD accuracy requirements can be defined depending on PRS parameters combination
    FR(frequency range)
    PRS BW (absolute BW)
    Number of PFLs and whether reference/neighbor cells belong to same PFL
  Companies are encouraged to bring analysis for dependency of margin on these parameters

## Slide 8: Measurement Accuracy Requirements for UE Rx-Tx time difference(3)
The requirements for the case of “FR1, PRS BW≥ [24], SCS=30kHz.” can be agreed as:
Table 1-1: UE Rx-Tx accuracy for AWGN in FR1
Accuracy, Tc | Es/Iot, dB | PRS BW, PRB | PRS SCS, kHz | Repetition factor (
[78+margin] | -3 | ≥[24] | 15 | ≥4
[59 +margin] |  | ≥[52] |  | All
[30 +margin] |  | >[104] |  | All
[57margin] |  | ≥[24] | 30 | ≥4
[30 +margin] |  | ≥[48] |  | All
[15 +margin] |  | ≥[132] |  | All
[29 +margin] |  | ≥[24] | 60 | ≥4
[15 +margin] |  | ≥[64] |  | All
[7+margin] |  | ≥[132] |  | All
[101 +margin] | -13 | ≥[24] | 15 | ≥4
[75 +margin] |  | ≥[52] |  | All
[39+margin] |  | >[104] |  | All
[58 +margin] |  | ≥[24] | 30 | ≥4
[37+margin] |  | ≥[48] |  | All
[16 +margin] |  | ≥[132] |  | All
[36 +margin] |  | ≥[24] | 60 | ≥4
[16+margin] |  | ≥[64] |  | All
[8 +margin] |  | ≥[132] |  | All
Note 1: Margin value is FFS |  |  |  | 
Accuracy, Tc | Es/Iot, dB | PRS BW, PRB | PRS SCS, kHz | 
[78+margin] | -3 | ≥[24] | 15 | ≥4
[59 +margin] |  | ≥[52] |  | All
[30 +margin] |  | >[104] |  | All
[57margin] |  | ≥[24] | 30 | ≥4
[30 +margin] |  | ≥[48] |  | All
[15 +margin] |  | ≥[132] |  | All
[29 +margin] |  | ≥[24] | 60 | ≥4
[15 +margin] |  | ≥[64] |  | All
[7+margin] |  | ≥[132] |  | All
[101 +margin] | -13 | ≥[24] | 15 | ≥4
[75 +margin] |  | ≥[52] |  | All
[39+margin] |  | >[104] |  | All
[58 +margin] |  | ≥[24] | 30 | ≥4
[37+margin] |  | ≥[48] |  | All
[16 +margin] |  | ≥[132] |  | All
[36 +margin] |  | ≥[24] | 60 | ≥4
[16+margin] |  | ≥[64] |  | All
[8 +margin] |  | ≥[132] |  | All
Note 1: Margin value is FFS |  |  |  | 
Accuracy, Tc | Es/Iot, dB | PRS BW, PRB | PRS SCS, kHz | Repetition factor (
[137+margin] | -3 | ≥[24] | 15 | ≥4
[96+margin] |  | ≥[52] |  | All
[62 +margin] |  | >[104] |  | All
[87+margin] |  | ≥[24] | 30 | ≥4
[68 +margin] |  | ≥[48] |  | All
[44 +margin] |  | ≥[132] |  | All
[59 +margin] |  | ≥[24] | 60 | ≥4
[42 +margin] |  | ≥[64] |  | All
[36 +margin] |  | ≥[132] |  | 
[180+margin] | -13 | ≥[24] | 15 | ≥4
[98+margin] |  | ≥[52] |  | All
[68 +margin] |  | >[104] |  | All
[87+margin] |  | ≥[24] | 30 | ≥4
[85 +margin] |  | ≥[48] |  | All
[44 +margin] |  | ≥[132] |  | All
[139 +margin] |  | ≥[24] | 60 | ≥4
[46 +margin] |  | ≥[64] |  | All
[30 +margin] |  |  |  | 
Note 1: Margin value is FFS Note 2: The requirements above are based on the simulation results under the TDL-A [TS38.101-4] |  |  |  | 
Accuracy, Tc | Es/Iot, dB | PRS BW, PRB | PRS SCS, kHz | 
[137+margin] | -3 | ≥[24] | 15 | ≥4
[96+margin] |  | ≥[52] |  | All
[62 +margin] |  | >[104] |  | All
[87+margin] |  | ≥[24] | 30 | ≥4
[68 +margin] |  | ≥[48] |  | All
[44 +margin] |  | ≥[132] |  | All
[59 +margin] |  | ≥[24] | 60 | ≥4
[42 +margin] |  | ≥[64] |  | All
[36 +margin] |  | ≥[132] |  | 
[180+margin] | -13 | ≥[24] | 15 | ≥4
[98+margin] |  | ≥[52] |  | All
[68 +margin] |  | >[104] |  | All
[87+margin] |  | ≥[24] | 30 | ≥4
[85 +margin] |  | ≥[48] |  | All
[44 +margin] |  | ≥[132] |  | All
[139 +margin] |  | ≥[24] | 60 | ≥4
[46 +margin] |  | ≥[64] |  | All
[30 +margin] |  |  |  | 
Note 1: Margin value is FFS Note 2: The requirements above are based on the simulation results under the TDL-A [TS38.101-4] |  |  |  | 
Table 1-2: UE Rx-Tx accuracy for fading channel in FR1

## Slide 9: Test case design principles(1)
Processing time for the assistance data and measurement request
  Starting point of T2 (measurement period) in the tests should be the first MG occasion with PRS after n+T, where n is the last PDSCH for the LPP messages including the assistance data and measurement request, and T=50ms
Update the PRS RMC to introduce PRS configurations with two PRS resources per resource set
Simplify the test procedure by using 2 time periods in the tests:
  T1: UE receives assistance data and measurement request
  T2: UE performs the measurement