## Slide 1: Title: Transmitter performance for pi/2 BPSK with spectral shaping
Source: Nokia, Nokia Shanghai Bell
Agenda item: 7.4.2
Document for: Discussion
3GPP TSG-RAN WG4#101bis-e Meeting R4-2200727
Electronic Meeting, 17st –25th January, 2022

## Slide 2: 1- Introduction
This contribution relates to a study item agreed in RAN#91-e, and revised in RAN#94e, namely “Revised SID: optimizations of pi/2 BPSK uplink power in NR” [1]. In this paper we study the transmitter performance with different shaping filters. This work is related to the following study item objective:
Identify shaping filter characteristics necessary to enable the new power capability while ensuring good and robust BS receiver performance.
  The choice of the filter is up to UE implementations and transparent to network.
  Evaluate possible filter requirement applicable to the identified new UE power capability if achievable
  Identify if necessary, changes are needed to EVM equalizer flatness mask requirements to capture necessary filter shaping. Changes to the existing 14 dB p-p baseline to be assessed in relation to any potential gains in UL link performance while still ensuring robust BS receiver performance for all UEs in a cell.

## Slide 3: 2- Discussion
According to the agreed way forward after RAN4#99e [2], different filters that conform to 38.101-1 Rel-16 are tested to study the transmitter performance. In this document, three different 3-tap filters (namely [-0.2 1 -0.2], [-0.28 1 -0.28] and [-0.335 1 -0.335]) are tested, as well as two triangular windows with different design parameters. For the filters mentioned, the DMRS are also shaped, following the assumption in the current specification that the spectral shaping is transparent to the gNB receiver, agreed in the way forward in RAN4#101e [3].
Additionally, the [1+D] filter is included in the evaluations with two different configurations, in one, the DMRS are shaped (as the rest of the filters) and in another, the DMRS are not shaped.
Table 1 shows the simulation parameters.
Following the agreed way forward after RAN4#100e [3], PC2 is addressed in the evaluations.
Parameter | Value
Pulse shaping filter | Filter configuration conforms to 38.101-1 Rel-16
Waveform | DFTS OFDM with pi/2 BPSK with Rel-16 DMRS
PRB/LCRB | Full sweep of all possible combinations of RB starting locations and RB lengths
# of DMRS symbols/slot | 2
# of data symbols/slot | 12
BW | [10, 15, 20, 30, 40, 50, 60, 80, 90, 100] MHz
SCS | 30 kHz
Table 1: Simulation parameters

## Slide 4: 2- Discussion
The figure shows the tested filters. The triangular filters are generated in such a way that the slope is the maximum slope that fits the maximum attenuation in the two frequency ranges that separate one half of the allocation (same frequency ranges as the EVM equalizer flatness mask). For the evaluations, the number in brackets corresponds to the attenuation (in dB) of the first and second frequency range.
In the continuation, the filters are referred as:
[-0.2 1 -0.2]  0.2
[-0.28 1 -0.28]  0.28
[-0.335 1 -0.335]  0.335
[1+D]  [1+D]
Triangular window [6 14]  Triang A
Triangular window [6 8]  Triang B
0.335 is the most aggressive 3-tap filter that meets the current spectral flatness requirements, less aggressive 3-tap filters are included too.
Triang A is the most aggressive triangular window that meets the current spectral flatness requirements, and Triang B is a less aggressive triangular window, with frequency shape quite similar as the 0.2 3-tap filter.

## Slide 5: 2.1- Discussion. Best filters per channel bandwidth.
The following slides show the best filter per channel BW and transmission configuration. The criteria followed is to select the filter that offers the lowest MPR, and in case there are more than one filter with the same lowest MPR, the one with the lowest EVM is chosen.

## Slide 6: 2.1- Discussion. Best filters per channel bandwidth.
10 MHz: For central and small-medium size transmission, 0.2 and Triang B (less aggressive filters) offer best performance. For edge transmission, 0.335 and 0.28 (more aggressive than Triang B and 0.2) are best. For the small allocations, less aggressive filters perform better.
15 MHz: Central and small-medium allocations, 0.2 and Triang B are best. For edge and medium-large allocations, small difference between 0.335, 0.28.

## Slide 7: 2.1- Discussion. Best filters per channel bandwidth.
20 MHz: Small and medium allocations, less aggressive filters perform better (0.2 and Triang B). For larger (and edge) allocations, more aggressive filters (0.28, 0.335 and Triang A). [1+D] is barely ever the best filter.
30 MHz: Small and medium allocations, less aggressive filters perform better (0.2 and Triang B). For larger allocations, closer to the edge, 0.335 is best, and 0.28 for allocations further from the edge.

## Slide 8: 2.1- Discussion. Best filters per channel bandwidth
40 MHz: For small and central allocations, 0.2 and Triang B are the best. For 1 PRB allocation, closer to the edges, [1+D] is the best. Again, for larger allocations, and edge allocations, more aggressive filters perform better.
50 MHz: For small and central allocations, 0.2 and Triang B are the best. Again, for larger allocations, and edge allocations, more aggressive filters perform better.

## Slide 9: 2.1- Discussion. Best filters per channel bandwidth
60 MHz: For small and central allocations, 0.2 and Triang B are the best. For 1 PRB allocation, closer to the edges, 0.335 is the best. Again, for larger allocations, and edge allocations, more aggressive filters perform better.
80 MHz: For small and central allocations, 0.2 and Triang B are the best. Again, for larger allocations, and edge allocations, more aggressive filters perform better.

## Slide 10: 2.1- Discussion. Best filters per channel bandwidth
90 MHz: For small and central allocations, Triang B and 0.2 are the best. Again, for larger allocations, and edge allocations, more aggressive filters perform better.
100 MHz: For small and central allocations, 0.2 and Triang B are the best. Again, for larger allocations, and edge allocations, more aggressive filters perform better. For closer to the edge allocations, 0.335 is the best, then 0.28 and Triang A are better for large allocations not next to the edge of the channel.

## Slide 11: 2.1- Discussion. Best filters per channel bandwidth
Observation 1: There is not a single solution for all the evaluated cases. Depending on the allocation configuration, different filters (i.e., more or less aggressive) perform differently.
Observation 2: For smaller allocations (e.g., ≤ 16 PRB), less aggressive filters show the best performance in terms of output power.

## Slide 12: 3- Conclusion
Observation 1: There is not a single solution for all the evaluated cases. Depending on the allocation configuration, different filters (i.e., more or less aggressive) perform differently.
Observation 2: For smaller allocations (e.g., ≤ 16 PRB), less aggressive filters show the best performance in terms of output power.

## Slide 13: References
[1] RP-210910, Optimizations of pi/2 BPSK uplink power in NR, Moderator (Huawei)
[2] R4-2108018, WF on Waveform configuration, parameters for link simulations and agreements, Qualcomm
[3] R4-2120057, WF on Optimisations of Pi/2 BPSK UL Power in NR, Huawei, HiSilicon, Qualcomm, Intel