## Slide 1: Resolving the Scell dropping using power limits on serving cells for FR1 and FR2 Background to the method and test aspects
Attachment to R4-2200853
Ericsson
3GPP TSG-RAN WG4 Meeting #101-bis-e
Electronic meeting, 17 – 25 January 2022
R4-2200853

## Slide 2: Background to the proposed solution
For any CA band combination, the UE configures
  a maximum output power PCMAX,f,c for each serving cell c of the configuration
  a maximum output power PCMAX for the total power of the configuration
When PCMAX is exceeded, the UE prioritizes transmissions according to rules in clause 7.5 of 38.213
Configure in RRC UE-specific relative limits DPCMAX,f,c on PCMAX,f,c on one or more serving cells c in the uplink configuration
  the PCMAX unchanged
These limits can be modified/enabled/disabled by MAC-CE for fast adaptation
The relative limits apply for concurrent UL transmissions
  if only transmission scheduled on one cell this would get all available power up to PCMAX

## Slide 3: No limits: dropping or scaling Scells, UE power limited
PCell
PUSCH
Scell
PUSCH
BW
BW
f
PCMAX
Total power back-off ≤ MPR
UE output power (PSD)
Ppower class
Reduced or dropped
PCMAX,f,c
PPUSCH,f,Pcell
PPUSCH,f,SCell
The intra-band case shown, the actual power back-off is not known to the gNB and for FR2 the plane of reference – and hence also the absolute level – of PCMAX is not known

## Slide 4: Limit on Pcell and the Scell scaled, UE power limited
PCell
PUSCH
Scell
PUSCH
BW
BW
f
PCMAX
Total power back-off ≤ MPR
UE output power (PSD)
DPCMAX,f,PCell
PPUSCH,f,PCell = PCMAX,f,Pcell (reduced)
Ppower class
PPUSCH,f,SCell
PCMAX,f,SCell
The limit is relative to the PCMAX configured by the UE (the actual value used not known to the gNB)
But the UE may still drop the Scell (no restriction in 38.213) instead of scaling the Scell power

## Slide 5: Limit on both cells, dropping will not occur
PCell
PUSCH
Scell
PUSCH
BW
BW
f
PCMAX
Total power back-off ≤ MPR
UE output power (PSD)
DPCMAX,f,Pcell = DPCMAX,f,Scell = 3 dB
Ppower class
The actual UE back-off can be any value, both cells are still 3 dB below, works for both FR1 and FR2

## Slide 6: If only one cell scheduled, limits do not apply
PCell
PUSCH
BW
BW
f
PCMAX
Total power back-off ≤ MPR
UE output power (PSD)
DPCMAX,f,Pcell = DPCMAX,f,Scell = 3 dB
Ppower class
No other transmission overlapping a slot of a scheduled transmission
Reduces the need for enabling/disabling limits by MAC-CE signaling

## Slide 7: Setting the power limits
For intra-band combinations of carriers with different channel bandwidths, constant PSD for full allocation at max power, e.g.
  DPCMAX,f,c = -10log10{1, 7/8, 5/6, 4/5, 3/4, 2/3, 1/2, 1/3, 1/4, 1/5, 1/6, 1/8, ...} =
  = {0, 0.6, 1.1, 1.3, 1.8, 3.1, 4.8, 6.1, 7.0, 9.1...} dB
  Specified in dB with an accuracy making sure the linear value is not exceeded
Examples for intra-band UL CA
  100 + 100 MHz, DPCMAX,f,c = {3.1,3.1} dB
  10 + 20 MHz, DPCMAX,f,c = {4.8,1.8} dB
For some bandwidth combinations the granularity of DPCMAX,f,c not small enough, but adequate
  50 + 100 + 200 MHz, DPCMAX,f,c = {1/8, 1/4, 1/2} (linear) but ”almost” equal PSD, within 0.5 dB
The above relative limits can also be used for inter-band combinations
Equal PSD for all PRB allocation sizes cannot be guaranteed by the limits – the PCMAX,f,c governs the total power per serving cell – but dropping will not occur
  Equal PSD is not the case in the field even for intra-band contiguous CA with colocation
  Smaller PRB allocations can still be operated with a higher/different PSD with limits configured

## Slide 8: Summary of the method
The solution feasible for both FR1 and at least for intra-band FR2
  Inter-band within FR2 not yet finalized
No RAN1 impact, only PCMAX,f,c per cell affected
  The priority mechanisms in 38.213 not affected, the UE power per cell is limited by PCMAX,f,c for any transmission regardless of its priority
Solves the ”equal PSD” issue in RAN5
Can also be used for setting UE-specific absolute limits on cells
...and can also be used in the field

## Slide 9: Test and verification

## Slide 10: Verifying the limits: per cell
For each serving cell c
  Limits are modified (verify that maximum is not exceeded, FR1 only),
  and verified that the Pcmax,f,c is actully decreased as measured at antenna port Pumax,f,c
  and can be further verified by checking the PHR (Pcmax,f,c is reported and the change recorded)
DPcmax,f,c can also be used for setting UE-specific absolute limits on cells (FR1 only), then only limits modified
Not for FR1 if DPcmax,f,c used for setting UE-specific absolute limits on cells. Always tested for FR2 (no absolute limits)

## Slide 11: Measuring the total power Pumax (e.g. CA MPR)
If limits on serving cells are such that the total power PCMAX can not attained, then DPUMAX > 0 dB and the lower limit of the measured power PUMAX is relaxed by DPUMAX
If e.g. DPCMAX,f,c = 3.1 dB on two cells (power split), then DPUMAX = 0 dB
PCMAX (total configured power) is not changed by any limits

## Slide 12: Verifying that dropping does not occur
When DPCMAX,f,c > 0 dB is configured then the measured power of the serving cell c should be decreased
Last but not least: verify that dropping does not occur, for two cells of equal bandwidth and DPCMAX,f,c = 3.1 dB (DPUMAX = 0 dB), then the PUMAX requirement shall be met with both cells transmitted
Example for FR2: