## Slide 1: 3GPP TSG-RAN WG4 Meeting #101-e R4-2120636 Electronic Meeting, November. 1 – 12, 2021
CATT…
WF on WF on sweep time for unwanted emission testing

## Slide 2: Background
The sweep time for unwanted emission test is discussed based on the inputs [1-3].
For unwanted emission testing, true RMS detection mode of measurement device is defined. While the sweep time for true RMS is not clarified in current specification. For NR/LTE system using OFDM waveform which has high PAPR, the sweep time will impact the measurements results significantly. When the sweep time is too short, the result is more like the peak value rather than an average value. Lacking of clarification on minimum reasonable sweep time for unwanted emission test might cause in appropriate test setting and error results.
During the discussion, majority of the involved equipment vendors were supportive to do such clarification or have further discussion [4]. There were requests from TE vendors to further study the appropriate sweep time and the impact on test equipment and test methodology.

## Slide 3: Way Forward
Companies are invited to analyze the appropriate time to get a stable test results for unwanted emissions. E.g. The following options should be consdiered as starting point,
  Option 1: The sweep time for a sample is an OFDM symbol
  Option 2: The Sweep time for a sample is [X]% of an OFDM symbol
  Option 3: the sweep time for a sample is a fix value of [TBD] irrespective of the OFDM length
  Option 4: Keep current text in BS conformance test specification
  Option 5: Other method is not precluded
TE vendors are invited to analyze the impact on test equipment and test methdology.

## Slide 4: Reference
R4-2117395, Discussion on sweep time for unwanted emission testing, CATT, RAN4#101-e
R4-2117396, Draft CR for TS 38.141-1: On sweep time for unwanted emission testing (Rel-15), CATT, RAN4#101-e
R4-2117399, draft CR for TS 38.141-2 On sweep time for unwanted emission testing (Rel-15), CATT, RAN4#101-e
R4-2120598, Email discussion summary for [101-e][302] NR_Conformance_Maintenance, Moderator (Huawei), RAN4#101-e