## Slide 1: 3GPP TSG-RAN WG4 Meeting #101-e R4-2120674 Electronic Meeting, November. 1 – 12, 2021
CATT…
WF on Tx RF requirements for satellite access node

## Slide 2: Background
The RF requirements for satellite access node was discussion based on the inputs in [1-4]. This contribution will capture the agreements from the moderator summary and GTW session [5] for Tx part.

## Slide 3: Reference point
It was agreed to replace “SATELLITE NODE” with “satellite access node” in the box and use the figure for RF requirement development.

## Slide 4: Tx requirements for satellite access node
Base station output power
  The power limitation on “satellite access node” is manufacture declaration basis, no limitation in RAN4 specification.
  Some background information from regulatory can be included in the TR for information.
RE power dynamic range
  The same requirement will be reused from TN.
Total power dynamic range
  The current total power dynamic range requirement can be reused.
  If the co-existence simulations indicate that there is no need to change the ACLR, SU can be reused from NR.
Frequency error
  The current requirement for WA BS can be reused, i.e. 0.05ppm.
Modulation quality (EVM)
  The current requirement can be reused for QPSK, 16 QAM in FR1.
  256QAM is not supported by Satellite Access node in Rel-17.
  FFS for 64QAM
Time alignment error
  CA is confirmed to be out of Rel-17 NTN WI scope for RAN4 requirements
  The baseline assumption: MIMO TAE requirement is not applicable pending further checking till Jan 2022 RAN4 meeting

## Slide 5: Tx requirement for satellite access node
ACLR
  Wait the conclusion from co-existence simulation.
Transmitter spurious emissions
  Specify satellite access node’ spurious emissions based on ERC 74-01 Space stations’ limits, i.e. ITU Radio Regulations Annex 3.
Protection of the own BS receiver
  Specify the requirement as initial assumption
Protection of the BS receiver of different BS
  This requirement not needed
Co-location with other BS
  This requirement is not needed since there is no co-location scenario foreseen for satellite.
Transmitter intermodulation
  This requirement is not needed since there is no nearby interfering signal reaching the transmitter unit via the antenna, RDN and antenna array.
Transmitter requirement for NTN BS type 1-O
  Companies are encouraged to input in this area in the next RAN4 meeting.

## Slide 6: Reference
R4-2119556, On the Variation of NTN ACLR and NTN ACS Parameters, Thales, RAN4#101-e
R4-2117381, Further discussion on Tx requirements for NTN BS, CATT, RAN4#101-e
R4-2118160, NTN - Satellite Node - Tx requirements, Ericsson, RAN4#101-e
R4-2119205, Discussion on Tx requirements of satellite gNB, ZTE, RAN4#101-e
R4-2120742, Email discussion summary for [101-e][311] NTN_Solutions_Part3, Moderator (CATT), RAN4#101-e