## Slide 1: Motivation for supporting non-colocated scenarios for band 42 and n77/n78
SoftBank
3GPP TSG RAN WG4 Meeting #101-e
Electronic Meeting, November 1 - 12, 2021
Agenda Item: 12.2.3
Document for: Discussion
R4-2117306

## Slide 2: Background – Spectrum point of view
Co-existence with other systems
Timing of Spectrum allocation
  The 3 blocks in C-band were allocated at different time
   This makes Tx antenna colocation cost-inefficient (or sometimes infeasible)
SoftBank
X
X
Y
SoftBank
3400
3440
3480
3520
3560
3600
X
Y
Z
SoftBank
Y
3600
3700
3900
3800
4000
Satellite Systems
Different co-existence conditions apply.
 As a result, Tx antenna co-location is not always available
1st allocation
2nd allocation
3rd allocation

## Slide 3: Background – 3GPP point of view
3GPP standards
  Rules for “intra-band” apply to EN-DC 42_n77
  TS38.133 cls. 7.6.3 defines MRTD limit for intra-band EN-DC (=3us)
  Power imbalance limit has been discussed in Rel-16
    One candidate value is 6dB
  It was decided in RAN#92e not to specify MRTD and MTTD requirements in Rel-16 and Rel-17 due to RAN4 overload
  The discussion on Type-2 UE for EN-DC is still ongoing
    The target power imbalance value will be specified, while no discussion on MRTD and MTTD was held so far
    No discussion on NR-CA as well
    The behavior for Type-1 UE (normal UE) will be left as “undefined” anyway
   These limitations reduce the availability of EN-DC in our network

## Slide 4: Scenario and target value for new perf. Req.
Conditions bw. eNB and gNB
Very short Rx time difference(3us)
Power imbalance (6dB)
Rel-16
eNB
gNB
Deployment scenario
Colocated
Different antenna pattern
Our Proposal
eNB
gNB
Conditions bw. eNB and gNB
Short Rx time difference([TBD]us)
Power imbalance ([TBD]dB)
More discussion is necessary to determine the target values
Deployment scenario
Non-colocated (at maximum 3 Tx points)
Different antenna pattern
Our goal: Define UE performance requirements for intra-band EN-DC and NR-CA for non-colocated scenarios

## Slide 5: Proposals
Given the continuous overload situation in RAN4, it is not expected to have a surprising progress on this matter
Therefore, it is proposed to approve a follow-up RAN4 WI in Rel-18 to complete the work on intra-band non-contiguous scenario
  The potential scope of the WI is given in the next slide

## Slide 6: Proposals
Potential scope of the new WI to support non-colocated scenario for intra-band non-contiguous EN-DC/NR-CA
  Demod part
Support of non-co-located scenario for FR1 intra-band non-contiguous EN-DC/NR-CA
RRM part
  Study and, if feasible, define requirements for UE other than FG 2-19 Type 2 operation in non-co-located deployment for FR1 intra-band non-contiguous NR-CA/EN-DC
    Study the following aspects
      Feasibility of UE RF architecture to support both DL and UL operation
      Feasible value of the power imbalance
      Feasible value of MRTD and MTTD in non-collocated deployment.
    Define MRTD and MTTD requirements
      Note: MTTD requirements are subject to the decision whether UL Tx is needed for both (or all) carriers
  Define requirements applicable to UEs capable of FG 2-19 Type 2
    First investigate the applicable MRTD and power imbalance level, considering the network deployment scenario and UE implementation feasibility.
      Specify MRTD Requirements for FR1 intra-band non-contiguous EN-DC applied for non-co-located scenario (including power imbalance limitation)
      Specify MRTD Requirements for FR1 intra-band non-contiguous NR-CA applied for non-co-located scenario (including power imbalance limitation)
Demod part
  Define PDSCH Requirements for non-colocated scenario for intra-band non-contiguous EN-DC and NR-CA
    Define PDSCH demodulation performance requirement based on the applicable MRTD and power imbalance values.
      Power imbalance between the carriers is limited to [X]dB
    [Work is limited to CA/EN-DC for EN-DC/NR-CA for bands 42, n77/n78]

## Slide 7: EOF