## Slide 1: Motivation on the support of CRS-IM for Redcap UE
3GPP TSG RAN WG Meeting #102-e
Electronic Meeting, Feb 21 - Mar 3, 2022
Agenda Item: 14.2
Document for: Discussion
R4-2205486

## Slide 2: Backgroud
For Rel-17 CRS-IM was well investigated to handle LTE CRS interfering in addition to RAN1 led Rate Matching scheme, however the evaluation scenarios mainly focus on antenna configuration 4x2 or 4x4 which is basically targeted for normal UE.
However for Redcap UE introduced in Rel-17, its receiver number could be relaxaed to be 1Rx for Low band and 2Rx or 1Rx for FR1 high band to reduce the cost.
in Rel-15, RAN4 defined the performance requirement of CRS-IM for LTE Single RX Chain UEs.

## Slide 3: Proposal
We propose to define CRS-IM Performance Requirements for Redcap UE with single receiver in Rel-17 to ensure that Redcap UE could have the same capability to handle LTE CRS interference similar as normal NR UE.
If there is no time for Rel-17 Redcap UE demod to support the CRS-IM, then it should be included in Rel-18 Demod package.

## Slide 4: Performance for CRS-IM on Redcap UE with single Rx
Based on the simulation results in slide #5 and #6, [1 dB ~ 1.8 dB] performance gain can achieved by , using the parameters agreed in Rel-17.
2 cases are simulated:
  4Tx 1Rx, MCS4 for target PDSCH
  4Tx 1Rx, MCS13 for target PDSCH

## Slide 5: Simulation results-Scenario 1
Reference (No CRS-IM) | CRS-IM LLR weighting
5.7dB | 3.9dB
  Required SNR (dB) at 70% max TP
Reference (No CRS-IM) | CRS-IM LLR weighting
15.8dB | 14.8dB
  Required SNR (dB) at 70% max TP

## Slide 6: Simulation results-Scenario 2
Reference (No CRS-IM) | CRS-IM LLR weighting
5.7dB | 4.3dB
  Required SNR (dB) at 70% max TP
Reference (No CRS-IM) | CRS-IM LLR weighting
17.8dB | 16.3dB
  Required SNR (dB) at 70% max TP

## Slide 7: Simulation assumptions
Simulation assumptions | Configurations
BW_servCell | 10MHz
SCS_servCell | 15kHz
Duplex_servCell | FDD
Antenna_servCell | 4T1R
number of HARQ | 4
servCell RI | 1
Mapping type | type A mapping
S* | If Rel-15 or Rel-16 Rate Matching pattern is configured: S = 3, else S =2
L* | For scenario 1: 9For scenario 2: L=9, [11] if RM is configured, 12 otherwise.
PRB bundle size | 2
PRB bundle type | static
precoding model | random
overhead for TBS | 18
DMRS | type1
number of additional DMRS | 1
nr of DMRS CDM group | 1
LTE CRS | vshift=0
SSB | slot 0 in every 20ms
MCS | 4,13

## Slide 8: Thank you