## Slide 1: R4-2210579 WF on carrierBandwidth in SIB1
Moderator (Ericsson)

## Slide 2: Issue 2-1: Configuration of CBW in SIB1 behaviour
The listed observations are not mutual exclusive. Please comment on each observation point listed below. If you do not agree with the observation point, please indicate the detail in which the observation cannot be agreeable. If there is a common understanding, then it shall be captured in a revised TP during second round.
Observation 1: the carrier bandwidth indicated by SIB1 is cell-specific UE channel bandwidth instead of BS channel bandwidth. It is ok to re-configure a UE-specific channel bandwidth wider than the one indicated in SIB1
Observation 2: The latest TR 38.844 clause 6.1.2.2 already allows a method to configure larger UE specific carrier bandwidth larger than the one in SIB1
Observation 3: The carrierBandwidth in SIB1 must correspond to the maximum transmission bandwidth configuration NRB defined in TS 38.101 so that UE can map it unambiguously to a regular UE channel bandwidth.
Observation 4: The channel bandwidth value indicated in dedicated signaling must correspond to the maximum transmission bandwidth configuration NRB defined in TS 38.101 so that UE can map it unambiguously to a regular UE channel bandwidth.
Observation 5: The uplink carrier bandwidth in SIB1 shall not exceed the irregular channel bandwidth to maintain the UE unwanted emissions, unless it is guaranteed by 3GPP spec that UE uses a channel filter based on initial BWP bandwidth.
Observation 6: Provided that the SIB1 carrier bandwidth for uplink does not exceed the irregular channel bandwidth, a risk of violating regulatory requirement in UE unwanted emissions can be avoided.
This WF is captured company views and understanding on Observation 3 and 4; with the guidance on how to proceed for next meeting.

## Slide 3: Companies in support of observations below
Any number of RBs can be indicated in carrierBandwidth in SIB1, there is no restrictions (Huawei, Intel, Ericsson, ZTE)
  The original idea of the design was to allow any number of RBs, however, if this is done then there is some ambiguity on the UE side on which channel BW to use. The channel BW that UE has to use needs to be unambiguous so that UE can meet RF requirements (Qualcomm)
  It’s unclear how devices would behave in practice if number of RBs signaled in carrierBandwidth SIB1 is undefined in 38.101 (China Telecom, Apple)
  UE capability might be required (TMUS)
Initial BWP is equal to or smaller than regular channel bandwidth confined in carrierBandwidth in SIB1 (Nokia)
UE specific channel bandwidth signaling only defined CBW can be configured (China Telecom, MediaTek, Ericsson)
UE-specific channel bandwidth: UE can map maximum transmission bandwidth configuration NRB defined in TS 38.101 unambiguously to a regular UE channel bandwidth (Ericsson, China Telecom, Nokia, ZTE, TMUS)

## Slide 4: Way Forward
The following are agreed:
carrierBandwidth in SIB1 has no restrictions
  less than 275 PRB
servingCellConfig is used to determine channel bandwidth (MHz) and location determination
  Location is determined with existing Rel-15 RRC specification
Notes: ZTE: for the first main bullet, does it mean it can be set to any values in terms of RPB. If that is the case it is not aligned with the spec.
Qualcomm: same question. RAN2 clearly say the bandwidth advertised by network should have the values specified in RAn1.
Apple: same as Qualcomm.
Ericsson: where exactly the grid size of resource is restricted to channel bandwidth in the specification? The carrier bandwidth can take any bandwidth. That is how UE locates its bandwidth. Bandwidth part in SIB 1 can take any value.
Huawei: We share the similar view as Ericsson. There is no restriction. We actually define the requirements based on channel bandwidth. The dedicated channel bandwidth should be the bandwidth defined in RAN4 spec. We try to avoid the case that we define CBW but it cannot be used.
Qualcomm: network can configure the channel bandwidth that corresponds the bandwidth to 38.101-x and 38.104. There is some discussion brought up by CMCC in maintenance email thread.
Nokia: our understanding is the same as Ericsson and Huawei. We should not restrict SIB1 to be the same as RAN4 defined NRB.
CMCC: for carrier bandwidth in SIB1, there is no restriction in RAN2. It can be any number of RB. Our proposal is for the dedicated channel bandwidth.
Ericsson: The carrier resource grid size advertised in SIB 1 should not be confused with UE dedicated bandwidth.
ZTE: we can confirm it to RAN2 to confirm SIB1 spec. There should be restricit.
Qualcomm: it should be sub-set of RAN4 defined rather any arbitrual value.
Ericsson: it is correct that UE uses the common information for configuration.
CTC:
Apple: There is not requirement for network to generate the dedicated channel bandwidth for UE. We do have to ensure the common bandwidth should be set of RAN4 specified channel bandwidth.
Ericsson: In certain deployment, you have to configure this field to let UE know where to locate the channel bandwidth.
CMCC: there is exact IE for carrierbandwidth. If we are talking about the carrierBandwidth in SIB1, there is no restriction.
T-Mobile: In RAN4 spec, any RB can be configured. ChannelBandwidth in SIB1 is more relevant.