## Slide 1: Motivation on basket WID on 4Rx and 8Rx support for NR FR1 bands in Rel-18
3GPP TSG-RAN WG4 Meeting # 103-e R4-2208718
Electronic Meeting, May. 9-May. 20, 2022
Source: ZTE Corporation
Agenda Item: 15

## Slide 2: Backgroud
The 4Rx requirements have been introduced for some FR1 bands for different form factors in the past. The purpose by introducing the 4Rx support for some bands is to provide higher throughput and better coverage.
A new WID [1] on 4Rx support for NR band n8 was approved, with the same consideration of 600MHz (n71) and 700MHz band (n28), i.e. 4 Rx operation is targeted for FWA form factor.
Currently, there were several NR bands already supported 4Rx. However, there were some other bands not supporting 4Rx.
In addition to 4Rx support, 8Rx support was also mentioned in some contributions in Rel-18 RAN4 package approval such as [2] [3] [4].
Reference:
[1] RP-213659, New WID: 4Rx support for NR band n8, CHTTL
[2] RP-213064, Motivation on defining 8Rx performance requirements for NR, SoftBank Corp.
[3] RP-213433, New WID on RF requirements enhancement for NR frequency range 1 (FR1), Huawei
[4] RP-212140, RAN4 projects proposals for Rel-18, Qualcomm Incorporated

## Slide 3: 4Rx
More bands may be requested by operators to support 4Rx in Rel-18, by using the current approach, individual WIDs will be needed for different bands, which is not an efficient way for RAN4 WIDs management. Therefore, it is proposed to create a basket WID to include all possible bands requested by operators to support 4Rx in Rel-18.
RF aspect:
  REFSEN requirements: only ΔRIB,4R value should be defined for the bands supporting 4Rx with the specific form factor
Performance aspect:
  Release independence in TS38.307 is needed to be updated
CA or MRDC combination updates
  MSD requirements for NR inter-band CA or MRDC band combination that consist of the band(s) support 4Rx should be updated

## Slide 4: 8Rx
Although the proposed WID including the objectives of 8Rx is still open, the suitations could be foreseen to be the same as 4Rx, in which individual WIDs may be needed if more bands are requested by operators to support 8Rx in future.
Comparing with 4Rx, many more benefits can be achieved for 8Rx. For example, it can further enhance the coverage for the users located at the cell edge. Also, it can significantly improve the downlink throughput for a single user.
For the RF requirement work, it could be foreseen that there would be limited impacts on the RF requirements when introducing 8Rx feature.
For a UE supporting 8Rx, different form factors are foreseen for different bands. The bands supporting 8Rx can be added to RAN4 specification if operators have the demands. Therefore, it is also feasible to use a basket WID to include all possible bands requested by operators to supprot 8Rx in Rel-18.
Considering the discussion on the 8Rx feature is still underway, the basket WID work will be started after all of the RF requirements of 8Rx are finished.

## Slide 5: Proposal
Create a basket WID to include all possible bands requested by operators to support both 4Rx and 8Rx in Rel-18.
  Note: The basket WID work for 8Rx will be started after all of the RF requirements for 8Rx are finished.

## Slide 6: Thank you