3GPP TSG-RAN WG4 Meeting #104-e	R4-2214459

Electronic Meeting, 15– 26 August 2022

Title: 	WF on co-existence evaluation for ATG

Agenda Item:	11.12.5

Source: 	Huawei, HiSilicon

Document for:	Approval

# Background

In RAN#95e meeting, a new work item [1] on Air-to-ground network for NR was established. In this RAN4 meeting, companies provided a lot of contributions [2~9] to discuss the co-existence study for ATG. In this way forward, we’d like to collect the outcome based on the 1st round discussion.

# General issues

<Way forward 1>: The following assumption can be acceptable.

- “The ATG network should be distinguished from TN network to enable/disable specific type of UE access”

<Way forward 2>: Discuss whether ATG BS can be co-located with TN BS

- Proposal: that the scenario of ATG BS non-co-located with TN BS is included. Whether the scenario of ATG BS co-located with synchronized TN BS should be included will be decided in the next meeting.

  - Note: working group can clarify if “the TN BS with ATG BS are synchronized then co-location” is a valid scenario.

<Way forward 3>: Clarify an assumption on the density of aircraft within the simulation area.

- Option 1: It’s assumed single UE per ATG BS as a starting point.

- Option 2: FFS

<Way forward 4>: How can RAN4 determine the ATG BS ISD and number of beams per BS?

- It’s encouraged to provide the ATG ISD evaluation based on both capacity and coverage.

<Way forward 5>: For commercial aircraft flight, what is the range of UE altitude?

- The following upper and lower boundary can be considered.

  - UE altitude (upper boundary): range: 10~15km

  - UE altitude (lower boundary): range: 3~7km

<Way forward 6>: Discuss whether to consider other scenarios with lower altitude and speed (in addition to commercial aircraft) when setting requirements, e.g. helicopters

- Only aircraft is considered in this WI.

# The outline for ATG co-existence study

<Way forward 7>: The following outline can be a starting point for ATG co-existence study.

- Co-existence simulation scenario

- Co-existence simulation assumption

  - Network layout model

    - Co-existence between ATG and NR terrestrial network

    - Co-existence between ATG and ATG (Moderator’s note: It depends on whether ATG co-existence with ATG will be simulated)

  - System parameters

    - ATG parameters

    - ATG UE parameters

    - TN BS and UE parameters

  - Antenna and beamforming pattern modelling

    - ATG BS antenna model

    - ATG UE antenna model

    - TN BS antenna model

    - TN UE antenna model

  - ACLR and ACS modelling

  - Propagation model

    - Propagation model between ATG BS and ATG UE

    - Propagation model between TN BS and TN UE

    - Propagation model between ATG BS and TN BS

    - Propagation model between ATG BS and TN UE

    - Propagation model between TN BS and ATG UE

    - Propagation model between TN UE and ATG UE

  - Transmission power control model

    - TN UL TPC

    - TN DL TPC

    - ATG UL TPC

    - ATG DL TPC

  - Received power model

  - Performance metric

  - Link level performance for NR ATG coexistence

- Co-existence simulation methodology

- Co-existence simulation results

<Way forward 8>: Is the co-existence scenario adjacent channel only or both adjacent channel and co-channel ?

- Only adjacent channel co-existence scenario is considered by RAN4.

# Co-existence simulation scenario

<Way forward 9>:

- The following scenarios can be assumed as starting point.

| No. | Combination | Aggressor | Victim | Simulation frequency | Notes | Study Phase |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | deployment scenario UL/DL | CBW duplex mode | deployment scenario UL/DL | CBW duplex mode |  |  |  |
| 1 | TN with ATG | ATG DL | 100MHz TDD | TN rural DL | 100MHz /TDD | 3.5 GHz |  | Phase 1 |
| 2 | TN with ATG | ATG UL | 100MHz TDD | TN rural UL | 100MHz TDD | 3.5GHz |  | Phase 1 |
| 3 | TN with ATG | TN rural DL | 100MHz TDD | ATG DL | 100MHz TDD | 3.5GHz |  | Phase 1 |
| 4 | TN with ATG | TN rural UL | 100MHz TDD | ATG UL | 100MHz TDD | 3.5GHz |  | Phase 1 |
| 5 | TN with ATG | ATG DL | 100MHz TDD | TN rural UL | 100MHz /TDD | 3.5GHz |  | FFS |
| 6 | TN with ATG | ATG UL | 100MHz TDD | TN rural DL | 100MHz TDD | 3.5GHz |  | FFS |
| 7 | TN with ATG | TN rural DL | 100MHz TDD | ATG UL | 100MHz TDD | 3.5GHz |  | FFS |
| 8 | TN with ATG | TN rural UL | 100MHz TDD | ATG DL | 100MHz TDD | 3.5GHz |  | FFS |
| 9 | TN with ATG | ATG DL | 20MHz FDD | TN rural DL | 20MHz FDD | 2 GHz |  | Phase 1 |
| 10 | TN with ATG | ATG UL | 20MHz FDD | TN rural UL | 20MHz FDD | 2 GHz |  | Phase 1 |
| 11 | TN with ATG | TN rural DL | 20MHz FDD | ATG DL | 20MHz FDD | 2 GHz |  | Phase 1 |
| 12 | TN with ATG | TN rural UL | 20MHz FDD | ATG UL | 20MHz FDD | 2 GHz |  | Phase 1 |
| 13 | TN with ATG | ATG UL | 20MHz FDD | TN rural DL | 20MHz TDD | 2 GHz | n1/n39 | FFS |
| 14 | TN with ATG | TN rural DL | 20MHz TDD | ATG UL | 20MHz FDD | 2 GHz | n39/n1 | FFS |
| 15 | ATG with ATG | ATG DL | 100/20M TDD/FDD | ATG DL | 100/20M TDD/FDD | 3.5/2 GHz |  | FFS |
| 16 | ATG with ATG | ATG UL | 100/20M TDD/FDD | ATG UL | 100/20M TDD/FDD | 3.5/2 GHz |  | FFS |

# Co-existence network layout

<Way forward 10>: Potential assumption for network layout of ATG.

- Option 1: ATG network can be deployed on the airline routes.

- Option 2: ATG network can be deployed in larger area

<Way forward 11>: The assumption for network layout of NR terrestrial network

- 19-sites 57 sectors with wrap-around can be assumed.

- FFS how to drop the TN cluster.

  - Option 1: drop TN clusters close to ATG BS

  - Option 2: Dropping clusters of TN cells randomly

<Way forward 12>: The assumption for network layout between ATG and ATG.

- Before addressing this issue, it’s better to conclude that the scenario (ATG to ATG) will be considered by working group firstly.

# Co-existence system parameters

<Way forward 13>:

- The initial system parameters outline for ATG BS is assumed as below.

| ATG BS altitude | FFS |
| --- | --- |
| Carrier frequency | 2GHz, 3.5GHz |
| Frequency reuse factor | 1 |
| Duplex mode | FDD@2GHz, TDD@3.5GHz |
| Channel bandwidth | 20MHz@2GHz, 100MHz@3.5GHz |
| Subcarrier spacing (SCS) | 15k@2GHz, 30k@3.5GHz |
| Number of cells | TBC |
| Environment1 | To be removed? |
| UE distribution | TBC |
| Indoor UE percentage | 0% |
| Number of DL active UEs per cell (NOTE 2) | FFS |
| Number of UL active UEs per cell (NOTE 2) | FFS |
| DL scheduled bandwidth per UE | FFS |
| UL scheduled bandwidth per UE | FFS |
| Traffic model | Full buffer |
| ATG BS maximum output power | FFS |
| ATG BS noise figure | 5dB |
| Handover margin | FFS |
| NOTE 1: ATG BS is assumed to serve UEs in the rural environment. NOTE 2: Same as the number of BS beam(s); NOTE 3: ATG BS max TX power is defined per polarization |

<Way forward 14>:

- The initial system parameters outline for ATG UE is assumed as below.

| ATG UE altitude | FFS based on outcome of WF 5 |
| --- | --- |
| Carrier frequency | 2, 3.5GHz |
| ATG UE max TX power in dBm | FFS |
| ATG UE min TX power in dBm | FFS |
| ATG UE noise figure | FFS |

<Way forward 15>:

- The initial system parameters outline for TN BS and TN UE is assumed as below.

| Parameters |  |  |  |
| --- | --- | --- | --- |
| Carrier frequency |  |  |  |
| Channel bandwidth |  |  |  |
| Scheduled channel bandwidth per UE (DL) |  |  |  |
| Scheduled channel bandwidth per UE (UL) |  |  |  |
| The number of active UE (DL) (Note 1) |  |  |  |
| The number of active UE (UL) (Note 1) |  |  |  |
| Traffic model |  |  |  |
| DL power control |  |  |  |
| UL power control |  |  |  |
| TN BS-UE min distance in meters |  |  |  |
| TN BS max TX power in dBm |  |  |  |
| TN UE max TX power in dBm |  |  |  |
| TN UE min TX power in dBm |  |  |  |
| TN BS Noise figure in dB |  |  |  |
| TN UE Noise figure in dB |  |  |  |
| Handover margin |  |  |  |
| Note 1 Same as the number of BS beam(s); Note 2: TN BS max TX power is defined per polarization |

# Antenna and beamforming pattern modelling

<Way forward 16>: Please discuss the initial Antenna and beamforming pattern modelling outline for ATG BS.

- Option 1: It’s listed as below

|  |  | ATG |
| --- | --- | --- |
| 1 | Base Station Antenna Characteristics |
| 1.1 | Antenna pattern |  |
| 1.2 | Element gain (dBi) (Note 2) |  |
| 1.3 | Horizontal/vertical 3 dB beam width of single element (degree) |  |
| 1.4 | Horizontal/vertical front-to-back ratio (dB) |  |
| 1.5 | Antenna polarization |  |
| 1.6 | Antenna array configuration (Row × Column) (Note 4) |  |
| 1.7 | Number of supported polarizations, P |  |
| 1.8 | Horizontal/Vertical radiating element spacing |  |
| 1.9 | Array Ohmic loss (dB) (Note 2) |  |
| 1.10 | Conducted power (before Ohmic loss) per antenna element (dBm) (Note 3) |  |
| 1.11 | Base station maximum coverage angle in the horizontal plane (degrees) |  |
| 1.12 | Base station vertical coverage range (degrees) (Note 1) |  |
| 1.13 | Mechanical uptilt (degrees) |  |

Note 1:	The vertical coverage range is given for the elevation angle θ, defined between 0° and 180° as 
in ITU-R M.2101.

Note 2:	The element gain in row 1.2 includes the loss given in row 1.9.

Note 3:	The conducted power per element assumes Row × Column ×Number of supported polarizations elements (i.e. power per H/V polarized element).

Note 4: Row × Column means there are Row vertical and Column horizontal radiating elements.

- Option 2: Date parameterized model in 38.803 section 5.2.3.2.4 should be used (apart from that the pre-set downtilt should be adjusted for ATG)

<Way forward 17>: Please discuss the initial Antenna and beamforming pattern modelling outline for ATG UE

- Option 1: Omni antenna assumption.

- Option 2: ATG UE has beam steering capability.

- Option 3: antenna mounted on the aircraft are directional without beam steering capability.

<Way forward 18>: Please discuss whether we need to consider both AAS BS and non-AAS BS

- Only consider AAS BS

<Way forward 19>: Please discuss the initial Antenna and beamforming pattern modelling outline for TN AAS BS.

- Option 1: It’s listed as below

|  |  | Rural/sub-urban….. |
| --- | --- | --- |
| 1 | Base Station Antenna Characteristics |
| 1.1 | Antenna pattern |  |
| 1.2 | Element gain (dBi) (Note 2) |  |
| 1.3 | Horizontal/vertical 3 dB beam width of single element (degree) |  |
| 1.4 | Horizontal/vertical front-to-back ratio (dB) |  |
| 1.5 | Antenna polarization |  |
| 1.6 | Antenna array configuration (Row × Column) (Note 4) |  |
| 1.7 | Number of supported polarizations, P |  |
| 1.8 | Horizontal/Vertical radiating element spacing |  |
| 1.9 | Array Ohmic loss (dB) (Note 2) |  |
| 1.10 | Conducted power (before Ohmic loss) per antenna element (dBm) (Note 3) |  |
| 1.11 | Base station maximum coverage angle in the horizontal plane (degrees) |  |
| 1.12 | Base station vertical coverage range (degrees) (Note 1) |  |
| 1.13 | Mechanical downtilt (degrees) |  |

Note 1:	The vertical coverage range is given for the elevation angle θ, defined between 0° and 180° as 
in ITU-R M.2101.

Note 2:	The element gain in row 1.2 includes the loss given in row 1.9.

Note 3:	The conducted power per element assumes Row × Column ×Number of supported polarizations elements (i.e. power per H/V polarized element).

Note 4: Row × Column means there are Row vertical and Column horizontal radiating elements.

- Option 2: The TN BS use the model of 38.803 section 5.2.3.2.4 using sub-arrays.

<Way forward 20>: Please discuss the initial Antenna and beamforming pattern modelling outline for TN UE

- The following assumption for TN UE antenna is agreeable.

| Characteristics | Handheld |
| --- | --- |
| Antenna type and configuration | (1, 1, 2) with omni-directional antenna element |
| Polarisation | Linear: +/-45°X-pol |
| Tx/Rx Antenna gain | 0 dBi per element |
| the number of Tx and Rx | 1T2R |

# Reference

[1] RP-220962, New WID: Air-to-ground network for NR, CMCC

[2] R4-2211916, General consideration on ATG, Apple

[3] R4-2212315, ATG simulation assumption, CMCC

[4] R4-2212383, Discussion on ATG FR1 co-existence evaluation for ATG network, LG Electronics UK

[5] R4-2212616, Discussion on scenarios and deployment assumptions for ATG, Ericsson

[6] R4-2213158, General discussion on coexistence scenario and assumption for ATG scenario, Huawei, HiSilicon

[7] R4-2213186, Coexistence scenarios of Air-to-ground network for NR, Qualcomm Incorporated

[8] R4-2213686, Discussion on coexistence evaluation for ATG network, ZTE Corporation

[9] R4-2211712, Discussion of the ATG co-existence simulation assumption, CATT